## Slide 1
VDatum
Vertical Datum Transformation Tool
Stephen A. White
(Program Manager)
January 11, 2018

## Slide 2: Outline:
Brief Datum Tutorial
VDatum Applications
Obtaining and Utilizing VDatum Software
Enhancements
Future Directions

## Slide 3
What Vertical Datum is My Data in?
GPS
RTK-GPS vertical referencing
Hydrographic Surveys
NOAA Bathymetry (MLLW)
USGS
Topography
Orthometric Datums
Tidal Datums
Ellipsoidal Datums
Lidar
?

## Slide 4
BUT there are a many different vertical datums in use around the nation
Ellipsoid Datums
Orthometric Datums
Tidal Datums
MHHW, MHW, MTL, DTL, LMSL, MLW, MLLW
NAVD 88, NGVD 29
ITRF,
WGS 84,
NAD 83 (NSRS)
```
For elevation data sets to be blended together they must be referenced to same vertical datum.
All elevation data is referenced to a vertical datum.

## Slide 5
Development and Use of VDatum
Mapping the Land-Sea Interface: VDatum converts elevation data (heights and soundings) among different vertical datums
VDatum is a Java application developed jointly by :
National Geodetic Survey (NGS)
Office of Coast Survey (OCS)
Center for Operational Oceanographic
Products & Services (CO-OPS)
NOAA Bathymetry
USGS Topography
Notes: Vertical Datum Transformation (VDatum) is a free software tool under development jointly by NOAA's National Geodetic Survey (NGS), Office of Coast Survey (OCS) and Center for Operational Oceanographic Products and Services (CO-OPS). VDatum is designed to vertically transform geospatial data among a variety of tidal, orthometric and ellipsoidal vertical datums - allowing users to convert their data from different vertical references to a common system , enabling the fusion of diverse geospatial data onto a preferred vertical datum.

## Slide 6
Foundational Data
Observations
(Geodetic and Tidal)
Modeling
(Hydrodynamic and
TSS)
and Uncertainty Development
Software Development
and Outreach/
Training/
Coordination
VDatum

## Slide 7: 3 Categories of Vertical Datums:
3D/Ellipsoidal Datums:
  Realized through space-based systems, such as GNSS/GPS
Orthometric Datums:
  Based on a form of mean sea level
Tidal Datums:
  a standard elevation defined from water level observations during a specific phase of the tide

## Slide 9: 3D/Ellipsoid Datums
Calculation of geographic position on this irregular surface is very complex. A simpler model is needed.
This simplified mathematical surface is the ellipsoid.
An ellipsoid approximates the shape of the earth, a datum defines the position of the ellipsoid relative to the center of the earth. A datum provides a frame of reference for measuring locations on the surface of the earth.
The GRS80 ellipsoid’s origin is approximately 2m from WGS84 ellipsoid’s. The Clarke 1866 ellipsoid’s origin is approximately 236 m from WGS84 ellipsoid’s
NAD83
(GRS 1980)
Earth Mass
Center
Approximately
2 meters
WGS84
(WGS84)
14-parameter transformation
Notes: The ellipsoid (in red) is a simplified mathematical surface that helps in positioning. GPS positions are based on the ellipsoid.

## Slide 10: Orthometric Datums and the GEOID
NAVD88 is based on an adopted elevation at Point Rimouski (Father's Point). It uses Helmert orthometric heights as an approximation to true orthometric heights.
GEOID: “The equipotential surface of the Earth’s gravity field which best fits, in the least squares sense, (global) mean sea level.”
Can’t see the surface or measure it directly.
Can be modeled from gravity data as they are mathematically related.
biquadratic interpolation

## Slide 11: Topography of the Sea Surface
This grid provides compensation for the local variations between a mean sea level surface and the NAVD88 geopotential surface.
A positive value specifies that the NAVD88 reference value is further from the center of the Earth than the local mean sea level surface.
bilinear interpolation
The Topography of the Sea Surface (TSS) is defined as the elevation of the North American Vertical Datum of 1988 (NAVD88) relative to local mean sea level (LMSL).

## Slide 12: Tidal Datums
A vertical datum is called a tidal datum when it is defined by a certain phase of the tide.
National Tidal Datum Epoch (NTDE): is a specific 19-year period that spans the longest periodic tidal variations resulting from astronomical tide-producing forces.
The fundamental base from which most coastal and marine boundaries are determined.
Also important for referencing soundings and depicting shorelines on nautical charts.
National Water Level Observation Network (NWLON)
bilinear interpolation

## Slide 13: VDatum: IGLD85
Conversions between IGLD 85 and NAVD 88 are provided based on the NAVD 88 gravity model (http://www.ngs.noaa.gov/TOOLS/Navdgrav/navdgrav.html) and the hydraulic corrector model.

## Slide 14
VDatum
Applications

## Slide 15: Integrated Ocean and Coastal Mapping (IOCM)
The practice of acquiring, managing, integrating and disseminating ocean and coastal geospatial mapping data in such a manner that permits these data and their derivative products to be easily accessed and used by and for the greatest range of users and purposes.
IOCM requires intra- and inter-agency coordination with a focus on streamlining operations, reducing redundancies, improving efficiencies, developing common standards, and stimulating innovation and technological development.
Notes: These objectives of increasing intra- and interagency coordination and promoting multi-use of geospatial data are gaining a lot of traction.
One important driver was a 2004 National Research Council Report titled “A Geospatial Framework for the Coastal Zone: National Needs for Coastal Mapping and Charting.”
  Key recommendation: increasing coordination and collaboration on ocean and coastal mapping across the federal gov.
Stimulated several other reports/initiatives, including the U.S. Ocean Action Plan. It turn, that led to the creation of the Interagency Working Group on Ocean and Coastal Mapping (IWG-OCM).
NRC Report
Consistent spatial framework for coastal data the allows a seamless transition from onshore to offshore
Increased collection and availability of data including land cover, shallow-water bathymetry, seafloor imagery, habitat distribution and classification standards
Easy access to up to date digital, geospatial data, imagery and mapping products
Compatibility among data formats – or standards and transformation protocols that allow each data exchange – and a means to evaluate data accuracy.
Increased inter- and intra-agency coordination, cooperation and communication.
U.S Ocean Action Plan
Develop and annual inventory of federal, federally-funded, and non-federal governmental ocean and coastal mapping programs and operations
Assess and report on common and shared needs for development of coordinated programs
Coordinate and leverage resources and efforts across the federal sector with industry, academic, NGO and non-federal government entities
Set priorities for standards development and developing strategies for promulgation of standards for data acquisition, data, metadata, tools and products
Develop shared and standardized mechanisms for processing, archiving, and distributing geospatial data, tools, products and services

## Slide 16: TopoBathy Lidar

## Slide 17
Topo/ Bathy Digital Elevation Model
Bathymetry
Topography
VDatum
VDatum: Used to Create Digital Elevation Models
Applications for Seamless Bathy/Topo Datasets:
Inundation modeling from storm surge, tsunamis, and sea level rise.
Erosion, accretion, renourishment
Analyzing storm impacts
Determining setback lines
Determining local, state, and national boundaries
Navigation products and services
Habitat restoration
Shoreline Change Analysis
Analyzing environmental and natural resources
Permitting
Notes: Merging data sets in coastal areas is important in a range of applications. VDatum enables spatial information from different environmental sectors to be mapped onto one uniform surface.

## Slide 18: Utilizing VDatum for Digital Elevation Model Creation: Tsunami Inundation

## Slide 19
Sea Level Rise/Coastal Flooding

## Slide 20
Emergency Response
Courtesy of USGS

## Slide 21: Additional Applications
  Coastal Inundation/Sea Level Rise/Tsunami Modeling
  Erosion/Accretion/Shoreline
  Change
  Habitat/Wetland Restoration
  Dredging and Infrastructure Engineering (levees, jetties)
  Floodplain Mapping
  Topobathy DEM Creation
  Civil and Water Works Projects
  Easement and Setback Planning
  Marine Construction
  Coastal Engineering
  Coral Reef Mapping
  Analyzing Storm Impacts
  Real Estate Mapping
  Evacuation Route Mapping
  Site Management
  Insurance Studies
  Hazardous Waste Site Studies
  Groundwater mapping and modeling
  Feasibility Studies and Planning,
  Determining Local, State and National Boundaries
  Permitting
  Analyzing Environmental and Natural Resources
  Emergency Response
  ??? What Can You Imagine ???

## Slide 22
Obtaining and Utilizing VDatum

## Slide 23: VDatum Website: vdatum.noaa.gov (Version 3.7 Released, September 11, 2017)

## Slide 24: VDatum Version 3.7 Release

## Slide 25: VDatum: Interfaces

## Slide 26: VDatum: Documentation and Support

## Slide 27
Utilizing VDatum: Horizontal

## Slide 28
Utilizing VDatum: Vertical

## Slide 29
Utilizing VDatum: Input

## Slide 30
Utilizing VDatum: Input

## Slide 31
With exception of small buffer region near coastline, user-input points falling on “land” side of MHW shoreline are assigned a null value.
Orthometric and ellipsoidal conversions may still be made at land points, as only conversions involving tidal datums will be invalid inland of the buffer zone along coastline.
Returned null value = -999999.0
Returned a valid conversion value
Notes: Older regions ½ cell length
Now working with NGS to extend 1-3 grid cells

## Slide 32
Utilizing VDatum: Input
File Name: ARRA-LFTNE_Maine_2010_06454966_utm.las
File Size: 137,992 kb
File Date: Thu Feb 21 10:57:06 2013
File Type: LAS
File Signature: LASF
File Source ID: 0
Global Encoding: 0
LAS Version: 1.2
System Identifier: vdatum.noaa.gov
Generating Software: vdatum 3.2
File Creation Date: February 24, 2012
Per-point Time: YES
Per-point RGB: NO
Georegistration
Coordinate System: NAD83 / UTM zone 19N
Vertical Citation: vert: MHW:m:height
Horizontal Units: Meters
Vertical Units: Meters

## Slide 33
VDatum Uncertainty Modeling
See: vdatum.noaa.gov/docs/est_uncertainties.html

## Slide 34: VDatum Uncertainty Modeling (cm)
(ITRFxx to the tidal datum, the transformation with the greatest uncertainty)
Uncertainties that are constant for all VDatum regions of the U.S.

## Slide 35: Operational: Vertical Datum Transformation Uncertainty

## Slide 36
VDatum
Enhancements

## Slide 37: Online VDatum Application

## Slide 38: HTDP

## Slide 39: xGEOID Support

## Slide 40: Geotiff (Null Value Enhancement)

## Slide 41: LAS1.4, LAZ, and Classification Selection

## Slide 42
  Reducing Regional Model Uncertainty to <10cm
  Increasing Coverage
  Next Generation TSS Model (utilizing gravimetric GEOID transformation roadmap)
  Spatially Varying Uncertainty
  Software Development
  Communication and Outreach
What’s Next: Strategic Priorities

## Slide 43: Vertical Datum Uncertainties By Region

## Slide 44
Foundational Data: Tidal

## Slide 45
Foundational Data: Geodetic

## Slide 46
Foundational Data: Geodetic

## Slide 47: Southeast Alaska

## Slide 48
New Proposed Transformation Roadmap
based on a purely Gravimetric GEOID
Future Enhancements: Next Generation TSS Development
A Must: GPS Campaign on bench marks to determine new relationships
Satellite Altimetry/Derived Products to better understand offshore TSS
Wish List: GPS tide buoys to be utilized for data input and validation
Re-tracked coastal altimetry data to capture nearshore sea surface height signal
New GEOID: Coastal gravity field improvement

## Slide 49
Spatially Varying Uncertainty (Transition to Operations)
Statistical data assimilation is used to blend model results and data, also providing the associated uncertainty.
Initial results for the Chesapeake Bay are shown below:
Product (MHHW) spatial distribution after data assimilation
Uncertainty in one standard derivation (m)

## Slide 50: Spatially Varying Uncertainty
NY Bight/ LIS
Gulf of Mexico

## Slide 51
Software: Future Enhancements
    Bug Fixes
    Change Request
    SVU Implementation
    Directed Assistance for Datum Selection with enhanced Logic/Validation
    GIS Format Support
      ERDAS Imagine (IMG)
    NADCON5
  Columbia River Datum
  Mississippi Low Water Reference Plane 2007
  Web Services (API?)

## Slide 52
VDatum
Production and Maintenance

## Slide 53
What’s Being Replaced with the Modernization of Reference Frames
Horizontal Vertical
  NAD 83(2011)
  NAD 83(PA11)
  NAD 83(MA11)
Latitude
Longitude
Ellipsoid Height
State Plane Coordinates
Heights
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface.
Does not include local subsidence issues

## Slide 54
Vertical Datum Transformation “Roadmap”

## Slide 55
VDatum: Updated NSRS

## Slide 56
Point Cloud Discrepancies
There should not be a crack in the bottom of pool !!
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 57
18m Offset
4-6 Degree sloping beach
Applying the new GEOID incorrectly
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 58: Current/Future Activities (NGS and VDatum)
  NGS Geodetic Toolkit: Several various independent tools/software (various computer languages)
    VDatum has been translating particular tools from FORTRAN/Others to JAVA over numerous years. (Can lead to discrepancies between tool results)
  NGS Toolkit Modernization
    NADCON5
    Vertical Transformations off of NADCON5 ??
    Others….(HTDP, IGLD85,…)
    NGS plans to build transformation modules that
    are consistent and can be integrated into other
    software (tools, web services, source code)
    VDatum will make available, the tidal version
    of these modules
    Strategically streamline above development with
    NGS Toolkit and Spatial Reference Modernization

## Slide 59
National Tidal Datum Epoch (NTDE)
Official time period of tidal observations that are used for primary datum calculations
  Time it takes the Earth, Moon, & Sun to complete an epoch tidal cycle
  19 year time period (Current NTDE is 1983-2001)
  Considered for revision every ~20-25yrs
  Includes the longest period tidal variations (18.6 year node cycle)
  Averages out seasonal fluctuations
  Provides a nationally consistent tidal datum network by accounting for seasonal and apparent environmental trends in sea level that affect the accuracy of tidal datums
1983-2001 EPOCH
  Anticipated release 2025 time frame
  Next NTDE will be computed on period of (2002-2020)

## Slide 60
The VDatum transformations tool from NOAA allows us to transform vertical datasets between ellipsoidal, orthometric and tidal datums...
Assuring data is transformed correctly
Enabling multiple uses for datasets across applications (Coastal Resilience, Intelligence, and place-based)
Permitting merging of disparate data sets to a common reference
And providing transformation uncertainty estimates for intelligent decision-making and analysis.
Summary

## Slide 61
VDatum: Contact Us

## Slide 62
Thank You!
Contact Information:
Email: vdatum.info@noaa.gov
Website: http://vdatum.noaa.gov
Stephen White
Email: stephen.a.white@noaa.gov
Phone: (240) 533-9588