## Slide 1
Some recent decisions:
Names and Blueprints
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Since 2008…
NGS has had two “ten year plans”
  Heavy on broad sweeping decisions
    e.g. “Replace NAD 83”
  Light on details
    How? What do we call it?
  2016 was a good year for filling in those details
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 3: So…what’s new?
Names

## Slide 4: Names
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 5: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 6: So…what’s new in 6 months?
Names
Scientific Decisions
  Codified in “Blueprint for 2022” documents

## Slide 7: Scientific Decisions
Blueprint for 2022, Part 1: Geometric
  Four plate-fixed Terrestrial Reference Frames
    And what “plate fixed” means
  Mathematical equation between IGS and TRFs
    Plate Rotation Model for each plate
    Coordinates at survey epoch
  Intra-frame velocity model
    To compare coordinates surveyed at different epochs

## Slide 8: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Remove long-standing non-geocentricity of NAD 83 frames
All four : identical to IGSxx at a TBD epoch
  2020.00?
All four : differ from IGSxx by plate rotation only
  Updated Euler Pole determination for rigid plate only

## Slide 9
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.

## Slide 10: NATRF2022 frame is rigid and fixed to rigid part of the N.A. plate
Non-rigid part of the N.A. plate
(deformation)
area

## Slide 11
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 12
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 13
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 14
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 15: Intra-frame velocities
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748
This is the velocity of the
point in ITRF. Includes all
movements, but the
dominant one is the
rotation of the N.A. Plate.
This is the velocity of the
point in NATRF2022.
Rotation of plate removed.
It is not constant because
the point still suffers small
“intra-frame” velocities.
Such IFVs will be captured
in a model by NGS.

## Slide 16: Scientific Decisions!!
Blueprint for 2022, Part 2: Geopotential
  Global 3-D Geopotential Model (GGM)
    Will contain all GRAV-D data
    Able to yield any physical value on/above surface
  Special high-resolution geoid, DoV and surface gravity products consistent with GGM
    Not global: NA/Pacific, American Samoa, Guam/CNMI
  Time-Dependencies
    Geoid monitoring service
      Impacts of deglaciation, sea level rise, earthquakes, etc

## Slide 17
GEOID2022 (et al) over the North America/Pacific/Caribbean/Central America/Greenland region will range from
0 to 90 latitude and from 170 to 350 longitude.
GEOID2022 (et al) over Guam/CNMI:
11-22, 143-148
GEOID2022 (et al) over American Samoa:
-16 to -10, 186-193

## Slide 18: Blueprint for 2022
Part 1: Geometric
Part 2: Geopotential
Part 3: Bluebooking

## Slide 19: Time-Dependencies as a service: NATRF2022 and actual survey epochs
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
NAD 83 forcibly combined data spanning many years (using HTDP with no vertical modeling) to compute and find one height at one epoch.
NATRF2022 will compute coordinates at survey epoch to show actual motion.
Even gridding surrounding CORS yields better subsidence rates than you have today.
Notes: Potential outline and speaker assignments; can be adjusted as needed.