## Slide 1
Modernizing the geometric reference frame
Daniel R. Roman (acting Chief Geodesist)
Stephen Hilla (GRD Chief)
Kevin Choi (CORS Branch Chief)
NOAA’s National Geodetic Survey

## Slide 2: Outline
Key Elements
Four New Frames
Euler Poles
NEV or IFV (hor. & vert.)
Velocity Models or DIY
NADCON 5.0
Poll Questions

## Slide 3: Key Elements
Drawn from Blueprint Part 1 (forthcoming)
Will be tied to most recent ITRF (2020?)
  Epoch date TBD – likely 2020.0
  Four Frames: North America, Pacific, Caribbean, and Mariana
At epoch date, all frames identical to ITRF
Then each frame rotates about an Euler pole
Velocity models describe motion in frame
Access to the four frames via OPUS tool

## Slide 4: NSRS Modernization: Four New Frames
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 5: Four Frames/Plates in 2022
NATRF2022
CTRF2022
PTRF2022
MTRF2022
Image from Snay 2003

## Slide 6: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Remove long-standing non-geocentricity of NAD 83 frames
All four : identical to ITRFxx at a TBD epoch
  2020.00?
All four : differ from ITRFxx by plate rotation only
  Updated Euler Pole determination for rigid plate only

## Slide 7: Plate-(pseudo)fixed frames
NAD 83(NSRS2007)
Epoch 2002.0
NAD 83(2011)
Epoch 2010.0
If NAD 83 were truly “plate
fixed” then an 8 year
epoch change would not
yield the systematic
plate rotation seen here.
(*)TRF2022 will determine
a new Euler Pole rotation
for each of 4 plates.
(*)=NA, C, T or P
NAD 83(2011) minus NAD 83(NSRS2007)

## Slide 8: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
ITRFxx origin
Earth’s Surface
hNAD83
hIGSxx
fNAD83 – fITRFxx
lNAD83 – lITRFxx
hNAD83 – hITRFxx
all vary
smoothly by latitude
and longitude
same
GRS-80
ellipsoid

## Slide 9
Each frame will
get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (rad/yr)
Used to compute
time-dependent TRF2022
coordinates from time-dependent ITRF coordinates.
Notes: Give an extended discussion as to the nature of an Eluer pole and how it is determined.

## Slide 10: Fixed-Epoch Transformation NAD 83 to “2022”

## Slide 11: NATRF2022 frame is rigid and fixed to rigid part of the N.A. plate
Non-rigid part of the N.A. plate
(deformation)
area

## Slide 12
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 13
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 14
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 15
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 16: NEV or IFV
Euler poles mostly account for horizontal vel.
  Remaining signal currently modeled by HTDP
  HTDP complicated to maintain and only horizontal
So if not HTDP, then what?
  A TBD velocity model needed for horizontal and vertical motions (e.g. 3D)
  Non-Eulerian Velocity (NEV) vs. Intra-Frame Velocity (IFV)
Simplest solution is to grid CORS velocities

## Slide 17: Horizontal velocities after Repro1
Note scale difference between West (10 mm/yr) and east (2 mm/yr)

## Slide 18: Residual Horizontal Velocities CONUS – gridded CORS
Eastern CONUS will largely be resolved
Western CONUS has some anomalies

## Slide 19: CORS Implied Vertical Velocities - Control
Courtesy Galen Scott
Notes: Note that this is an expanded list beyond just CORS – some are of lesser quality. Still many systematic features point to regional impacts.

## Slide 20: CORS Implied Vertical Velocities – Heat Map
Courtesy Galen Scott

## Slide 21: CONUS with 1+ mm/yr
Courtesy Galen Scott
Red is uplift, Blue is subsidence

## Slide 22: CONUS with 2+ mm/yr
Courtesy Galen Scott
Red is uplift, Blue is subsidence

## Slide 23: CONUS with 3+ mm/yr
Courtesy Galen Scott
Red is uplift, Blue is subsidence

## Slide 24: CONUS with 4+ mm/yr
Courtesy Galen Scott
Red is uplift, Blue is subsidence

## Slide 25: AK CORS Implied Vertical Velocities – Control
Courtesy Galen Scott

## Slide 26: AK CORS Implied Vertical Velocities – Heat Map
Courtesy Galen Scott

## Slide 27: How to use this information?
Assuming CORS spacing is sufficient – grid
  Yields horizontal (NEV & GIA) plus vertical signal
Vertical important for orthometric heights:
  Ht = (ht0 + (t-t0)*dh/dt) - (Nt0 + (t-t0)*dN/dt)
    Where Ht is orthometric height at desired time
    ht0 is ellipsoidal height at epoch (maybe 2020.0)
    Nt0 is geoid height at epoch
    dh/dt is change in ellipsoid height over time
    dN/dt is change in geoid height over time (GeMS)

## Slide 28: Velocity Models or DIY
We will investigate sufficiency of gridded CORS
Concern is dynamic areas: horizontal & vertical
  Will gridded CORS work in Alaska?
  What if this isn’t enough?
Will look at other models to evaluate
Cost – benefit
  What we can easily do in-house and support
  increased complexity from outside models
Alternatively, users can model their own …

## Slide 29: Time-Dependencies as a service: NATRF2022 and actual survey epochs
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
NAD 83 forcibly combined data spanning many years (using HTDP with no vertical modeling) to compute and find one height at one epoch.
NATRF2022 will compute coordinates at survey epoch to show actual motion.
Even gridding surrounding CORS yields better subsidence rates than you have today.
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 30: Time Dependencies as a service: Intra-plate motions
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748
Notes: DI4044 STATE/COUNTY- LA/EAST BATON ROUGE

## Slide 31: NADCON 4.2 in the new Geodetic Toolkit
https://beta.ngs.noaa.gov/gtkweb/

## Slide 32: The new Geodetic Toolkit with NADCON 5.0
https://dev.ngs.noaa.gov/gtkweb/
Notes: COMING SOON TO BETA!!

## Slide 33
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83
Notes:

## Slide 34
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 35: Thank you!
Daniel R. Roman, acting Chief Geodesist Dan.Roman@noaa.gov
Dru A. Smith, NSRS Modernization Manager Dru.Smith@noaa.gov
Stephen Hilla, Chief Geosciences Research Division Steve.Hilla@noaa.gov
Kevin Choi, Chief CORS Branch Kevin.Choi@noaa.gov

## Slide 36: Up Next
Poll Questions
Q& A period