## Slide 1
Proposal for a comprehensive vertical datum for North America, Central America and the Caribbean
Dru Smith, Dan Roman, Vicki Childers,
Mark Eckl, Monica Youngman
NOAA’s National Geodetic Survey

## Slide 2: Outline
Status of Vertical Datums in the Region
Why isn’t NAVD 88 good enough anymore?
GRAV-D
North American Gravity Holdings
Future Work
Notes: This is a listing of the parts of subject matters to be covered.

## Slide 3
CGVD 28*
No official
Vertical datum
NAVD 88
No official
Vertical datum
* NAVD 88 exists; also soon (2013) to be
replaced by a new geoid/GNSS based datum
Notes: Status of known vertical datums in North America, ca 2013

## Slide 4
PRVD02
San José(1)
VIVD09
La Unión 1960(1)
Puerto Cortéz(1)
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Corinto 1952(1)
Puntarenas(1)
Cristóbal(1)
Santo Domingo(1)
(1) Información cortesía de David Avalos
(1)
Notes: Status of known vertical datums in North America, ca 2013

## Slide 5
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Weren’t adopted in Canada
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good
enough anymore?
PID: EZ0840
Notes: Clarification on the word “convenient” – this is used to mean “there isn’t always a bench mark around when you need one – sometimes you have to find one far away and level from it to your site of interest”

## Slide 6
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface:
Why isn’t NAVD 88 good
enough anymore?
Notes: This map reflects the sort of height changes that users could expect if NAVD 88 were replaced with a geoid-based vertical datum.
This is only a large scale approximation and should not be used as an absolute guide. Each benchmark might have its own level
Of mismatch, say from uplift or subsidence, not captured by this broad brush.
Also, this is the difference between the zero level of NAVD 88 and the actual geoid. The difference between NAD 83 ellipsoid heights and
ITRF/GRS-80 ellipsoid heights has NO influence on this graph and should not be part of the story.
Updated October 2010

## Slide 7: Canada Height Modernization - 2013
1. Time consuming
2. Expensive
3. Limited coverage
4. BMs are unstable
5. BMs disappear
6. Local networks
Levelling Networks:
1. Established over the
last 100 years
2. 120,000 km of levelling
lines
3. Some 80,000
benchmarks
The geoid model:
1. Entire coverage of the
Canadian territory
(land, lakes and oceans)
2. Compatible with space-
based positioning
(e.g., GNSS, altimetry)
3. Less expensive for
maintenance
4. Fairly stable reference
surface
H = hGNSS – NModel
Notes: As mentioned, in 2013 this is Canada’s plan to switch from a benchmark-based CGVD28 to a geoid-based vertical datum.

## Slide 8
Gravity for the Redefinition of the American* Vertical Datum
An NGS project whose target is to redefine the official civilian vertical datum as the geoid, realized through the use of GNSS technology and a gravimetric geoid model over at least the United States and its territories
What is GRAV-D? (1 of 3)
Notes: *American = “of or pertaining to North or South America”
Updated Oct 2010

## Slide 9
GRAV-D means fast, accurate, consistent orthometric heights everywhere in the USA
GPS already gives fast accurate ellipsoid heights
If the geoid were modeled (and monitored) to highest accuracy…fast, accurate orthometric heights, anywhere, anytime
No need to use leveling to “bring in the datum”
What is GRAV-D? (2 of 3)
Notes: Monitoring of the geoid will be done a combination of satellite derived geoid changes (such as from the GRACE mission or its follow-ons), geophysical modeling and a coordinated field campaign of absolute and relative gravimeters and CORS.
Updated October 2010.

## Slide 10
GRAV-D will mean:
  Primary access to the vertical datum will be through a GNSS receiver and a gravimetric geoid model
  One consistent vertical datum for all of North America
    CONUS, Alaska, Hawaii, PR, VI
    Available for adoption by
      Canada, Mexico, Caribbean, Central America
What is GRAV-D? (3 of 3)

## Slide 11
Hawaii
Alaska
“CONUS”
Puerto Rico / Virgin Islands
Guam / Northern Marianas
American Samoa
GRAV-D
Planned
Coverage
Expected GRAV-D airborne gravity coverage by 2022
Notes: The coverage of GRAV-D that is expected by 2022.

## Slide 12
Extent of 2022 geoid
model used for
new vertical datum

## Slide 13
Hawaii
Many US Pacific Territories
(not Guam, CNMI nor American Samoa)

## Slide 14
Canada
Alaska, including
entire Aleutian
Island Chain
CONUS (USA)

## Slide 15
Mexico
All Central
American Countries
All Caribbean
Countries
Bermuda

## Slide 16: Gravity Holdings
GRAV-D is only funded to collect over USA by 2022
  Data collection plans beyond 2022:
    Geoid monitoring across the continent
    Airborne collection in surrounding countries if necessary and through cooperative agreements
Existing gravity holdings
  Sparse
  Metadata issues

## Slide 17
Alaska: Sparse coverage;
GRAV-D has concentrated here first
Guatemala, Belize, El Salvador: Gap between two
historic computations: MEXICO97 and CARIB97
Cuba: Political issues
mean a gap on the largest
Island in the Caribbean
Greenland: Multiple airborne
surveys, but not currently in
NGS holdings

## Slide 18: Close-up of gravity holdings currently available at NGS

## Slide 19
Available on the Website
In Processing
Partially Collected
Planned
FY13
FY13
FY13
FY13
FY14
FY13/14
FY14
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
Status of and plans for data collection – more information and data available at www.ngs.noaa.gov/GRAV-D
FY13
FY13
FY14

## Slide 20: Future Work
Engage all countries in North American Geoid working group (IAG Sub-commission 2.3c)
  Chair: David Avalos (INEGI)
Collect up existing terrestrial gravity in gaps
Organize new collections collaboratively with other countries
  Terrestrial
  GRAV-D

## Slide 21: Future Work
Agreement on W0 value
  USA and Canada have agreed to create all geoid models until 2022 using this new value
    Done, in French and English

## Slide 22
Future Work

## Slide 23: Future Work
Make geoid-based orthometric heights available via OPUS
  Done, in extended output

## Slide 24
Future Work
  www.ngs.noaa.gov/OPUS

## Slide 25: Future Work
Develop a geoid-monitoring service
  Plan with and without GRACE-type satellites
  Likely to include:
    A tracking network
      Co-located CORS with gravimeters?
    Geophysical Models
  Working group established
    Boulder conference in 2009
    Unstaffed at the moment

## Slide 26
The “secular” geoid change from the monthly GRACE models (2002-2008).
The solution represents the effect due to total mass changes.
The solution uses a 400-km Gaussian filter.
Deglaciation
Glacial Isostatic
Adjustment
Drought
Notes: Secular is between quotation marks because only GIA is secular, the deglaciation and drought are currently more recent multi-year systematic variations of the geoid. I used the term “secular” not to confuse with seasonal variations of the geoid.

## Slide 27
Geoid / Vertical Datum Contacts:
  NA Geoid Working Group Chair & Mexico Geoid:
    David Avalos (david.avalos@inegi.org.mx)
  USA: Dan Roman (dan.roman@noaa.gov)
  Canada: Marc Véronneau (marc.veronneau@nrcan-rncan.gc.ca)
Interested?
Notes: This PPT is the October 2010 update (by Dru Smith) to a set of slides that was originally created in November 2009 by Dru Smith.
Until such time as a project manager for the new vertical datum is announced, any updates to this PPT will be his responsibility.

## Slide 28: Extra Slides

## Slide 29: Geoid Slope Validation Survey of 2011 (GSVS11)
325 km
218 points
1.5 km spacing
Terrestrial Survey using:
GPS
Leveling
DOVs
To quantify accuracy of:
Current geoid models
Geoids with GRAV-D added
Notes: The final line was a 325 km stretch from downtown Austin, Texas (North end) to Rockport, Texas (South end). There were 218 official survey points along the line, with an average spacing of 1.5 km between them. The shaded areas in the above picture were the existing GRAV-D data at the time of planning GSVS11 (since expanded). Although the weather report looks extreme, most surveying was done in the milder times of day.

## Slide 30: GSVS11: Proving why we need GRAV-D
Geoids without new GRAV-D data: 1-3 cm differential accuracy
over distances from 0.4 to 325 km
Geoids with new GRAV-D data:
1 cm differential accuracy over distances from 0.4 to 325 km
Notes: GSVS11: Geoid Slope Validation Survey of 2011 – a 325 km long terrestrial survey intended to quantify the accuracy of gravimetric geoid modeling in a low, flat, gravimetrically benign area.

## Slide 31
How will I access the new
vertical datum? (3 of 3)
H2022=5.000m +/- 0.020m
(GNSS/geoid)
H2024=4.960m +/- 0.030m
(GNSS/geoid)
H2029=4.860m +/- 0.150m
(modeled)
Height
Year
2022
2024
2029
H2029=4.830m +/- 0.020m
(GNSS/geoid)
V(modeled 22/24) = -2 cm/yr +/- 2.5 cm/yr
V(modeled 22/29) = -2.1 cm/yr +/- 0.3 cm/yr
Notes: NGS will eventually stop making the claim that we “know” the heights of bench marks as the method of providing access to the vertical datum. What NGS will do is provide the orthometric height to a user on the day of their survey (and with the disclaimer that this height should not be taken as “known” for very long, due to the dynamic nature of the Earth). If possible, height changes (velocities) will be computed and provided to
assist in predicting heights in the future.
Updated October 2010.

## Slide 32: Monumented NGS Data

## Slide 33: Spot NGS + Canadian data

## Slide 34: Spot DMA

## Slide 35
Long term fix: Replace NAVD 88
Find a method of defining a vertical datum that seeks to fix all of the known issues with NAVD 88
Best option: Define the datum as a given geoid model and realize it through GNSS technology
  GRAV-D
Possible ways to fix
NAVD 88 (1 of 1)
Notes: Why is this the best option? Because it addresses:
Different datums existing for CONUS, Hawaii, PR/VI (and, theoretically, Canada, Mexico, and the Caribbean and Central American countries)
Sparseness of bench marks
Error build up as one gets far from an origin point
Financial and personnel realities
Fragility of bench mark network