## Slide 1
The modernized National Spatial Reference System

## Slide 2: Note to international attendees
Much of this talk is relevant to surveying in the United States, but…
  There are certainly many aspects to our modernization efforts relevant to any national reference system
  Many of the tools NGS is building can be used by anyone, anywhere.
Notes: So I hope everyone finds something relevant and useful herein

## Slide 3: Outline
Why is NGS modernizing the NSRS?
What changes are coming?
How this will impact you
How to prepare
Tools and transformations
Current status

## Slide 4
Notes: It is possible that you view the future with slightly less enthusiasm than we do at NGS….

## Slide 5
Notes: It is our hope that this talk can help alleviate some of that anxiety…so let’s look at the topics we’ll be covering.

## Slide 6: Decision to modernize
In 2007, NGS publicly announced their decision to completely change how it approached its mission.
In a word, they chose to modernize the NSRS
Let’s look at the issues that drove that decision, and the direction they decided to go

## Slide 7: Issues
NAVD 88 suffers from use of infrequently surveyed geodetic control marks that:
Are almost never re-checked for movement
Disappear by the thousands every year
Are not funded for replacement
Are not necessarily in convenient places
Don’t exist in most of Alaska
Weren’t adopted in Canada
Were part of a level network constrained to a single point, allowing cross-country error build up
PID: EZ0840

## Slide 8: Issues
NAVD 88 suffers from a known bias (50 cm) and tilt (about 1 meter across CONUS)
PID: EZ0840
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface:

## Slide 9: Issues
~2.24 m
NAD 83 origin
ITRF origin
Earth’s Surface
hNAD83
hITRF
NAD 83 suffers from a 2+ meter non-geocentricity (which misaligns it with ITRF and all GNSS orbits)

## Slide 10: Issues
Geodetic control is usually affixed to a crust that is moving
  Even so-called “plate fixed” frames are only as stable as:
    The rigidity of a plate
    The complete lack of subsidence or uplift

## Slide 11: General Direction
Future details would come, but in 2007 the general direction was:
  Replace both NAD 83 and NAVD 88, at the same time
  Transition to a geoid-based vertical datum
  Leverage the rise of GNSS and RTNs

## Slide 12
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
Sep 2017
NOAA TR NOS NGS 62
32 pages
Geopotential:
Nov 2017
NOAA TR NOS NGS 64
41 pages
Working in the
modernized NSRS:
April 2019
NOAA TR NOS NGS 67
77 pages

## Slide 13: Replacing the NAD 83’s
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 14
Notes: -there’s four reference frames because there are four major tectonic plates within the NGS Area of Responsibility.
-As the National Geodetic Survey, we’re part of the DoC so we must cater to all US States and Territories
-thus we’ve got four tectonic plates in our Area of Operations, so four Ref Frames
-But…

## Slide 15: The TRFs
All are global frames (no “boundary”)
  This was true for the NAD 83’s also, BTW
  But each frame will rotate with one tectonic plate
    Put another way: “The frame rotates so your coordinates don’t have to”

## Slide 16
ITRF2020 – constant frame, rotating plate

## Slide 17: “Plate-Fixed”
NATRF2022 – rotating frame, constant with plate

## Slide 18
ITRF2020 or NATRF2022 – your choice, just use EPP2022

## Slide 19: Shift and Drift
When transitioning off of NAD 83, your coordinates will experience shift and drift
  Shift: A one-time jump somewhere in the 0 to 4 meter range (latitude, longitude, ellipsoid height)
    From fixing NAD 83’s non-geocentricity
  Drift: Coordinates are now time-dependent. The shift will take you to 2020.00. Working at any other epoch means you must account for the drift (velocity) of your coordinates
    As well as any other motions over time

## Slide 20: NAD 83(2011) epoch 2010.0 to NATRF2022 epoch 2020.00 (estimate)

## Slide 21: Drift
What does it mean to provide time-dependent coordinates in 5 frames?
  Let’s look at the known velocities of an active control station in ITRF2020, NATRF2022, PATRF2022, CATRF2022 and MATRF2022

## Slide 22: BSMK (North Dakota)

## Slide 23: BSMK (North Dakota)
Note the time-dependent coordinate in latitude in NATRF2022 is stable! That means the NATRF2022 IFVM for latitude will be ZERO for this point.
t0=2020.0, when all five frames are identical
Notes: * Intra-Frame Velocity Model: More on this later, but it is basically “all of the movement that is left over at a point after I take away the simple tectonic rotation of a plate”

## Slide 24: BSMK (North Dakota)
Similarly, the time-dependent coordinate in longitude in NATRF2022 is stable! That means the NATRF2022 IFVM for longitude will be ZERO for this point.

## Slide 25: BSMK (North Dakota)
However, in every frame, this point is subsiding! That will be captured in the ellipsoid height component of the IFVM for each frame.

## Slide 26: IFVM2022 Velocities – ITRF2020/CONUS

## Slide 27: IFVM2022 Velocities – NATRF2022/CONUS
Notes: Note that even in “stable North America”, these velocities are not absolutely zero! The IFVM2022 model will contain these tiny deviations from simple plate rotation!

## Slide 28: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 29: The three gridded regions
“North American region”
¼ of the Earth
“Guam/CNMI region”
“American Samoa region”

## Slide 30: Shift and Drift
When transitioning off of NAVD 88 or other vertical datum, your coordinates will experience shift and drift
  Shift: A one-time jump somewhere in the 0 to 2 meter range (orthometric height)
    From fixing biases and/or tilts in NAVD 88 and others
  Drift: Coordinates are now time-dependent. The shift will take you to 2020.00. Working at any other epoch means you must account for the drift (velocity) of your coordinates
    As well as any other motions over time

## Slide 31: NAVD 88 (epoch ?) to NAPGD2022 epoch 2020.00 (estimate)

## Slide 32: NAVD 88 (epoch ?) to NAPGD2022 epoch 2020.00 (estimate)

## Slide 33: Definitional Relationship
All work is done in ITRF2020 XYZ coordinates first.
We end with orthometric height in NAPGD2022 at the same epoch as the ellipsoid height.
Conversion to orthometric heights is definitional through GEOID2022.

## Slide 34: Impacts
All existing data will need to be transformed
NGS’s default NADCON transformations will be:
Expect 0.5-4.0 meters of shift in f, l, h
Region | From | To
CONUS | NAD 83(2011) epoch 2010.00 | NATRF2022 epoch 2020.00
Alaska | NAD 83(2011) epoch 2010.00 | NATRF2022 epoch 2020.00
Hawaii | NAD 83(PA11) epoch 2010.00 | PATRF2022 epoch 2020.00
PR / VI | NAD 83(2011) epoch 2010.00 | CATRF2022 epoch 2020.00
American Samoa | NAD 83(PA11) epoch 2010.00 | PATRF2022 epoch 2020.00
Guam / CNMI | NAD 83(MA11) epoch 2010.00 | MATRF2022 epoch 2020.00

## Slide 35: Impacts
All existing data will need to be transformed
NGS’s default VERTCON transformations will be:
Expect 0.5-2.0 meters of shift in H
Region | From | To
CONUS | NAVD 88 | NAPGD2022 epoch 2020.00
Alaska | NAVD 88 | NAPGD2022 epoch 2020.00
PR | PRVD 02 | NAPGD2022 epoch 2020.00
VI | VIVD 09 | NAPGD2022 epoch 2020.00
Guam | GUVD 04 | NAPGD2022 epoch 2020.00
CNMI | NMVD 03 | NAPGD2022 epoch 2020.00

## Slide 36: Impacts
Future NGS tools (OPUS) will yield:
  All 5 frames (ITRF2020, NATRF2022, PATRF2022, CATRF2022, MATRF2022)
  At various epochs:
    Your mean survey epoch
    The most recent “Reference Epoch” (5 year intervals, starting with 2020.00)
  You can choose to adjust your data to any epoch

## Slide 37: Impacts – Many things will be similar to today
If today you… | Then in the future you will…
Use OPUS-S | Use OPUS
Use OPUS-Projects | Use OPUS
Adjust projects to NAD 83(2011) epoch 2010.0 | Adjust projects to *ATRF2022 epoch 2020.00
Work in the ITRF | Work in the ITRF

## Slide 38: Impacts – And many new services will be added
If today you… | Then in the future you will…
Use GNSS but can’t use OPUS | Use OPUS
Use Leveling but can’t use OPUS-Projects | Use OPUS
Pull datasheets from the NGS IDB | Use the data delivery system to see full coordinate history of a mark

## Slide 39: Get prepared…
NGS has a new mobile-friendly mark recovery webpage. Please try it out!
https://www.ngs.noaa.gov/cgi-bin/mark_recovery_form.prl

## Slide 40: Get prepared…
Check out NCAT (now with NADCON and VERTCON!)
https://www.ngs.noaa.gov/NCAT/

## Slide 41: Ways to use NCAT
Browser: Interactive, 1 point at a time
Browser: Upload a file / get a file back (text, xlsx)
As a Web Service
Download and run locally
  Beware: this works, but NCAT is updated frequently, so the copy you have may be outdated, so always download the latest version

## Slide 42: Get prepared…
Check out NGS’s website
www.ngs.noaa.gov

## Slide 43: Status
Numerous issues have strained NGS resources recently
  Staffing issues
  Current events
The likelihood of completing the modernization by the end of 2022 is growing vanishingly small
  An official delay message will be released in a few months

## Slide 44: Status
But still good works are happening:
  The SPCS is on track to be designed by 2022
  RTK/N support in OPUS-Projects by end of 2020
  GRAV-D is over 80% done
  A complete overhaul of the NOAA CORS Network is underway
    Evaluating all SOPs
    Grading of stations for data quality/availability

## Slide 45: Summary
The NSRS of today is based on
  pre-space-age geodetic technology
  The concept of one unique coordinate assigned to a point, in perpetuity
The modernized NSRS will
  Leverage GNSS
  Embrace the movements of points on Earth’s crust

## Slide 46: Summary
All of your geometric coordinates will change by 2-4 meters
All of your orthometric heights will change by 2 meters (or more)
And that just gets you to a “reference epoch”
  Which looks like it supports the “one coordinate forever” myth
  After that, real motions kick in and become part of the world of geodetic control

## Slide 47: Summary
But it’s not all “change”…
  You will still be able to:
    Get a position using OPUS
    Adjust your projects to some reference epoch
    Look at a mark’s “datasheet”
  Only now, there will be a lot more information and a lot more service provided

## Slide 48: Thank you

## Slide 49: Questions?

## Slide 50: The preeminence of ITRF
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
Rotation of the
North American Plate
Rotation of the
Caribbean Plate
Rotation of the
Pacific Plate
Rotation of the
Mariana Plate
ITRF2020
EPP2022
EPP for “Euler Pole Parameters”
(a way of describing a plate’s rotation)

## Slide 51: Definitional Relationship
OPUS does everything
in ITRF2020 XYZ…
A simple 3x3 matrix from
EPP2022 (built into OPUS)…
And OPUS gives you coordinates in NATRF2022. Same epoch as ITRF2020.
Same goes for the other 3 frames.