## Slide 1: Giovanni Sella CORS Program Manager NOAA-National Geodetic Survey
CORS Program Updates FY2010-2011
Especially New Revised Coordinates
CGSIC - Portland, OR
19 September, 2011

## Slide 2: CORS News for FY10-11
New CORS coordinates released September 6
New absolute antenna calibrations released
Updated HTDP to 3.1.2
Passive network adjustment in the works
Network grows to +1,800 stations
OPUS supports two reference frames

## Slide 3: Previous CORS Coordinates
Mixed coordinates and velocities from: last reprocessing (1994-2002), and adjustments using 8-3 IGS ref. sites
Mixed HTDP vs. computed vel.; Vertical vel. = 0 mm/yr
NGS’s global frame was ITRF00 epoch 1997.0 projecting 14 yrs is unreliable; NAD 83(CORS96,MARP00,PACP00) epoch 2002.0 projecting 9 yrs becoming a problem
Metadata issues, discontinuities/offsets
Significant software changes
Absolute vs relative antenna phase center values
Need to revise CORS coordinates and velocities

## Slide 4: Positions and Velocities Change!
Plate fixed
CORS Multiyear soln.

## Slide 5: Reference Frame Definitions
ITRF frame (global) multi-technique—vlbi, slr, doris, gnss
IGS frame (global) GNSS only
NAD frame (plate fixed) related to ITRF/IGS
Critical to pay attention to frame tags and epoch dates and antenna calibration values
Frame Name | Epoch | Antenna PCV* | Data Duration
ITRF2000 | 1997.00 | Rel | 1994.0-2002.0
ITRF00 (NGS’s soln) | 1997.00 | Rel NGS | 1994.0-present
NAD 83(CORS96,MARP00,PACP00) | 2002.00 | Rel NGS | 1994.0-present
IGS08 | 2005.00 | Abs IGS08 | 1997.0-2009.5
IGS08 (NGS’s soln) | 2005.00 | Abs IGS08 | 1994.0-2011.5 (ongoing)
NAD 83(2011,MA11,PA11) | 2010.00 | Abs IGS08 | 1994.0-2011.5 (ongoing)
*PCV – phase center value; Abs-Absolute, Rel-Relative

## Slide 6: Reference Frames Used
Basis is global frame inherited from ITRF2008 but not the same as ITRF2008
  Name: IGS08
  Epoch date: 2005.00 (same as ITRF2008, IGS08)
  NGS has more discontinuities and weekly solutions than ITRF2008; and has applied IGS05_ATX -> IGS08_ATX corrections to be consistent with IGS08
Related to ITRF, but plate fixed (NAD 83)
  Name: NAD 83(2011,MA11,PA11)
  Epoch date: 2010.00
  NAD 83(CORS96,MARP00,PACP00) to NAD 83(2011,MA11,PA11) identity transformation (i.e. same axes)
  NAD 83(2011) axes origin different (~2m) from ITRF/IGS08 (expect reconciliation ~2022)

## Slide 7: Reference Frames Used
NAD 83(2011) epoch 2010.00
  “2011” is datum tag i.e. year adjustment complete
  “2010.00” is “epoch date” (January 1, 2010)
    Date associated with coordinates of control station
  Frame fixed to North American tectonic plate
    Includes California, Alaska, Puerto Rico, and US Virgin Islands
NAD 83(PA11) epoch 2010.00
  Frame fixed to Pacific tectonic plate (Hawaii and American Samoa, and other islands)
NAD 83(MA11) epoch 2010.00
  Frame fixed to Mariana tectonic plate (Guam and CNMI)

## Slide 8: Reference Frames and Orbits
IGS08 positions are not equal to ITRF2008
ITRF2008 is multi-technique solution VLBI, SLR, DORIS, GPS
IGS08 is a GPS only solution
ITRF2008 GPS’s component was processed using IGS05 absolute antenna calibrations
To create IGS08 IGS took the ITRF2008 positions and applied a station specific correction to account for differences between IGS05 and IGS08 absolute antenna calibrations. Corrections of up to 5 cm
All IGS orbit products in NGS online storage from 1994-Jan-1 to 2011-Apr-16 are aligned to IGS05 and then to IGS08. For most non-research applications the orbits can be mixed

## Slide 9: Tying CORS to Global Frame
Global
Global+CORS
global tracking network used for estimating:
  GPS satellite orbits (15-min intervals)
  terrestrial framework
    Earth Orientation (EOPs)
    global station positions (weekly averages)
CORS tied to global framework via single baselines radiating from global stations
  minimizes frame distortions from local effects in dense regional networks

## Slide 10: CORS IGS08 Velocity Field

## Slide 11: What is the new NAD 83?
Same datum, so no transformation between NAD 83(CORS96,MARP00,PACP00) epoch 2002.00 and NAD 83(2011,MA11,PA11) epoch 2010.00
  NAD 83 (2011,MA11,PA11) velocities should be used to move positions through time
To assess differences in frames, need to compare positions at same epoch date (2002.00).
  Will do this by taking new positions at CORS at 2010.00 and using NAD 83(2011,MA11,PA11) velocities to move to 2002.00

## Slide 12: Changes in Horizontal NAD 83 Positions NAD 83(2011) epoch 2002.00 – NAD 83(CORS96) epoch 2002.00
Avg. shifts: E = -0.141.04 (ME -0.10) cm N = 0.190.94 (ME 0.20) cm
  prescribing velocities using numerical models (i.e. HTDP)
  smaller random part probably caused by change to absolute antenna calibrations

## Slide 13: Changes in Vertical NAD 83 Positions NAD 83(2011) epoch 2002.0 – NAD 83(CORS96) epoch 2002.0
avg. shift: U = 0.801.89 (ME -0.70) cm
  random part mostly caused by switch to absolute antenna calibrations
  shifts also caused by assuming Vu = 0 in NAD 83(CORS96)

## Slide 14: The NAD 83 datum is the same. So what are the shifts caused by changing reference epoch to 2010?
Previous 2 slides show consequences of new realization:
  approx. 1-2 mm avg. horiz. shift
  less than 1 cm avg. vert. shift
BUT reference epoch has changed from 2002.00 to 2010.00
  velocities are therefore critical
Let’s compare NAD 83(CORS96) positions @ 2002.00 to NAD 83(2011) positions @ 2010.00
  differences dominated by effects of crustal motion, i.e., NAD 83 velocities are non-zero
  e.g. 2 mm/yr velocity after 8 years = 1.6 cm change in position

## Slide 15: Changes in Horizontal NAD 83 Positions Different Epochs NAD 83(2011) epoch 2010.0 – NAD 83(CORS96) epoch 2002.0
Avg. shifts: E = 0.055.25 (ME -0.12) cm N = 2.126.08 (ME 0.00) cm
  combination of position and velocity differences
  due mostly to updated velocities (including up to 8 more years of data)
WA+OR
4.4E,5N cm
CA+NV
10.8E, 14.4N
cm
East
1.4E, -0.2N cm
UT+CO+NM+AZ
0.5E,1.0N cm
ID+MT+ND+SD+WY
1.7E,0.5N cm

## Slide 16: Changes in Vertical NAD 83 Positions Different Epochs NAD 83(2011) epoch 2010.0 – NAD 83(CORS96) epoch 2002.0
Avg. shifts: U = -0.662.24 (ME -0.80) cm
  combination of position and velocity differences from additional data, tectonics
  assuming vertical velocity ≈ 0.00 in NAD 83(CORS96)

## Slide 17: Changes with New Frames
Change from relative to IGS08 absolute antenna phase center values (PCV)
The global frame (IGS08) pos/vel are aligned to full global frame >100 sites
Change in epoch from 2002.00 to 2010.00 in NAD 83(2011/MA11/PA11)
No longer support coordinates in ITRF00 or NAD 83 (CORS96,MARP00,PACP00)
What amount of change/tolerance are permitted?
  No change 2 cm horizontal, 4 cm vertical

## Slide 18: Changes with New Frames
CORS coordinates clearly divided
>2.5 yrs of data with positions and velocities from stacked solution (i.e. computed). Valid for “fixed” coordinates.
<2.5 yrs of data positions from stacked solution, but velocities via HTDP (i.e. modeled).
Users encouraged not to use CORS with modeled velocities, until computed vels. are avail. (may take up to 3 yrs). Important if holding coordinates fixed.
CORS with unexplained coordinates changes marked as “questionable” until resolved/stable.

## Slide 19: HTDP 3.1.2
HTDP supports new frames
Includes a basic gridded velocity field for Alaska
A detailed and robust velocity and block model for Alaska should be available next year
Preliminary work on a 3-dimensional has been completed, but more work is needed before it a beta version is ready

## Slide 20: Antenna Calibrations
Hear Next talk by Andria Bilich

## Slide 21: Information on New Coordinates

## Slide 22: Info on New Coordinates

## Slide 23: Info on New Coordinates

## Slide 24: What About the Passive Network?
National Adjustment of 2011 (NA2011)
  New adjustment of GPS passive control
  GPS vectors tied (and constrained) to CORS NAD 83(2011/MA11/PA11) epoch 2010.00
  Approximately 80,000 stations and more than 400,000 GPS vectors
Realization will be the same for CORS and passive marks
National Adjustment of 2011
  Goal: Complete by end of CY 2011/early 2012
  Deadline for submitted projects: Aug 31, 2011

## Slide 25: What About the Passive Network?
Optimally align passive control with new CORS
Add >1000 projects submitted since 2007
  Also observations for Hawaii, other Pacific islands
Network and local accuracies on all stations
  Including future submitted projects
More consistent results in tectonically active areas
  More current data, better tectonic modeling (HTDP 3.1.2)
Better computations and analysis techniques
  Improved outlier detection
  Incorporation of lessons learned from previous national adjustment

## Slide 26: Orthometric Heights and Geoid Model
New hybrid geoid model (GEOID12)
  Use NAD 83(2011) epoch 2010.00 ellipsoid heights on NAVD 88 benchmarks
  Might also use OPUS-Database results on NAVD 88 benchmarks
Available after passive adjustment is completed
Considering performing a national vertical adjustment
  Constrain vertically to NAVD 88 benchmarks
    Perform a simultaneous nationwide adjustment
  GNSS-derived orthometric heights
    NAD 83(2011) ellipsoid heights with GEOID12
    NOT a readjustment of NAVD 88 leveling

## Slide 27: New Datasheets
Update to new Datasheet version (8.00)
  Changed location, length, and text for many fields
  Added new fields, deleted fields, augmented existing fields
  Implemented by end of calendar year 2011
  Will add announcement and prototype to NGS web site soon

## Slide 28: OPUS
No changes in processing engines (OPUS-S and OPUS-RS)
User can choose to get results in either old or new frames
  Old frame available till passive adjustment is completed
OPUS-DB results currently available in both frames.
  When passive adjustment is completed all COR96/MARP00/PACP00 will be recomputed to 2011/MA11/PA11
OPUS-Projects still beta hopefully operational next year

## Slide 29: OPUS cont’d

## Slide 30: Summary
Users must use appropriate antenna calibrations with particular reference frames
All NGS Products and Services will be in consistent frames in 2012:
  IGS08 epoch 2005.00
  NAD 83(2011,MA11,PA11) epoch 2010.00
User should start thinking that transforming between frames is problematic need to plan to reprocess with new frames

## Slide 31: Questions/Comments
We recognize that NGS and the public want CORS to be the primary access to the NSRS, but accuracy and constancy are not always possible.
We are keen to hear your comments/concerns
Check: geodesy.noaa.gov/CORS/news.shtml
geodesy.noaa.gov/CORS
        Choose Data Products
giovanni.sella@noaa.gov

## Slide 32: Questions?
- What is the reliability of new velocities compared with current published values - especially in the vertical?
- If the new reference frame is called NAD 83(2011) epoch 2010.0 what efforts will NGS make to educate the user to minimize confusion with NAD 83(CORS96) epoch 2002.0?
What period of overlap will occur with solutions in both NAD 83(CORS96) epoch 2002.0 and NAD 83(2011) epoch 2010.0?
What format changes occur to NGS products e.g. data sheets, coordinate page, OPUS output?
Will there be a transformation between NAD 83(CORS96) and NAD 83(2011)?

## Slide 33: Work Completed
CORS RINEX observations from 1994 thru 2011.4 processed in fully consistent global framework
  evaluated approx. 90 billion double-difference observation eqs.
  using latest IERS models and processing methods
    switch to absolute antenna calibrations
    reduced positioning errors and distortions of global frame
912 weekly (full history) CORS+global SINEX files containing X,Y,Z positions and full variance-covariance information
used CATREF software from Institut Géographique National (IGN) to stack weekly CORS+global SINEX files in three steps:
  step 1: focused on attenuating aliasing of Helmerts from local non-linear motions
  step 2: impose “unbiased” Helmert parameters on whole network & stack
  step 3: obtain MYCS—i.e., align “unbiased” stacked TRF to ITRF2008 via GPS sites common to both SNXs
resulted in a set of new positions and velocities for CORS
  4,906 position and velocity estimates for 2,264 CORS+global stations
  solution aligned to ITRF2008 with negligible distortions of the frame
  solution calibrated to be used with IGS08 absolute antenna calibrations