## Slide 1: OPUS Projects 5: Supporting Real-Time Kinematic Measurements for Establishment of Geodetic Control
Dan Gillins, Ph.D., P.L.S.,
Nick Forfinksi-Sarkozi, Ph.D.,
Ira Sellars,
Weibing Wang

## Slide 2: Real-Time Kinematic (RTK) Surveying
Single-base RTK
  Stationary single “base” station
  Transmits precise coordinates and GNSS observables to moving “rover”
  < 10-20 km baseline length
Base
Rover
http://www.gcfarm.com/siteart/precision-farming/case-accuguide.jpg
VRS
(Landau et al. 2002)
RTN Base
RTN Base
RTN Base
Control
Center
Network RTK
Notes: Applications
  Survey engineering
  Mobile mapping
  Precision agriculture
  Mining
  Construction

## Slide 3: Empirical Evaluation of the Accuracy of Network RTK
[Allahyari et al. 2018]
Ellipsoid Height
Horizontal
3

## Slide 4: What is OPUS-Projects?
Free, web-based application
Upload static GPS data via OPUS-S
Supports campaign-style surveys
Custom survey network design
Easy addition of CORS’ data
Data management and visualization aids
Baseline processing using the PAGES engine
Survey network adjustments
Selection of reference frames , geoid models, State Plane Coordinates, etc.
4

## Slide 5: Why use OPUS-Projects?
Organizes data for multiple occupations on more than one mark
  Campaign-style surveys for control
Performs least squares adjustments of control survey networks
  Estimate relative accuracy between marks
Constrains NAVD 88 bench marks – check/establish NAVD 88 heights
Ensures survey is tied to the National Spatial Reference System (NSRS)
  CORS data and published coordinates/heights
  Official models (HTDP, GEOID18)
Submits survey to NGS for review, loading in database, and publication on datasheets
  Establishment of geodetic control
  NGS will use data for making models (e.g., future transformation model for the new datums)

## Slide 6: GNSS Vector Exchange (GVX) Flow Chart: https://www.ngs.noaa.gov/data/formats/GVX/index.shtml
Notes: Explain URL has example files, details on the file format
XML based, open-source, machine and human readable

## Slide 7: Design for OPUS-Projects and GVX
[Adapted from Weaver et al. 2018]
GVX file (from RTK survey or baseline processing in other software)
375-800 km
OPUS-Projects (from static GNSS session processing)
RTK Base or “From” Mark
RTK Rover or “To” Mark
Vector
Vector in GVX File
375-800 km
7

## Slide 8: Example of GVX to OPUS-Projects
8

## Slide 9: Example of GVX to OPUS-Projects (cont.)
https://geodesy.noaa.gov/OPUS-Projects/OpusProjects.shtml
9

## Slide 10: Example of GVX to OPUS-Projects (cont.)
10

## Slide 11: Example of GVX to OPUS-Projects (cont.)
https://geodesy.noaa.gov/OPUS-Projects/OpusProjects.shtml
11

## Slide 12: Example of GVX to OPUS-Projects (cont.)
12

## Slide 13: Example of GVX to OPUS-Projects (cont.)
13

## Slide 14: Status of GVX Exporters
i-Gage X-PAD
Available Now
Coming Soon
Reachview 3
Trimble Business Center (TBC) 5.80
Topcon MAGNET Field v. 7.3
JAVAD in Triumph-LS device
Carlson SurvCE7
Leica Infinity 4.0.0
14
Notes: Trimble Business Center (TBC) 5.60 (11/15/2021)updated to 5.80 to fix bugs
Topcon MAGNET Field v. 7.2 (11/18/2021) updated to v.7.3 to fix bugs
JAVAD in Triumph-LS device
Leica Infinity 4.0.0 (05/2022)runs well

## Slide 15: OPUS-Projects 5.1
Supports static GPS baseline processing & network adjustments
Uploader for GVX files
  RTK vectors; vectors from post-processing
Automatically “weights” uploaded vectors in a network least squares adjustment
Builds all necessary files for publication on datasheets

## Slide 16: More Help with OPUS-Projects and GNSS Surveying
Completed Work:
New digital user guide
New web content for GPSonBM using network RTK and OPUS-Projects 5.1
Ongoing Work:
New GNSS surveying standards & specifications—NGS-92
Training videos to support independent learning
Tutorial lesson with example data
16

## Slide 17: NGS 92: New Standards for GNSS Surveying
Description | Primary | Secondary | Local
Ellipsoid height (cm) | 2 cm | 3 cm | 5 cm
Horizontal (cm) | 1 cm | 1.5 cm | 2.5 cm
Orthometric height (cm) | 3 cm | 4 cm | 6 cm
All accuracies are at 95% confidence; network & local
Requirement for Network RTK method | Primary | Secondary | Local
Repeat number & duration of occupations | (6) 5 min. | (3) 5 min. | (3) 5 min.
Longest allowable vector | 40 km | 40 km | 40 km
Precision of repeat vectors | N/E: 3 cm Up: 6 cm | N/E: 4 cm Up: 8 cm | N/E: 5 cm Up: 10 cm
Maximum vector residuals (observed minus adjusted) | N/E: 1.5 cm Up: 3.0 cm | N/E: 2.0 cm Up: 4.0 cm | N/E: 2.5 cm Up: 5.0 cm
17

## Slide 18: Key Takeaways
Software developers are adopting GVX as a standard file format for GNSS vectors
GVX facilitates uploading GNSS vectors to OPUS-Projects 5 for quality control, adjustment, and (optionally) submission to NGS for publication
OPUS-Projects 5.1 is now live and freely available for use
18

## Slide 19
Questions?
Please feel free to contact me with any questions.
daniel.gillins@noaa.gov