## Slide 1: Modernizing the National Spatial Reference System Foundation Continuously Operating Reference Stations 2018 NSRS Modernization Industry Workshop May 5, 2018

## Slide 2: Continuously Operating Reference Stations (CORS)
  ~1800 Continuously Operating Reference Stations
  Run by more than 200 organizations (various government, academic, and private organizations)
  Provide access to the U.S. National Spatial Reference System
1

## Slide 3: Guiding Principles for Continuously Operating Reference Stations
By 2022, the National Spatial Reference System (NSRS) will be modernized, with CORS becoming a more foundational component.
The International Earth Rotation and Reference Systems Service (IERS) International Terrestrial Reference System (ITRF) will continue to be the worldwide standard reference system.
NGS will continue to support the ITRF through International GNSS Service (IGS) reference sites—or “Foundation CORS.”
The NSRS will continue to be defined in relation to the ITRF.
2

## Slide 4: Foundation CORS Requirements
Baseline Foundation CORS Network:
Collocate: All sites within the Foundation CORS
target area of the United States,
with existing space geodetic techniques
(SLR, VLBI or DORIS), will have
a collocated Foundation CORS.
  Additional Desired Foundation CORS Network Requirements:
  Density: Install or adopt new stations within the Foundation CORS target area of the United States. (Fulfill the spacing criteria of 800 kilometers within the Foundation CORS target area.)
  Plate Rotation (Euler Pole): Install or adopt new stations within the U.S. Foundation CORS target area to raise the minimum number of Foundation CORS to three on each of the four plates of interest, once the above criteria are met.
  Additional (Gap Filling): Install or adopt new stations, on a case-by-case basis, once the above criteria is met (*).
3

## Slide 5: Foundation CORS Requirement Breakdown
Frame | Requirement | Comment | Count
CATRF2022 |  |  | 3
 | #1 - Collocate | 1 collocated site | 1
 | #2 - Density | 800 km spacing achievable once above criteria are met | 0
 | #3 – Euler | A total of 3 per plate requires that 2 more FC’s be installed | 2
 | #4 – Gap Filling | none | 0
MATRF2022 |  |  | 3
 | #1 - Collocate | none | 0
 | #2 - Density | 1 station for achievable 800 km spacing | 1
 | #3 – Euler | A total of 3 per plate requires that 2 more FC’s be installed | 2
 | #4 – Gap Filling | none | 0
NATRF2022 |  |  | 26
 | #1 - Collocate | Collocations required, several sites have multiple space based systems only requiring 1 CORS | 17
 | #2 - Density | 800 km notional spacing requires at least 6 more sites to be installed | 7
 | #3 – Euler | Achievable once the above criteria are met | 0
 | #4 – Gap Filling | 1 additional station at Bermuda | 2
PATRF2022 |  |  | 4
 | #1 - Collocate | Three collocations required (all Hawaii) | 3
 | #2 - Density | 800 km spacing requires 1 installation (American Samoa) | 1
 | #3 – Euler | Achievable with current station | 0
 | #4 – Gap Filling | none | 0
Total Number of Foundation CORS Required |  |  | 36
4

## Slide 6: Collocated with NASA Spaced-Based Technology (SBT)
DORIS = Doppler Orbitography and Radiopositioning Integrated by Satellite
SLR = Satellite Laser Ranging
VLBI = Very Long Baseline Interferometry
5

## Slide 7: Collocated + Density + Plate Rotation + Additional
6

## Slide 8
Phase 1: Incorporate ~28 existing NASA and NSF partner stations and NGS stations into the Foundation CORS network.
Phase 2: Upgrade existing CORS to GNSS to meet Foundation CORS requirements
Phase 3: Construct ~8 new Foundation CORS
Foundation CORS Development Phases
7

## Slide 9: Foundation CORS Project Timeline
2017
2017
Today
9/3 - 9/17
9/3 - 9/4
9/5 - 9/9
9/10 - 9/16
9/17
9/18 - 10/3
9/18 - 9/23
9/24 - 9/26
9/27 - 10/3
9/27 - 10/2
8