## Slide 1
U.S. Datums: Where We’ve Been,
Where We’re Going
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
University of Florida Geomatics Program
Webinar Presentation
October 2, 2018

## Slide 2: Presentation Outline
1. - Introductions.
- National Geodetic Survey.
- Horizontal Datums / New Reference Frames.
- Vertical Datums / New Geopotential Datum.
- Update on NGS Products.
- Questions.

## Slide 3: U.S. Department of Commerce National Oceanic & Atmospheric Administration National Geodetic Survey
Mission: To define, maintain & provide access to the
National Spatial Reference System (NSRS)
to meet our Nation’s economic, social & environmental needs
National Spatial Reference System
* Latitude * Scale
* Longitude * Gravity
* Height * Orientation
& their variations in time
Notes: - NSRS benefit to the nation = $2.5B/year
est. 300K precision GPS users worldwide (2008); ¼ in US
- Very exciting to us at NGS to see how it has evolved over the years – now cm-accuracy capability / tracking with time

## Slide 4: NGS MISSION - The NSRS
Define - National Coordinate Sys. (NSRS)
Maintain - the NSRS
Provide Access
Notes: Define: explain how NSRS was developed through the passive network, status of passive network, and how NSRS now based on CORS network.
Maintain: determination of CORS positions and the changes to those positions, datum (ref. frame) updates (ex. NAD (2011), updated hybrid geoid models, programs and tools for transformations, inverses, on-line vertical leveling adjustments, Geodetic Tool kit.
Access: provide access to the NSRS through CORS static data, control mark datasheets, and the suite of OPUS products.

## Slide 5: U.S. Horizontal (& Geometric) Datums

## Slide 6
Datums - Horizontal
Horizontal
North American Datum Of 1927
- Used early triangulation surveys (first called US Std Datum).
- Based at Meades Ranch, KS & used Clarke 1866 spheroid.
North American Datum of 1983 (1986)
- Used 250,000 points (triangulation, Doppler, a few GPS pts).
- Based at geocentric location using Geodetic Ref. Sys. 1980.
Updates*
NAD83 (1990’s) – State HARN / FBN surveys.
NAD83 (late 90’s – early 2000’s) – Efforts to establish ellipsoid heights.
NAD83 (2007) – Remove regional distortions, better with align CORS.
NAD83 (2011) – Adjustment to realign CORS / passive control.
* Not a new datums

## Slide 8: National Spatial Reference System(NSRS) Improvements in the Horizontal Datums
TIME NETWORK METHOD
NETWORK SPAN ACCURACY OF REFERENCE
NAD 27 1927-1986 10 meter (1 part in 100,000)
NAD83(86) 1986-1990 1 meter (1 part in 100,000)
NAD83(199x)* 1990-2007 0.1 meter B-order (1 part in 1 million)
HARN A-order (1 part in 10 million)
NAD83(2007) 2007 - 2011 0.01 meter 0.01 meter
(CORS)
NAD83(2011) 2011 - 2022 0.01 meter 0.01 meter
(CORS)
TRAVERSE & TRIANGULATION -
GROUND MARKS USED FOR REFERENCING THE NSRS.
GPS BECOMES MEANS OF POSITIONING – STILL GRND MARKS.
GPS – CORS STATIONS ARE MEANS OF REFERENCE FOR THE NSRS.

## Slide 9
NSRS Reference Basis
Old Method - Ground
Marks (Terrestrial)
New Method - GNSS Stations
(CORS)

## Slide 10: NGS Published CORS

## Slide 12
NAD83 is NON-geocentric & hence inconsistent w/GNSS
(datum is near 40 years old)
Difficult to maintain consistency between CORS & passive networks
NAD 83 does not track / report passive mark motion
Lack of monument stability / permanency
Necessary for agreement with future ubiquitous positioning capability
Why Replace NAD83?

## Slide 13
Why Replace NAD83? – Future Uses of the NSRS
Notes: Use of GNSS technology is widely used today in surveying, mapping, navigation will cell. Phones, auto on-board navigation, and autonomous driving is fine in open pit mines, but do we really want autonomously driven trucks operating with maps that may be in error because of the difference between NAD83 and GNSS positioning?

## Slide 15: Future Geometric (3-D) Reference Frame
Blueprint for 2022: Part 1 – Geometric Datum
Replace NAD83 with new geometric reference frame – by 2022.
CORS-based, accessed via GNSS observations.
Coordinates & velocities in ITRF (IGS) & new US reference frame.
Passive control tied to new reference frame (not a component).
Transformation tools will relate NAD83 to new US reference
frame (NCAT with 2022 transformation).

## Slide 16: Four Frames/Plates in 2022
Tectonic plates modeled by NGS
July 12, 2017
2017 Esri User Conference
13

## Slide 17: Datum Names
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 18
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.
NSRS Plate Rotation Modeling
EULER Pole
18

## Slide 19: Intra-frame velocities
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748
This is the velocity of the
point in ITRF. Includes all
movements, but the
dominant one is the
rotation of the N.A. Plate.
This is the velocity of the
point in NATRF2022.
Rotation of plate removed.
It is not constant because
the point still suffers small
“intra-frame” velocities.
Such IFVs will be captured
in a model by NGS.

## Slide 20: Horizontal velocities after Repro1
Note scale difference between West (10 mm/yr) and east (2 mm/yr)
Intra Frame Velocity Models to be defined for each TRF.

## Slide 21
New geometric datum minus NAD 83 (horizontal)
For Florida = 0.8 > 1.02 m (2.6 > 3.3 ft.)

## Slide 22
New geometric datum minus NAD 83 (ellipsoid height)
For Florida = -1.39 > -1.62 m (-4.5 > -5.3 ft.)

## Slide 23: Determining Geometric Positions After 2022
GNSS Lat., Long., Hght
CORS Ref. Positions
TRF Referenced
Positions
Real-Time
Positioning
Post Processing
GNSS Lat., Long., Hght
Notes: Use of GNSS technology is widely used today in surveying, mapping, navigation will cell. Phones, auto on-board navigation, and autonomous driving is fine in open pit mines, but do we really want autonomously driven trucks operating with maps that may be in error because of the difference between NAD83 and GNSS positioning?

## Slide 24: U.S. Vertical Datums

## Slide 25
VERTICAL CONTROL USED FOR NGVD 1929 DATUM

## Slide 27
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good enough anymore?
* NAVD 88 is a terrestrial based vertical datum that changes as the land changes.

## Slide 28
Long term fix: Re-level some/all of NAVD 88
  81,500 km of 1st order leveling at least
  625,000 km of mixed 1st and 2nd order leveling
Re-leveling NAVD 88 estimated to cost between
  $200 Million and $2 Billion
Time factor in that amount of leveling
Still would have problems related to passive control
Can NAVD 88 be fixed?
Notes: Re-leveling NAVD 88 won’t fix:
Sparseness of the bench marks
Continued subsidence or uplift of bench marks
Destruction of bench marks
Canada’s decision not to adopt NAVD 88
Whatever errors caused a continent-wide 1 meter build up in the leveling the first time around

## Slide 30: NEW VERTICAL DATUM (Rationale)
  A move away from differentially leveled passive control as the defining mechanism of the reference surface
  To be consistent with the shift in the geometric reference frame/ellipsoid (2022)
  Improvement in our technical abilities in reference surface realization (geopotential gravimetric reference surface - 1cm accuracy of the geoid (GNSS/GRAV-D))
  Goal - ability to establish 2cm orthometric height anywhere in U.S. using a minimum of 15 min. of GNSS data.
  The new geopotential reference surface will be aligned with the geometric reference frame/ellipsoid (i.e., no hybrid geoid)

## Slide 31: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 32: Expected changes to orthometric heights
For Florida = 0.1 > -0.3 m (4 > -11 in.)

## Slide 33
Decades of gravity surveys are inconsistent with one another (1755 surveys)
Airborne gravity will provide a baseline for removing these inconsistencies… … as well as “filling in” information between the resolutions of satellite and ground data.
Problems with Gravity Holdings
%
Notes: This slide shows “crossovers” between any of the 1755 terrestrial gravity surveys which NGS holds in its database. These are
basically mismatches between surveys that overlap one another, plotted at the point of overlap. Note that the color bar
is +/- 2 mGals, and how many surveys disagree with one another at that level. GRAV-D flights should yield about 2 mGal
accuracy surveys, and help reduce the level of disagreement to that range.
The vertical axis of the lower plot is “Percent of points with this level of crossover error” So while it is bell-shaped around -0.26 mGals, the “wings” at the >+2 or <-2 range contain a good 45-50% of all crossovers.
Added October 2010.

## Slide 34: Current and Best NGS Geoid: USGG2012
GRACE + 2 yrs. of GOCE + other satellite data
+ World Gravity Model (EGM2008)
+ Estimated Gravity from Topography
+ Around Two Million Surface Gravity Points
But even this isn’t good enough for a 1-2 cm accuracy vertical reference surface

## Slide 35
Replace the Vertical Datum of the USA by 2022 (at today’s funding)
GRAV-D is:
  An airborne gravity survey of the entire country and its holdings
  A 2022 gravimetric geoid accurate to 1 cm
  Long-term monitoring of geoid change over time
  Partnership surveys
Working to launch a collaborative effort with the USGS for simultaneous magnetic measurement
Acting Manager: Monica Youngman
Monica.Youngman@noaa.gov
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
Gravity and Heights are
inseparably connected
Notes: GRAV-D is the NGS project designed to replace NAVD88 with a vertical datum based upon a gravimetric geoid accurate to 1 cm. Heights above this datum will be accessed via GNSS measurements. Three thrusts of project. Launch USGS collaboration for simultaneous mag measurement.

## Slide 36
Building a Gravity Field
Long Wavelengths
(≥ 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths
(500 km to 20 km)
Airborne Measurement
Surface Measurement and
Predicted Gravity from Topography
Short Wavelengths
(< 100 km)
+
+
Notes: Give example of how short wavelength information is like low altitude aerial photos (1/2” pixel accuracy) in that it provides very accurate and detailed information. The long wavelength gravity can be likened to the old LANDSAT imagery (3 meter pixel accuracy) in that it was good over large areas, but didn’t give much detail for local areas. The intermediate wavelength gravity data gives us a connection between the two (the short and long), allowing the NGS gravity team to use all available gravity information in working toward the production of a 1 cm accurate gravitational surface.

## Slide 37
“Action speaks louder than words but not nearly as often.” ― Mark Twain
Prove that our goal with GRAV-D is possible:
“...the gravimetric geoid used in defining the future vertical datum of the United States should have an absolute accuracy of 1 centimeter at any place and at any time.”
-- The NGS 10 year plan (2008-2018)
Notes: The above quote refers to one of many ambitious goals in the NGS 10 year plan. While admirable, its achievability remains an open question. In order to begin addressing the actual achievable accuracy of a gravimetric geoid model, NGS will engage in a variety of testing methods prior to the 2022 date when the gravimetric geoid will serve as the reference surface for a new vertical datum. The first such testing method took place in the summer of 2011 and is known as the Geoid Slope Validation Survey of 2011, or GSVS11. As its name implies, this survey tested the accuracy of differential geoid undulations between points ("geoid slopes") from NGS's gravimetric geoid models. The baseline for comparison will be independently computed geoid slopes from two methods, GPS and leveling as well as Deflections of the Vertical.

## Slide 38: Validating Geoid Accuracy
NGS has performed 3 surveys to validate the accuracy of the gravimetric geoid model
  Geoid Slope Validation Survey (GSVS) 2011
    2011; Low/Flat/Simple: Texas; Done; Success!
  GSVS14
    2014; High/Flat/Complicated: Iowa; Field work Complete
  GSVS17
    2017; High/Rugged: Colorado; Field work complete.

## Slide 39: Surveys Performed
GPS: 20 identical units, 10/day leapfrog, 40 hrs. ea.
Leveling: 1st order, class II, digital barcode leveling
Gravity: FG-5 and A-10 anchors, 4 L/R in 2 teams
DoV: ETH Zurich DIADEM GPS & camera system
LIDAR: Riegl Q680i-D, 2 pt/m2 spacing, 0.5 km width
Imagery: Applanix 439 RGB DualCam, 5000’ AGL
Other: RTN, short-session GPS, extra gravity marks around Austin, gravity gradients

## Slide 40: GSVS11 Results
Chart: Predicted Errors of various geoid models over GSVS11 after removal of GPS/Leveling error budget
| 0.4 - 15 | 15 - 30 | 30 - 46 | 46 - 63 | 63 - 81 | 81 - 101 | 101 - 122 | 122 - 145 | 145 - 172 | 172 - 204 | 204 - 247 | 247 - 325
USGG2009 | 0.87101 | 1.0601 | 1.364 | 1.665 | 1.8562 | 2.2611 | 2.5576 | 2.6428 | 2.8322 | 2.8066 | 2.4464 | 1.4332
EGM2008 | 0.87101 | 1.1721 | 1.5813 | 1.8794 | 1.9635 | 2.0475 | 2.1311 | 2.4299 | 2.6195 | 2.5918 | 2.774 | 1.9324
xEGM-G | 0.87101 | 1.2821 | 1.6884 | 2.091 | 2.491 | 2.7861 | 2.9768 | 2.9588 | 2.7261 | 2.1534 | 1.9962 | 2.618
xEGM-GA | 0.75409 | 0.82689 | 0.90587 | 0.98594 | 0.94092 | 1.021 | 1.1006 | 0.9134 | 0.67938 | 0.56322 | 0.80921 | 1.5634
xUSGG-GA-R-K480 | 0.75409 | 0.94538 | 1.025 | 1.1055 | 1.0655 | 1.1456 | 1.2253 | 0.9134 | 0.14682 | 0.29532 | 0.62034 | 1.1551
“1 cm geoid”
Geoids
without
GRAV-D
Geoids with
GRAV-D
xUSGG2011
Notes: This slide is a companion to the previous one, but the h-H errors have been removed, in an RMS sense, from the total h-H-N errors, leaving gravimetric geoid model errors only.
As seen previously, the geoids based on airborne gravity data are the best performers, and the very slight degradation using new high resolution software at short wavelengths is noticeably offset by the significant improvement at medium wavelengths.
In fact, as a general statement, it could be said that adding airborne gravity data to the gravimetric geoid model has yielded about 1 cm differential geoid undulation accuracy across all distances (orange and red bars), in the region of GSVS11, and that this can be further improved by continued improvement to the high resolution modeling software.

## Slide 41: Determining Orthometric Heights After 2022
Ellipsoid Height
Geoid Height
Orthometric Height
Notes: Use of GNSS technology is widely used today in surveying, mapping, navigation will cell. Phones, auto on-board navigation, and autonomous driving is fine in open pit mines, but do we really want autonomously driven trucks operating with maps that may be in error because of the difference between NAD83 and GNSS positioning?

## Slide 42: Geoid Monitoring Service (GeMS)
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Aspects included:
  Shape, Secular: e.g. Hudson Bay
  Shape, Episodic: e.g. Massive Earthquakes
  W0, Secular: Global Sea Level Change (see next slides)
Examples of things excluded:
  Size, Secular: Mass quantity of Earth is effectively static
  Shape, Periodic: Seasonal glacier cycle

## Slide 43
Extent of 2022 gravimetric geoid model used for NAPGD2022

## Slide 44: Preparing for New Reference Frames

## Slide 45: How to Plan for 2022
Move to newest realizations
  NAD 83(2011) epoch 2010.00
  GEOID12B (hybrid geoid)
Move to NAVD 88
  understand the accuracy of VERTCON in your area
Utilize passive marks that are up to date
  Stay aware of what marks are included in datum updates
  Use OPUS & Hgt. Mod procedures to update mark positions
Use OPUS for GPSBMs
  Help improve future geoid models & relationship with new datum
NGS Outreach Efforts
  Participate in NGS webinars, Geospatial summits, contact NGS Regional Advisor, etc.

## Slide 46: Metadata is Critical
Your positional metadata should include:
  datum
  epoch
  source / methods
These will facilitate transforming from current to new datum
Maintaining your original survey data will provide more accurate results
Notes: Metadata related to how someone establishes control is important. Important for today’s positions, but especially as we moving toward and into the coming new datums in 2022.

## Slide 47: State Plane Coordinates System 2022

## Slide 49: SPCS Special Publication
History of NGS projections (1853 to present)
SPCS policies and legislation
Departures from policy and convention
Recent developments in projected coordinate systems
Appendices
  Defining parameters for ALL zones of ALL versions of SPCS, plus additional information
  Status of SPCS 83 legislation and foot conversions

## Slide 54: GPS on Bench Mark Project & Geoid 18

## Slide 55
www.ngs.noaa.gov

## Slide 56: What is “GPS on Bench Marks“ ?
Collecting GPS observations on a bench mark that has a NGS published orthometric height from leveling, which provides accurate information:
latitude, longitude, and ellipsoid height

## Slide 57
  Why have another GPS on BM Project?
In preparation for new U.S. datums in 2022 (NATREF2022 / NAPGD2022).
Transformation model between NAVD88 & NAPGD2022 using NCAT.
Significant amount of new Blue Booking projects across U.S. (leveling, GNSS (GPS)) since the publishing of Geoid 12B. (FL - 203 new BM’s)
Many new OPUS Share submittals since Geoid 12B
(FL – 878 on NGS BM’s).
Will help in the production of Geoid 18 (April 2019).

## Slide 59
Notes: https://www.youtube.com/playlist?list=PLsyDl_aqUTdFY6eKURmiCBBk-mP4R10Dx

## Slide 60: Coordinate Conversions - NCAT

## Slide 61: NADCON5 in the Geodetic Toolkit

## Slide 62
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83

## Slide 63
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 64
? ? QUESTIONS ? ?