## Slide 1: OPUS Adds New Functionality OPUS Projects Beta goes to Production!
NGS Webinar Series
Thursday, February 11 2021
Philippe Hensel, PhD, and the OP4.0 Team

## Slide 2: Acknowledgments
Thank you to the entire OP4.0 Team!
Mark Schenewerk
Julie Prusky
Boris Kanazir
Daniel Gillins
Dave Zenk
Jeff Jalbrzikowski
Bill Stone
Kevin Jordan
Erika Little
Michael Dennis
John May
Dan Prouty
Rick Foote

## Slide 3: Major OPUS Milestones
2002: NGS’ new Online User Position Service is launched
Free, online GPS post-processing software for accurate positioning! >2hr observation files required. This is commonly referred to as “OPUS Static.”

## Slide 4: Major OPUS Milestones
2002: NGS’ new Online User Position Service is launched!
2007: OPUS Rapid-Static processes 0.25-2hr observation files

## Slide 5: Major OPUS Milestones
2002: NGS’ new Online User Position Service is launched
2007: OPUS Rapid-Static processes 0.25-2hr observation files
2009: OPUS Share goes live
Users can upload their >4hr GPS observations and metadata, “sharing” their data with others online via OPUS datasheets

## Slide 6: Major OPUS Milestones
2002: NGS’ new Online User Position Service is launched
2007: OPUS Rapid-Static processes 0.25-2hr observation files
2009: OPUS Share goes live
2012: OPUS Projects is launched
OPUS Projects enables users to process simultaneous GPS observations (sessions) and conduct a least-squares network adjustment.

## Slide 7: Major OPUS Milestones
2002: NGS’ new Online User Position Service is launched
2007: OPUS Rapid-Static processes 0.25-2hr observation files
2009: OPUS Share goes live
2011: OPUS Projects is launched
2021: OPUS Projects provides a path to publication

## Slide 8: Major OPUS Milestones
2021: OPUS Projects automates and provides intuitive output for most of the steps traditionally involved in “bluebooking” a GPS project
Before:
FCGS
Blue Book
You had to know BB file formats, you had to know how to resolve errors
After:
You are freed from having to learn & understand BB files!
Let OPUS Projects do the heavy lifting so you can fly!

## Slide 9
What the new OPUS-Projects will do for you
Automatically selects recommended session processing defaults
Arranges data files into intuitive (simultaneously observed) sessions
Selects appropriate CORSs/IGS stations to control your project
Suggests appropriate Session Processing
Suggests appropriate Preliminary Network Adjustment
Suggests appropriate sequence of Final Network Adjustments
Allows you to upload all files needed for submission to NGS

## Slide 10
What OPUS-Projects won’t do for you.
OPUS-Projects does not make a project proposal obsolete.
OPUS-Projects does not make field logs obsolete.
OPUS-Projects does not make mark descriptions obsolete.
OPUS-Projects does not make mark photos obsolete.
OPUS-Projects does not make obstructed marks GNSS-able.
OPUS-Projects does not make bad data good.
OPUS-Projects does not automate all processing decisions but it will make good suggestions.
OPUS-Projects does not quality control results as well as you.

## Slide 11: Guiding Principles
Support all users of OP, but especially the new pathway to the IDB
Create new, comprehensive User Guide & associated training materials
Provide direction
Keep things simple (if possible)
Be clear
Avoid repetition
Project Planning
NGS Survey Project Proposal Review
OP4.0 Project
Survey Mark 1 GPS File 1
Survey Mark 2 GPS File 1
Survey Mark 3 GPS File 1
Survey Mark 4 GPS File 1
Survey Mark 1 GPS File 3
Survey Mark 2 GPS File 3
Survey Mark 3 GPS File 3
Survey Mark 4 GPS File 3
Survey Mark 1 Description
Survey Mark 2 Description
Survey Mark 3 Description
Survey Mark 4 Description
Survey Mark 1 Photos
Survey Mark 2 Photos
Survey Mark 3 Photos
Survey Mark 4 Photos
OPUS
NGS Publication
NGS Datasheets
Session 1
Session 2
Session 3
OPUS Solutions
Survey Mark 1 GPS File 2
Survey Mark 2 GPS File 2
Survey Mark 3 GPS File 2
Survey Mark 4 GPS File 2
Survey Mark 1 All Field Logs
Survey Mark 2 All Field Logs
Survey Mark 3 All Field Logs
Survey Mark 4 All Field Logs
Preliminary Adjustments
Preliminary Adjustments
Preliminary Adjustment
Preliminary Adjustments
Preliminary Adjustments
Horizontal Fee Adjustment
Preliminary Adjustments
Preliminary Adjustments
Horizontal Constrained Adjustment
Preliminary Adjustments
Preliminary Adjustments
Vertical Free Adjustment
Preliminary Adjustments
Preliminary Adjustments
Vertical Constrained Adjustment
QA/QC
Project Report
Preliminary Adjustments
Preliminary Adjustments
Session Baseline Processing
Steps that remain unchanged from previous versions of OPUS Projects
Optional steps available with advanced features of OPUS Projects 4.0
Preliminary Adjustments
Preliminary Adjustments
Network Adjustment
No Project ID
With Project ID
Survey Project Proposal

## Slide 12: The New OPUS Projects User Guide
Only ONE OPUS Projects and User Guide
User Guide is:
  Step-by-step guide to help you successfully use OP to meet your project goals and get your project through submission to NGS
User Guide is NOT:
  New NGS 58/59 guidelines
  Guarantee your project will be published
  Substitute for least squares adjustment course
  Substitute for learning good survey field practices

## Slide 13: Where we are today
The User Guide has been successfully reviewed both internally and externally
NGS is preparing the document for release in the coming weeks, timed with the release of BetaOP to Production
Training will be provided at two levels
  “OP101” –OPUS Projects for Managers Training
  “OP102” –Using the advanced features of OPUS Projects for submitting your project to NGS (released later this spring)

## Slide 14
Work Flow for OPUS Projects 102… in 12 easy steps!
Project Development
Mark Recovery, Photos
Project Proposal
Create Project in OP
Mark Descriptions
Field Campaign
Load files into project
QA/QC OPUS solutions
Session Processing
Preliminary Network Solution
Network Solutions
Submit to NGS
Topics covered in OP102
Topics covered in OP101

## Slide 15: Submit your Project Proposal for Review
Recommended to submit your Project Proposal prior to conducting the survey

## Slide 16: NGS Survey Project Proposal Form
Why submit your GNSS Project Plan to NGS (https://geodesy.noaa.gov/SurveyProposal/):
Subject Matter Expert will review your plan, make sure it will meet project objectives
NGS will assign a Project Tracking ID, which will enable you to use the advanced features of OPUS Projects
With a Project Tracking ID, you will be able to submit your project to NGS for consideration of inclusion into the national database of geodetic control, available through published datasheets
If you do not intend on submitting your project to NGS, but still wish your project to be tied to the national reference frames/datums, you can use the “dummy” tracking ID “0000”

## Slide 17: CORS Selection
One of the more critical aspects of designing your project
OP will select good CORSs, but don’t assume they are the best
OP’s selection of CORSs based on independent OPUS solutions; they may differ among sessions
Ideally, you will have the same, best CORSs in all sessions
You will have to add a “distant” CORS for tropospheric modeling
The OP User Guide steps you through the process of CORS selection

## Slide 18: CORS Selection – choosing the hub
One of the CORSs selected will be chosen as the hub in session processing
Ideally, the hub should be centrally located to the project and within 100 km from any user mark
If hub lies more than 100 km away from any user mark, you should consider multiple hubs
All hubs have to have data for each session
All hubs must connect in all sessions
For more guidance on hubs, refer to the User Guide

## Slide 19: Network Solutions
Preliminary Network Solution
Horizontal Network Solutions
Seen in OP101: OP recommends holding the hub (CORS) constrained in 3D; many other adjustments possible*
Uses adjustment (and error reduction) software GPSCOM
Network solutions apply least squares adjustments (and error reduction) to session baselines.
Network solutions will not recreate different baselines than the ones already created in session processing.
Only available with NGS Project Tracking ID
Uses adjustment software ADJUST
Requires a Preliminary Network Solution using GPSCOM
*User should use hub design for submitting project to NGS
Vertical Network Solutions
Notes: In this slide, we discuss the differences between OP101 and OP102 with regards to Network Solutions.
In OP101, we discussed how one goes about processing sessions, and then running a network solution on the baselines solved in session processing.
OP will always recommend constraining the hub in 3D, but other adjustments are possible (user beware!!)
Note that in OP101, network adjustments are run using the baseline adjustment (and error reduction) software GPSCOM.
This is where OP101 ends.
GPSCOM is a very robust and highly effective network adjustment program, in many ways superior to ADJUST. However, it is not ideally configured to align the network solution to the latest realization of NAD83.
For this reason, for submitting a GPS project to NGS, we must use ADJUST. OP now supports the use of ADJUST in a sequential set of network solutions.
So in OP102, we take up where OP101 left off: the network adjustment we saw recommended after session processing is now called the “Preliminary Network Solution.”
This GPSCOM-based network solution is still REQUIRED, but additional horizontal ad vertical adjustments using ADJUST are needed.
In this module, we’ll cover the two separate horizontal adjustments needed to submit your project to NGS.

## Slide 20: OPUS Projects Live Demo
http://beta.ngs.noaa.gov/OPUS/

## Slide 21: Questions?