## Slide 1: OPUS Projects Improvements
Mark Schenewerk
mark.schenewerk@noaa.gov
816-994-3067

## Slide 2
I’ve chosen to look to the future - but only about one year.
This list is not comprehensive, but I think the enhancements mentioned will be of particular interest to OPUS-Projects users.
The items are listed chronologically by their planned deployment.
I apologize that this presentation will not include any pictures, plots or screen captures. Get your favorite caffeine source in hand!
OPUS Projects Improvements
May 7, 2019
2

## Slide 3
Beta: ITRF2014 coordinates for the CORS network. https://beta.ngs.noaa.gov/CORS/coords.shtml
  Completed March, 2019.
  Production uses the IGS08 reference system.
  Beta OPUS uses the ITRF2014 reference system.
  BETA OPUS-Projects offers a one-time choice to use the ITRF2014 or IGS08 for new projects.
  You will have the option to continue in the IGS08 if your project existed before the ITRF2014 release.
OPUS Projects Improvements
May 7, 2019
3

## Slide 4
Beta: GEOID18. https://beta.ngs.noaa.gov/GEOID/GEOID18/
  Completed(?)
  Production will continue to use GEOID12B.
  Beta OPUS will use GEOID18.
  BETA OPUS-Projects will default to GEOID18 for ITRF2014 projects and to GEOID12B for IGS08 projects.
  Improvements in computing the orthometric height error estimate will be included.
OPUS Projects Improvements
May 7, 2019
4

## Slide 5
Production: ITRF2014 and GEOID18.
  Late June, 2019. (You’ll have plenty of advanced warning.)
  Production OPUS will use ITRF2014/GEOID14.
  Production OPUS-Projects will offer the option to continue in the IGS08 if your project existed before the ITRF2014 release.
  Beta OPUS will be rolled-back to IGS08/GEOID12B as a means for continuity in current user activities.
  BETA OPUS-Projects will continue to offer options for IGS08 or ITRF2014.
OPUS Projects Improvements
May 7, 2019
5

## Slide 6
Beta: Better support for CORS decisions.
  Late summer, 2019.
  I’m currently testing:
    Improved CORS information from inside your project.
    Improved automated selection of hub(s).
    Automated selection of nearby CORS.
    Automated selection of distant CORS.
    “One-click” clean-up of unused CORS.
OPUS Projects Improvements
May 7, 2019
6

## Slide 7
Production: OPUS-Projects 4.0.
  Early 2020.
  This is the operational version of BETA OPUS-Projects and, as BETA OPUS-Projects does now, will facilitate submitting results for publication.
  The roll-out will include updated documentation and training.
  This is a first step towards OPUS Projects for Everything.
OPUS Projects Improvements
May 7, 2019
7

## Slide 8
Beta: OPUS for Real Time Kinematic Data.
  Early 2020.
  Incorporating RTK results into static GPS survey projects significantly increases the utility of OPUS-Projects.
  This is the first step in ingesting other types of vector survey results … and the next step in OPUS Projects for Everything.
OPUS Projects Improvements
May 7, 2019
8

## Slide 9
Beta: Cloud OPUS (or maybe OPUS-Cloud).
  Later next year? (Sooner rather than later I hope.)
  Cloud computing is “the on demand availability of computer system resources, especially data storage and computing power.” https://en.wikipedia.org/wiki/Cloud_computing
  Imagine OPUS running on dozens of servers rather than the handful that NGS can maintain.
    Waiting-in-queue delays will almost disappear.
    Access outages will almost disappear.
OPUS Projects Improvements
May 7, 2019
9