## Slide 1
The Modernized National Spatial Reference System
Boris Kanazir, Geodesist, RPLS
boris.kanazir@noaa.gov
TRB Geospatial Data Acquisition Technologies (AKD70)
2020 Summer Meeting
August 4, 2020

## Slide 2
2022: Will it be this grim?

## Slide 4: Geodetic Control
OMB A-16: “The NSRS is the fundamental geodetic control for the United States.”
Easiest way to think of “geodetic control”: Points with Coordinates
  But please do start to think of “Coordinates” as “Coordinates as a function of time”

## Slide 5: Active vs. Passive Geodetic Control
It might be best to set aside the terms “active” and “passive” and think solely in terms of trusted geodetic control
However, sometimes this shorthand will be used for simplicity:
  Passive control: Infrequently observed marks
  Active control: A station with continuous data collection

## Slide 6: Geodetic Control — Purpose
NGS defines and provides access to a datum
  Points with given coordinates
  The “foundational layer” of any geospatial work
  To be more accurate than any survey or map which builds upon it

## Slide 7: Horizontal Datums of the NSRS
* Actually state-by-state realizations feathered together over a decade or so
** Not an official name at creation. Little public documentation.
CONUS | U.S. Standard Datum | NAD 27 | NAD 83(1986) | NAD 83(“HARN”)* | NAD 83(“FBN”)* | NAD 83(NSRS2007) | NAD 83(2011) epoch 2010.00
Alaska | NAD 27 | NAD 83(1986) | NAD 83(2002:AK) | NAD 83(NSRS2007) | NAD 83(2011) epoch 2010.00 |  | 
Hawaii | Old Hawaiian Datum** | NAD 83(1986) | NAD 83(1993:HI) | NAD 83(PA11) epoch 2010.00 |  |  | 
PR/VI | Puerto Rico 1940** | NAD 83(1986) | NAD 83(1993:PR) | NAD 83(1997:PR) | NAD 83(2002:PR) | NAD 83(NSRS2007) | NAD 83(2011) epoch 2010.00
Am. Samoa | American Samoa 1962 | NAD 83(1993:AS) | NAD 83(2002:AS) | NAD 83(PA11) epoch 2010.00 |  |  | 
Guam/CNMI | Guam 1963 | NAD 83(1993:GU) | NAD 83(2002:GU) | NAD 83(MA11) epoch 2010.00 |  |  | 
St. Paul | St. Paul 1897** | St. Paul 1952** | NAD 83(1986) | NAD 83(2002:AK) | NAD 83(NSRS2007) | NAD 83(2011) epoch 2010.00 | 
St. George | St. George 1897** | St. George 1952** | NAD 83(1986) | NAD 83(2002:AK) | NAD 83(NSRS2007) | NAD 83(2011) epoch 2010.00 | 
St. Lawrence | St. Lawrence 1952** | NAD 83(1986) | NAD 83(2002:AK) | NAD 83(NSRS2007) | NAD 83(2011) epoch 2010.00 |  | 
St. Michael | St. Michael 1952** |  |  |  |  |  | 
Columns not aligned between regions

## Slide 8: Vertical Datums of the NSRS
CONUS | NGVD 29 | NAVD 88
Alaska | NGVD 29 | NAVD 88
Hawaii |  | 
PR | PRVD 02 | 
USVI | VIVD 09 | 
Am. Samoa | ASVD 02 | 
Guam | GVD 1963 | GUVD 04
CNMI | NMVD 03 | 
St. Paul |  | 
St. George |  | 
St. Lawrence |  | 
St. Michael |  | 
Great Lakes | IGLD 55 | IGLD 85
Columns not aligned between regions

## Slide 9: Reminder…
WGS 84 is not part of the NSRS
  It is a military-controlled system
All civilian federal agencies are required to work in the NSRS (as per OMB A-16)
  NAD 83 is part of the NSRS
  NAD 83 ≠ WGS 84
    (unless 2+ meters of systematic bias doesn’t bother you)
Many states and municipalities choose to work in the NSRS
  And often legislate this use

## Slide 10: Decision to Modernize
In 2007 NGS announced its decision to completely change how it approached its mission.
In a word, they chose to modernize the NSRS
Let’s look at the issues that drove that decision, and the direction they decided to go

## Slide 11: Issues
NAVD 88 suffers from use of passive control that:
Is almost never re-checked for movement
Disappears by the thousands every year
Is not funded for replacement
Is not necessarily in convenient places
Doesn’t exist in most of Alaska
Wasn’t adopted in Canada
Was determined by leveling from a single point, allowing the build up of cross-country error
PID: EZ0840

## Slide 12: Issues
NAVD 88 suffers from a known bias (50 cm) and tilt (about 1 meter across CONUS) relative to the gravimetric geoid
PID: EZ0840
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface

## Slide 13: Issues
~2.24 m
NAD 83 origin
ITRF origin
Earth’s Surface
hNAD83
hITRF
NAD 83 suffers from a 2+ meter non-geocentricity (which misaligns it with ITRF and all GNSS orbits)

## Slide 14: Issues
Geodetic control is usually affixed to a crust that is moving
  Even so-called “plate fixed” frames are only as stable as:
    The rigidity of a plate
    The complete lack of subsidence or uplift

## Slide 15: General Direction
Future details would come, but in 2007 the general direction was:
  Replace both NAD 83 and NAVD 88, at the same time
  Transition to a geoid-based vertical datum
  Leverage the rise of GNSS and RTNs
  Completely re-invent “bluebooking”
    Reduce complexity
    Retain ability to standardize geodetic survey files

## Slide 16
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
Sep 2017
NOAA TR NOS NGS 62
32 pages
Geopotential:
Nov 2017
NOAA TR NOS NGS 64
41 pages
Working in the
Modernized NSRS:
April 2019
NOAA TR NOS NGS 67
77 pages
All three documents are being updated and re-released in 2020!!

## Slide 17: Replacing the NAD 83s
The Old | The New
NAD 83 (2011) | NATRF2022 - The North American Terrestrial Reference Frame of 2022
NAD 83 (2011) | CATRF2022 - The Caribbean Terrestrial Reference Frame of 2022
NAD 83 (PA11) | PATRF2022 - The Pacific Terrestrial Reference Frame of 2022
NAD 83 (MA11) | MATRF2022 - The Mariana Terrestrial Reference Frame of 2022

## Slide 18
Four Tectonic Plates

## Slide 19: The TRFs
All are global frames (no “boundary”)
  This was true for the NAD 83s also, BTW
  But each frame will rotate with one tectonic plate
    Put another way: “The frame rotates so your coordinates don’t have to”

## Slide 20
ITRF2020: Constant Frame, Rotating Plate

## Slide 21: “Plate-Fixed”
NATRF2020: Constant Frame, Rotating Plate

## Slide 22
ITRF2020 or NATRF2022 — Your choice, just use EPP2022

## Slide 23: Shift and Drift
When transitioning off of NAD 83, your coordinates will experience shift and drift
  Shift: A one-time jump somewhere in the 0 to 4 meter range (latitude, longitude, ellipsoid height)
    From fixing NAD 83’s non-geocentricity
  Drift: Coordinates are now time-dependent. The shift will take you to 2020.00. Working at any other epoch means you must account for the drift (velocity) of your coordinates
    As well as any other motions over time

## Slide 24: NAD 83(2011) epoch 2010.0 to NATRF2022 epoch 2020.00 (estimate)

## Slide 25: Drift
What does it mean to provide time-dependent coordinates in 5 frames?
  Let’s look at the known velocities of some active control stations in ITRF2020, NATRF2022, PATRF2022, CATRF2022 and MATRF2022

## Slide 26: BSMK (North Dakota)

## Slide 27: BSMK (North Dakota)
Note the time-dependent coordinate in latitude in NATRF2022 is stable! That means the NATRF2022 IFVM* for latitude will be ZERO for this point.
t0=2020.0, when all five frames are identical

## Slide 28: BSMK (North Dakota)
Similarly, the time-dependent coordinate in longitude in NATRF2022 is stable! That means the NATRF2022 IFVM for longitude will be ZERO for this point.

## Slide 29: BSMK (North Dakota)
However, in every frame, this point is subsiding! That will be captured in the ellipsoid height component of the IFVM for each frame.

## Slide 30: What did all that mean?
Anyone can work in any frame anywhere
“Stable” time-dependent coordinates may look “constant” – don’t get complacent!
  A slight drift, or one earthquake can upset that
Plate fixed frames are nice, but
  Even in “stable” areas (Kansas, for instance) one cannot assume stability

## Slide 31: IFVM2022 Velocities – ITRF2020/CONUS

## Slide 32: IFVM2022 Velocities – NATRF2022/CONUS

## Slide 33: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 34: Shift and Drift
When transitioning from NAVD 88 or another vertical datum, your coordinates will shift and drift:
  Shift: A one-time jump somewhere in the 0 to 2 meter range (orthometric height)
    From fixing biases and/or tilts in NAVD 88 and others
  Drift: Coordinates are now time-dependent. The shift will take you to 2020.00. Working at any other epoch means you must account for the drift (velocity) of your coordinates
    As well as any other motions over time

## Slide 35: NAVD 88 (epoch ?) to NAPGD2022 Epoch 2020.00 (estimate)

## Slide 36: Definitional Relationship
All work is done in ITRF2020 XYZ coordinates first.
They are associated with the epoch of the data collection (survey) “t”, then converted to f, l and (especially relevant here) h.
We end with orthometric height in NAPGD2022 at the same epoch as the survey.
Conversion to orthometric heights is definitional through GEOID2022.
Contrast with NGS hybrid geoids where the equation H=h-N did not close.

## Slide 37: Drift
In geometric coordinates we needed to only concern ourselves with the movement of marks themselves
In the geopotential datum we must also account for the movement of the geoid

## Slide 38: New Types of Coordinates
NGS anticipates that 5 types of coordinates will be used in the NSRS. They are:
Reported
OPUS
Survey Epoch
Reference Epoch
Active

## Slide 39: New Types of Coordinates
Reported
  “These are from any source where the coordinate is directly reported to NGS without the data necessary for NGS to replicate the coordinate.”
    Scaled from a map
    Transformed using NCAT or VDatum
    Smartphone
    Reported directly from an RTK rover without data files

## Slide 40: Reported Coordinates

## Slide 41: Speaking of Smartphones…
NGS has a new mobile-friendly mark recovery webpage. Please try it out!
https://www.ngs.noaa.gov/cgi-bin/mark_recovery_form.prl

## Slide 42: Buyer Beware!
Reported coordinates might be very wrong!
  Reported in NAD 27 or NAD 83 or WGS 84
    Systematic Error: 2–100 meters
  Scaled off of a USGS topographic map
    Random Error: ± 600 meters
  Smartphone
    Random Error: ± 10–50 meters
NGS will show you reported coordinates
  But their function is to get you “in the neighborhood” of a mark, not to use as geodetic control!

## Slide 43: New Types of Coordinates
OPUS
  “These are coordinates at any epoch the user wishes to use that have been computed by that user in OPUS”
    User-computed values, such as they might get today from either OPUS-S or OPUS-Projects
    “OPUS” coordinates are the only coordinates a user will get directly from OPUS
    NGS will not evaluate your OPUS coordinates!

## Slide 44: New Types of Coordinates
Reference epoch coordinates (RECs)
  “These are coordinates which have been estimated by NGS, from time-dependent age-limited historic survey data, CORS coordinate functions and an intra-frame velocity model, at an official NSRS reference epoch
    NAD 83(2011) epoch 2010.00 (sort of) would’ve fallen under this category
    These will be computed by NGS every 5 years
      On a schedule 2–3 years past the reference epoch
        2020.00 coordinates are computed in CY 2022, etc

## Slide 45: New Types of Coordinates
Survey epoch coordinates (SECs)
  “These are coordinates computed by NGS using submitted data and metadata, checked and adjusted and referenced to distinct epochs through time.”
    These represent the best estimates NGS has of the time-dependent coordinates at any mark
    Adjusting multiple surveys in timespans called “adjustment windows”, to a single epoch within that window.
      Initial plan: 4 weeks for GNSS; 1 year for leveling

## Slide 46: New Types of Coordinates
Active coordinates (ACs)
  Not discrete, but rather a function through time assigned to some point
    At a CORS GRP*, they will be the coordinate function
      Which will be generated by a “fit” to regularly computed coordinates on a TBD basis, perhaps daily, perhaps weekly
        These daily or weekly coordinates will not generally be used as geodetic control by themselves
* This is the physical point to which coordinates refer at a station like a CORS

## Slide 47: What “Access” to the NSRS Will Mean
Very similar philosophically:
  The NSRS remains “geodetic control” for you to “access”
    Geospatial information and metadata about various points
    Passive control will exist…we aren’t getting out bulldozers and shovels
      But gone are the days of getting “the coordinate” on a point from a “datasheet”

## Slide 48: What “Access” to the NSRS Will Mean
Very different practically
  Information: from the Data Delivery System (DDS)
    Graphics (pictures, graphs, maps)
  Computations: OPUS
    Do-it-all (mark reporting, positioning, adjustments, etc)
  Heavy emphasis on using GNSS to get to the NSRS
    All constellations will be supported
    Real time helpful CORS information (data availability & quality)
    Use new GNSS
      Or, maybe, some “trusted” passive control
      Otherwise, your OPUS coordinates may say “not NSRS coordinates”
yet

## Slide 49: OPUS
The Online Positioning User Service
  NGS will cease the expanding “hyphenated” versions
    OPUS-Projects, OPUS-S, OPUS-RS, OPUS-Share, etc
  Will replace
    All internal versions of OPUS
    All user versions of OPUS
    All forms of “Bluebooking”
      Analyzing, adjusting, submitting geodetic survey data to NGS
    Mark Recovery and Reporting Tool

## Slide 50: GNSS Is Key
Leveling can (and will) still tell you differential heights
  But for OPUS to provide you absolute NSRS coordinates, you’ll need to “get into the datum”
    Trusted geodetic control:
      Primary: New GNSS to get ellipsoid heights
        Maybe (still under consideration): “Recently” surveyed passive control
        Then GEOID2022 to get orthometric heights
      Then pick an “appropriate” epoch for your adjustment
      Now you’re “in the datum”.

## Slide 51: OPUS will soon take in RTK vectors!

## Slide 52: Example: Upload RTN Vectors to OPUS-Projects
User Mark
Processed Vector (OPUS-Projects)
Uploaded Vector
CORS
LEGEND
Upload Vectors

## Slide 53: Conversion? Transformation?
Historically NGS has been inconsistent with these two words. Going forward, we will use them as:
  Conversion: Changing the type of coordinate without changing the datum or frame
    e.g. change NAD 83(1986) latitude and longitude to NAD 83(1986) State Plane Coordinates
  Transformation: Changing the datum or frame, without changing the type of coordinate
    e.g. changing an NAD 27 latitude & longitude to an NAD 83(1986) latitude & longitude
So, for example, “NADCON” which transforms coordinates between datums really should have been called “NADTRAN.” C’est la vie.

## Slide 54: NCAT - with NADCON & VERTCON!

## Slide 55: Ways to Use NCAT
Browser: Interactive, 1 point at a time
Browser: Upload a file / get a file back (text, xlsx)
As a Web Service
Download and run locally
  Beware: This works, but NCAT is updated frequently, so the copy you have may be outdated, so always download the latest version

## Slide 56: A New State Plane for 2022
State Plane Coordinate System of 2022 (SPCS2022)
  Referenced to 2022 Terrestrial Reference Frames (TRFs)
  Based on same reference ellipsoid as SPCS 83 (GRS 80)
  Same 3 conformal projection types as SPCS 83 and 27:
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 57: Overall SPCS2022 characteristics
Minimize distortion at topo surface, not ellipsoid
NGS will design:
  Statewide zone for every state
  Default zones if no input from stakeholders (most with same zone extents and projection type as SPCS 83)
Max of up to 3 zone “layers” allowed
  1 statewide plus 0, 1, or 2 multiple-zone layers
  Most states will have total of 2 layers

## Slide 58: Overall SPCS2022 characteristics
Stakeholders can request and propose preferences
  Proposal and request deadline was March 31, 2020
  Can still change/add/remove zones after 2022
See SPCS2022 policy and procedures for details https://geodesy.noaa.gov/SPCS/policy.shtml
Many states requested and proposed preferences
  All zone designs will be finalized in 2021
  Can change/add/remove zones after official rollout

## Slide 59
Grid distance < ellipsoidal distance (distortion < 0)
Grid distance > ellipsoidal distance (distortion > 0)
Projection axis
Projection surface (secant)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid and ground
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
Ellipsoid surface
Positive and negative distortion with respect to ellipsoid is balanced over width of zone; distortion at topo surface not considered.

## Slide 60
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
Ellipsoid surface
Grid distance = ground distance at many points
Topographic surface
This design approach is used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis
Non-intersecting
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance outside area of interest
Grid distance ≈ ground distance over finite distance
Topographic surface
ONLY way to reduce variation in distortion is to change projection axis location (or change projection type).
Area of interest

## Slide 61: SPCS2022 zones designed by NGS
Linear distortion design criterion
  Parts per million (ppm), e.g., ±20 , ±50 , ±100 ppm, etc.
Criterion must satisfy all of following:
  90% of population
  75% of all cities and towns (by location only)
  50% of entire zone area
Limitations for designs by NGS
  Minimum design criterion ±50 ppm (1:20,000)
  May be less for default zones if existing zone small
Low distortion projections (LDPs): < ±50 ppm
  Must be designed by others

## Slide 62: Bye, bye, U.S. survey foot…
In modernized NSRS, NGS will support only one definition of the “foot”
  Previously called the “international foot”
  Now, just the “foot”
  1 foot = 0.3048 meter (exact)
However
  Recommend using term “international foot” when there is potential for confusion with other foot
  NGS will continue to support U.S. survey foot for legacy applications (e.g., SPCS 83 and 27)

## Slide 63: NSRS Modernization: DELAY
It’s official: we are delayed beyond 2022
On June 23, 2020, this message was rolled out via:
  NGS Web Page
  NSRS Modernization News Special Issue
  Granicus Announcement
  Notifications to NSPS, AAGS, FGDC/FGCS

## Slide 64: NSRS Modernization: DELAY
A list of FAQs is available. Some summary highlights:
  Why are we delayed?
    GRAV-D issues (COVID-19, airspace, unforeseen maintenance)
    Personnel issues (Losses, hiring issues, probably some “burn out” too)
  How long is the delay?
    Unknown. If we don’t change anything about how we will roll things out, it’ll be in the 2024–2025 timeframe
  Will names change?
    No, “GEOID2022”, “NATRF2022”, etc. will remain the same

## Slide 65: Summary
The NSRS of today is based on:
  Pre-space-age geodetic technology
  The concept of one unique coordinate assigned to a point, in perpetuity
The modernized NSRS will:
  Leverage GNSS
  Embrace the movements of points on Earth’s crust

## Slide 66: Summary
Your NAD 83 coordinates may change by 2–4 meters
Your orthometric heights may change by up to 2 meters (or more)
Magnitude of change will vary with location:
  NAD 83 will change by about 0.5 to 4 meters horizontally
  Orthometric and NAD 83 ellipsoid heights will change by up to about 2 meters
And that just gets you to a “reference epoch”
  Which continues to perpetuate the “one coordinate in perpetuity” myth
  After that, real motions kick in and become part of the world of geodetic control

## Slide 67: Summary
But it’s not all “change”…
  You will still be able to:
    Get a position using OPUS
    Adjust your projects to some reference epoch
    Look at a mark’s “datasheet”
  Only now, there will be a lot more information and a lot more service provided

## Slide 68: Thank You