## Slide 1: Absolute Gravimetry in NGS: Instrumentation and Applications
by Daniel Winester, NOAA-NGS-OAD
Table Mountain Geophysical Observatory
17 September 2012

## Slide 2: Overview of talk
Acknowledgements to colleagues
Historic gravity work in US C&GS and NOAA
Instrumentation used
NOAA AG sites and their research
GRAV-D
GSVS-11 in Texas
SAVSARP in Arizona
AG site reconnaissance
2

## Slide 3: Other NGS-ers doing Absolute Gravity Observations since 1986
LT Brent Bernard
Knute Berstis
David Conner
Greg DeAngelo
Mark Eckl
Jack Fried
Lt JG John Griffin
Fred Klopping
Dave McAdoo
George Peters
Glenn Sasagawa
David Schmerge
Timothy Wilkins
JD Williams
3

## Slide 4: Cooperators with NGS & OES Absolute Gravimetry Program
4

## Slide 5: Gravimeters over the decades
Mendenhall pendulum gravimeter
Accuracy: ±1 to 5 mGals
Used from 1891 to ~1930 for geoid and base stations control (predecessors used from 1871 to 1891)
5

## Slide 6
Brown pendulum gravimeter
Accuracy: ±0.6 to 2 mGals
Used from 1931 to ~1960 for geoid and base stations control
6

## Slide 7: Spring-based relative gravimeters Worden and LaCoste & Romberg land meters
7

## Slide 8
Courtesy of V. Kelly Bellis, PLS, copyrighted material used with permission.
8

## Slide 9
NGS Gravity Network (1986)
9

## Slide 10: GWR Cryogenic meter
Cryogenic (superconducting) gravimeter – one at TMGO since 1995
10

## Slide 11: Absolute gravimeters JILAg-4 FG5-102 A10-025
None of pictured meters match serial numbers above.
11

## Slide 12: Absolute gravity research programs by area
12
Plate & local tectonics: Alaska, Chesapeake Bay, Los Angeles basin & other California, Mississippi River embayment, Oregon, Utah, Walker Lane (NV), Himalayas (Nepal & India), Japan, Mexican trench (Mexico & Central America) , Taiwan, Pacific NW
Volcanism: Yellowstone, Hawaii, Central America, Pacific NW
Post-glacial rebound: Fennoscandia, mid-continent & eastern U.S. & Canada, Alaska
Glacial ice mass: Greenland, Antarctica
Sea level change: coastal CONUS, Hawaii, Fennoscandia, Bermuda
Gravity base stations, Geoid & Height Modernization: Central America, Brazil, American Samoa, various CONUS, New Zealand, Nepal, Alaska
Metrology, intercomparisons & calibration lines: CA, CO, MD, NC, VA, eastern U.S, Rocky Mtn. front, France, Germany, Japan, Taiwan
Ground water: Arizona, Florida, Nebraska, Texas
VLBI & SLR overlap: AK, CA , FL, HI, IA, MD, MA, OK, TX, Bermuda, British Columbia, Brazil, Germany, Japan

## Slide 13: Worldwide Absolute Gravity Sites in NOAA database
NOAA sites
Others agencies’ sites in USA
13

## Slide 14: North American Absolute Gravity Sites
NOAA sites
Others agencies sites
14

## Slide 15
15
PACES GRAVMAG Website
http://gis.utep.edu
Data Catalog
http://gis.utep.edu/index.php?option=com_content&view=article&id=45&Itemid=54
Gravity Base Station for the United States
http://gis.utep.edu/index.php?option=com_content&view=article&id=157%3Agravity-base-stations&catid=50%3Agravity-base-stations&Itemid=54
Pick a State; Pick a Station

## Slide 16
16

## Slide 17: Richmond soil moisture
5
, FL
17
(Miami suburb)

## Slide 18: Manitoba
18
International Falls
Manitoba absolute gravity stations ( ) and inferred uplift rates (mm/year)
Note: Drainage is to the north. Lake Winnipeg will tilt southward; affecting flooding in Selkirk area and Manitoba Hydro’s hydroelectric dams
Lake Winnipeg
Hudson Bay
Lake Winnipegosis
Lake Manitoba
Churchill River
Nelson River
11
8
5
5
Pinawa
3
Lake of the Woods

## Slide 19: Churchill
2 cm uplift
Gravity changes at Churchill, MB (south side of Hudson Bay)
Gravity actually deceases and plot is inverted to accommodate GRACE data. Elevation is increasing 9 to11 mm/year.
Slide courtesy of Joe Henton, GSC
19

## Slide 20: New Orleans
20
g – 979 317 000 mGals
NEW ORLEANS AA, LA
2 cm subsidence
Observed trend corresponds to 10 mm/year of subsidence

## Slide 21
GRAV-D Program Gravity for the Redefinition of the American Vertical Datum
21
Geoid: The equipotential surface of the Earth's gravity field which best fits, in a least squares sense, global mean sea level.
The specific goal of GRAV-D is to model and monitor Earth’s geoid to serve as a zero reference surface for all heights in the nation (or North America) accurate to one cm. This should allow for orthometric heights coming from GPS to be accurate to two cm.
Current geoid model is a hybrid of terrestrial gravity data and leveling data. NAVD-88 H=0 is not the geoid; and it has a half meter bias and one meter tilt across CONUS. And is worse in Alaska.

## Slide 22
Part 1: Link precise satellite gravity data via new airborne gravity data to legacy terrestrial data. This will allow for a computation of purely gravimetric geoid.
22
GRAV-D Program Gravity for the Redefinition of the American Vertical Datum
NGS has two TAGS (airborne) meters.
Will fly USA (inc. territories) at 10 km flight spacing. Will take about 15 years to complete.
TAGS measurements tied to AG observations

## Slide 23: GRAV-D in the Continental US
White = FY13
Orange = FY12
Green = FY11 and earlier
Complete
In FY13
Complete
In FY13
23

## Slide 24: GRAV-D in Alaska
White = FY13
Orange = FY12-13
Green = FY11 and earlier
24

## Slide 25
25
GRAV-D Program Gravity for the Redefinition of the American Vertical Datum
Part 2: Monitor geoid changes over decadal time scales.
Ideally this would be done with satellites. However, with uncertainties in satellite programs (budgets, satellite longevity, replacement satellites etc.), a network of FG5 absolute gravity stations is envisioned to do temporal gravity monitoring, which can be modelled into geoid change.

## Slide 26
26

## Slide 27: Geoid Slope Validation Survey of 2011
Objective: to see if GRAV-D can hope to achieve 1 to 2 cm geoid accuracies
Observe geoid shape (slope) using multiple independent terrestrial survey methods
  GPS + Leveling
  Deflections of the Vertical
Compare observed slopes (from terrestrial surveys) to modeled slopes (from gravimetry or satellites)
  With / Without new GRAV-D airborne gravity
Notes: Although a geoid slope validation survey won’t validate the absolute accuracy of the geoid model, it will help point out weakness in data and theory. The accuracy of the terrestrial surveys will be best achievable, and formal accuracy estimates will be used to bound allowable disagreements with modeled geoid slopes.

## Slide 28
325 km
218 points
1.5 km spacing
28

## Slide 29
29
GPS: 20 identical. units, 10/day leapfrog, 40 hrs ea.
Leveling: 1st order, class II, digital barcode leveling
Gravity: FG-5 and A-10 anchors, 4 L/R in 2 teams
DoV: ETH Zurich DIADEM GPS & camera system
LIDAR: Riegl Q680i-D, 2 pt/m2 spacing, 0.5 km width
Imagery: Applanix 439 RGB DualCam, 5000’ AGL
Other: RTN, short-session GPS, extra AG around Austin, gravity gradients
Geoid Slope Validation Survey of 2011

## Slide 30: High Resolution Geoids (vs GPS / Leveling; cm)
Bins of dij, km | h/H error budget | USGG2009 (1’x1’) | EGM2008 (5’x5’) | USGG2012x01 (1’x1’) New software | USGG2012x02 (1’x1’) New software + Airborne data
0.4 - 15 | 0.0 ± 0.4 | 0.0 ± 1.0 | -0.0+/-1.0 | -0.0+/-1.0 | -0.0+/-0.9
15-30 | 0.0 ± 0.5 | 0.0 ± 1.0 | 0.0+/-1.3 | -0.0+/-1.4 | -0.0+/-1.1
30-46 | 0.0 ± 0.6 | -0.1 ± 1.5 | 0.0+/-1.7 | -0.2+/-1.8 | -0.2+/-1.1
46-63 | 0.0 ± 0.6 | -0.3 ± 1.7 | -0.1+/-2.0 | -0.4+/-2.1 | -0.3+/-1.2
63-81 | 0.0 ± 0.7 | -0.4 ± 2.0 | -0.2+/-2.1 | -0.6+/-2.5 | -0.3+/-1.3
81-101 | 0.0 ± 0.8 | -0.6 ± 2.3 | -0.4+/-2.2 | -0.7+/-2.8 | -0.4+/-1.4
101-122 | 0.0 ± 0.8 | -0.7 ± 2.6 | -0.6+/-2.3 | -0.8+/-3.0 | -0.4+/-1.4
122-145 | 0.0 ± 0.9 | -0.9 ± 2.7 | -0.8+/-2.4 | -0.7+/-2.9 | -0.3+/-1.3
145-172 | 0.0 ± 1.0 | -1.0 ± 2.8 | -1.0+/-2.6 | -0.6+/-2.6 | -0.1+/-1.0
172-204 | 0.0 ± 1.0 | -1.2 ± 2.7 | -1.2+/-2.5 | -0.9+/-2.1 | -0.2+/-1.0
204-247 | 0.0 ± 1.1 | -1.4 ± 2.4 | -1.3+/-2.7 | -1.7+/-1.4 | -0.7+/-1.0
247-325 | 0.0 ± 1.4 | -1.0 ± 1.6 | -0.2+/-2.3 | -1.9+/-1.4 | -1.3+/-1.0
All separation distances
show improvement
with GSVS11 survey when
airborne gravity are
introduced.
New software shows modest
improvement at medium wavelengths
30
Notes: This chart speaks to the ability of a gravimetric geoid model to be as accurate over distances as GPS and leveling combined. The basic messages here are that currently, gravimetric geoids aren’t as accurate as GPS and leveling, but they aren’t bad either. They are certainly cheaper than leveling! Furthermore, it shows that for this survey, at least, USGG2009 has some improvements to make to beat EGM2008. As such, NGS embarked on a rigorous re-examination of their geoid modeling methods. The new software will likely be complete later in 2012. But some new experimental geoids with the new software show an improvement over USGG2009, but still not quite as good as EGM2008. The real story of columns 3/4/5 can be summarized as follows: “No matter what software is used, massaging the same old, uncorrected terrestrial gravity data isn’t going to yield
However, when adding in airborne gravity from GRAV-D, these new geoids blow everything else away.

## Slide 31
Map Colors, Lithologies, and Densities (g/cm3) for all mapped units in CONUS
Geologic maps Density maps (denser =lighter color)
New York
Nevada
National Density Map
31
Convert GIS lithologies into density map at one arc-minute scale

## Slide 32
Southern Avra Valley Storage and Recovery Project (SAVSARP), west of Tucson, AZ
Joint project between University of Arizona – Hydrology Dept., USGS Water Resources Dept., GWR Instruments, GeoForschungsZentrum-Potsdam and NOAA-NGS
Study the direct effect on gravity due to the recharge and withdrawal of ground water in managed situation.
32

## Slide 33
Southern Avra Valley Storage and Recovery Project (SAVSARP), west of Tucson, AZ
Basins filled with known volume of water and time
Water removed (pumped) at known time, volume, locations and depths
SG (iGrav), tidal (g-phone), AG (FG5 and A10) and GPS observations at bldgs. A-10 and relative grav. observations at well heads
About a one year expt. (on going)
33

## Slide 34
205
206
207

## Slide 35: SAVSARP Recharge Facilities
34
Slide courtesy of Jeff Kennedy, USGS and Benjamin Creutzfeldt, GFZ
N
iGrav & FG5
35
Notes: Unconfined conditions
Recharge is primarily downward - perching layers appear to be minimal.
Lateral extent of groundwater mound is small.
Recharge rates vary from pond to pond

## Slide 36: How can different gravimeters be used together?
36
Slide courtesy of Jeff Kennedy, USGS

## Slide 37: A10 data
Chart: Gravity change, microGals
| 40934 | 40949 | 40967 | 40977 | 40984 | 40991 | 41003 | 41005 | 41016 | 41037 | 41054 | 41062 | 41062 | 41072
RB205 | 140 | 170.42 | 166.32 | 143.31 | 126.23 | 130.01 | 124.41 | 123.47 | 161.91 | 193.56 | 206.43 | 170.63 | 172.1 | 144.28
RB206 | 140 | 191.83 | 173.42 | 145.67 | 126.43 | 110.86 | 105.6 | 111.73 | 164.22 | 243.59 | 257.7 | 183.42
RB207 | 140 | 139.93 | 130.38 | 125.64 | 123.42 | 127.88 | 120.06 | 117.91 | 121.48 | 121.09 | 133.7 | 200.69 | 247.44 | 226.53
SA011A | 60 | 50.34 | 42.09 | 47.01 | 50.43 | 54.59 | 78.5 | 94.5 | 144.73 | 155.08 | 155.99
SA014A | 40 | 71.68 | 99.99 | 93.64 | 76.34 | 75.72 | 59.36 | 63.41 | 91.76 | 119.07 | 152.44 | 156.55 | 129.24
SA015A | 40 | 73.23 | 70.83 | 58.62 | 67.92 | 68.84 | 76.77 | 103.09 | 131.43 | 161.8 | 164.56 | 150.76 | 132.22
SA009A | 20 | 19.68 | 16.25 | 23.98 | 15.01 | 24.04 | 20.82 | 18.69 | 33.65 | 32.92 | 22.97
SA001A | 20 | 17.46 | 18.9 | 17.86 | 6.37 | 13.68 | 18.17 | 15.9 | 13.88 | 23.48 | 30.24
AV020A | 20 | 13.29 | 23.99 | 10.27 | 24.27 | 25.66 | 23.47 | 20.61 | 24.21 | 40.91 | 36.73
37
Slide courtesy of Jeff Kennedy, USGS
Recharge starts

## Slide 38: Absolute Site Reconnaissance
Meets project needs (e.g. station spacing, geologic setting or other geodetic control)
Site permanence for re-observations: Gov’t bldg., interested host, historic bldg.
Micro-seismic noise: Bedrock = good, Soil = mediocre, Swamp/Beach = poor.
Hammer test
Others: power, control, space, temp control…
38

## Slide 39: Site Monumentation
Flat disk: harder to level to, but is easier to transfer height to AG; older AG have alcohol bottle on ground.
Indoors: Host may prefer unobtrusive mark; e.g 2 cm plug. Others may want ‘trophy disk.’
Monument should be sized to handle different types of g-meters; as well as GPS or levels
39

## Slide 40: Dat’s all folks…
I will now fend off questions

## Slide 41
Notes: 41
This shows the extent of the gravity data that went info the USGG2009
Terrestrial data onshore; shipborne and altimetric data offshore.
Note the disparity in coverage. This is further reason for GRAV-D.

## Slide 42: How to read the next chart
Pick any 2 (of the 218) points (Pi and Pj) separated by a distance “dij”
  23,871 possible (i,j) pairs of points
  0.4km < dij < 325km
Compute residuals: D(h-H-N) over distance:
  D(h-H-N) = (hi-Hi)-(hj-Hj) – (Ni-Nj)
Accumulate statistics on residuals for all (i,j) pairs in a bin
Each dij bin contains ~2000 pairs of points

## Slide 43: High Resolution Geoids (vs GPS / Leveling; cm)
Bins of dij, km | h/H error budget | USGG2009 (1’x1’) | EGM2008 (5’x5’) | USGG2012x01 (1’x1’) New software | USGG2012x02 (1’x1’) New software + Airborne data
0.4 - 15 | 0.0 ± 0.4 | 0.0 ± 1.0 | -0.0+/-1.0 | -0.0+/-1.0 | -0.0+/-0.9
15-30 | 0.0 ± 0.5 | 0.0 ± 1.0 | 0.0+/-1.3 | -0.0+/-1.4 | -0.0+/-1.1
30-46 | 0.0 ± 0.6 | -0.1 ± 1.5 | 0.0+/-1.7 | -0.2+/-1.8 | -0.2+/-1.1
46-63 | 0.0 ± 0.6 | -0.3 ± 1.7 | -0.1+/-2.0 | -0.4+/-2.1 | -0.3+/-1.2
63-81 | 0.0 ± 0.7 | -0.4 ± 2.0 | -0.2+/-2.1 | -0.6+/-2.5 | -0.3+/-1.3
81-101 | 0.0 ± 0.8 | -0.6 ± 2.3 | -0.4+/-2.2 | -0.7+/-2.8 | -0.4+/-1.4
101-122 | 0.0 ± 0.8 | -0.7 ± 2.6 | -0.6+/-2.3 | -0.8+/-3.0 | -0.4+/-1.4
122-145 | 0.0 ± 0.9 | -0.9 ± 2.7 | -0.8+/-2.4 | -0.7+/-2.9 | -0.3+/-1.3
145-172 | 0.0 ± 1.0 | -1.0 ± 2.8 | -1.0+/-2.6 | -0.6+/-2.6 | -0.1+/-1.0
172-204 | 0.0 ± 1.0 | -1.2 ± 2.7 | -1.2+/-2.5 | -0.9+/-2.1 | -0.2+/-1.0
204-247 | 0.0 ± 1.1 | -1.4 ± 2.4 | -1.3+/-2.7 | -1.7+/-1.4 | -0.7+/-1.0
247-325 | 0.0 ± 1.4 | -1.0 ± 1.6 | -0.2+/-2.3 | -1.9+/-1.4 | -1.3+/-1.0
All separation distances
show improvement
with GSVS11 survey when
airborne gravity are
introduced.
New software shows modest improvement
at medium wavelengths
Notes: This chart speaks to the ability of a gravimetric geoid model to be as accurate over distances as GPS and leveling combined. The basic messages here are that currently, gravimetric geoids aren’t as accurate as GPS and leveling, but they aren’t bad either. They are certainly cheaper than leveling! Furthermore, it shows that for this survey, at least, USGG2009 has some improvements to make to beat EGM2008. As such, NGS embarked on a rigorous re-examination of their geoid modeling methods. The new software will likely be complete later in 2012. But some new experimental geoids with the new software show an improvement over USGG2009, but still not quite as good as EGM2008. The real story of columns 3/4/5 can be summarized as follows: “No matter what software is used, massaging the same old, uncorrected terrestrial gravity data isn’t going to yield
However, when adding in airborne gravity from GRAV-D, these new geoids blow everything else away.

## Slide 44
Chart: RMSE (h-H-N) over GSVS11
| 0.4 - 15 | 15-30 | 30-46 | 46-63 | 63-81 | 81-101 | 101-122 | 122-145 | 145-172 | 172-204 | 204-247 | 247-325
h/H error budget RMS (cm) | 0.4 | 0.5 | 0.6 | 0.6 | 0.7 | 0.8 | 0.8 | 0.9 | 1 | 1 | 1.1 | 1.4
USGG2009 (1'x1') RMS (cm) | 1 | 1 | 1.5033 | 1.7263 | 2.0396 | 2.377 | 2.6926 | 2.846 | 2.9732 | 2.9547 | 2.7785 | 1.8868
EGM2008 (5'x5') RMS (cm) | 1 | 1.3 | 1.7 | 2.0025 | 2.1095 | 2.2361 | 2.377 | 2.5298 | 2.7857 | 2.7731 | 2.9967 | 2.3087
USGG2012x01 (1’x1’) New software RMS(cm) | 1 | 1.4 | 1.8111 | 2.1378 | 2.571 | 2.8862 | 3.1048 | 2.9833 | 2.6683 | 2.2847 | 2.2023 | 2.3601
USGG2012x02 (1’x1’) New software + Airborne data RMS (cm) | 0.9 | 1.1 | 1.118 | 1.2369 | 1.3342 | 1.456 | 1.456 | 1.3342 | 1.005 | 1.0198 | 1.2207 | 1.6401
Notes: This slide shows to RMS error (disagreement) between h, H and N for various geoid models as compared to the best GPS and leveling on GSVS11. Note first the black bars, which are the allowable h and H error build up over further distances. Compare these to the total error of the h-H-N values. USGG2009 and EGM2008 have similar patterns, with EGM2008 being slightly better behaved. The new model, USGG2012x01 has patterns of improvement and degradation relative to EGM2008 and USGG2009, showing the need to keep working on theory and software. However, the geoid model with airborne data, USGG2012x02 shows clear improvement over all models, and even begins to approach the level of accuracy of h-H at medium wavelengths.

## Slide 45
Chart: "Geoid only" RMSE over GSVS11
| 0.4 - 15 | 15-30 | 30-46 | 46-63 | 63-81 | 81-101 | 101-122 | 122-145 | 145-172 | 172-204 | 204-247 | 247-325
USGG2009 (1'x1') DRMS (cm) | 0.91652 | 0.86603 | 1.3784 | 1.6186 | 1.9157 | 2.2383 | 2.571 | 2.7 | 2.8 | 2.7803 | 2.5515 | 1.2649
EGM2008 (5'x5') DRMS (cm) | 0.91652 | 1.2 | 1.5906 | 1.9105 | 1.99 | 2.0881 | 2.2383 | 2.3643 | 2.6 | 2.5865 | 2.7875 | 1.8358
USGG2012x01 (1’x1’) New software DRMS(cm) | 0.91652 | 1.3077 | 1.7088 | 2.0518 | 2.4739 | 2.7731 | 3 | 2.8443 | 2.4739 | 2.0543 | 1.9079 | 1.9
USGG2012x02 (1’x1’) New software + Airborne data DRMS (cm) | 0.80623 | 0.9798 | 0.9434 | 1.0817 | 1.1358 | 1.2166 | 1.2166 | 0.98489 | 0.1 | 0.2 | 0.52915 | 0.8544
The “1 cm geoid”
Notes: This slide is a companion to the previous one, but the h-H errors have been removed, in an RMS sense, from the total h-H-N errors, leaving, ostensibly, gravimetric geoid errors only. As seen previously, the airborne geoid is the best performer, by far. In fact, as a general statement, it could be said that USGG2012x02, an airborne gravity data enhanced geoid model, is effectively at the 1 cm differential geoid undulation accuracy level across all distances, in the region of GSVS11.