## Slide 1
NGS Geoids, OPUS, NCAT, etc.
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
WVSPS Annual Convention
February 2020

## Slide 2: My Background
Licensed Surveyor in OH, PA, and WV (PS)
Certified GIS Professional (GISP)
Certified Floodplain Surveyor (CFS)
BS in Surveying & Mapping, Univ. of Akron
Came to NGS from USACE Pittsburgh District
  primary experience is engineering surveys, including structural deformation, hydrographic/bathymetric, terrestrial lidar, GNSS control, local/legacy datum resolution

## Slide 3: So much more to NSRS Modernization!
New version of PAGES
  Multi-Constellation  GPS, Galileo, GLONASS, Beidou, QZSS, etc.
  Target: 15 minute occupations
OPUS expansion plan
  RTK/RTN: 2020 rollout, already mentioned
  Leveling, Classical (Total Station), Gravity: 2020-2025
  Fully integrated (GPS projects with leveling and gravity? No problem!)
  Ease of submission to NGS for inclusion in the NSRS
New Mark Recovery Tool
  mentioned earlier, search: “NGS mark recovery” and go to Beta
Fully integrated toolkit
  NCAT and VDatum

## Slide 4: Using the modernized NSRS
OPUS
  Guidance (such as pre-selected CORSs and assistance in locating marks in project areas)
  Users will decide what control to hold fixed and what epochs they wish to set for the adjustment
    “Preliminary coordinates”
  If submitted to NGS (aka “Shared”), we will harvest your raw GNSS data and use it to compute Final Discrete coordinates

## Slide 5: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 6: Not just new datums…
  NSRS Modernization
-OPUS enhancements/additions
-new types of coordinates
-new methods for establishing control
-streamlined Bluebooking
-retire the US Survey Foot

## Slide 7: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 8: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 9: Ecosystem and Climate Operations

## Slide 10: Ecosystem and Climate Operations

## Slide 11: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 12: Aeronautical Survey Program
Interagency Program: FAA and NGS
  Primary Airport Control Station (PACS) and Secondary Airport Control Stations (SACS)
  Airports GIS (AGIS)
  Airport Obstruction Charts (AOC)
Primary function of NGS is to serve as QA and subject-matter expert for ASP surveys that are contracted by airports

## Slide 13: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 14: NOAA VDatum - online

## Slide 15: NOAA VDatum - download

## Slide 16: NOAA VDatum - download

## Slide 20: NOAA VDatum Website
vdatum.noaa.gov

## Slide 21: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 22: GPS Orbit Data aka Ephemerides
NGS orbit analysis and computation is performed together with, and as a component of, the International GNSS Service (IGS)
  IGS coordinates the collection of satellite tracking data
  these orbits are what give us post-processed accuracy
Designated with this responsibility by the Civil GPS Service Interface Committee (CGSIC)
If you’re using OPUS, it’s all behind-the-curtain!

## Slide 23
Link to NGS GPS Calendar
.sp3 file

## Slide 24: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 25: National Shoreline
The official shoreline for the Nation, in support of NOAA’s nautical charting mission
Available for download as shapefile in Mean High Water and Mean Lower Low Water datum
Organized by “Project Area” – the blue boxes
hyperlink to the National Shoreline homepage

## Slide 26: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 27: https://www.ngs.noaa.gov/ADVISORS/

## Slide 28: Regional Geodetic Advisor Program
www.ngs.noaa.gov/ADVISORS/
query any major search engine: “ngs advisors”

## Slide 29: State Geodetic Coordinators
Not an NGS employee, rather:
  State/Commonwealth government
    RTN (aka “VRS”) Manager
    DOT survey lead
    Geospatial Information Officer
  Academia
    Professor or Program Director
  Professional society representative
Serves as a liaison between the State’s geospatial community and the NGS

## Slide 30: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 31: Emergency Response Imagery
Mission of our Remote Sensing Division
Pre-Storm and Post-Storm photos are taken mostly along the coastal CONUS, and some other disasters natural or human
Supports Dept. of Homeland Security (DHS) and other emergency management organizations (FEMA, State, local, etc.)

## Slide 32: Emergency Response Imagery

## Slide 33: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 34: Phase Center Offset - conceptual
Orange dot = mean point of signal reception
Blue dot = Antenna Reference Point (ARP)
Red line = Phase Center Offset (PCO)

## Slide 35: Phase Center Offset
The PCO is one reason it is important to select the correct antenna for OPUS upload!
choose
carefully!
if you have questions… drop me a line

## Slide 36: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 37: NGS Coordinate Conversion And Transformation Tool (NCAT)

## Slide 38
NGS Coordinate Conversion And Transformation Tool (NCAT)

## Slide 39: Coordinate Transformation Tool
X, Y, Z
USN G
UTM
SP C
X, Y, Z
USN G
UTM
SP C
X, Y,
Z
USN
G
UTM
SP
C
, , h
(NCAT / NADCON 5.0)
USSD
NAD 27
NAD 83 (1986)
Relating coordinates: then & now
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
, , h
NAD 83 (HARN)
, , h
2022

## Slide 40: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 41: Continually Updated Shoreline Product
Just as the name says… it’s dynamic
Available for download as shapefiles
Developed by image interpretation and/or vertical modeling using water level stations (tide or lake gages)
Referenced to a computed Mean High Water
hyperlink to the CUSP homepage

## Slide 42: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 43: Beta CBL Map Viewer
https://www.ngs.noaa.gov/CBLINES/

## Slide 44: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 45: Cooperative program for Operational Meteorology, Education, and Training
Meteorology… why?
The origin of the program was the National Weather Service, also a NOAA office
It expanded to various NOAA missions, including NGS

## Slide 46: Outreach & Educational Resources

## Slide 47
Geoids and Gravity

## Slide 48
Geoids and Gravity
or
“Ramblings on the geoid”

## Slide 49
“Equipotential surface of the Earth’s gravity field that approximates Mean Sea Level more closely.”
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 314.
equi-huh?
More closely than what?
One textbook geoid definition

## Slide 50
“The equipotential surface of the Earth's gravity field which best fits, in a least squares sense, global Mean Sea Level.”
-website of the National Geodetic Survey
A surface of constant geopotential.
-some lecture notes of mine…
Two more geoid definitions

## Slide 51
  “The geoid is the equipotential surface that most closely coincides with the undisturbed mean sea level (and its continuation through the continents).”
    - Sjöberg, L. E., & Bagherbandi, M. (2017). Gravity Inversion and Integration, Theory and Applications in Geodesy and Geophysics. Springer.
  equipotential – equal potential
  potential – as in energy… or gravitational pull
My favorite verbage

## Slide 52
It is not uniform, both strength and direction vary.
Can be defined by a vector
-distance (from ellipsoid) and direction
Gravitational Pull

## Slide 53
A modeled surface to represent the location of equal gravitational force.
It’s an undulating surface, hence the phrase “geoid undulation” often used.
Gravity is acting perpendicular to every point on this surface.
Equipotential Surface

## Slide 54
… coincides with the undisturbed mean sea level…
Equipotential Surface

## Slide 55
There are an infinite number of equipotential surfaces.
We use the term geoid to refer to one of those surfaces that aligns to a best-known global mean sea level.
Equipotential Surface

## Slide 56
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
Equipotential Surface

## Slide 57
Geopotential

## Slide 58
Geopotential

## Slide 59
Geopotential

## Slide 60
In all scenarios, the water only flows when it has a path to lower geopotential – this is always a combination of gravity and height.
Geopotential
(-∫g dH)

## Slide 62
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
Orthometric Heights

## Slide 64
H = h + N
Orthometric Heights

## Slide 65
H = h + N
Orthometric Heights

## Slide 66
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
H = h + N
Deflection of the Vertical
DoV (symbolized ε)
ε
ε
Orthometric Heights

## Slide 69
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid warped to fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid

## Slide 70
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88

## Slide 71
NAD83(2011) 
NAD83(2007) 
NAD83(HARN/FBN)
NAD83(CORS96)
GEOID18
GEOID12B
GEOID09
GEOID06 (AK only)
GEOID03
GEOID99
GEOID96
Which NAD83 with which geoid?

## Slide 72: EGM08
GRACE
GOCE
USGG2012 GEOID12A/B
2012
2008
2014
2015
2016
xGeoid14B
xGeoid15B
xGeoid16B
+
GRAV-D
GOCO03s GOCO05S
Evolution of recent NGS geoid models

## Slide 74: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 75: Online Positioning User Service
  OPUS Rapid Static (OPUS-RS)
      dual frequency receiver data
      static sessions only
      30 seconds epoch rate (aka recording interval)
      15 minutes to 2 hours of GPS data
  OPUS Static (OPUS-S)
      same requirements as above
      2 to 48 hours of GPS data
  OPUS Projects (OP)  also Beta OPUS Projects
      adds session processing and network adjustment
      training by NGS required; typically 12 hours
      upload to OPUS with a “Project ID” keyed in Options

## Slide 76: 30 seconds epoch rate

## Slide 77: OPUS-RS – 15 min to 2 hours
Rapid-static: OPUS first creates an atmospheric delay model from surrounding CORS data.
  -Atmospheric model

## Slide 78: How does OPUS-RS work?
Selects three to nine “best” CORS based upon:
    Having common satellite visibility with the user data.
    50 < distance <250 km from the user's mark.
    Orientation relative to the user's mark.
The star represents the user’s mark; the triangles are CORS.
No CORS farther than 250 km from the user's mark will be included.
A minimum of three, and no more than nine CORS are used.
s
250km
>250km

## Slide 79: How does OPUS-RS work?
In addition, user's mark must be no more than 50 km from the (convex) polygon created by the selected CORS.
If the user’s mark is more than 50 km outside this polygon, alternate CORS will be considered.
If none can be found, the processing will abort.

## Slide 80: OPUS-S – 2 to 48 hours
baseline 1
baseline 3
baseline 4
baseline 2
baseline 5
  -Best 3 of 5 baselines

## Slide 81
“peak to peak” error ranges, explained:
LAT: 59 42 33.45847 0.003(m)
W LON: 151 27 27.92482 0.007(m)
EL HGT: 503.684(m) 0.032(m)
ORTHO HGT: 494.346(m) 0.055(m)
LAT range
baseline 3
LON range
CORS baseline 1
=
JGE, 2015
2 outermost baselines are ignored
baseline 4
baseline 2
baseline 5
position: averaged from the 3 most coherent baselines
ORTHO HGT range
ranges: a bounding box enclosing 3 most coherent baselines
for ORTHO HGT, geoid model uncertainty is added
EL HGT range

## Slide 82: Static vs. Rapid Static
 | Static | Rapid Static
Input | 2-48 hours | 15 minutes-2 hours
Output | normal, extended, XML Shared, Projects | normal, extended, XML
Accuracy (95%confidence) | 1-2 cm horizontal 3-6 cm ellipsoidal height | 1-2 cm horizontal 4-8 cm ellipsoidal height
Network Geometry | 3 CORS, preferably within 1000 km of rover | 3-9 CORS, surrounding & within 250 km of rover
Availability | global | 90% of CONUS (subject to geometry, above)

## Slide 83: RMSE of Horizontal Results

## Slide 84: RMSE of Vertical Results

## Slide 85: OPUS Projects – 2 to 48 hours
  -Control network via OPUS

## Slide 86: OPUS Projects
Web-based access, nothing to download
Visualize/map your OPUS Solutions
Manage multiple Projects at once
Processing for multiple marks and multiple occupations, or repeat occupations of single mark
Advantages include:
Data uploading through OPUS
Process using PAGES… without learning PAGES (GUI)
Graphic visualization versus text Solution Reports
Support for Bluebooking!

## Slide 87: OPUS Projects – enter a Project ID
Project ID
for OP

## Slide 88: Why complicate OPUS?
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5

## Slide 89: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5

## Slide 90: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N

## Slide 91: Why complicate OPUS?
network adjustment
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N

## Slide 92: Typical OP Network Diagram
"Hub” design recommended
Hub CORS to marks ≤ ~100 km
Use multiple CORS
Add one very long baseline from Hub to CORS, to improve tropospheric modeling
OPUS-Projects does session baseline processing
Hub
CORS
CORS
CORS
CORS
24hr
24hr
24hr
>2hr
>2hr

## Slide 93: What’s in it for you?
OPUS solutions = pretty good… but each treated as independent and assumes “perfect” CORS
Sessions = simultaneously-observed marks processed together in sessions increases consistency
Adjustments = interlinking sessions through least squares increases accuracy

## Slide 94
OPUS-Projects can’t work magic.
  does not make a project plan obsolete.
  does not make field logs obsolete.
  does not make mark descriptions obsolete.
  does not make mark photos obsolete.
  does not make remove sky obstructions.
  does not make bad data good.
  does not make processing decisions as well as you.
  does not quality control processing results as well as you, the Professional Surveyor

## Slide 95
GPS survey
data files
photos
descriptions
etc.
Process data using vendor software or PAGE-NT.
Construct bluebook files using software and editor.
Run ADJUST.
geodesy.noaa.gov/ project_tracking/
review and publish to IDB
Bluebooking a Project now

## Slide 96
review and publish to IDB
Upload to OPUS-Projects
Process in OPUS-Projects
GPS survey
data files
photos
descriptions
etc.
Process data using vendor software or PAGE-NT.
Construct bluebook files using software and editor.
Run ADJUST.
geodesy.noaa.gov/ project_tracking/
Bluebooking with OPUS Projects in the future
Available now!
(with certain caveats)

## Slide 97
But wait… there’s more!
Coming soon…

## Slide 98: Hybrid Control Networks = Static + RTK/RTN
OPUS for RTK/RTN-GNSS

## Slide 99: “What’s the benefit?” they say…
OPUS for RTK/RTN-GNSS
Run least squares adjustment(s) of the combined Static and RTN vectors
Hold NCN CORS (and possibly other published coordinates) in adjustments
Check quality of results
Submit survey project to NGS for review and publication in national database
…you’ll be able to Bluebook RTK/RTN data!

## Slide 100: What happened to GPSonBM?
The program continues!
All submittals up until 31 Dec 2021 will be incorporated into the NAVD88NAPGD2022 Transformation Tool
How do I get a mark included?
  collect/submit 2+ OPUS Shared Solutions
Tracking map (AGOL)
  NGS committed to biweekly updates

## Slide 101: Mark Recovery – mobile browser compatible
use your smartphone to submit recovery
Any major search engine:
  “NGS survey mark recovery”
beta.ngs.noaa.gov/cgi-bin/recvy_entry_www.prl
Try it out! Give us feedback!
NGS.Feedback@noaa.gov

## Slide 102: Mark Recovery – mobile browser compatible

## Slide 103
www.ngs.noaa.gov
beta.ngs.noaa.gov

## Slide 104
https://www.ngs.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486