## Slide 1: Kentucky Aerial Photography and Elevation Data Program - KYAPED
National Height Mod Partner Meeting
May 1, 2013
Danielle Kelly and Dan Farrell

## Slide 2
KYAPED Program Information
This initiative will provide statewide elevation data (LiDAR) and color leaf-off aerial photography.
The multi-million dollar project is expected to span a three to four year period which began in January 2012.
Funding partners for this effort have include federal agencies such as the Federal Emergency Management Agency (FEMA), the Department of the Interior (DOI) U.S. Geological Survey (USGS), the USDA Farm Services Administration (FSA), and the USDA Natural Resources Conservation Service (NRCS), as well as local governments and several state agencies. The Kentucky Transportation Cabinet (KYTC) is a major partner in this effort.
More information regarding the Digital Aerial Photography and Elevation Data Program including agency uses, partner listings, wiki definitions, specifications, and data examples can be found on the program website @: http://kygeonet.ky.gov/kyfromabove/

## Slide 3
Why KYAPED?
This program will provide significant savings to government and the private sector by using a common basemap, avoiding duplication, and encouraging the standardization of Geographic Information Systems (GIS) assets throughout the Commonwealth.

## Slide 4
  • To acquire statewide leaf-off color aerial photography for the entire Commonwealth
  • To acquire high-resolution elevation data for the entire Commonwealth
  • Pool funding resources from Local, Regional, State, and Federal Agencies
Program Goals
Kentucky Aerial Photography & Elevation Data (KYAPED) Program

## Slide 5
2012 Program Partners
  • Kentucky Transportation Cabinet (KYTC)
  • Kentucky Division of Abandoned Mine Lands (AML)
  • Kentucky Division of Geographic Information (DGI)
  • Kentucky Division of Water (DOW)
  • United States Geological Survey (USGS)
  • National Geospatial Intelligence (NGA)
  • Boone County Planning Commission (BCPC)
  • Frankfort Plant Board (FPB)
  • Louisville-Jefferson County Information Consortium (LOJIC)
  • Northern Kentucky Area Planning Commission – LINK GIS
  • Fort Knox
  • Hardin County
  • Kentucky State University (KSU)

## Slide 6
2012 Program Status
  • All priority areas have been delivered on schedule
  • Review has been completed on 11 of the 12 Priority Areas
  • 100% of the LiDAR data collected has been delivered
  • All Program Partner data has been distributed
  • Image Server Services are being created as final data is received
  • The remaining data is being staged for distribution processing

## Slide 7
2013 Program Plans
  • Program will focus on extreme Western Kentucky
  • There will be NO Federal Funding in 2013
  • City of Florence will acquire 6 inch imagery
  • Paducah/McCracken County is doing a full buy-up (Elevation & Imagery)
  Program Partners for 2013 Kentucky Transportation Cabinet Division of Geographic Information Paducah/McCracken County City of Florence

## Slide 8
Elevation Data – 10 Meter

## Slide 9
Elevation Data – 5 Foot

## Slide 10
Elevation Data – 10 Meter

## Slide 11
Elevation Data – 5 Foot

## Slide 12
Elevation Data (KYAPED 2012)

## Slide 13
Elevation Data (KYAPED 2012)

## Slide 14
Elevation Data (KYAPED 2012)

## Slide 15
Elevation Data (KYAPED 2012)

## Slide 16
Point Cloud (KYAPED 2012)

## Slide 17
Elevation Project Planning Map

## Slide 18
Specifications
LiDAR
http://kygeonet.ky.gov/kyfromabove/pdfs/Specs_LiDAR_Production.pdf
Orthophotography
http://kygeonet.ky.gov/kyfromabove/pdfs/Specs_OrthoPhoto_Production.pdf
Collection: NAD83(CORS96), NAVD88, Geoid 09
Project Deliverables: Kentucky Single Zone

## Slide 19: Additional Considerations
Staff – DGI
  The main thing this project has consumed is time. Lots of time. Everything from Project Management to Imagery Review to creating ArcGIS Server Services and everything in between. DGI estimates that it takes 1.5 staff members to manage the data.
Storage Requirements
  DGI has increased its SAN storage from 10TB to over 26TB and have invested in 20TB of portable storage as well.

## Slide 20: TYPICAL QUESTIONS WHEN USING LIDAR DATA
What’s the Accuracy?
In open, flat areas, ground contours can be recorded from an aircraft flying overhead providing accuracy within 6 inches of actual elevation. In steep, forested areas accuracy is typically in the range of 1 to 2 feet and depends on many factors, including density of canopy cover and the spacing of laser shots.
What’s the difference between "raw" LIDAR data and "classified" LIDAR data?
The points of the "raw" LIDAR data include elevations for the ground, buildings, highway overpasses, forest canopy, and anything else that the laser beam encountered. In data processing, each of these points is classified into one of the LAS classification values.
LiDAR generates an accurate 3D model of the earth’s surface. GPS provides the 3D position.
Why LiDAR?

## Slide 21: What Classification are we using for modeling a surface? Model Key-Point!

## Slide 22: ADVANTAGES OF LIDAR OVER TRADITIONAL PHOTOGRAMMETRY AND CONVENTIONAL SURVEYING
Ease of data acquisition
Increased ability to determine surface elevations in difficult areas and less time for creation of elevation data
Less dependent of weather, time of year, time of day
The speed and accuracy of LiDAR make it feasible to map large areas with the kind of detail that before had only been possible with ground survey crews.
LiDAR data (point cloud) is easily used with GIS software and can be used with Microstation

## Slide 23
Multiple LIDAR Returns
Returns
1
2
3

## Slide 25
What about the Breaklines?
LiDAR technology, however, does not inherently collect the breaklines necessary to produce traditional DTMs. Breaklines have to be developed separately through a variety of techniques, and either used with the LiDAR points in the generation of the DTM, or applied as a correction to DTMs generated without breaklines.
Mobile Mapping and Stationary Scans datasets are highly accurate. However breaklines from Traditional Survey methods are ready for use, while Breaklines from Mobile Mapping and Stationary Scanning are extracted in post processing.
Note: Manual editing is necessary to produce a Quality LiDAR project.

## Slide 26: Merging Datasets Example 1

## Slide 27: Breaklines collected Edge of Pavement, Crown, Edge of shoulder, Curb, Median, Ditches, etc

## Slide 28: Merged Airborne LiDAR surface with collected field data to make 1 surface

## Slide 29: Example 2 Airborne LiDAR Data (notice stream)

## Slide 30: Field data collected by District Survey Staff and Modeled

## Slide 31: Merged Datasets Airborne + Field Data Combined

## Slide 32: Highway Design Comments
As with traditional photogrammetry, specific features can added to the DTM from field surveys such as utilities, UST, retaining walls, drainage structures TG/IE, etc.
These features are added as-normal by using "survey edit" on the existing DTM. The “point cloud” inside the perimeter of the ground survey is re-triangulated to include the ground survey features. Control points utilized from original LIDAR (KY Single Zone) should be the control points for the ground survey.
Depending on the accuracy of the LIDAR data, the DTM could be more accurate by reducing the contour interval. File sizes and RAM may become an issue on workstations.

## Slide 33: CONTACT INFORMATION AND LINK
Contact Information
Inquiries regarding the Commonwealth's
Aerial Photography & Elevation Data
Program can be directed to:
Thomas Rossman, Director
Commonwealth Office of Technology,
Office of Application Development,
Division of Geographic Information
100 Fair Oaks Lane
Frankfort, KY 40601
(502) 564-6412
Thomas.Rossman@ky.gov
http://kygeonet.ky.gov/kyfromabove/

## Slide 34: QUESTIONS?
REFERENCE LINKS
http://technology.ky.gov/gis/Pages/default.aspx
http://kygeonet.ky.gov/kyfromabove/
http://liaisons.usgs.gov/geospatial/
http://www.fema.gov/national-flood-insurance-program-flood-hazard-mapping/map-modernization#1