## Slide 1: Connecticut Height Modernization 2010
Thomas H Meyer (UConn)
Robert Baron (CT DOT)
Darek Massalski (CT DOT)
Kazi Arifuzzaman (UConn)

## Slide 2: Overview
Goal: to assess the accuracy of GEOID03 and GEOID09 in Connecticut
Means: how well do GPS-determined orthometric heights compare with NAVD 88 published heights

## Slide 3: Markers
70 markers
  22 class A
  10 class B
  11 class C
  2 class D
  25 transfers

## Slide 5: Occupations
2007-2008
Summer, Fall
Only First-Order bench marks
At least three occupations per mark
4 hour duration
Re-level range pole each hour

## Slide 6: GPS Equipment
Receivers
  UConn
    TOPCON HipPer Lite+ (internal)
    Javad Legacy (LegAnt)
    Odyssey (internal)
  CTDOT
    Trimble 5700 (Zephyr)
2-m, fixed-height tripods

## Slide 7: GPS Processing
Pinnacle and OPUS
RINEX v.2
IGS precise ephemerides
NGS guidelines
CORS for control (no benchmarks)

## Slide 8: Checks
Pinnacle vectors against CORS inversed vectors
  None statistically different (95%)
Pinnacle and OPUS
  Compare ellipsoid heights
  Different differencing kernels

## Slide 9: Pinnacle h – OPUS h
Letters/colors indicate stability classes
Box-whisker plot
Dots indicate outliers.

## Slide 10: Pinnacle – OPUS no outliers
Error-bar plot
Frequency histogram

## Slide 11: Conclusion
Pinnacle seems to be producing ellipsoid heights that are consistent with PAGES

## Slide 12: Networks
NGS specifications
  No “bad” vectors
All vectors, including substandard
No phase-center variation correction

## Slide 13: Marker Locations
Letter indicates stability class. Circles indicate stdev (1-s) of HG03 and HG09. Black: too low; red: too high.

## Slide 14: General Results
HG03 – H88 and HG09 – H88
Box-whisker plots

## Slide 15: Frequency Histogram

## Slide 16: By Stability Class
Class A and transfers the same.
Others indicate settling.

## Slide 17: Residual Trend Analysis
Normalize eastings and northings
  (-1, 1), unit variance
Fit a plane through differences
Constant terms (These are consistent with Tranes et al. [2007])
  GEOID03: -0.012 m (significant (99%) )
  GEOID09: -0.017 m (significant (99%) )
Slope terms
  GEOID03: significant (99%)
  GEOID09: not significant (99%)

## Slide 18: Conclusions
GEOID03 and GEOID09 are accurate at their stated levels in CT
GEOID09 out-performed GEOID03
HG03 and HG09 too low by about 1 cm
  Subsidence
  Re-observe the bench marks
  No “correction surface” warranted

## Slide 19
Thomas.meyer@uconn.edu
http://www.nre.uconn.edu/Faculty_and_Staff/Meyer.php