## Slide 1: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
The 6 P’s: Proper Prior Planning Prevents Poor Performance
Planning and Execution of a typical OPUS Project
Draft
Draft

## Slide 2: Advanced Training
Advanced training modules are needed to enable:
Using OPUS Projects (5.1 and later) to plan, process, and submit GNSS campaign surveys to NGS for incorporation into the National Spatial Reference System, and publication through NGS datasheets.
Draft
In development

## Slide 3: OPUS STATIC
2 hours minimum observation duration, dual frequency
Uses PAGES processor, but M-PAGES may replace it (multi-constellations)
  Could shorten the minimum observation duration and improve results. Need to wait for final research.
Draft
NGS Presentations Library
https://geodesy.noaa.gov/web/science_edu/presentations_library/
Search for “M-PAGES”
M-PAGES

## Slide 4: Redundancy / No Check
All projects submitted to NGS for publication require at least 2 observations that agree with each other.
So, if one fails, then a new session must be scheduled – or reject the mark or session.
If you have 3 observations, you can reject one and still have two.
Cost to observe vs cost to re-mobilize?
Draft

## Slide 5: Plan Occupations and Sessions
OPUS PROJECTS will attempt to group your submitted RINEX files into “sessions” based on their overlapping start/stop times.
You can make this more reliable by planning coordinated observation schedules for your crew.
Individual observations meet minimum duration, start/stop on schedule, ARP heights, etc.
Draft

## Slide 6: Plan Occupations and Sessions
Ideal session has well-defined and well-coordinated start/stop time, well-matched durations, and maximized overlap.
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
Easy for OPUS PROJECTS to define sessions
Time
Gap
Time
Gap
Time
Overlap Time
Overlap Time
Overlap Time
Draft
Session 1
Session 2
Session 3

## Slide 7: Work Flow for OPUS Projects 101 & 102… in 13 easy steps!
Topics covered in OP102
Project Development
Mark Recovery, Photos
Project Proposal
Create Project in OP
Mark Descriptions
Field Campaign
Load obs. into project
QA/QC OPUS solutions
Session Processing
Preliminary Network Solution
Horizontal Network Solutions
Vertical Network Solutions
Topics covered in OP101
Report, Final Check and Submit to NGS
Draft
Today, we will work on the GREEN boxes.
Notes: Project Development, Project Proposal, Create Project in OP: Module 1
Mark Recovery, Photos, Mark Descriptions: Module 2
Field Campaign: that’s on YOU!!
Load observations into OP: we covered that in OP101
QA/QC of OPUS solutions: we covered that in OP101
Session Processing: covered in OP101 & we’ll recap that shortly
Preliminary network solution: covered in OP101, & we’ll recap it shortly

## Slide 8: OP102 Course Outline
OP102 will have 5 separate modules building on the basic OPUS Projects Manager’s Training (OP101)
Module 1:
Planning your Project
Module 2:
Mark descriptions and other required files
Module 3:
Horizontal adjustments
Module 4:
Vertical adjustments
Module 5:
Submitting to NGS
Run your survey, collect data, process your GNSS data according to OP101
Draft

## Slide 9: Great news!
There’s a User Guide with full details
Draft

## Slide 10: Module 1: Planning Your Project
What is the project’s objective?
Exploring the requirements for planning a successful GNSS project for submission to NGS for publication
What survey marks will I use as control?
How accurate does my survey need to be?
Draft
Notes: Geometric coordinates are always considered a triplet: Lat, Lon, EH. So height accuracy always plays into the equation, regardless of whether or not you want NAVD 88.

## Slide 11: Project Objectives
If your project objectives include any of the following, OPUS-Projects is an excellent tool…
Verify existing survey control
  Verification of published coordinates and/or heights on existing marks
Least squares adjustment of a static GPS survey network
  Network solution for simultaneously occupied user marks
  Aligned to NAD 83, NAVD 88 or other datums in the NSRS
Establishment and publication of new control
  Submittal of survey to NGS for consideration of inclusion in national database of survey control, available through NGS datasheets
Draft

## Slide 12: Important Considerations
1. Is the project horizontal (lat/lon/ellht) only?
What are good horizontal control stations? (Hint: CORSs)
2. Do you need vertical (orthometric heights), too?
What are valid vertical control marks? (Hint: BMs)
Draft
Notes: If the projects objectives are restricted to geometric coordinates, there is no need to observe valid NAVD 88 control. It s

## Slide 13: Important Considerations
GPS is 3-D technology
  Latitude
  Longitude
  Ellipsoid height
  Orthometric height
GPS is more accurate horizontally than vertically
  Therefore, the vertical requirements will “drive” survey design
Horizontal Survey
Horizontal+Vertical Survey
Draft

## Slide 14: Planning Your Survey
Horizontal – only GPS Survey
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Horizontal + Vertical GPS Survey
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 15: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 16: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 17: Setting New Marks
NGS Publications Library
Smith, C.L. (2010). “Bench Mark Reset Procedures”, National Geodetic Survey, Silver Spring, MD
Set the most stable, permanent mark possible for the local conditions.
Draft

## Slide 18: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 19: Select CORSs for Control
One of the more critical aspects of designing your project
OPUS-Projects automatically loads CORSs into each session from the OPUS-S solutions
Best practice is to check the quality of the CORSs prior to starting your project—have a plan before your survey!
The User Guide provides more details
Let’s look at the considerations
Draft

## Slide 20: CORS Considerations
Hub
CORS
CORS
CORS
24hr
24hr
24hr
>2hr
>2hr
Recommend a “hub” design for each session
  Designate a local CORS close to project area as the local hub
Use multiple local CORSs to have redundant control
  1 local hub within 0 to 200 km of user marks
  3 or more CORSs as redundant control within 0 to 300 km of the hub
Include 1 or more distant CORS to aid in tropospheric corrections.
  1 (or more) distant CORS (400 – 800 km from the hub) for tropospheric delay modeling
CORS
User
User
User
24hr
User
100 km
300 km
400 - 800 km
Draft

## Slide 21: CORS Selection Criteria
Data must be available at the time of the survey!
Small data gaps are usually OK.
Draft
Not OK
OK

## Slide 22: CORS Selection Criteria
Data must be available at the time of the survey!
Longer time series likely leads to better coordinates
Draft

## Slide 23: CORS Selection Criteria
Data must be available at the time of the survey!
Longer time series likely leads to better coordinates
Computed velocities - from CORS Position and Velocities page
  May also see “published velocities”
  May also see “modeled velocities”.
Draft

## Slide 24: CORS Selection Criteria
Data must be available at the time of the survey!
Longer time series likely leads to better coordinates
Computed velocities (from CORS Position and Velocities page)
Good network accuracies (< 3cm EH, <1.5cm Lat/Lon) – see CORS datasheet.
Draft

## Slide 25: CORS Selection Criteria
Data must be available at the time of the survey!
Longer time series likely leads to better coordinates
Computed velocities (from CORS Position and Velocities page)
Good network accuracies (< 3cm EH, <1.5cm Lat/Lon) – see CORS datasheet
Short term plots show low RMS, no bias, and consistent data
Bias shown here
Draft
Notes: Show BRTW as an example of a bad station

## Slide 26: CORS Selection Criteria
Data must be available at the time of the survey!
Longer time series likely leads to better coordinates
Computed velocities (from CORS Position and Velocities page)
Good network accuracies (< 3cm EH, <1.5cm Lat/Lon) – see CORS datasheet
Short term plots show low RMS, no bias, and consistent data
Better Data!
Draft

## Slide 27: CORS Network Accuracies (Chesapeake Tutorial Project)
CORS | Network Accuracies
 | FGDC (95% conf, cm) Standard deviation (cm) CorrNE Horiz Ellip SD_N SD_E SD_h (unitless)
ASUB | NETWORK 0.15 0.45 0.06 0.06 0.23 -0.03664600
LOY2 | NETWORK 0.12 0.32 0.05 0.05 0.16 -0.03478100
LOYW | NETWORK 0.09 0.20 0.03 0.04 0.10 -0.25218600
LOYZ | NETWORK 0.12 0.18 0.03 0.06 0.09 -0.01925400
LS03 | NETWORK 0.12 0.24 0.03 0.05 0.12 -0.38625600
NCEL | NETWORK 0.09 0.20 0.03 0.04 0.10 -0.31335900
NCGA | NETWORK 0.13 0.39 0.05 0.05 0.20 -0.09434300
VAGP | NETWORK 0.13 0.35 0.05 0.06 0.18 -0.11339600
All network accuracies are:
- less than 1.5 cm Horiz and
- less than 3 cm Ellip
Source: NGS Datasheets November 01, 2022

## Slide 28: CORS Velocity Status (Chesapeake Tutorial Project)
All are COMPUTED velocities.
Source: NGS CORS Position and Velocities November 01, 2022
CORS | Velocity Status
ASUB | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
LOY2 | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
LOYW | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
LOYZ | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
LS03 | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
NCEL | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
NCGA | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.
VAGP | ITRF2014 VELOCITY - Computed in Jun 2019 using data through gpswk 1933.

## Slide 29: CORS Selection Criteria
Data must be available at the time of the survey!
Longer time series likely leads to better coordinates
Computed velocities (from CORS Position and Velocities page)
Good network accuracies (< 3cm EH, <1.5cm Lat/Lon) – see CORS datasheet
Short term plots show low RMS, no bias, and consistent data
Select a distant CORS (400 - 800 km away) for tropospheric modeling
“Place X” draws a 250 km radius circle to guide selection
Draft

## Slide 30: CORS Selection –additional thoughts
For most projects, plan to use the same hub in every session
EXCEPT:
But, for large projects, you may need more than one hub in a session
If user marks are spread out so far in a session that it is not possible to have one hub within 100 km, then designate more hub(s) at about 200 km spacing.
For multi-hub projects, designate the same CORSs as hubs in every session (HUB1, HUB2, HUB3). This will limit hub-to-mark baseline lengths to 100 km or so.
HUB2
HUB3
HUB1
CORS1
100 km
300 km
375 - 800 km
~ 200 km
~ 200 km
Draft
Notes: Session: Correlations among marks uses common-mode errors to increase accuracies
Note that vendor software typically goes straight to network solution, but OPUS Projects requires session processing first
ALSO, note that in the (near) future, you will be able to import Real-Time VECTORS (RTK, RTN) into your project

## Slide 31
CORS11
HUB2
CORS12
HUB3
CORS10
HUB1
CORS1
DISTANT CORS1
DISTANT CORS2
CORS8
CORS2
CORS3
CORS4
CORS5
CORS7
CORS6
Detailed Multi-hub Project
200 km = 125 mi
200 km = 125 mi
Draft

## Slide 32: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 33: Passive Control
How to find control in your area: NGS Data Explorer (https://geodesy.noaa.gov/NGSDataExplorer/)
Input city, state, or lat/lon
Once marks appear, you can manually mark the center of your area with an “x” and specify a search radius
This will show you what control may be present. Use the NGS “Passive Mark Page” to get more detailed information on each mark of interest
Draft

## Slide 34: Passive Control
Try the NGS Passive Mark Page to get more information on each mark of interest (https://beta.ngs.noaa.gov/datasheets/passive-marks/index.html)
Input Permanent Identifier (PID)
Draft

## Slide 35: Recommended Vertical Control
Find bench marks that are either:
GPS-Derived Orthometric Height
  Height Mod Heights (2cm/5cm)
Leveled heights (ADJUSTED and RESET)
“HT_MOD” = Height published to 2 decimal places
Leveled Heights are published to 3 decimal places
Draft
Notes: What marks could be used to tie your survey to NAVD 88?
Leveled Heights of First or Second Order are best
Next, you could consider using GPS-derived

## Slide 36: Mark Recovery
Try the NGS mark recovery tool for existing marks: https://geodesy.noaa.gov/cgi-bin/mark_recovery_form.prl
Note: Online mark recovery will not help you build your WinDesc file (see Module 2)
Draft
Notes: Note: You may need to request a NGS Agency Code! You’ll need that later to create your OPUS Project project for submission to NGS
Take all three photos available on the Mark Recovery Form –these are the three photos that get loaded. They are already named correctly if you use the form.

## Slide 37: Field validation
Time to hit the field!
Are the marks still in good condition?
  Send in Mark Recoveries for those marks which will not be in the project.
  Send in Mark Recoveries for those marks which will be in the project.
  But (if Submit to NGS) the project Marks will be submitted via WinDesc
Do they have clear, unobstructed sky view (10 to 15 degrees above horizon)?
Sky view from fish-eye camera lens
Draft
Notes: Never assume that marks will be found in good condition
Sky view: talk about the importance of obstructions in degrading GNSS signals. There is a lot of confusion about what an obstruction really is. Sky view is covered in OP101.
Elevation mask: doesn’t really matter if you set it in the receiver or set it in OP. However, if you set mask too high in receiver, there’s nothing you can do in OP to recover that missing data.

## Slide 38: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 39: Requirements for Vertical Control
Non-control or “new” benchmarks must be within a certain distance of 2 (or more) valid, existing vertical control marks. (typically 30 km)
Maximum distance between new benchmarks and valid, existing vertical control is between 30-50 km, based on occupation duration. See Chart.
Maximum Distance to Valid, Existing Vertical Constraints based on Occupation Duration (hr)
Average Duration of 2 Longest Occupations (tavg)
Average Duration of 2 Longest Occupations (tavg) | Maximum Distance (km)
2 hours or less | 30 km
3 hours | 35 km
4 hours | 40 km
5 hours | 45 km
6 hours or more | 50 km

## Slide 40: Requirements for Vertical Control
Deep dive on control mark spacing
Occupy bench marks with “valid” existing orthometric heights
  Distributed every ~30-50 km
  Minimum of two (2) valid control marks per non-control or new mark
  Adhere to Maximum Distance to Vertical Constraints requirement (see Chart)
30km radius
Existing vertical control survey mark (7)
New non-control survey mark (8)
New Marks falling in the overlap of 2 circles are within 30 km of 2 existing benchmarks (j, m, p).
Benchmark Spacing Diagram
j
m
p

## Slide 41
Requirements for Vertical Control
Existing Valid BenchmarkList | New Benchmark List |  |  |  |  |  |  |  | 
 |  | h | i | j | k | l | m | n | p
 | A | 20 | 34 | 44 | 46 | 47 | 52 | 48 | 40
 | B | 50 | 20 | 25 | 37 | 40 | 53 | 40 | 37
 | C | 46 | 38 | 23 | 19 | 35 | 43 | 52 | 49
 | D | 49 | 46 | 47 | 35 | 18 | 25 | 44 | 51
 | E | 45 | 44 | 43 | 39 | 32 | 14 | 32 | 40
 | F | 37 | 42 | 47 | 46 | 44 | 40 | 34 | 21
 | G | 34 | 35 | 39 | 34 | 35 | 38 | 32 | 25
Benchmark Distance Tabulation
Color Code: 0 to 30 km = bold font w/green color, 30 km or more = normal font w/pink color
A column with 2 or more bold font w/green color is within 30 km of 2 or more existing valid benchmarks.
Non-control or “new” marks must be within a certain distance of 2 (or more) vertical control marks. (typically 30 km)
Measure these distances using engineer’s scale or compute via coordinates.

## Slide 42
Non-control or “new” marks must be within a certain distance of 2 (or more) vertical control marks. (typically 30 km)
Increasing the occupation duration will allow larger radius, thereby including more benchmarks.
Refer to “Maximum Distance to Vertical Constraints” chart
Requirements for Vertical Control
Benchmark Spacing Diagram

## Slide 43: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 44: Mark Eckl et al paper from 2001
Before we move on to NGS’ recent guidance, we should look at some past guidance for review.
In 2001, Mark Eckl and others wrote a research report that investigated the relationship between occupation time, baseline length and relative accuracy.
  NGS Publications Library
    https://geodesy.noaa.gov/CORS/Articles/Accuracy.pdf
  “Accuracy of GPS-derived Relative Positions as a Function of Interstation Distance and Observing-session Duration” February 2001
Draft

## Slide 45: Mark Eckl et al paper from 2001
Conclusions:
Shorter duration observations led to weaker solutions.
Distance between stations was less influential.
4 hours or more was more reliable
Draft
Eckl’s study was limited to 4 hours and longer sessions.

## Slide 46: Mark Eckl et al paper from 2001
Session Duration vs Accuracy
The trend is clear at all distances
  Longer Duration of Observations leads to better accuracy.
T>4 hours
Draft
Eckl’s study was limited to 4 hours and longer sessions.

## Slide 47: Mark Eckl et al paper from 2001
Let’s return to NGS’ Current Guidance
Session Duration vs Accuracy Applied to OPUS PROJECTS
Draft

## Slide 48: Accuracy of OPUS versus Occupation Duration
How long should each occupation be?
-A look at OPUS Accuracies
RMS at 1σ
Multiply by 2.5  95%CI
Multiply by 2. 95%CI
RMS at 1σ
Source: Gillins et al. 2019
Note that the values are ONE SIGMA. Horizontal needs to be multiplied by 2.5 to get 95% CI (bivariate)
A single 4-hour observation per session gets you close to +/- 3 cm 3D, 2.4 cm Up.
Draft
HORIZ
UP
T>4 hours
T>4 hours
Gillins’ study extends below 4 hours
Notes: Note that the values are ONE SIGMA. Horizontal needs to be multiplied by 2.5 to get 95% CI (bivariate)\
One, 4-hour observation per session gets you close to +/- 3 cm 3D, 2,4 cm Up.

## Slide 49: Accuracy of OPUS-Projects
OPUS Projects Network Accuracies
Most important variable for reducing error is TOTAL TIME
Note! Cumulative time, not individual occupations
Plots show that:
Four 5 hour (20 hours total) occupations
  are “equivalent” to
Seven 3 hour (21 hours total) occupations
Ten 2 hour (20 hours total) occupations
Draft
Notes: From Dan Gillins: This slide shows difference between minimum OP requirements (2, 2hr sessions) and more/longer sessions. Longer sessions give you more of a reduction in error than more sessions. Total time on the mark is key. HOWEVER, this assumes that all sessions are good. You can easily have a bad sessions, so it’s ALWAYS better to have more sessions than you need. Problem with 2 sessions: you cannot tell which session might be off: all you could tell is that the two sessions are different, but you wouldn’t necessarily tell which one is correvt.

## Slide 50: Accuracy of OPUS-Projects
95% CI values shown (Ellipsoid Height)
Total Time (T) on mark (hrs)
Upper Curve ≈ Design Curve
(see next slide)
Draft

## Slide 51: “Design Curve” for OPUS-Projects
Vertical Network Accuracies, OPUS Projects
TOTAL time on mark
95% CI values shown
Source: Park et al. 2017
Desired Vertical Network Accuracy vs Total Occupation Time per Mark
Draft
Notes: Final curve is shown, not individual data points (variability not shown)

## Slide 52: Recommendations
Summary of Expected Accuracy of OPUS Projects
Expected Ellipsoid Height Accuracy | Expected Horizontal Accuracy | Total Time on Mark | Recommended Sessions and Durations |  | 
3.0 cm | 1.5 cm | 4 hrs | (2) 2-hr |  | 
2.5 cm | 1.3 cm | 8 hrs | (2) 4-hr | or (3) 3-hr | 
2.0 cm | 1.0 cm | 20 hrs | (2) 10-hr | or (3) 7-hr | or (4) 5-hr
Refer to design curve
Draft
95% CI values shown

## Slide 53: Planning Your Project
Recap:
You have identified your project goals/objectives
You have determined the number/distribution of control marks required in your project area to meet these objectives
You have identified and recovered potential marks to control your project
You have identified CORSs that you intend to use as control for your project
Draft

## Slide 54: Additional project considerations
FAA Airport Control Surveys: PACS and SACS/AC-16 -these project have separate requirements vis-a-vis control and occupation lengths
Equipment requirements and recommendations
  L1 & L2 calibrated antennas, same antenna types if possible
  Calibrated fixed-height GPS tripods
Best practices (see video: Best Practices for Minimizing Errors During GNSS Data Collection, also GNSS Positioning: Survey Planning and Data Acquisition)
Draft

## Slide 55: Submit your Project Plan for Review
Now that you have your Project Plan, time to submit it to NGS for review!
Draft

## Slide 56: NGS Survey Project Proposal Form
Why submit your GNSS Project Plan to NGS (https://geodesy.noaa.gov/SurveyProposal/):
Subject Matter Expert will review your plan, make sure it will meet NGS standards
NGS will assign a Project Tracking ID, which will enable you to use the advanced features of OPUS Projects
With a Project Tracking ID, you will be able to submit your project to NGS for consideration of inclusion into the national database of geodetic control, available through published datasheets
If you do not intend on submitting your project to NGS, but still wish your project to be tied to the national reference frames/datums, you can use the “dummy” tracking ID “0000”
Draft
Notes: If you do not want to go through the project proposal review process, you can still unlock the advanced features of OPUS Projects by assigning the “dummy” tracking ID “0000”

## Slide 57: Creating your OPUS Project
Ready to create your project!
Draft

## Slide 58: Creating your OPUS Project
Insert your NGS Project Tracking ID here if you have it. The Tracking ID can also be added later.
By associating a NGS Project Tracking ID to your project, the advanced features of OP (which support submitting a project to NGS) will become available
Draft

## Slide 59: Ready to Upload Data!
Congratulations!
You have successfully created a project:
The project plan has been reviewed by NGS
The advanced features of OPUS Projects are now enabled
Now you are ready to upload your data files
Draft

## Slide 60: Outline
Set/identify new marks for survey
Choose horizontal control
  Select CORSs
  Recover passive marks in project vicinity (if desired)
Find vertical control distributed throughout the project
  Recover valid bench marks
  Spacing requirements
Develop a session schedule
  Occupation durations
  Repeat occupations
Assign a 4-character ID to your user marks
Draft

## Slide 61: GNSS observation files
GNSS observation files are typically exported from GNSS receivers in proprietary files, with manufacturer-specific naming rules.
Assume that OPUS cannot read your raw data file.
NGS recommends using the vendor-specific RINEX converter to make the conversions.
RINEX Converters
Rinex File
Draft

## Slide 62: Best practices for GNSS observation files
OPUS STATIC (upload page) does not care how you name your observation file.
Your OPUS Projects, though, DOES CARE.
It will attempt to use the first 4 characters of the observation (RINEX) file name as the name for the user mark associated with the file.
Manufacturers often use the serial number of the receiver as the start of the observation file name.
If one receiver is used on multiple marks, OPUS Projects will realize this and start using it’s own name of each user mark (e.g. A001).
Furthermore, some marks may be located very close to each other, so you want to make sure each observation file is associated with the correct mark.
To ensure this, start the RINEX file name with the 4-character ID you will assign to each user mark.
More on this in Module 2.
Draft
Notes: OPUS STATIC (upload page) does not care how you name your observation file.
Your OPUS Projects, though, DOES CARE.
It will attempt to use the first 4 characters of the observation (RINEX) file name as the name for the user mark associated with the file.
Manufacturers often use the serial number of the receiver as the start of the observation file name.
If one receiver is used on multiple marks, OPUS Projects will realize this and start using it’s own name of each user mark (e.g. A001).
Furthermore, some marks may be located very close to each other, so you want to make sure each observation file is associated with the correct mark.
To ensure this, start the RINEX file name with the 4-character ID you will assign to each user mark.
More on this in Module 2.

## Slide 63: Best practices for GNSS observation files
When converting raw data files to RINEX, best practice is to ensure all header information is correct
For ease of associating specific RINEX files to specific user marks in your project, start each RINEX file name with the corresponding OPUS Projects 4-Character mark ID
Recommended RINEX file naming structure: start w/ 4CharID, Day-of-year, session#
e.g. PIP1281A.20O
More on 4-Character IDs in
Module 2:
Mark Descriptions and other required files
4CharID
DOY
Session Letter
YR
Obs
Draft

## Slide 64: Module 1: Planning Your Project
Literature Cited
Gillins, D.T., Kerr, D., and Weaver, B. (2019). “Evaluation of the Online Positioning User Service for Processing Static GPS Surveys: OPUS-Projects, OPUS-S, OPUS-Net, and OPUS-RS,” J. Surv. Eng. (ASCE), 145(3):05019002.
Park, J., Kim, S., Shahbazi, A., Gillins, D., and Dennis, M. (2018). “Evaluation of Static GPS Surveying Campaigns Processed in OPUS-Projects,” Final Technical Report FY17 NA293P, National Geodetic Survey, 58 pp.
Draft

## Slide 65: End

## Slide 66: Extra slides

## Slide 67: Requirements for Vertical Control
*Future developments of OP will permit real-time vectors from shorter occupations
Non-control or “new” marks must be within a certain distance of 2 (or more) vertical control marks
OPUS-Projects currently* requires a minimum of 2-hour occupations (= the OPUS Static minimum)
Maximum distance between new marks and vertical control is between 30-50 km, based on occupation duration. See Chart.
Chart: NAVD 88 Control Spacing (km)
| 30 | 50
 | 2 | 6
Recommended/Permitted
Not Permitted
(need 2 hr minimum time)
Not Permitted
(too far apart)
Not Permitted
Draft

## Slide 68: Requirements for Vertical Control
Deep dive on control mark spacing
Occupy bench marks with “valid” existing orthometric heights
  Distributed every ~30-50 km
  Minimum of two (2) valid control marks per non-control or new mark
  Adhere to distance-occupation requirement
Use latest hybrid geoid model (i.e., GEOID18)
  H = h - N
Perform constrained vertical least squares adjustments of the GNSS network holding the vertical control heights constrained
30km radius
Existing vertical survey control mark (7)
New survey control mark (9)
Draft

## Slide 69: Requirements for Vertical Control
If you choose 2 hour occupations - how many valid existing vertical control marks would you need* to “cover” the new marks?
*At a minimum
Existing vertical survey control mark (7)
New survey control mark (9)
30km radius
Draft

## Slide 70
30km radius
Only 3 new marks (red) are within the 30 km overlapping spacing of the 7 existing valid marks.
2-hour occupations mean 30 km or less spacing between existing valid marks.
Existing survey control mark
New survey control mark
New survey control mark with sufficient vertical control
If you choose 2 hour occupations - how many valid existing vertical control marks would you need* to “cover” the new marks?
Draft
Requirements for Vertical Control

## Slide 71: Requirements for Vertical Control
40km radius
By increasing your spacing to 40km all 9 new marks (red) would be covered by at least two vertical control marks.
Existing survey control mark
New survey control mark
New survey control mark with sufficient vertical control
If you choose 4 hour occupations - how many valid existing vertical control marks would you need* to “cover” the new marks?
4-hour occupations allow 40 km or less spacing between existing valid marks.
Draft
Notes: Note that we’re talking about MINIMUM requirements. It’s always best to include redundant control in case one of your control marks doesn’t fit well with the network