## Slide 1: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Step 2 : Uploading Data

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment

## Slide 3: What’s in this training?
This presentation shows how to upload data to a project.
The format is as a series of steps like a cookbook. Like most cookbooks, the justification for and discussion of variations in those steps will be minimal. The intent is to get you started quickly, then leave you free to explore OPUS Projects on your own.
We assume familiarity with OPUS so some steps will be quite terse. If you are unfamiliar with OPUS, mention this your instructor during a break.

## Slide 4
We’ll start at the OPUS upload web page: http://geodesy.noaa.gov/OPUS/

## Slide 5
At this time, only OPUS Static is allowed to upload to a project. The conventional OPUS Static rules apply.
Notes: We anticipate both the Rapid-static and Static will be allowed to upload to projects before the end of 2011.

## Slide 6
Let’s upload a RINEX file from the training data set. The antenna type and height appropriate for this and all the other files are given in the associated Observation Logs.
Notes: Again, we’re assuming everyone is familiar with the normal OPUS upload procedure and will not cover that in detail. If this is not the case, please mention this to your instructor during the next break.

## Slide 7: RINEX Files (user naming)
BM02121A.13o
Standard RINEX File Naming
Last 2 digits of Year (2013)
Session Letter of the Day (A, B, C, based on user sequence in the field)
Day of Year (001-366)
4 Character MARK NAME
Letter O = Observation File

## Slide 8: RINEX Files (OPUS PROJECTS)
BM02121A.13o
Standard RINEX File Naming
Session Letter of the Day
(A, B, C, etc)
UTC | Rinex File
0:00 AM (midnight) | a
1:00 AM | b
2:00 AM | c
3:00 AM | d
4:00 AM | e
5:00 AM | f
6:00 AM | g
7:00 AM | h
8:00 AM | i
9:00 AM | j
10:00 AM | k
11:00 AM | l
12:00 PM (noon) | m
13:00 PM | n
14:00 PM | o
15:00 PM | p
16:00 PM | q
17:00 PM | r
18:00 PM | s
19:00 PM | t
20:00 PM | u
21:00 PM | v
22:00 PM | w
23:00 PM | x
User Assigned Naming
OPUS Projects Re-naming
Based on actual start times.
BM02121T.13o

## Slide 9: RINEX Header (BM02121A.13o)
2.11 OBSERVATION DATA GPS(GPS) RINEX VERSION / TYPE
cnvtToRINEX 2.14.0 convertToRINEX OPR 04-May-13 16:51 UTC PGM / RUN BY / DATE
----------------------------------------------------------- COMMENT
BM02 MARKER NAME
1005 MARKER NUMBER
Will ULM AIRPORT CREW OBSERVER / AGENCY
4738139036 R6 4.43 REC # / TYPE / VERS
4738139036 TRM R6 ANT # / TYPE
-352723.0133 -4558645.8471 4432311.8395 APPROX POSITION XYZ
2.0000 0.0000 0.0000 ANTENNA: DELTA H/E/N
1 1 0 WAVELENGTH FACT L1/2
4 C1 L1 L2 P2 # / TYPES OF OBSERV
2013 5 1 19 20 0.0000000 GPS TIME OF FIRST OBS
2013 5 1 23 53 15.0000000 GPS TIME OF LAST OBS
0 RCV CLOCK OFFS APPL
16 LEAP SECONDS
17 # OF SATELLITES
G01 63 63 63 63 PRN / # OF OBS
G03 997 996 996 997 PRN / # OF OBS
G32 205 205 205 205 PRN / # OF OBS
CARRIER PHASE MEASUREMENTS: PHASE SHIFTS REMOVED COMMENT
END OF HEADER
Session letter = “t”
based on starting time

## Slide 10
Complete the OPUS upload form normally, but before clicking the “Upload to Static” button, click the “Options” button.

## Slide 11
This causes the Options to “accordion” into view.

## Slide 12
Enter your project ID into the “Project Identifier” field. Remember that you can share your project ID so others can upload data to your project, for example a field crew.
uab9c2mv

## Slide 13
Step 2 : Uploading Data
We’ll leave the other options as they are. Now click the Upload button to have this data file uploaded to your project.
uab9c2mv

## Slide 14
After clicking the upload button, the upload confirmation window will appear, but with some differences from “normal”.
Notes: This essentially appears very similar to using the publish options, but the OPUS results are not published. Publishing a project is done using products created from a network adjustment and then proceeding through the conventional steps for publishing to the NGS Integrated Database.

## Slide 15
You project ID and other metadata will be listed (and should be visually confirmed) …
Note “converted” file name!

## Slide 16
… and you may be prompted to provide a mark description.
These 3 options don’t show up in OP5.1.
You might see them in other OPUS applications, so let us look at each of them briefly.
“SKIP DESCRIPTION” will be the best choice for OPUS PROJECTS.
  “Mark has a PID” and “Mark is NEW to NGS” are better used in OPUS Share.
For the sake of completeness, I will show you all 3 methods.

## Slide 17
Because it’s a little more interesting, let’s start by pretending this is a NEW mark. Click the “mark is NEW to NGS” button.

## Slide 18
In a moment, the “Describe new mark” form will appear. Through this form, the minimal information needed to identify a mark, and describe its location and condition can be uploaded.

## Slide 19
Consider reviewing “Help File: Mark Description”. http://geodesy.noaa.gov/marks/descriptors.shtml

## Slide 20
The descriptive data for all the marks used in the training materials can be found in the Observation Logs, Recovery Notes, and Photos files. The form is too large for a single slide, so we’ll focus on the top half first.

## Slide 21
If the mark is a disk, the stamping should be copied exactly as it appears on the mark. In other cases, the designation may come from historical or other documentation. Usually stamping and designation will be similar.
5202 G
5202 G 1987

## Slide 22
Example Mark (5202 G) is a vertical control disk on an aluminum rod, so we select the type appropriately. Remember to enter the rod and sleeve depths in these cases.

## Slide 23
A variety of settings for the mark are provided via the pull-down menu. Use the “Specific setting” field for unique information.

## Slide 24
Next, describe how to find the mark. The description is limited to 500 characters, but that’s OK. Assume the next person will be able to get close to the mark using their handheld GNSS, and include just the last few critical steps needed to find the mark.

## Slide 25
Stability, Magnetic, Application, Antenna S/N, and Receiver Model, S/N and Firmware fields aren’t required, but still important to the description of the mark and traceability of the work. Complete these if possible.
Continue entering the data in each field, when finished, click Upload Description, or select Discard to cancel.

## Slide 26
After another moment, the description upload confirmation appears. Uploading this data file and description are complete (and probably in the project by now).

## Slide 27: Status Check
Having uploaded BM02 and its description, the project should now show an ICON for BM02 and the MARKS and CORS Tables will show content. There will also be a MARKS Table at the bottom of the page.

## Slide 28
Let’s upload another RINEX file, but follow a slightly different path. Complete the upload form normally …

## Slide 29
… once again, make sure the project ID is provided and click the Upload to Static button …

## Slide 30
… but this time, let’s follow the “mark has a PID” path.

## Slide 31
The description for a recovered mark is simpler still. Provide the PID, new photos, the mark’s condition and additional descriptive text. When complete, click Upload Description or Discard to cancel.

## Slide 33: Status Check
Having uploaded BM02 and CBN1 and their description, the project should now show an ICON for BM02 and CBN1 and the MARKS and CORS Tables will show content. There will also be a MARKS Table at bottom of page.

## Slide 34: Recommendation
Since the same mark(s) will be observed several times in a project,
  it is repetitive, confusing, and wasteful to enter the descriptive data EACH TIME.
The descriptive data can be entered later just ONCE for each mark (in OP, on the Mark Page)
So, better to choose SKIP DESCRIPTION.

## Slide 35: .ZIP Upload via OPUS STATIC
You can ZIP several Rinex files together in a single ZIP file for submission, IF they are…
  a single antenna type
  a single antenna height
OPUS Static will unzip them and apply the chosen antenna type and antenna height to all the files in the ZIP. And send them all to a Project ID if entered in Options.
  There is a maximum size for a .ZIP (20Mb?)
  No obvious limit on number of files (I’ve done 93)
Pro Tip

## Slide 36: What a field member would see.
Let’s review the emails that would be sent to a person uploading data to your project.
Sample GMAIL Inbox
Note “smart” subject line enables filtering to dedicated folders
Project ID
Your Filename
OPUS Static Solution number

## Slide 37
The project team member uploading the data files will still get the OPUS solution report. The report will also be available to you, the project manager. Review the usual OPUS STATIC Quality Indicators.
Is this the MARK and Distance you expected?
I save this output as a TXT file in my “OPUS Static Results” folder. This allows me to use WinTeqc later to harvest a useful report summary.

## Slide 38
However, the project team member might also receive a second email if the OPUS solution doesn’t meet the project’s solution quality threshold preferences. Highlighting added for emphasis.
Part of your job as project manager, is to prepare your field teams for this eventuality. This does not mean this data was omitted from the project. It simply means that this solution will be flagged for easier identification.
Notes: OPUS quality control report for 2123275a.06o.

## Slide 39: Let’s look at what we’ve got so far.
Before we upload any more data, let’s look at what we’ve got so far with the understanding that this mimics what you might see after the first day of an active project.

## Slide 40
This is the Manager’s Page. We’re broadly familiar with the page, but let’s look at how this page has changed now that some data has been uploaded.

## Slide 41
The marks represented by the two data files we’ve uploaded now appear on the map and in the Mark List to the right. The CORS used in the OPUS solutions are included too. A Marks and Sessions Table appears to the lower left.

## Slide 42
Clicking on a map icon or a table entry causes a short summary of the data files for that mark to appear. The observer’s name is also a convenience link to send that person an email.

## Slide 43
The OPUS solution reports are available through the Show File control on the left.

## Slide 44
At the bottom of the page, a new table has appeared. This lists the marks and indicates the sessions to which their data files belong.

## Slide 45
The column and row headers are convenience links. The mark names on the left and right take you to the MARK PAGE for that mark. The session names across the top take you to the SESSION PAGE for that session.

## Slide 46
Let’s briefly visit the session 2013-121-A session page. Click on the link …

## Slide 47
This page contains information and controls specific to this session: 2013-121-A. Here again, we see the marks and CORS on the map and in the tables.

## Slide 48
The Session Page is limited to information specific to the session.
The Manager’s Page includes all sessions.

## Slide 49
And there are new tables on this page too. The “Solution Quality Indicators” table lists the solution values checked against the quality threshold preferences. The “Data Availability” table gives a representation of the satellite availability in each data file.

## Slide 50
The row headers in these tables are convenience links to the individual mark pages, just as on the manager’s page. Let’s visit the page for mark BM02.

## Slide 51
Here, you can review, edit or enter the mark description. Many other tools are available, but we’ll save those for later.
This is why we Skipped Description – we can edit it here on this page.

## Slide 52: Let’s look a little farther ahead.
Let’s jump to the point where all project data has been uploaded.

## Slide 53
Note that all 6 marks in our training project are now shown and 4 sessions have been defined.

## Slide 54
The sessions have been designated as: yyyy-ddd-a, where
yyyy = year
ddd = day of year
a = sequence during the day

## Slide 55
Let’s click the Marks&CORS button on the map. The map’s center and zoom level changes to encompass all project marks and the included CORS.

## Slide 56: Let’s take a short break.
The preliminaries are now complete.
Let’s take a break, stretch our legs and clear our heads.
Use this break to upload all 22 of the RINEX files - skip the “wlp2041r_short.21o” file as it is only a few hours long and does not overlap in any sessions.
The next step will be the all-important QA/QC of the uploaded data.

## Slide 57: QA/QC Circle of Trust
CONTINUE
START
Verify
Modify Input
Select/Reject
Recompute
Process/ Compute
Trust
Yes
No
The QA/QC Circle

## Slide 58: QA/QC of Upload Step
No need to go further if we have flaws.
Observation Field Logsheets
RINEX Filenames and File Headers
OPUS PROJECTS Mark Pages
OPUS Upload Page
The QA/QC Circle
START
VERIFY

## Slide 59: Compare OPUS STATIC Solutions
For the Chesapeake Tutorial Project, there are 22 solutions to verify.
Inspect each one as it is submitted by the field crew. (see slide 37)
Make a final tabulation for the Report.
  (WinTEQC or OPUS Accumulator)
Verify each Mark Page against the Observation Field Logsheets.
Any discrepancies imply that the RINEX file needs editing and resubmitting.
  Resubmitted RINEX files overwrite the previous.

## Slide 60: WinTEQC Software
NGS has a software called WinTEQC on its webpage. Look under User-Contributed Software page.
Download / Install
OPUS Accumulator
  Similar option

## Slide 61: Organize your Folders
Capture all 22 of the OPUS STATIC solutions as .TXT files in a folder. Here’s what I use:

## Slide 62
WinTeqc – OPUS Utilities Screen Layout

## Slide 63
WinTeqc tabulates the OPUS STATIC Solutions

## Slide 64
File | Antenna | HI | Start | Stop | Lat | Acc | Lon | Acc | Northing | Easting | El Hgt | Acc | Ortho | Acc | Geoid Model | %Amb | %Used | RMS | iDOP | Res | PID | Mark | Distance | IGS h
863f041l.21o | TRM115000.0 | 1.9991 | 2/10/2021 11:55 | 2/10/2021 19:05 | 36 56 33.74452 | 0.003 | 76 19 43.29916 | 0.004 | 1069848.928 | 3693394.142 | -34.677 | 0.010 | 2.225 | 0.047 | GEOID18 | 95% | 81% | 0.014 |  | 6,16,12 | FX0099 | F 452 | 105.40 | -36.031
863f048n.21o | TRM115000.0 | 1.9991 | 2/17/2021 13:43 | 2/17/2021 21:07 | 36 56 33.74466 | 0.004 | 76 19 43.29912 | 0.004 | 1069848.932 | 3693394.143 | -34.695 | 0.005 | 2.207 | 0.045 | GEOID18 | 96% | 79% | 0.013 |  | 6,15,12 | FX0099 | F 452 | 105.40 | -36.049
863f054l.21o | TRM115000.0 | 1.9991 | 2/23/2021 11:50 | 2/23/2021 19:15 | 36 56 33.74462 | 0.011 | 76 19 43.29926 | 0.004 | 1069848.931 | 3693394.139 | -34.692 | 0.006 | 2.210 | 0.046 | GEOID18 | 99% | 92% | 0.015 |  | 6,18,13 | FX0099 | F 452 | 105.40 | -36.046
brmr041l.21o | TRM115000.0 | 1.9999 | 2/10/2021 11:52 | 2/10/2021 19:04 | 36 51 16.85016 | 0.003 | 76 18 0.44334 | 0.002 | 1060141.929 | 3696166.071 | -36.064 | 0.011 | 1.017 | 0.047 | GEOID18 | 98% | 93% | 0.014 |  | 6,16,12 | DG9069 | BREADMAKER | 0.00 | -37.421
brmr048m.21o | TRM115000.0 | 1.9999 | 2/17/2021 12:56 | 2/17/2021 21:06 | 36 51 16.85005 | 0.003 | 76 18 0.44334 | 0.001 | 1060141.925 | 3696166.071 | -36.066 | 0.009 | 1.015 | 0.045 | GEOID18 | 97% | 93% | 0.013 |  | 6,15,11 | DG9069 | BREADMAKER | 0.00 | -37.422
brmr054l.21o | TRM115000.0 | 1.9999 | 2/23/2021 11:31 | 2/23/2021 19:50 | 36 51 16.85020 | 0.010 | 76 18 0.44330 | 0.002 | 1060141.930 | 3696166.072 | -36.063 | 0.008 | 1.018 | 0.045 | GEOID18 | 99% | 93% | 0.015 |  | 4,14,12 | DG9069 | BREADMAKER | 0.00 | -37.419
gp99041l.21o | TRM115000.0 | 2.0003 | 2/10/2021 11:41 | 2/10/2021 20:20 | 36 53 11.57719 | 0.009 | 76 17 42.87304 | 0.003 | 1063687.683 | 3696518.617 | -34.974 | 0.019 | 2.078 | 0.051 | GEOID18 | 90% | 89% | 0.018 |  | 6,19,15 | FX3179 | BABE | 481.60 | -36.328
gp99048n.21o | TRM115000.0 | 2.0003 | 2/17/2021 13:55 | 2/17/2021 21:07 | 36 53 11.57726 | 0.001 | 76 17 42.87289 | 0.004 | 1063687.686 | 3696518.621 | -34.985 | 0.023 | 2.067 | 0.054 | GEOID18 | 80% | 89% | 0.017 |  | 7,22,16 | FX3179 | BABE | 481.60 | -36.340
gp99054l.21o | TRM115000.0 | 2.0003 | 2/23/2021 11:36 | 2/23/2021 19:16 | 36 53 11.57723 | 0.004 | 76 17 42.87293 | 0.004 | 1063687.684 | 3696518.620 | -34.988 | 0.007 | 2.064 | 0.048 | GEOID18 | 88% | 85% | 0.018 |  | 8,26,19 | FX3179 | BABE | 481.60 | -36.343
ou03041l.21o | TRM115000.0 | 1.9999 | 2/10/2021 11:54 | 2/10/2021 19:05 | 36 53 11.86980 | 0.010 | 76 18 13.50356 | 0.003 | 1063679.023 | 3695760.151 | -34.326 | 0.004 | 2.710 | 0.045 | GEOID18 | 96% | 87% | 0.013 |  | 6,17,13 | AJ4598 | ODU 3 | 0.00 | -35.681
ou03048n.21o | TRM115000.0 | 1.9990 | 2/17/2021 13:56 | 2/17/2021 21:05 | 36 53 11.86984 | 0.008 | 76 18 13.50353 | 0.003 | 1063679.024 | 3695760.152 | -34.325 | 0.012 | 2.711 | 0.047 | GEOID18 | 96% | 87% | 0.014 |  | 7,19,14 | AJ4598 | ODU 3 | 0.00 | -35.679
ou03054l.21o | TRM115000.0 | 1.9990 | 2/23/2021 11:49 | 2/23/2021 19:10 | 36 53 11.86987 | 0.013 | 76 18 13.50356 | 0.004 | 1063679.025 | 3695760.151 | -34.323 | 0.014 | 2.713 | 0.048 | GEOID18 | 100% | 85% | 0.015 |  | 6,20,16 | AJ4598 | ODU 3 | 0.00 | -35.678
ou18041l.21o | TRM115000.0 | 2.0000 | 2/10/2021 11:44 | 2/10/2021 19:05 | 36 53 8.99419 | 0.011 | 76 19 0.94235 | 0.005 | 1063563.160 | 3694587.854 | -35.300 | 0.007 | 1.715 | 0.051 | GEOID18 | 92% | 80% | 0.022 |  | 10,28,21 | FX3225 | LAMBERT POINT WEST INCINER | 267.70 | -36.655
ou18048n.21o | TRM115000.0 | 2.0004 | 2/17/2021 13:48 | 2/17/2021 21:07 | 36 53 8.99405 | 0.004 | 76 19 0.94238 | 0.009 | 1063563.155 | 3694587.853 | -35.287 | 0.034 | 1.728 | 0.063 | GEOID18 | 91% | 73% | 0.021 |  | 14,32,26 | FX3225 | LAMBERT POINT WEST INCINER | 267.70 | -36.642
ou18054l.21o | TRM115000.0 | 2.0004 | 2/23/2021 11:52 | 2/23/2021 19:11 | 36 53 8.99423 | 0.011 | 76 19 0.94235 | 0.003 | 1063563.161 | 3694587.854 | -35.288 | 0.013 | 1.727 | 0.052 | GEOID18 | 90% | 72% | 0.022 |  | 8,30,26 | FX3225 | LAMBERT POINT WEST INCINER | 267.70 | -36.643
w416041l.21o | TRM115000.0 | 2.0000 | 2/10/2021 11:51 | 2/10/2021 19:03 | 36 57 29.21101 | 0.006 | 76 15 34.14974 | 0.004 | 1071702.294 | 3699516.669 | -33.723 | 0.009 | 3.274 | 0.050 | GEOID18 | 90% | 83% | 0.019 |  | 11,25,17 | FX0049 | W 416 | 0.00 | -35.077
w416048n.21o | TRM115000.0 | 2.0000 | 2/17/2021 13:50 | 2/17/2021 21:09 | 36 57 29.21108 | 0.005 | 76 15 34.14960 | 0.004 | 1071702.297 | 3699516.672 | -33.726 | 0.012 | 3.271 | 0.051 | GEOID18 | 89% | 81% | 0.019 |  | 14,27,19 | FX0049 | W 416 | 0.00 | -35.080
w416054m.21o | TRM115000.0 | 2.0000 | 2/23/2021 12:15 | 2/23/2021 19:18 | 36 57 29.21123 | 0.006 | 76 15 34.14974 | 0.001 | 1071702.301 | 3699516.668 | -33.714 | 0.009 | 3.283 | 0.051 | GEOID18 | 87% | 77% | 0.020 |  | 8,28,21 | FX0049 | W 416 | 0.00 | -35.067
wlp20480.21o | TRM57971.00 | 0.0000 | 2/17/2021 0:00 | 2/17/2021 23:59 | 36 45 59.76770 | 0.006 | 76 15 30.56738 | 0.004 | 1050457.659 | 3700109.841 | -13.233 | 0.003 | 23.994 | 0.043 | GEOID18 | 96% | 90% | 0.017 |  | 4,9,7 | FX0439 | S 307 | 189.20 | -14.592
wlp20540.21o | TRM57971.00 | 0.0000 | 2/23/2021 0:00 | 2/23/2021 23:59 | 36 45 59.76770 | 0.005 | 76 15 30.56735 | 0.005 | 1050457.659 | 3700109.842 | -13.234 | 0.001 | 23.993 | 0.042 | GEOID18 | 95% | 91% | 0.017 |  | 4,10,7 | FX0439 | S 307 | 189.20 | -14.594
wlp20550.21o | TRM57971.00 | 0.0000 | 2/24/2021 0:00 | 2/24/2021 23:59 | 36 45 59.76778 | 0.008 | 76 15 30.56731 | 0.004 | 1050457.661 | 3700109.843 | -13.227 | 0.002 | 24.000 | 0.042 | GEOID18 | 95% | 91% | 0.017 |  | 3,9,7 | FX0439 | S 307 | 189.20 | -14.587
wlp20630.21o | TRM57971.00 | 0.0000 | 3/4/2021 0:00 | 3/4/2021 23:59 | 36 45 59.76767 | 0.006 | 76 15 30.56731 | 0.003 | 1050457.658 | 3700109.843 | -13.232 | 0.002 | 23.995 | 0.043 | GEOID18 | 93% | 91% | 0.017 |  | 4,10,8 | FX0439 | S 307 | 189.20 | -14.591
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100% | 100% |  | OPUS-RS results only | G-file Std Dev (3rd of 3 C-records) | Nearest PID notification | Nearest PID designation | Nearest PID distance | IGS14 Ell Ht
COPY / PASTE the WinTEQC output to EXCEL
Included in your training .zip file
OPUS Static Results:
WinTEQC Summary.xlsx
?
Check the columns for any out-of-tolerance non-repeatability.
WinTeqc tabulates the OPUS STATIC Solutions

## Slide 65: Individual Mark Page – upper half
Did mark icon plot where expected?
Verify Hardware Summary
BRMR - Breadmaker

## Slide 66: Mark Icon Plot
Hover cursor on yellow Mark Icon – shows Mark ID (brmr)
Hover cursor on black Triangle – shows PID of nearest published mark (DG9069)
Is the Mark Icon plotted where expected? Did field crew occupy wrong mark?
BRMR - Breadmaker

## Slide 67: Hardware Summary
Verify that Antenna and Receiver Model is correct and matches field log sheet
Verify that Antenna and Receiver serial number is correct and matches field log sheet
Verify that Antenna Height is correct and matches field log sheet
Q1) Where did OPUS PROJECTS find the serial numbers?
Q2) Where did OPUS PROJECTS find the receiver model reference?
A) In the RINEX Header, so that’s where the corrections must be made.
BRMR - Breadmaker

## Slide 68: RINEX Header (brmr041i.21o)
BRMR MARKER NAME
BRMR MARKER NUMBER
JORDAN, K.S. NATIONAL GEODETIC SURVEY OBSERVER / AGENCY
5832R50274 TRIMBLE NETR9 5.45 REC # / TYPE / VERS
6122223925 TRM115000.00 NONE ANT # / TYPE
1210149.3333 -4964281.2933 3804480.4561 APPROX POSITION XYZ
1.9990 0.0000 0.0000 ANTENNA: DELTA H/E/N
1 1 WAVELENGTH FACT L1/2
6 L1 L2 C1 P1 C2 P2 # / TYPES OF OBSERV
30.0000 INTERVAL
0 RCV CLOCK OFFS APPL
18 LEAP SECONDS
2021 2 10 11 52 0.0000000 GPS TIME OF FIRST OBS
END OF HEADER
BRMR - Breadmaker
The RECEIVER SN matches the Field Log (5832R0274).
The ANTENNA SN does not match the Field Log (6122223925, should be 6122223766).
The RECEIVER Type matches the Field Log (TRIMBLE NET R9)
The ANTENNA Type matches the Field Log (TRM115000.0)
The ANTENNA Height does not match the Field Log (1.9990, should be 1.9999)

## Slide 69: RINEX Header (BM02121A.13o)
2.11 OBSERVATION DATA GPS(GPS) RINEX VERSION / TYPE
cnvtToRINEX 2.14.0 convertToRINEX OPR 04-May-13 16:51 UTC PGM / RUN BY / DATE
----------------------------------------------------------- COMMENT
BM02 MARKER NAME
1005 MARKER NUMBER
Will ULM AIRPORT CREW OBSERVER / AGENCY
4738139036 R6 4.43 REC # / TYPE / VERS
4738139036 TRM R6 ANT # / TYPE
-352723.0133 -4558645.8471 4432311.8395 APPROX POSITION XYZ
2.0000 0.0000 0.0000 ANTENNA: DELTA H/E/N
1 1 0 WAVELENGTH FACT L1/2
4 C1 L1 L2 P2 # / TYPES OF OBSERV
2013 5 1 19 20 0.0000000 GPS TIME OF FIRST OBS
2013 5 1 23 53 15.0000000 GPS TIME OF LAST OBS
0 RCV CLOCK OFFS APPL
16 LEAP SECONDS
17 # OF SATELLITES
G01 63 63 63 63 PRN / # OF OBS
G03 997 996 996 997 PRN / # OF OBS
G32 205 205 205 205 PRN / # OF OBS
CARRIER PHASE MEASUREMENTS: PHASE SHIFTS REMOVED COMMENT
END OF HEADER
BM02
(New Ulm Project)

## Slide 70: RCVR_ANT.TAB
https://files.igs.org/pub/station/general/rcvr_ant.tab
| TRMR6 | Integrated GPS L1/L2+L2C GLO L1/L2 Trimble R6 antenna|
| TRMR6-2 | Integrated GPS L1/L2+L2C GLO L1/L2 Trimble R6 model 2|
| TRMR6-3 | Integrated GPS L1/L2+L2C GLO L1/L2 Trimble R6 model 3|
| TRMR6-4 | Integrated GPS L1/L2+L2C GLO L1/L2 Trimble R6 model 4|
| TRMR8_GNSS | Integrated GPS L1/L2+L2C/L5 GLO L1/L2 Trimble R8 |
| | GNSS antenna |
| TRMR8_GNSS3 | Integrated GPS L1/L2+L2C/L5 GLO L1/L2 Trimble R8 |
| | GNSS 3 antenna |
| TRMR8-4 | Integrated GPS L1/L2+L2C/L5 GLO L1/L2 Trimble R8 |
| | GNSS 3 antenna, model 4 |
| TRMR8S | Integrated L1/L2/L5/G1/G2/G3/E1/E5ab/B1/B2 GPS, |
| | GLONASS, Galileo & BeiDou antenna |
Verify that antenna and receiver are correctly entered and match the RCVR_ANT.TAB file entries.
ANTENNA LISTINGS
BM02
(New Ulm Project)

## Slide 71: RCVR_ANT.TAB
https://files.igs.org/pub/station/general/rcvr_ant.tab
Verify that antenna and receiver are correctly entered and match the RCVR_ANT.TAB file entries.
| TRIMBLE R6 | L1/L2+L2C GLO L1/L2 integrated receiver/antenna |
| | with Maxwell-5 + SBAS |
| TRIMBLE R6-2 | L1/L2+L2C GLO L1/L2 integrated receiver/antenna |
| | with Maxwell-5 + SBAS |
| TRIMBLE R6-3 | L1/L2+L2C GLO L1/L2 integrated receiver/antenna |
| | with Maxwell-6 + SBAS |
| TRIMBLE R6-4 | L1/L2+L2C/L5 GLO L1/L2/L3 SBAS L1/L5 GAL E1/E5A/E5B |
| | BDS B1/B2/B3 w/Maxwell-6 integrated receiver/antenna |
| TRIMBLE R8 | L1/L2+L2C integrated receiver/antenna w/ Maxwell-5 |
| TRIMBLE R8 GNSS | L1/L2+L2C/L5 GLO L1/L2 integrated receiver/antenna |
| | with Maxwell-5 + SBAS |
| TRIMBLE R8 GNSS3 | L1/L2+L2C/L5 GLO L1/L2 integrated receiver/antenna |
| | with Maxwell-6 + SBAS |
| TRIMBLE R8-4 | L1/L2+L2C/L5 GLO L1/L2/L3 SBAS L1/L5 GAL E1/E5A/E5B |
| | BDS B1/B2/B3 w/Maxwell-6 integrated receiver/antenna |
| TRIMBLE R8S | L1/L2+L2C/L5 GLO L1/L2/L3 SBAS L1/L5 GAL E1/E5a/E5b |
| | BDS B1/B2 w/Maxwell-6 integrated receiver/antenna |
| | (scalable: track types dependent on purchase options)||
RECEIVER LISTINGS
BM02
(New Ulm Project)

## Slide 72: NGS ANTCAL page
https://geodesy.noaa.gov/ANTCAL/
Verify that antenna and receiver are correctly entered and match the NGS ANTCAL file entries.
BAM = bottom of antenna mount
MMI = man-machine interface
BM02
(New Ulm Project)

## Slide 73: RINEX Header (BM02121A.13o)
2.11 OBSERVATION DATA GPS(GPS) RINEX VERSION / TYPE
cnvtToRINEX 2.14.0 convertToRINEX OPR 04-May-13 16:51 UTC PGM / RUN BY / DATE
----------------------------------------------------------- COMMENT
BM02 MARKER NAME
1005 MARKER NUMBER
Will ULM AIRPORT CREW OBSERVER / AGENCY
4738139036 R6 4.43 REC # / TYPE / VERS
4738139036 TRM R6 ANT # / TYPE
-352723.0133 -4558645.8471 4432311.8395 APPROX POSITION XYZ
2.0000 0.0000 0.0000 ANTENNA: DELTA H/E/N
1 1 0 WAVELENGTH FACT L1/2
4 C1 L1 L2 P2 # / TYPES OF OBSERV
2013 5 1 19 20 0.0000000 GPS TIME OF FIRST OBS
2013 5 1 23 53 15.0000000 GPS TIME OF LAST OBS
0 RCV CLOCK OFFS APPL
16 LEAP SECONDS
17 # OF SATELLITES
G01 63 63 63 63 PRN / # OF OBS
G03 997 996 996 997 PRN / # OF OBS
G32 205 205 205 205 PRN / # OF OBS
CARRIER PHASE MEASUREMENTS: PHASE SHIFTS REMOVED COMMENT
END OF HEADER
TRMR6
ANT: TRMR8_GNSS3
TRIMBLE R6
REC: TRIMBLE R8 GNSS3
Re-upload after editing, over-writes previous upload.
BM02
(New Ulm Project)

## Slide 74: Chesapeake Tutorial Project
Clip from RCVR_ANT.TAB
| TRIMBLE MS750 | Dual freq. L1 C/A; L1/L2 full cycle RTK rcvr |
| TRIMBLE NETR3 | L1/L2+L2C/L5 GLONASS L1/L2 Maxwell-5 ASIC,ethernet |
| TRIMBLE NETR5 | L1/L2+L2C/L5 GLONASS L1/L2 Maxwell-5 ASIC,eth + SBAS |
| TRIMBLE NETR8 | L1/L2+L2C/L5 GLONASS L1/L2 Maxwell-5 ASIC,eth + SBAS,|
| | with external frequency support |
| TRIMBLE NETR9 | L1/L2+L2C/L5 GLONASS L1/L2 with 2 Maxwell-6 ASIC, |
| | eth + SBAS, 440 channel |
| TRIMBLE NETRS | L1/L2+L2C with Maxwell-5 ASIC, ethernet, ext freq. |
| TRIMBLE R10 | L1/L2/L5/G1/G2/G3/E1/E2/E5ab/E6/B1/B2/B3, GPS, |
| | GLONASS, Galileo, BeiDou integrated rec/ant Maxwell 6|
| TRIMBLE R10-2 | L1/L2/L5/G1/G2/G3/E1/E2/E5ab/E6/B1/B2/B3, GPS, |
| | GLONASS, Galileo, BeiDou integrated rec/ant Maxwell 7|
Clip from NGS ANTCAL webpage
Antenna Code
TRM115000.00 NONE
TRM57971.00 NONE
RINEX Headers should show these codes correctly.

## Slide 75: Individual Mark Page – lower half
Individual OPUS Solutions (grey) should be within 2 cm
Inspect Solution Quality Summary
Individual OPUS Solutions (grey) should be within 4 cm
BM02
(New Ulm Project)

## Slide 76: Individual Mark Page – lower half
BRMR - Breadmaker
Individual OPUS Solutions (grey) should be within 2 cm
Inspect Solution Quality Summary
Individual OPUS Solutions (grey) should be within 4 cm

## Slide 77: Edit RINEX Files and Re-submit
If discrepancies or blunders are found
  trace the source all the way from Field Log  RINEX Header  OPUS STATIC Submission  OPUS PROJECT Mark Page.
  Re-upload the edited RINEX files. They will over-write the previous.
All RINEX files should (must) agree with Field Logs.
Major confusion and re-work later (especially if Submit to NGS)
Confidence here means confidence later.

## Slide 78: Edit RINEX Files and Re-submit
Q) Why have I not edited the RINEX Headers for the Chesapeake Tutorial Project before uploading?
A) I wanted you to see the ease with which errors can and do occur in the chain from Field Log  RINEX  Upload  OPUS Mark Page
Since the Field Logs & RINEX files are part of the OPUS Project, they all MUST be mutually correct.
See QA/QC Circle on slide 58.
Timesaver Hint: Do the Field Log  RINEX QA/QC before uploading anything.

## Slide 79: Compare & Edit Field Log and RINEX Header
BRMR MARKER NAME
BRMR MARKER NUMBER
JORDAN, K.S. NATIONAL GEODETIC SURVEY OBSERVER / AGENCY
5832R50274 TRIMBLE NETR9 5.45 REC # / TYPE / VERS
6122223925 TRM115000.00 NONE ANT # / TYPE
1210149.3734 -4964281.5903 3804480.8686 APPROX POSITION XYZ
2.0000 0.0000 0.0000 ANTENNA: DELTA H/E/N
1 1 WAVELENGTH FACT L1/2
6 L1 L2 C1 P1 C2 P2 # / TYPES OF OBSERV
30.0000 INTERVAL
0 RCV CLOCK OFFS APPL
18 LEAP SECONDS
2021 2 23 11 31 30.0000000 GPS TIME OF FIRST OBS
END OF HEADER
Example BRMR, Day 054, 2021-02-23
Field Log H.I. = 1.9999 meters
RINEX H.I. = 2.0000 meters
It’s only different by 0.0001 meters, but why accept “close enough”, when exact is what’s required?

## Slide 80: Upload a File
Upload each RINEX file.

## Slide 81: Upload a File
Verify your entries.

## Slide 82: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Step 2 : Uploading Data
End