## Slide 1
OPUS Projects Manager Training
Step 3 : Session Processing
ngs.opus.projects@noaa.gov

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment

## Slide 3: What’s in this training?
This presentation begins after all the RINEX observation data files and all GVX files for the project have been uploaded.
Then, it describes the session web pages, important QA/QC steps, and how to process the data in a session.

## Slide 4: Allow (Limited) Access to Session Page
Although you, being the project manager, would usually navigate to a session web page from the manager’s web page, others can access your project’s sessions from the OPUS Projects gateway web page. They would require the project ID and session keyword that you would provide, and a valid email address.
hrdb86fc
d_ssvk68
your.name@your.address
You could delegate session processing to field crew leader
Or, login as Manager
Notes: Using your project manager keyword rather than the session keyword is also permitted and you’ll be recognized as the project manager.

## Slide 5
The project is always scanned for changes when accessed so the information will be up-to-date.

## Slide 6
In a few moments, the web page for the earliest session in the project will appear.
In this case, session 2013-121-A.
No baselines are shown because the sessions have NOT been processed.

## Slide 7
Lets explore this session web page. The web page is too long to fit and be readable on a single slide, so we’ll first focus on the top portion.

## Slide 8
The web page is built around a Google Map Services™ interactive map showing the locations of marks and included CORS. The map is centered on the project’s marks.
Before we get into QA/QC and Session Processing – let’s review the screen navigation and other options available.

## Slide 9
You can use the controls on the map to zoom in (+) or out (-) …
Notes: Double-clicking will also cause the map to zoom into that point.

## Slide 10
… center and zoom to show the project’s marks in this session …
Notes: This is the default.

## Slide 11
… or center and zoom to show the marks and included CORS.

## Slide 12
You can set the map’s background to look like a digital elevation terrain rendering with towns and roads indicated …
Notes: This is the default.

## Slide 13
… satellite imagery (if available) …
This view is helpful when zoomed in – you can see the MARK in relationship to its surroundings.

## Slide 14
… or a simple map.

## Slide 15
You can “click and drag” the map if you’d like to examine a nearby area.

## Slide 16
Hovering the cursor over a map icon causes its Mark ID to appear.

## Slide 17
Clicking on a map icon will cause information about the data file for that mark to be shown in an information “bubble.”

## Slide 18
… and the observer’s name is a convenience link to send that person an email.

## Slide 19
To the right of the map is a list of the marks in this session.

## Slide 20
Although difficult to show here, moving the cursor over a mark or CORS ID causes the List icon to “lighten.” The corresponding mark icon on the map will also “lighten”.

## Slide 21
Clicking on a list entry also causes that mark’s information bubble to appear on the map.
Pro Tip

## Slide 22
The “Add MARKS” button acts as a link to the OPUS upload web page.

## Slide 23
Below that is a list of the CORS included in this session.

## Slide 24
At the bottom-right is the “Add/Del CORS” button. Clicking that opens a window with controls to add/delete other CORS to this session only. But, remember to add “distant” CORS to ALL sessions via the Managers Page.
Add “distant” CORS to ALL sessions via the Managers Page.

## Slide 25
If you ADD/DEL CORS from a SESSION Page, it will affect only that Session!
If you ADD/DEL CORS from Manager’s Page, it will affect all Sessions!

## Slide 26
Let’s take a moment to explore this new window.
The map in this window is similar to the map on the primary web page: you can zoom in and out, drag the map to other areas …
… you can move the cursor over a map icon to see the mark’s ID or click on it for more information. Note the ADD and DEL buttons.

## Slide 27
To add a CORS to this session, click the “Add” button in its information bubble or type its four character ID into the “To Be Added” box on the left.
To delete a CORS, click the “Del” button, or type its four character ID into the “To Be Deleted” box on the right.
Notes: CORS with longer existences are recommended but not required. Why? The longer a CORS has existed, the better defined are its coordinates and velocity.

## Slide 28
When the list of CORS to be added or deleted is complete, click the “Add/Del CORS” button on the control bar near the top of the window to begin the process. In this example, we’ll just close the window.

## Slide 29
The Add/Del CORS Information Bubble also shows how many years that the CORS has been ACTIVE. Longer is better! Note also that the Map Legend is color coded.
recommended
caution
use freely
avoid

## Slide 30
The pull-down menus at the top of the web page identify the session and solution results shown on this web page: OPUS solutions from session 2013-121-A in this case.

## Slide 31
You can use the session menu to navigate to another session…

## Slide 32
…or review other processing results for this session.
In this example, only OPUS SOLUTIONS exist, so far.
Notes: Only the OPUS solutions are available at this point in session processing.

## Slide 33
The controls for this web page are to the left of the map.

## Slide 34
The controls include help, back and refresh controls. If you navigated here from the manager’s web page, a button to return to the manager’s web page will appear too.
HELP (brings up USER MANUAL)
BACK
REFRESH
RETURN to Managers Page

## Slide 35
The OPUS solution and other processing reports can be reviewed in a separate window using the “Show File” button.

## Slide 36
Any available report for this session can be displayed using the menus on the control bar.

## Slide 37
If you wish to print this report, click somewhere on the report, then right-click. In Mozilla based browsers, the “standard” browser web page menu should appear. On this, you’ll see the “This Frame” entry. Following that, you can “Print Frame”.

## Slide 38
With Internet Explorer, you’ll have to select the report’s text. Then, by right-clicking on the text, you can “Convert to Adobe PDF”.

## Slide 39
With Google Chrome, allegedly there is an extension to allow you to print the text box frame, but this has not been tested. Without this extension, you’ll have to select the report’s text and copy it into a file for printing.

## Slide 40
The “Send Email” button gives you a limited means to send an email to others in the project.
Notice that you can send the email to yourself, the project manager, other project members and the OPUS Projects team.

## Slide 41
You can also attach processing reports to the email.

## Slide 42: Sequence of Processing Steps
Recommended Sequence of Processing Steps for OPUS Projects
  1 NGS Survey Proposal
  2 Create your Project in OP
  3 Review and Edit Project Preferences
  4 Load Static GNSS Observation Files
  5 Check your OPUS Static Solution Results
  6 Selecting CORS
  7 Upload GVX Vectors
  8 Mark Descriptions
  9 Session Processing
  10 Network Adjustments
  11 Final Steps - QA/QC & Reportage

## Slide 43: Sequence of Processing Steps
Upload Description - use the action button

## Slide 44: Sequence of Processing Steps
Upload WinDesc files before Session Processing.
IMPORTANT NOTE:
This action may update the a priori coordinates for marks in your project.
If that is the case, session baseline solutions (if any) involving these marks will be automatically deleted and reprocessed using the updated coordinates.
You will receive notification emails for each new session solution. The reprocessing may take a few minutes to complete.
Affected network solutions will also be deleted, and you will need to re-run the network adjustments after receiving the new session solutions.

## Slide 45: The WinDesc Files
There are 5 WinDesc Files to upload
Correct and free of Error Messages
Look at them in Text Editor or from inside WinDesc.

## Slide 46: The .DES File
The DES file is a heavily-formatted file that is NOT intended to be edited by the User at any time. It is easily corrupted.
  Explanation, the file is column-specific and many columns wide. Any inadvertent changes will corrupt the file.
  There are many blank columns within the file, making it essentially impossible to notice any inadvertent changes.

## Slide 47: The .DSC File
The DSC file contains the information needed by OPUS Projects to enable the Recoveries and New Marks to be loaded in the NGS database.
Descriptions in the .DSC file are matched to the Marks in the Project by co-location (1.000 meter) and by 4 character ID. If no match is found, a dialogue box will allow the user to manually match the marks.
The DSC file is also column-specific.

## Slide 48: The .DIS File
The .DIS file checks for discrepancies between the DSC file and the NGS Database.
Discrepancies are not errors!
But, a simple explanation of each occurrence in the file should be placed in the Project Report.
A Blanket Statement might read:
  All discrepancies in the DIS file have been checked and verified as being correct in the DSC file, except as follows:

## Slide 49: The .ERR File
The .ERR file checks for logical correctness.
In some cases, there may be several such messages for a single underlying mistake.
  Reason: In a series of logically-related checking algorithms, it is not possible to isolate a discrepant entry.
    Analogy. A circular curve on a plat may show Δ, L, R which, if correct, must must be geometrically consistent. If not consistent, which is in error?
    3 “error” statements could be generated:
      Δ and L do not match R
      Δ and R do not match L
      L and R do not match Δ

## Slide 50: The .ERR File
The ERR file must be free of ERROR messages
It may contain a few WARNING messages.
Explain in the Project Report why you could not eliminate the error message.
Example:
  ACCESSION: GPS
  --(ERROR) Accession prefixes (project types) of 'GPS' must be
  followed by an accession (project) number 1-5 digits in length.
  --(ERROR) The accession number is blank.
Reason: NGS assigns accession numbers after submittal.

## Slide 51: The .NBR File
The NBR file checks for near neighbors of the submitted mark and lists them in order by distance (km).
It does this to help users discover a mis-identified mark.
A simple affirmation should be placed in the Project Report. It might read:
  The NBR Report has been checked. All marks in the DSC file are correctly identified.

## Slide 52: Sequence of Processing Steps
If all 5 WinDesc files are correct, then they can be uploaded.

## Slide 53: Sequence of Processing Steps
Read the message.
NCN CORS do not need to be in the WinDesc files.

## Slide 54: Sequence of Processing Steps
The contents of the DSC file will be written to the individual Mark Pages.
  That’s why we SKIPPED DESCRIPTION earlier.

## Slide 55
The “Set up Processing” button displays the session processing controls. Let’s leave this until we finish exploring the web page.

## Slide 56
Scrolling to the bottom of the web page, we see a table below the map with the solution values that are checked against the solution quality thresholds. If a value exceeds its threshold, the value is highlighted using an orange color and the mark’s icon is changed to reflect this condition. This table shows that the OPUS solutions for this session meet the project’s preferences.
All ICON’s are GREEN

## Slide 57
At the bottom of the web page is a Data Availability plot.
The numbers and colors indicate the approximate satellite count in each time block. (1 to 9, then A,B,C etc)
Notes: The time limits and cell size will change from session to session as the table adjusts itself to fit into this area.

## Slide 58
The Mark ID’s labeling in each row are convenience links to navigate to the Mark Summary web pages.
Notes: The mark summary web pages will be described in detail in the next presentation.

## Slide 59
Now let’s scroll back to the top of the web page and describe the processing controls.

## Slide 60
Clicking the “Set up Processing” button causes two things to happen: the processing set up window appears and the baselines implied by the processing selections are shown on the session map.

## Slide 61
After shrinking both windows and placing them side by side, we see that the baselines are indeed drawn on the map. Let’s focus on the session processing form, but keep a small copy of the map for the remainder of this discussion.

## Slide 62
If processing has not been performed in this session, the default selections are used as is the case here: all marks are included, a CORS is suggested as a hub and it is constrained in 3D.
Include/exclude mark
HUB Selection
Constraint Choices

## Slide 63
… and the PROCESSING PREFERENCES located at the bottom of the window are the defaults chosen when we initially set the project preferences (see the Managers Page).

## Slide 64
But if processing has previously occurred in this session (say by your designated field crew leader) the previous processing selections will be shown. But, remember that you can make different choices for the re-processing.

## Slide 65
Use the SOLUTION NAME as a reminder about this solution. Normally, you’ll leave it as the letter identifier for this session: “A” from 2013-121-A in this case. If you’re experimenting with alternate processing configurations, use a name like “A test 1.”

## Slide 66: Session Naming
OPUS Projects creates a name for each session as you submit files via the OPUS interface.
When you PROCESS a session, OPUS Projects allows you to specify a name for the processed solution.
I suggest that you retain the “root” name and add a logical extender name.
Note:
A Session is not the same as a Solution.
See slides 120-122.

## Slide 67: Session Naming
Example:
Submitted session “root” name: 2013-121-A
  Suggested extender name: 2013-121-A-Trial 1
  Suggested extender name: 2013-121-A-No ALDR2
If you re-use the same name, OP will over-write the solution.
Bad idea to not retain the root in your naming.

## Slide 68
The SOLUTION SPAN is informational, not an input field. It gives the time span of the data, excluding the CORS, in this session.

## Slide 69
The MARK and CORS tables control information about the marks for the processing.

## Slide 70
You can select marks to be included or excluded from the processing. All are included here. To change a mark’s status, click the checkbox.

## Slide 71
For this training, let’s exclude the CORS MNLC and WDLM.
Effect of Include/Exclude

## Slide 72
First, note how the baselines changed in response. Also note that the MNLC and WDLM rows are disabled (grey’d out) now that they are excluded.
Effect of Include/Exclude
Notes: A standard way to depict a disabled form element is to lighten its color. Some call this “graying it out.”

## Slide 73
Marks can be designated as hubs. We do that by clicking the checkboxes. After the changes, the baselines for this session will look radically different.
Effect of Hub Selection
1 Hub

## Slide 74
For dramatic effect, let’s select a project mark and 2 more CORS as hubs. Note the baselines update right away.
Effect of Hub Selection
4 Hubs

## Slide 75
You can also select which marks will be constrained.
Note that they don’t have to be hubs.
Unless special circumstances exist, suggest only 1 constraint in 3D

## Slide 76
Four options are available: NONE (no constraint). HOR-ONLY (constrain only the horizontal coordinates). VER-ONLY (constrain only the vertical coordinate).
3-D (constrain the horizontal and vertical coordinates).

## Slide 77
OPUS solution values are used as the a priori coordinates for the project’s marks; the published coordinates are used for the CORS.
The USER can hand-enter other LATITUDE, LONGITUDE, ellipsoid or orthometric HEIGHT values and have them used as constraints. (Not recommended!)
Notes: The CORS coordinates come from a database of information about the sites. This is maintained by the CORS team daily and reflects changes to and more data from the CORS. Therefore, the information may differ from that published for these sites.

## Slide 78
OPUS computations are always in best available international terrestrial reference frame (ITRF) at the epoch of the data, so the solution results are always given in that frame.
“LET OPUS CHOOSE” implies the NAD 83 datum realization that best corresponds to the constraint reference frame will be used
ITRF2014(2010.00) ↔ NAD 83(2011)
ITRF2000 ↔ NAD 83(2007)

## Slide 79
The computed ellipsoid heights are transformed to orthometric heights using a geoid or hybrid-geoid model when possible. The model can be selected.
“LET OPUS CHOOSE” implies the hybrid geoid model that best corresponds to the constraint reference frame will be used.
ITRF2014(2010.00) ↔ NAD 83(2011) ↔ GEOID18
ITRF2000 ↔ NAD 83(2007) ↔ GEOID09

## Slide 80
The satellite system or systems whose data are to be used in the processing can be selected. The only option is GPS-only at this time.
Notes: For now, GPS is the only valid selection.

## Slide 81
Some control over the tropo (wet, neutral atmospheric) correction is available via two parameters: the model or “shape” of the correction and the interval for updating the correction.

## Slide 82
The Tropo Model correction can be constructed as a simple offsets for each interval. When plotted, these adjustments reminiscent of a staircase. Thus the name Step-Offset.
Time 
Tropo Intervals
Step-Offset

## Slide 83
Alternately, the Tropo Model can be corrected as a series of straight line segments whose ends connect. Thus, the name Piecewise Linear.
Time 
Tropo Intervals
Piecewise Linear
Recommended

## Slide 84
Tropo Interval (7200 sec) and Elevation Cutoff (15 deg) are excellent general choices but some projects (or data) may require a different parameterization.

## Slide 85
The Elevation Cutoff omits data from satellites whose elevations are below this limit. Common choices are 12° and 15°. Here again, your project may specify this limit.
Notes: The most advantageous compromise is preferred. A lower cutoff means more but often noisier observations. A higher cutoff means fewer but less noisy observations.

## Slide 86
The Constraint Weights specify how “tight” the coordinates are constrained. In other words, these limit the maximum change in constrained coordinates. The weights are based upon the uncertainties associated with each coordinate.
Recommend NORMAL because as you’ll see the CORS aren’t perfect.
Constraint Type | Implied coordinate uncertainty
Loose | 1.0 meters
Normal | 0.01 meters
Tight | 0.0001 meters

## Slide 87
The Network Design offers some common strategies for connecting marks via baselines in the processing. Picking one of these strategies may change the hub selections, but will not change which marks are included nor their coordinates.
We will demonstrate the various network strategies at a later time. The strategies seem to change the results, but that is not the case.

## Slide 88
Let’s return to the default design of all marks included, choose 1 CORS (MNLS) as the hub and as the 3D constraint, distant CORS (AMC2) added, and submit our selections for processing.
ADD “distant” CORS to all sessions via the Managers Page

## Slide 89
Choose a HUB Strategy

## Slide 90: The SINEX File (example for 2013-121-A)
In this example there are 12 marks (4 passive + 8 CORS).
The SINEX File (.snx) contains computed ECEF XYZ positions for all 12 marks, making 36 results.
The SINEX File also contains variance / covariance entries for all 36 results in a 36 x 36 matrix which is symmetrical, so only the upper right half plus the diagonal are listed.
The 36 positions (12 marks) can form any combination of 11 interconnected baselines, so long as one accounts for the variance/covariance terms correctly. No approximations.
The HUB Selections drive the baseline creations.
So ALL HUB Strategies deliver mathematically-interconvertible results, making any HUB Strategy is as good as any other.

## Slide 91
36 rows
the diagonal
upper half of matrix
lower half of matrix
(not needed due to symmetry)
1
36
1
36
36 columns
Symmetric entries
(mirrored)

## Slide 92: The SINEX File (example for 2013-121-A)
+SOLUTION/ESTIMATE
*INDEX TYPE CODE PT SOLN _REF_EPOCH__ UNIT S __ESTIMATED VALUE___ _STD_DEV___
1 STAX BM02 - 1 13:121:77980 m 2 -0.352721611657472E+6 .333399E-03
2 STAY BM02 - 1 13:121:77980 m 2 -0.455864616712488E+7 .164644E-02
3 STAZ BM02 - 1 13:121:77980 m 2 0.443231585519171E+7 .164094E-02
4 STAX CBN1 - 1 13:121:76962 m 2 -0.333911970795278E+6 .318963E-03
5 STAY CBN1 - 1 13:121:76962 m 2 -0.455746979835712E+7 .152395E-02
6 STAZ CBN1 - 1 13:121:76962 m 2 0.443503047084937E+7 .150192E-02
7 STAX E115 - 1 13:121:78016 m 2 -0.352831395031778E+6 .318478E-03
8 STAY E115 - 1 13:121:78016 m 2 -0.456015197912549E+7 .149347E-02
9 STAZ E115 - 1 13:121:78016 m 2 0.443076406468935E+7 .147064E-02
10 STAX ULMA - 1 13:121:78333 m 2 -0.358533713609866E+6 .309097E-03
11 STAY ULMA - 1 13:121:78333 m 2 -0.455703008829559E+7 .145282E-02
12 STAZ ULMA - 1 13:121:78333 m 2 0.443358317780991E+7 .144253E-02
13 STAX AMC2 A 4 13:121:54493 m 2 -0.124859631090512E+7 .320256E-03
14 STAY AMC2 A 4 13:121:54493 m 2 -0.481942820609568E+7 .112536E-02
15 STAZ AMC2 A 4 13:121:54493 m 2 0.397650594770331E+7 .110694E-02
16 STAX MNBE A 3 13:121:43769 m 2 -0.332213463534256E+6 .257134E-03
17 STAY MNBE A 3 13:121:43769 m 2 -0.460968003019403E+7 .111960E-02
18 STAZ MNBE A 3 13:121:43769 m 2 0.438127957043821E+7 .109913E-02
19 STAX MNJF A 3 13:121:54750 m 2 -0.409557733847783E+6 .255211E-03
20 STAY MNJF A 3 13:121:54750 m 2 -0.457100344601202E+7 .108887E-02
21 STAZ MNJF A 3 13:121:54750 m 2 0.441505004372878E+7 .107509E-02
22 STAX MNLC A 3 13:121:43565 m 2 -0.261803918351368E+6 .257308E-03
23 STAY MNLC A 3 13:121:43565 m 2 -0.455107083980174E+7 .112199E-02
24 STAZ MNLC A 3 13:121:43565 m 2 0.444636248561124E+7 .110631E-02
25 STAX MNLK A 3 13:121:54228 m 2 -0.412504576549909E+6 .254931E-03
26 STAY MNLK A 3 13:121:54228 m 2 -0.460514517858203E+7 .109288E-02
27 STAZ MNLK A 3 13:121:54228 m 2 0.437942559896384E+7 .107447E-02
28 STAX MNLS A 5 13:121:54587 m 0 -0.310793095703722E+6 .224556E-03
29 STAY MNLS A 5 13:121:54587 m 0 -0.455085933077128E+7 .863075E-03
30 STAZ MNLS A 5 13:121:54587 m 0 0.444338934917038E+7 .863547E-03
31 STAX MNMN A 2 13:121:54379 m 2 -0.396503348042565E+6 .254101E-03
32 STAY MNMN A 2 13:121:54379 m 2 -0.453610547067024E+7 .108721E-02
33 STAZ MNMN A 2 13:121:54379 m 2 0.445157900691974E+7 .107508E-02
34 STAX WDLM A 4 13:121:54871 m 2 -0.431414980776897E+6 .255668E-03
35 STAY WDLM A 4 13:121:54871 m 2 -0.452295564025948E+7 .108817E-02
36 STAZ WDLM A 4 13:121:54871 m 2 0.446172449238400E+7 .107682E-02
12 triads = 36 entries
Note: Scientific Notation in both columns
the 36 component coordinates of the 12 marks

## Slide 93: The SINEX File Matrix (example for 2013-121-A)
+SOLUTION/MATRIX_ESTIMATE U COVA
1 1 0.111154651228499E-06 0.136084248125083E-06 -.735681530996255E-07
1 4 0.617273536866020E-07 0.645370720469201E-07 -.145034736374522E-07
1 7 0.616857731468334E-07 0.646588125602462E-07 -.142899485112735E-07
1 10 0.610190113810344E-07 0.636724405480656E-07 -.135605702788791E-07
1 13 0.567208181318511E-07 0.579520966426191E-07 -.977085741811538E-08
1 16 0.574071484752050E-07 0.583869603653447E-07 -.989212676016241E-08
1 19 0.571396340691135E-07 0.580909024469072E-07 -.954912041155452E-08
1 22 0.573655366912292E-07 0.581161891629666E-07 -.961475860651931E-08
1 25 0.571218875869544E-07 0.581183382109001E-07 -.959198886174607E-08
1 28 0.503632192096922E-07 0.466207221662809E-07 0.785219408126183E-09
1 31 0.570712926206525E-07 0.577792529706426E-07 -.923338687476055E-08
1 34 0.571146983908952E-07 0.581660006324038E-07 -.955652693117281E-08
2 2 0.271077903464155E-05 -.187016264440054E-05 0.645199613824845E-07
2 5 0.108151623506348E-05 -.312422694999910E-06 0.645949218416899E-07
2 8 0.107714733845970E-05 -.308004678573134E-06 0.633604338829759E-07
2 11 0.106159400527245E-05 -.295221624196330E-06 0.265142026067824E-07
2 14 0.943619566072369E-06 -.213022430060283E-06 0.591022984164512E-07
2 17 0.964270396808497E-06 -.206115673419223E-06 0.559688387421385E-07
2 20 0.955626933907049E-06 -.195477553640142E-06 0.612641815371842E-07
2 23 0.963545219746535E-06 -.200693285114473E-06 0.559388070667324E-07
2 26 0.954823308576010E-06 -.197383251256848E-06 0.476849107487170E-07
2 29 0.744488122794893E-06 0.677512083323357E-10 0.561768303987948E-07
2 32 0.955501033928786E-06 -.192589433758638E-06 0.552403619109972E-07
2 35 0.956259452956815E-06 -.192176233866394E-06
3 3 0.269268572326136E-05 -.147167943916128E-07 -.313000465843602E-06
3 6 0.106422102392420E-05 -.143871973403845E-07 -.308723968931822E-06
.
.
33 36 0.943119664078174E-06
34 34 0.653659327352433E-07 0.748062982257856E-07 -.249569068302189E-07
35 35 0.118411631034006E-05 -.405416715044360E-06
36 36 0.115953674967001E-05
-SOLUTION/MATRIX_ESTIMATE U COVA
Row and Column Indices
Last Entry = Row 36 Column 36
This symmetrical MATRIX is 36 x 36
But only the upper right half plus the diagonal are listed. A total of 666 entries in this case.
36x36 = 1296
Minus 36 in diagonal = 1260
Minus lower left half = 630
Plus add back the diagonal = 666
Q) Why is Row 2, Column 1 not listed?
A) It’s in the lower left half of the matrix.
upper half of matrix + the diagonal

## Slide 94: Mathematical, but not Graphical Equivalence
=
ALL HUB Strategies deliver mathematically-interconvertible results, making any HUB Strategy is as good as any other.
1 Hub
3 Hubs

## Slide 95: Mathematical, but not Graphical Equivalence
=
For pictorial clarity, OP shows only the hub-selected baselines
1 Hub
3 Hubs

## Slide 96: Optimize CORS included in Project
The collection of included CORS is inherited from the OPUS STATIC submissions.
Need to edit the CORS selections:
  Need to add at least one distant CORS before session processing
  Probably too many CORS – prefer 3 to 5 local + 1 distant
  Some CORS may be unstable
  Some CORS lack data in some sessions
The question is WHEN to edit the CORS Selection?
  Before session processing? After? Iterative?
BEFORE is usually best

## Slide 97: Chesapeake Tutorial Project
When to Edit the CORS Selections - before session processing (after, iterative) ?
  Distant CORS – add BEFORE
  If we know which CORS can be trusted – add them to the project BEFORE
  If we know which CORS can’t be trusted – remove them from the project BEFORE
Let’s look at the short-term CORS Plots for Chesapeake Tutorial Project and decide.

## Slide 98: Obtain Short-term CORS Plots (Beta )
October 03, 2023
https://beta.ngs.noaa.gov/OPUS-Tools/cors-time-series-tool/index.html?utm_medium=email&utm_source=GovDelivery

## Slide 99: Chesapeake Tutorial Project
ASUB - a “distant CORS”
LOY2
LS03
NCEL
NCGA
VAGP
OK
OK
OK
OK
OK
OK

## Slide 100: Chesapeake Tutorial Project
Exclude LOYX - spotty data availability
Missing daily solutions

## Slide 101: Chesapeake Tutorial Project
Exclude LOYX - spotty data availability
Chesapeake Project was active on days 041 thru 063

## Slide 102: Chesapeake Tutorial Project
Add ASU-BOONE CORS ARP to act as the distant CORS.
DF4365 ***********************************************************************
DF4365 HT_MOD - This is a Height Modernization Survey Station.
DF4365 CORS - This is a GPS Continuously Operating Reference Station.
DF4365 DESIGNATION - ASU-BOONE CORS ARP
DF4365 CORS_ID - ASUB
DF4365 PID - DF4365
DF4365 STATE/COUNTY- NC/WATAUGA
DF4365 COUNTRY - US
DF4365 USGS QUAD - BOONE (2019)
DF4365
DF4365 *CURRENT SURVEY CONTROL
DF4365 ______________________________________________________________________
DF4365* NAD 83(2011) POSITION- 36 12 50.84476(N) 081 40 54.64796(W) ADJUSTED
DF4365* NAD 83(2011) ELLIP HT- 957.909 (meters) (06/??/19) ADJUSTED
DF4365* NAD 83(2011) EPOCH - 2010.00
DF4365* NAVD 88 ORTHO HEIGHT - 989.12 (meters) 3245.1 (feet) GPS OBS
DF4365 ______________________________________________________________________
DF4365 NAVD 88 orthometric height was determined with an earlier geoid model
DF4365 GEOID HEIGHT - -31.223 (meters) GEOID18
DF4365 NAD 83(2011) X - 745,449.796 (meters) COMP
DF4365 NAD 83(2011) Y - -5,098,563.214 (meters) COMP
DF4365 NAD 83(2011) Z - 3,747,953.199 (meters) COMP
DF4365
DF4365 Network accuracy estimates per FGDC Geospatial Positioning Accuracy
DF4365 Standards:
DF4365 FGDC (95% conf, cm) Standard deviation (cm) CorrNE
DF4365 Horiz Ellip SD_N SD_E SD_h (unitless)
DF4365 -------------------------------------------------------------------
DF4365 NETWORK 0.15 0.45 0.06 0.06 0.23 -0.03664600
DF4365 -------------------------------------------------------------------

## Slide 103: Chesapeake Tutorial Project
Add ASUB, Exclude LOYX.
6 CORS and 6 or 7 Marks in 5 sessions.
ASUB is distant CORS, no constraint
Use LOY2 as local hub, 3D, Normal constraint.
No other constraints
Piecewise linear
7200 sec
15 degrees

## Slide 104: Chesapeake Tutorial Project
LOYX excluded
LOY2 set as
HUB and 3D

## Slide 105
The selections are checked, inserted in the processing queue and a printable summary is created. Check it for intended results.
Chesapeake Tutorial Project
Confirmation Pop-up Screen
Session 2021-041-A

## Slide 106: Break
Take a break now and SUBMIT all 5 sessions.
We’ll cover the resulting solutions when we get back.

## Slide 107
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.005 m (0.001 m) E: -0.005 m (0.001 m) H: -0.017 m (0.002 m)
asub N: -0.002 m (0.001 m) E: 0.005 m (0.001 m) H: 0.006 m (0.002 m)
brmr N: 0.001 m (0.001 m) E: -0.003 m (0.001 m) H: -0.010 m (0.002 m)
gp99 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: 0.003 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.003 m (0.001 m) H: -0.003 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: -0.003 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.005 m (0.001 m) H: 0.014 m (0.002 m)
ou03 N: 0.000 m (0.001 m) E: -0.003 m (0.001 m) H: -0.007 m (0.002 m)
ou18 N: -0.003 m (0.001 m) E: -0.004 m (0.001 m) H: 0.017 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.004 m (0.002 m)
w416 N: 0.001 m (0.001 m) E: -0.002 m (0.001 m) H: 0.006 m (0.002 m)
ATTACHMENT INVENTORY:
------------------------ ---------------------------------------------------
Processing Report (.txt) : 2021-041-A.txt
G-file (.gfile) : 2021-041-A.gfile
Vector Table (.vec) : 2021-041-A.vec
Processing Log (.sum) : 2021-041-A.sum
SINEX Output (.snx) : 2021-041-A.snx
Processing Report (.xml) : 2021-041-A.xml
Serfil (.serfil) : serfil
In a few minutes (often longer depending upon the number of marks in the session), an email with the results will be sent. It is a summary of the results with full reports attached.

## Slide 108
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
Using this summary, you should perform a minimal quality control evaluation of this solution. Later we’ll see that some evaluations are indicated on the session web page, but it is always prudent to manually verify your results.
Although the summary looks different than an OPUS solution, its evaluation is similar.

## Slide 109
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
First, review processing option information. It should match your expectations and selections.

## Slide 110
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
The STANDARD ERROR OF UNIT WEIGHT should be ≈1.
How close to 1 is good enough? Be wary of order of magnitude differences: 0.624 is OK; 6.24 or 0.062 are not.
Notes: I (MSS) offer this rule of thumb 0.1 – 1.1 is probably OK but the extremes of this range are troubling.

## Slide 111
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
The OVERALL RMS should be less than the preference threshold. The threshold value we’ve selected is ≤0.025 meters ( ≤2.5 cm)

## Slide 112
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
Each baseline’s RMS should meet our RMS preference threshold of ≤2.5 cm.

## Slide 113
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
Make sure the TOTAL NUMBER OF OBSERVATIONS and the OBS by BASELINE are near our expectations.

## Slide 114
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
Check the percentages of OMITTED observations. We have a preference of ≥80% OBS used implying ≤20% OBS omitted.

## Slide 115
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
FOR 2021-041-A
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-16T09:56:17 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%
The number of ambiguities FIXED to integers should also meet our preference of ≥80%.

## Slide 116
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.005 m (0.001 m) E: -0.005 m (0.001 m) H: -0.017 m (0.002 m)
asub N: -0.002 m (0.001 m) E: 0.005 m (0.001 m) H: 0.006 m (0.002 m)
brmr N: 0.001 m (0.001 m) E: -0.003 m (0.001 m) H: -0.010 m (0.002 m)
gp99 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: 0.003 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.003 m (0.001 m) H: -0.003 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: -0.003 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.005 m (0.001 m) H: 0.014 m (0.002 m)
ou03 N: 0.000 m (0.001 m) E: -0.003 m (0.001 m) H: -0.007 m (0.002 m)
ou18 N: -0.003 m (0.001 m) E: -0.004 m (0.001 m) H: 0.017 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.004 m (0.002 m)
w416 N: 0.001 m (0.001 m) E: -0.002 m (0.001 m) H: 0.006 m (0.002 m)
ATTACHMENT INVENTORY:
------------------------ ---------------------------------------------------
Processing Report (.txt) : 2021-041-A.txt
G-file (.gfile) : 2021-041-A.gfile
Vector Table (.vec) : 2021-041-A.vec
Processing Log (.sum) : 2021-041-A.sum
SINEX Output (.snx) : 2021-041-A.snx
Processing Report (.xml) : 2021-041-A.xml
Serfil (.serfil) : serfil
Finally, scan through the rest of the summary checking for abnormally large coordinate shifts or coordinate shift uncertainties.
ESTIMATED means “computed”
A-PRIORI means “from before”.
In this case:
OPUS STATIC results for Passive Marks (but, if a mark has a PID, that may be used as a-priori) See the MARK Page!
Published coordinates for CORS.
Amount of “SHIFT” from A-PRIORI
UNCERTAINTY of the SHIFT

## Slide 117
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.005 m (0.001 m) E: -0.005 m (0.001 m) H: -0.017 m (0.002 m)
asub N: -0.002 m (0.001 m) E: 0.005 m (0.001 m) H: 0.006 m (0.002 m)
brmr N: 0.001 m (0.001 m) E: -0.003 m (0.001 m) H: -0.010 m (0.002 m)
gp99 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: 0.003 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.003 m (0.001 m) H: -0.003 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: -0.003 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.005 m (0.001 m) H: 0.014 m (0.002 m)
ou03 N: 0.000 m (0.001 m) E: -0.003 m (0.001 m) H: -0.007 m (0.002 m)
ou18 N: -0.003 m (0.001 m) E: -0.004 m (0.001 m) H: 0.017 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.004 m (0.002 m)
w416 N: 0.001 m (0.001 m) E: -0.002 m (0.001 m) H: 0.006 m (0.002 m)
ATTACHMENT INVENTORY:
------------------------ ---------------------------------------------------
Processing Report (.txt) : 2021-041-A.txt
G-file (.gfile) : 2021-041-A.gfile
Vector Table (.vec) : 2021-041-A.vec
Processing Log (.sum) : 2021-041-A.sum
SINEX Output (.snx) : 2021-041-A.snx
Processing Report (.xml) : 2021-041-A.xml
Serfil (.serfil) : serfil
The ATTACHMENT INVENTORY lists the 7 attached files, with their names.

## Slide 118
Returning to the session web page and refreshing it if needed, you’ll see the results of our processing are now evident. The baselines are now shown.

## Slide 119
The default results are the Session Solution now, and the OPUS Solutions are still available.

## Slide 120
The session processing reports are available via the SHOW FILE.

## Slide 121: Session 2021-048-A
And the Solution Quality Indicators Table now reflects the Session Solution.
Once satisfied with the quality of these results, you can start an alternate processing set up or another session.

## Slide 122: Alternative “Solutions” of a “Session”
OPUS PROJECTS uses the terms “session” and “solution” in seemingly synonymous ways. Let’s clarify the terms.
A “SESSION” is a collection of RINEX data files and supporting metadata, grouped logically by their near-simultaneous observation times.
A “SOLUTION” is a set of calculations (based on user-selected parameters) which produces vectors, positions, and associated uncertainties. The vectors are then adjusted to fit your chosen constraints. A “solution” therefore includes vector computation PLUS an adjustment to constraints.
An “ADJUSTMENT” will use the computed vectors, remove any prior adjustment, and apply the new constraints.

## Slide 123: Alternative “Solutions” of a “Session”
So, deleting a SOLUTION, does not delete the underlying SESSION.
Deleting an ADJUSTMENT, does not delete the underlying SOLUTIONS or SESSIONS.
On the flip side, deleting or overwriting a SESSION (or a RINEX file) would invalidate subsequent SOLUTIONS and ADJUSTMENTS which depended on it.
Deleting or overwriting a SOLUTION would invalidate subsequent ADJUSTMENTS which depended on it.
logical dependencies

## Slide 124: Alternative “Solutions” of a “Session”
RAW DATA
COMPUTED RESULTS
Session
Solution 1
User-Selected Parameters
(session setup)
Name: 2013-121-A
Name: 2013-121-A
(unless you add a name extender)
User-Selected Parameters
(session setup)
COMPUTED RESULTS
Solution 2
Name: 2013-121-A-NO_ALD2
You can see that one SESSION can be logically processed several times using a variety of parameters to create several SOLUTIONS (each of which needs a unique name to avoid “over-write”
2013-121-A
2013-121-A-NO_ALD2

## Slide 125: Choosing a Network Design Method
What’s the “best” option?
  USER, CORS, MST, TRI
Consider these topics:
  Vector repeats between sessions
  Coordinate position results
  Redundant / Independent / Trivial
  Lat/lon/ellht network accuracies

## Slide 126: Choosing a Network Design Method
USER, CORS, MST
  Each produces (n-1) independent vectors
  With careful choice of hub, one may get a few repeated vectors to compare between sessions.
TRI option (has been discontinued in OP4.0)
  Extra vectors produced – can’t all be independent
  More repeated vectors for comparison

## Slide 127: Choosing a Network Design Method
USER, CORS, MST, and TRI will yield similar coordinates (within error budgets)
USER, CORS, MST will produce similar network accuracies.
TRI will produce more “optimistic” network accuracies due to apparent extra redundancy
Any of the 3 methods will produce more realistic network accuracies than the sequential processing (n)(n-1)/2 method.

## Slide 128: Choosing a Network Design Method
USER, CORS, MST methods are ACCEPTABLE for submission of projects to NGS.
  TRI is NOT acceptable for bluebooking of projects. Hence it was discontinued.
TRI
NGS recommends the Single Hub method for most projects.
This will be a USER-type method choice.

## Slide 129: Effect of Bad Occupation
If local conditions reveal a “bad” occupation the session must be reprocessed without the bad occupation (see how on slide 49 etc).
Real world example of bad occupation caused by local conditions - USCG Cutter ALDER

## Slide 130: The ALDER Project Experience
US Coast Guard Cutter ALDER needed marks on its dock to check its navigational systems.
  Advisor installed 4 marks along dock.
  Observed 2 sessions while ship was docked.
    307-A and 307-B
    Multipath from ship caused concern – see results.
  Re-processed sessions 307-A and 307-B with ALDER 2 removed.
  Re-observed 2 new sessions with ship not present
    320-A and 320-B
  Compare with/without ship – see results

## Slide 131: The ALDER Project Experience
OPUS PROJECTS Network Diagram
ALDER 1 is hub for all sessions
No distant CORS
  Did not have guidance at that time in 2011

## Slide 132: The ALDER Project Experience
Sessions 307-A and 307-B, obvious problem around ALDER 2 – was either one correct?
ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH SESSION NAME
------------------------------------------------------------------------------------------
ald2 TO ald1 -22.8248 -6.5969 -6.6349 24.6681 2011-307-A *** ???
ald2 TO ald1 -23.0531 -6.4129 -6.6865 24.8451 2011-307-B *** ???
ald3 TO ald1 -42.5872 -12.1459 -12.7446 46.0827 2011-307-A ***
ald3 TO ald1 -42.5886 -12.1524 -12.7432 46.0854 2011-307-B ***
ald4 TO ald1 -62.1348 -16.9338 -18.1851 66.9193 2011-307-A ***
ald4 TO ald1 -62.1359 -16.9379 -18.1813 66.9202 2011-307-B ***
mnjc TO ald1 89213.5609 -20890.8441 -15902.8820 92996.7122 2011-307-A ***
mnjc TO ald1 89213.5614 -20890.8383 -15902.8895 92996.7126 2011-307-B ***
mnpl TO ald1 91270.6681 30722.0783 32831.5918 101745.2425 2011-307-A ***
mnpl TO ald1 91270.6693 30722.0799 32831.5857 101745.2421 2011-307-B ***
mnvi TO ald1 33107.2933 -62539.7505 -57078.8435 90913.7373 2011-307-A ***
mnvi TO ald1 33107.3182 -62539.8253 -57078.7923 90913.7657 2011-307-B ***
wis6 TO ald1 -5637.3052 5535.9629 5010.9973 9356.0776 2011-307-A ***
wis6 TO ald1 -5637.3065 5535.9632 5010.9928 9356.0762 2011-307-B ***
wisn TO ald1 24266.7450 75452.8563 72795.9242 107616.2396 2011-307-A ***
wisn TO ald1 24266.7443 75452.8578 72795.9177 107616.2360 2011-307-B ***

## Slide 133: The ALDER Project Experience
Reprocessed Sessions 307-A and 307-B by excluding the ALDER 2 data file.
  Results show that the presence or absence of a bad data file does have an effect on the whole session.
  In this case, minimal effect, but still in doubt
  see results, next slide

## Slide 134: The ALDER Project Experience
ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH SESSION NAME
------------------------------------------------------------------------------------------
ald2 TO ald1 -22.8248 -6.5969 -6.6349 24.6681 2011-307-A *** ???
ald2 TO ald1 -23.0531 -6.4129 -6.6865 24.8451 2011-307-B *** ???
ald3 TO ald1 -42.5872 -12.1459 -12.7446 46.0827 2011-307-A ***
ald3 TO ald1 -42.5886 -12.1524 -12.7432 46.0854 2011-307-B ***
ald3 TO ald1 -42.5875 -12.0815 -12.8121 46.0848 2011-307-A (NO ALD2)
ald3 TO ald1 -42.5862 -12.0977 -12.8035 46.0855 2011-307-B (NO ALD2)
ald4 TO ald1 -62.1348 -16.9338 -18.1851 66.9193 2011-307-A ***
ald4 TO ald1 -62.1359 -16.9379 -18.1813 66.9202 2011-307-B ***
ald4 TO ald1 -62.1324 -16.8826 -18.2424 66.9197 2011-307-A (NO ALD2)
ald4 TO ald1 -62.1335 -16.8838 -18.2410 66.9206 2011-307-B (NO ALD2)
mnjc TO ald1 89213.5609 -20890.8441 -15902.8820 92996.7122 2011-307-A ***
mnjc TO ald1 89213.5614 -20890.8383 -15902.8895 92996.7126 2011-307-B ***
mnjc TO ald1 89213.5606 -20890.8013 -15902.9364 92996.7115 2011-307-A (NO ALD2)
mnjc TO ald1 89213.5634 -20890.7962 -15902.9444 92996.7145 2011-307-B (NO ALD2)
mnpl TO ald1 91270.6681 30722.0783 32831.5918 101745.2425 2011-307-A ***
mnpl TO ald1 91270.6693 30722.0799 32831.5857 101745.2421 2011-307-B ***
mnpl TO ald1 91270.6676 30722.1200 32831.5363 101745.2367 2011-307-A (NO ALD2)
mnpl TO ald1 91270.6713 30722.1224 32831.5303 101745.2389 2011-307-B (NO ALD2)
mnvi TO ald1 33107.2933 -62539.7505 -57078.8435 90913.7373 2011-307-A ***
mnvi TO ald1 33107.3182 -62539.8253 -57078.7923 90913.7657 2011-307-B ***
mnvi TO ald1 33107.2942 -62539.7076 -57078.8963 90913.7413 2011-307-A (NO ALD2)
mnvi TO ald1 33107.3202 -62539.7832 -57078.8472 90913.7720 2011-307-B (NO ALD2)
wis6 TO ald1 -5637.3052 5535.9629 5010.9973 9356.0776 2011-307-A ***
wis6 TO ald1 -5637.3065 5535.9632 5010.9928 9356.0762 2011-307-B ***
wis6 TO ald1 -5637.3028 5536.0123 5010.9393 9356.0744 2011-307-A (NO ALD2)
wis6 TO ald1 -5637.3042 5536.0119 5010.9358 9356.0731 2011-307-B (NO ALD2)
wisn TO ald1 24266.7450 75452.8563 72795.9242 107616.2396 2011-307-A ***
wisn TO ald1 24266.7443 75452.8578 72795.9177 107616.2360 2011-307-B ***
wisn TO ald1 24266.7462 75452.8970 72795.8678 107616.2302 2011-307-A (NO ALD2)
wisn TO ald1 24266.7463 75452.9005 72795.8622 107616.2289 2011-307-B (NO ALD2)

## Slide 135: The ALDER Project Experience
Re-observe in Sessions 320-A and 320-B
  Ship was away from the dock – no multipath
  Needed a position for ALDER 2 anyway
  Interesting results, next slide

## Slide 136: The ALDER Project Experience
MARK-TO-MARK COMPARISONS GROUPED BY MARKS AND SORTED BY LENGTH
ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH SESSION NAME
------------------------------------------------------------------------------------------
ald2 TO ald1 -22.8248 -6.5969 -6.6349 24.6681 2011-307-A *** ???
ald2 TO ald1 -22.8866 -6.3808 -6.7963 24.7124 2011-320-B
ald2 TO ald1 -22.8874 -6.3763 -6.8006 24.7131 2011-320-A
ald2 TO ald1 -23.0531 -6.4129 -6.6865 24.8451 2011-307-B *** ???
ald3 TO ald1 -42.5816 -12.0954 -12.7977 46.0789 2011-320-B
ald3 TO ald1 -42.5815 -12.0927 -12.8037 46.0799 2011-320-A
ald3 TO ald1 -42.5872 -12.1459 -12.7446 46.0827 2011-307-A ***
ald3 TO ald1 -42.5875 -12.0815 -12.8121 46.0848 2011-307-A (NO ALD2)
ald3 TO ald1 -42.5886 -12.1524 -12.7432 46.0854 2011-307-B ***
ald3 TO ald1 -42.5862 -12.0977 -12.8035 46.0855 2011-307-B (NO ALD2)
ald4 TO ald1 -62.1318 -16.8811 -18.2355 66.9168 2011-320-B
ald4 TO ald1 -62.1327 -16.8805 -18.2371 66.9180 2011-320-A
ald4 TO ald1 -62.1348 -16.9338 -18.1851 66.9193 2011-307-A ***
ald4 TO ald1 -62.1324 -16.8826 -18.2424 66.9197 2011-307-A (NO ALD2)
ald4 TO ald1 -62.1359 -16.9379 -18.1813 66.9202 2011-307-B ***
ald4 TO ald1 -62.1335 -16.8838 -18.2410 66.9206 2011-307-B (NO ALD2)
Advisor could have retained 307-A (NO ALD2) and 307-B (NO ALD2) sessions,
But, chose to include only sessions 320-A and 320-B in final adjustment.
The 320-A and 320-B sessions are clearly better!

## Slide 137: The ALDER Project Experience
MARK-TO-MARK COMPARISONS GROUPED BY MARKS AND SORTED BY LENGTH
ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH SESSION NAME
------------------------------------------------------------------------------------------
mnjc TO ald1 89213.5606 -20890.8013 -15902.9364 92996.7115 2011-307-A (NO ALD2)
mnjc TO ald1 89213.5609 -20890.8441 -15902.8820 92996.7122 2011-307-A ***
mnjc TO ald1 89213.5635 -20890.7806 -15902.9520 92996.7123 2011-320-B
mnjc TO ald1 89213.5614 -20890.8383 -15902.8895 92996.7126 2011-307-B ***
mnjc TO ald1 89213.5634 -20890.7962 -15902.9444 92996.7145 2011-307-B (NO ALD2)
mnjc TO ald1 89213.5707 -20890.8126 -15902.9396 92996.7243 2011-320-A
mnpl TO ald1 91270.6676 30722.1200 32831.5363 101745.2367 2011-307-A (NO ALD2)
mnpl TO ald1 91270.6713 30722.1224 32831.5303 101745.2389 2011-307-B (NO ALD2)
mnpl TO ald1 91270.6762 30722.1068 32831.5374 101745.2408 2011-320-A
mnpl TO ald1 91270.6693 30722.0799 32831.5857 101745.2421 2011-307-B ***
mnpl TO ald1 91270.6681 30722.0783 32831.5918 101745.2425 2011-307-A ***
mnpl TO ald1 91270.6800 30722.1235 32831.5258 101745.2455 2011-320-B
mnvi TO ald1 33107.2933 -62539.7505 -57078.8435 90913.7373 2011-307-A ***
mnvi TO ald1 33107.2942 -62539.7076 -57078.8963 90913.7413 2011-307-A (NO ALD2)
mnvi TO ald1 33107.3182 -62539.8253 -57078.7923 90913.7657 2011-307-B ***
mnvi TO ald1 33107.3202 -62539.7832 -57078.8472 90913.7720 2011-307-B (NO ALD2)
mnvi TO ald1 33107.3251 -62539.7871 -57078.8510 90913.7788 2011-320-A
mnvi TO ald1 33107.3278 -62539.7725 -57078.8681 90913.7805 2011-320-B
wis6 TO ald1 -5637.2984 5536.0170 5010.9158 9356.0619 2011-320-B
wis6 TO ald1 -5637.2981 5536.0051 5010.9305 9356.0626 2011-320-A
wis6 TO ald1 -5637.3042 5536.0119 5010.9358 9356.0731 2011-307-B (NO ALD2)
wis6 TO ald1 -5637.3028 5536.0123 5010.9393 9356.0744 2011-307-A (NO ALD2)
wis6 TO ald1 -5637.3065 5535.9632 5010.9928 9356.0762 2011-307-B ***
wis6 TO ald1 -5637.3052 5535.9629 5010.9973 9356.0776 2011-307-A ***
wisn TO ald1 24266.7275 75452.8971 72795.8331 107616.2026 2011-320-B
wisn TO ald1 24266.7524 75452.8831 72795.8755 107616.2271 2011-320-A
wisn TO ald1 24266.7463 75452.9005 72795.8622 107616.2289 2011-307-B (NO ALD2)
wisn TO ald1 24266.7462 75452.8970 72795.8678 107616.2302 2011-307-A (NO ALD2)
wisn TO ald1 24266.7443 75452.8578 72795.9177 107616.2360 2011-307-B ***
wisn TO ald1 24266.7450 75452.8563 72795.9242 107616.2396 2011-307-A ***

## Slide 138: The ALDER Project Experience - 2022
Given all the improvements in OPUS PROJECTS 4.0 since 2011, I re-processed the ALDER project using WIS6 as a local hub and AMC2 as the distant CORS.
Then recompiled the various .VEC and .POS tables.
Details differ, but similar conclusions as before

## Slide 139: The ALDER Project Experience - 2022
The ALDER marks
ALD1
ALD2
ALD3
ALD4
WIS6
AMC2

## Slide 140: The ALDER Project Experience - 2022
From | To | Avg DX | P2P | Avg DY | P2P | Avg DZ | P2P | Avg Length | P2P
ald1 | WIS6 | 5637.30490 | 0.00650 | -5535.95580 | 0.01770 | -5010.99560 | 0.02630 | 9356.07240 | 0.00780
ald2 | WIS6 | 5614.39730 | 0.05930 | -5542.31420 | 0.24170 | -5017.78870 | 0.18860 | 9349.70090 | 0.07740
ald3 | WIS6 | 5594.71620 | 0.00800 | -5548.10990 | 0.03690 | -5023.72700 | 0.03920 | 9344.52820 | 0.01140
ald4 | WIS6 | 5575.16910 | 0.00390 | -5552.88360 | 0.06600 | -5029.18410 | 0.06220 | 9338.61440 | 0.00450
AMC2 | WIS6 | 1094483.86390 | 0.00780 | 440424.39880 | 0.00660 | 642955.70580 | 0.00580 | 1343599.87310 | 0.00930
MNJC | WIS6 | 94850.87330 | 0.00290 | -26426.80310 | 0.01070 | -20913.89410 | 0.01190 | 100660.09660 | 0.00270
MNPL | WIS6 | 96907.98100 | 0.00300 | 25186.11610 | 0.00960 | 27820.58130 | 0.01090 | 103920.55600 | 0.00340
MNVI | WIS6 | 38744.63100 | 0.00330 | -68075.77930 | 0.00970 | -62089.80480 | 0.00780 | 99952.99910 | 0.00340
WISN | WIS6 | 29904.05650 | 0.00190 | 69916.89400 | 0.00800 | 67784.91460 | 0.00690 | 101869.61920 | 0.00210
Excel screen – peak-to-peak summary
All 3 of the P2P columns show ALD2 to WIS6 as an outlier compared to other baseline repeats. But, which session is the outlier coming from?

## Slide 141: The ALDER Project Experience - 2022
File | Session | Stn1 | Stn2 | DX | RX | DY | RY | DZ | RZ | Length | RL
2011-307-B.vec | 11-307-B | ald4 | WIS6 | 5575.16820 | 0.00100 | -5552.90630 | 0.02300 | -5029.16540 | -0.01900 | 9338.61730 | -0.00300
2011-307-B (NO ALD2).vec | 11-307-B | ald4 | WIS6 | 5575.16820 | 0.00100 | -5552.90620 | 0.02300 | -5029.16550 | -0.01900 | 9338.61730 | -0.00300
2011-307-A.vec | 11-307-A | ald4 | WIS6 | 5575.16780 | 0.00100 | -5552.89850 | 0.01500 | -5029.16630 | -0.01800 | 9338.61290 | 0.00100
2011-307-A (NO ALD2).vec | 11-307-A | ald4 | WIS6 | 5575.16760 | 0.00100 | -5552.89670 | 0.01300 | -5029.16820 | -0.01600 | 9338.61280 | 0.00200
2011-320-B.vec | 11-320-B | ald4 | WIS6 | 5575.17150 | -0.00200 | -5552.85370 | -0.03000 | -5029.21140 | 0.02700 | 9338.61280 | 0.00200
2011-320-A.vec | 11-320-A | ald4 | WIS6 | 5575.17100 | -0.00200 | -5552.84030 | -0.04300 | -5029.22760 | 0.04400 | 9338.61320 | 0.00100
Average |  |  |  | 5575.16910 |  | -5552.88360 |  | -5029.18410 |  | 9338.61440 | 
P2P |  |  |  | 0.00390 |  | 0.06600 |  | 0.06220 |  | 0.00450 | 
2011-307-A.vec | 11-307-A | ald3 | WIS6 | 5594.71180 | 0.00400 | -5548.08780 | -0.02200 | -5023.74430 | 0.01700 | 9344.52170 | 0.00600
2011-307-A (NO ALD2).vec | 11-307-A | ald3 | WIS6 | 5594.71430 | 0.00200 | -5548.09440 | -0.01600 | -5023.74050 | 0.01300 | 9344.52500 | 0.00300
2011-320-B.vec | 11-320-B | ald3 | WIS6 | 5594.71940 | -0.00300 | -5548.12470 | 0.01500 | -5023.70510 | -0.02200 | 9344.52700 | 0.00100
2011-320-A.vec | 11-320-A | ald3 | WIS6 | 5594.71980 | -0.00400 | -5548.10880 | -0.00100 | -5023.72600 | -0.00100 | 9344.52910 | -0.00100
2011-307-B.vec | 11-307-B | ald3 | WIS6 | 5594.71610 | 0.00000 | -5548.12210 | 0.01200 | -5023.72290 | -0.00400 | 9344.53300 | -0.00500
2011-307-B (NO ALD2).vec | 11-307-B | ald3 | WIS6 | 5594.71600 | 0.00000 | -5548.12170 | 0.01200 | -5023.72340 | -0.00400 | 9344.53310 | -0.00500
Average |  |  |  | 5594.71620 |  | -5548.10990 |  | -5023.72700 |  | 9344.52820 | 
P2P |  |  |  | 0.00800 |  | 0.03690 |  | 0.03920 |  | 0.01140 | 
2011-307-A.vec | 11-307-A | ald2 | WIS6 | 5614.35420 | 0.04300 | -5542.16210 | -0.15200 | -5017.89850 | 0.11000 | 9349.64380 | 0.05700
2011-320-A.vec | 11-320-A | ald2 | WIS6 | 5614.41060 | -0.01300 | -5542.38870 | 0.07400 | -5017.72480 | -0.06400 | 9349.71880 | -0.01800
2011-320-B.vec | 11-320-B | ald2 | WIS6 | 5614.41070 | -0.01300 | -5542.40380 | 0.09000 | -5017.70990 | -0.07900 | 9349.71980 | -0.01900
2011-307-B.vec | 11-307-B | ald2 | WIS6 | 5614.41350 | -0.01600 | -5542.30220 | -0.01200 | -5017.82160 | 0.03300 | 9349.72120 | -0.02000
Average |  |  |  | 5614.39730 |  | -5542.31420 |  | -5017.78870 |  | 9349.70090 | 
P2P |  |  |  | 0.05930 |  | 0.24170 |  | 0.18860 |  | 0.07740 | 
2011-320-A.vec | 11-320-A | ald1 | WIS6 | 5637.30210 | 0.00300 | -5535.95340 | -0.00200 | -5010.99340 | -0.00200 | 9356.06810 | 0.00400
2011-320-B.vec | 11-320-B | ald1 | WIS6 | 5637.30110 | 0.00400 | -5535.96910 | 0.01300 | -5010.97770 | -0.01800 | 9356.06840 | 0.00400
2011-307-A (NO ALD2).vec | 11-307-A | ald1 | WIS6 | 5637.30510 | 0.00000 | -5535.95270 | -0.00300 | -5010.99930 | 0.00400 | 9356.07270 | 0.00000
2011-307-A.vec | 11-307-A | ald1 | WIS6 | 5637.30600 | -0.00100 | -5535.95600 | 0.00000 | -5010.99590 | 0.00000 | 9356.07330 | -0.00100
2011-307-B (NO ALD2).vec | 11-307-B | ald1 | WIS6 | 5637.30760 | -0.00300 | -5535.95190 | -0.00400 | -5011.00340 | 0.00800 | 9356.07590 | -0.00400
2011-307-B.vec | 11-307-B | ald1 | WIS6 | 5637.30760 | -0.00300 | -5535.95140 | -0.00400 | -5011.00400 | 0.00800 | 9356.07590 | -0.00400
Average |  |  |  | 5637.30490 |  | -5535.95580 |  | -5010.99560 |  | 9356.07240 | 
P2P |  |  |  | 0.00650 |  | 0.01770 |  | 0.02630 |  | 0.00780 | 
Excel screen – vectors summary

## Slide 142: The Fort Peck Experience
Surveyor was having trouble analyzing B-Order Survey near Fort Peck, Montana.
Local labor was used under surveyor’s supervision.
Surveyor also needed help with Pages/ Bluebooking

## Slide 143: The Fort Peck Experience
Surveyor furnished field logs and data files.
Advisor submitted them to OPUS PROJECTS.
Advisor adopted a single hub network model to maximize vector comparisons.
  Surveyor’s original choice of network model had yielded insufficient comparability to track down problem occupations. He was suspicious but not certain of the flaws.
Analysis showed which occupations were flawed and which ones needed to be re-observed.
See Tables next slides

## Slide 144: The Fort Peck Experience
Advisor adopted a single hub network

## Slide 145: The Fort Peck Experience
Note: All processing was done in OPUS-PROJECTS, using CORS station P052 as the hub. Sorted by “RANGE in L”
SESSION ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH RANGE in L
-----------------------------------------------------------------------------------------------------
173-A mtlw TO p052 182685.1452 -32364.7339 23935.9816 187067.5533
174-A ndmb TO p052 -433344.6983 20680.6358 -77363.9480 440681.8543
174-A mtms TO p052 158787.2319 -154181.3600 -86784.3878 237732.6371
173-A mtms TO p052 158787.2288 -154181.3678 -86784.3816 237732.6379 0.0008 m
199-A p054 TO p052 -156525.7880 172507.3852 116557.7168 260470.3853
174-A p054 TO p052 -156525.7904 172507.3835 116557.7187 260470.3864
173-A p054 TO p052 -156525.7889 172507.3873 116557.7152 260470.3865 0.0012 m
173-A mdr6 TO p052 -264157.1247 111089.6354 35524.7956 288759.2505
199-A mdr6 TO p052 -264157.1273 111089.6281 35524.8006 288759.2506
174-A mdr6 TO p052 -264157.1273 111089.6345 35524.7962 288759.2526 0.0021 m
174-A p053 TO p052 16910.9182 -122424.2423 -100422.1062 159242.8135
199-A p053 TO p052 16910.9189 -122424.2388 -100422.1111 159242.8141
173-A p053 TO p052 16910.9194 -122424.2412 -100422.1082 159242.8141
p053 TO p052 16910.9188 -122424.2440 -100422.1067 159242.8152
p053 TO p052 16910.9180 -122424.2456 -100422.1051 159242.8154
p053 TO p052 16910.9180 -122424.2455 -100422.1055 159242.8156
p053 TO p052 16910.9191 -122424.2446 -100422.1067 159242.8157
p053 TO p052 16910.9184 -122424.2439 -100422.1077 159242.8158
p053 TO p052 16910.9184 -122424.2455 -100422.1059 159242.8158
p053 TO p052 16910.9180 -122424.2460 -100422.1052 159242.8158 0.0023 m
p052 TO g547 212877.6529 46046.3610 91565.5799 236265.5664
g547 TO p052 -212877.6565 -46046.3675 -91565.5791 236265.5706 0.0042 m

## Slide 146: The Fort Peck Experience
SESSION ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH RANGE in L
-----------------------------------------------------------------------------------------------------
173-A p052 TO e091 59993.3863 80911.6084 85444.1892 132085.5944
e091 TO p052 -59993.3808 -80911.6265 -85444.1780 132085.5957
e091 TO p052 -59993.3802 -80911.6178 -85444.1912 132085.5987 0.0043 m
199-A p055 TO p052 -164237.5554 68394.5250 19615.9937 178987.6332
p055 TO p052 -164237.5569 68394.5236 19615.9951 178987.6342
p055 TO p052 -164237.5569 68394.5235 19615.9962 178987.6343
p055 TO p052 -164237.5569 68394.5242 19615.9953 178987.6345
p055 TO p052 -164237.5570 68394.5245 19615.9948 178987.6347
p055 TO p052 -164237.5570 68394.5250 19615.9939 178987.6347
p055 TO p052 -164237.5567 68394.5253 19615.9944 178987.6347
173-A p055 TO p052 -164237.5574 68394.5243 19615.9954 178987.6350
p055 TO p052 -164237.5581 68394.5251 19615.9950 178987.6359
174-A p055 TO p052 -164237.5604 68394.5221 19616.0007 178987.6375 0.0043 m
mcab TO p052 -210744.8646 -16575.0642 -65902.2585 221429.9853
mcab TO p052 -210744.8745 -16575.0713 -65902.2458 221429.9915 0.0062 m
t272 TO p052 -167245.3299 -46585.0279 -82018.1592 192010.7904
t272 TO p052 -167245.3301 -46585.0011 -82018.1884 192010.7966
t272 TO p052 -167245.3345 -46585.0304 -82018.1667 192010.7983 0.0079 m
199-A p052 TO powb 147758.4577 20206.2171 54520.8550 158787.2056
powb TO p052 -147758.4599 -20206.2161 -54520.8623 158787.2101
powb TO p052 -147758.4661 -20206.2290 -54520.8530 158787.2142 0.0086 m
p052 TO s544 175777.7542 17654.4943 58911.7675 186225.9284
p052 TO s544 175777.7683 17654.4991 58911.7528 186225.9375
p052 TO s544 175777.7706 17654.4891 58911.7583 186225.9404 0.0120 m

## Slide 147: The Fort Peck Experience
SESSION ST 1 TO ST 2 DELTA X DELTA Y DELTA Z LENGTH RANGE in L
-----------------------------------------------------------------------------------------------------
v358 TO p052 -89340.0651 -32424.5444 -51031.5607 107875.9403
174-A v358 TO p052 -89340.0717 -32424.5489 -51031.5548 107875.9444
v358 TO p052 -89340.0733 -32424.5464 -51031.5673 107875.9508
173-A v358 TO p052 -89340.0825 -32424.5465 -51031.5552 107875.9527 0.0124 m
173-A todd TO p052 -107495.4336 -60846.1531 -80204.9437 147276.4597
174-A todd TO p052 -107495.4562 -60846.1805 -80204.9195 147276.4744 0.0147 m
174-A p052 TO x046 140373.3911 57701.8269 85179.3582 174039.4002
x046 TO p052 -140373.3989 -57701.8641 -85179.3263 174039.4032
x046 TO p052 -140373.4149 -57701.8959 -85179.3160 174039.4216 0.0214 m
074-A n360 TO p052 -104763.8174 -61617.4611 -80171.0096 145600.6859 <--- outlier
075-A n360 TO p052 -104763.8242 -61617.4739 -80171.0221 145600.7031
069-A n360 TO p052 -104763.8303 -61617.4647 -80171.0316 145600.7088 0.0229 m
069-A p052 TO mdoc 154657.5898 78643.5300 106426.9340 203544.7547 <--- outlier
062-A mdoc TO p052 -154657.5838 -78643.5614 -106427.0019 203544.7978
074-A p052 TO mdoc 154657.5882 78643.5712 106426.9960 203544.8018 0.0471 m
199-A k542 TO p052 -117344.4357 -28084.4376 -54102.7182 132232.9624
068-A k542 TO p052 -117344.4447 -28084.4617 -54102.6979 132232.9672
075-A p052 TO k542 117344.4782 28084.5421 54102.7293 132233.0268 <--- outlier
0.0644 m
074-A q256 TO p052 -48494.3526 -54342.3166 -59620.0087 94124.0407 <--- outlier
173-A q256 TO p052 -48494.3956 -54342.3199 -59620.0728 94124.1054
069-A q256 TO p052 -48494.3841 -54342.3423 -59620.0641 94124.1069 0.0662 m
Note: All processing was done in OPUS-PROJECTS, using CORS station P052 as the hub.
Can’t select outlier from only 2 choices

## Slide 148: The Fort Peck Experience
In the Fort Peck case, OPUS PROJECTS revealed its power as a debugging/project management tool.
Mobile field crews will be able to verify data quality in OPUS PROJECTS before de-mobilizing. Re-observe right away.

## Slide 149: The Fort Peck Experience - 2022
Given all the improvements in OPUS PROJECTS 4.0 since 2011, I re-processed the Fort Peck HARN Project using P052 as a local hub and AMC2 as the distant CORS.
Then recompiled the various .VEC and .POS tables.
Details differ, but similar conclusions as before

## Slide 150: The Fort Peck Experience - 2022
AMC2
P052

## Slide 151: The Fort Peck Experience - 2022
From | To | Avg DX | P2P | Avg DY | P2P | Avg DZ | P2P | Avg Length | P2P
AMC2 | P052 | -18052.00120 | 0.00650 | 681233.63090 | 0.01140 | 694203.54730 | 0.01170 | 972791.70410 | 0.00260
e091 | P052 | -59993.38550 | 0.00350 | -80911.62050 | 0.01480 | -85444.17970 | 0.01160 | 132085.59530 | 0.00230
g547 | P052 | -212877.66020 | 0.00110 | -46046.36540 | 0.00340 | -91565.57410 | 0.00160 | 236265.57160 | 0.00220
k542 | P052 | -117344.45570 | 0.05190 | -28084.48540 | 0.10530 | -54102.70650 | 0.03140 | 132232.98540 | 0.07090
mcab | P052 | -210744.87330 | 0.01400 | -16575.07020 | 0.00470 | -65902.24600 | 0.00820 | 221429.99030 | 0.01130
mdoc | P052 | -154657.59070 | 0.00470 | -78643.55230 | 0.04630 | -106426.96780 | 0.08130 | 203544.78170 | 0.06220
MDR6 | P052 | -264157.12230 | 0.00510 | 111089.63420 | 0.00650 | 35524.79650 | 0.00600 | 288759.24790 | 0.00630
n360 | P052 | -104763.82810 | 0.01040 | -61617.46440 | 0.01160 | -80171.01950 | 0.01680 | 145600.70040 | 0.01920
P053 | P052 | 16910.91830 | 0.00160 | -122424.24340 | 0.00580 | -100422.10600 | 0.00320 | 159242.81430 | 0.00310
P054 | P052 | -156525.78890 | 0.00370 | 172507.38300 | 0.00360 | 116557.71770 | 0.00390 | 260470.38480 | 0.00260
P055 | P052 | -164237.55650 | 0.00380 | 68394.52410 | 0.00490 | 19615.99530 | 0.00750 | 178987.63410 | 0.00420
powb | P052 | -147758.46310 | 0.01440 | -20206.22280 | 0.01830 | -54520.85140 | 0.01640 | 158787.21010 | 0.01540
q256 | P052 | -48494.38020 | 0.03770 | -54342.32410 | 0.03140 | -59620.04830 | 0.05650 | 94124.08440 | 0.06140
s544 | P052 | -175777.76740 | 0.01520 | -17654.49580 | 0.01040 | -58911.75380 | 0.01870 | 186225.93670 | 0.00930
t272 | P052 | -167245.33500 | 0.00570 | -46585.01810 | 0.02050 | -82018.16930 | 0.01420 | 192010.79680 | 0.00580
todd | P052 | -107495.44480 | 0.02050 | -60846.16910 | 0.02620 | -80204.92710 | 0.02530 | 147276.46540 | 0.01200
v358 | P052 | -89340.07520 | 0.01320 | -32424.54960 | 0.00720 | -51031.55330 | 0.00760 | 107875.94680 | 0.01020
x046 | P052 | -140373.40380 | 0.02780 | -57701.85710 | 0.06110 | -85179.33530 | 0.03360 | 174039.40930 | 0.02630
Excel screen – peak-to-peak summary

## Slide 152: The Fort Peck Experience - 2022
2011-199-A.vec | 11-199-A | k542 | P052 | -117344.43430 | -0.02100 | -28084.44190 | -0.04300 | -54102.71300 | 0.00700 | 132232.95990 | 0.02600
2011-068-A.vec | 11-068-A | k542 | P052 | -117344.44650 | -0.00900 | -28084.46700 | -0.01800 | -54102.68750 | -0.01900 | 132232.96560 | 0.02000
2011-075-A.vec | 11-075-A | k542 | P052 | -117344.48620 | 0.03100 | -28084.54720 | 0.06200 | -54102.71890 | 0.01200 | 132233.03080 | -0.04500
Average |  |  |  | -117344.45570 |  | -28084.48540 |  | -54102.70650 |  | 132232.98540 | 
P2P |  |  |  | 0.05190 |  | 0.10530 |  | 0.03140 |  | 0.07090 | 
File | Session | Stn1 | Stn2 | DX | RX | DY | RY | DZ | RZ | Length | RL
2011-074-A.vec | 11-074-A | q256 | P052 | -48494.35800 | -0.02200 | -54342.31000 | -0.01400 | -59620.01480 | -0.03400 | 94124.04360 | 0.04100
2011-069-A.vec | 11-069-A | q256 | P052 | -48494.38700 | 0.00700 | -54342.34140 | 0.01700 | -59620.05880 | 0.01000 | 94124.10450 | -0.02000
2011-173-A.vec | 11-173-A | q256 | P052 | -48494.39570 | 0.01500 | -54342.32090 | -0.00300 | -59620.07130 | 0.02300 | 94124.10500 | -0.02100
Average |  |  |  | -48494.38020 |  | -54342.32410 |  | -59620.04830 |  | 94124.08440 | 
P2P |  |  |  | 0.03770 |  | 0.03140 |  | 0.05650 |  | 0.06140 | 
Excel screen – vectors summary (partial table)
2011-174-A.vec | 11-174-A | x046 | P052 | -140373.39070 | -0.01300 | -57701.82860 | -0.02900 | -85179.35350 | 0.01800 | 174039.39810 | 0.01100
2011-063-A.vec | 11-063-A | x046 | P052 | -140373.40220 | -0.00200 | -57701.85300 | -0.00400 | -85179.33260 | -0.00300 | 174039.40530 | 0.00400
2011-075-A.vec | 11-075-A | x046 | P052 | -140373.41850 | 0.01500 | -57701.88970 | 0.03300 | -85179.31990 | -0.01500 | 174039.42440 | -0.01500
Average |  |  |  | -140373.40380 |  | -57701.85710 |  | -85179.33530 |  | 174039.40930 | 
P2P |  |  |  | 0.02780 |  | 0.06110 |  | 0.03360 |  | 0.02630 | 
2011-069-A.vec | 11-069-A | mdoc | P052 | -154657.58870 | -0.00200 | -78643.52380 | -0.02800 | -106426.91470 | -0.05300 | 203544.74150 | 0.04000
2011-062-A.vec | 11-062-A | mdoc | P052 | -154657.58990 | -0.00100 | -78643.56290 | 0.01100 | -106426.99600 | 0.02800 | 203544.80000 | -0.01800
2011-074-A.vec | 11-074-A | mdoc | P052 | -154657.59340 | 0.00300 | -78643.57010 | 0.01800 | -106426.99270 | 0.02500 | 203544.80370 | -0.02200
Average |  |  |  | -154657.59070 |  | -78643.55230 |  | -106426.96780 |  | 203544.78170 | 
P2P |  |  |  | 0.00470 |  | 0.04630 |  | 0.08130 |  | 0.06220 | 

## Slide 153
OPUS Projects Manager Training
Step 3 : Session Processing
ngs.opus.projects@noaa.gov
End