## Slide 1
OPUS Projects Manager Training
Step 3 : Session Processing QA/QC
ngs.opus.projects@noaa.gov

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing QA/QC
Step 4 : Network Adjustment

## Slide 3: What’s in this training?
This presentation begins after all the sessions have been processed.
Then, it describes the session web pages, important QA/QC steps (.VEC and POS), how to evaluate and select CORS, and how to compare computed results to published control.

## Slide 4: The Manager’s Page
Select the session to be processed.
Process all sessions the same way.
  1 hub (local CORS) and make it 3D constraint
  1 distant CORS (add it from the Manager’s Page)
  All marks included (we may need to exclude later)
  All CORS included (we’ll select better later)
  7200 seconds
  15 degrees
  Piecewise Linear
  Normal weighting
OPUS will suggest a session processing strategy like this, but you can modify it if you want to.

## Slide 5
Manager’s Page showing five sessions have been processed.
Vectors show up in a color after session processing.

## Slide 6
Session Page (2021-041-A)

## Slide 7
Exclude LOYX,
One HUB,
One 3D Constraint,
PW Linear, 7200 sec, 15 deg, Normal Weight
Session Processing

## Slide 8: EMAIL Results
For each of the 5 sessions you process, you’ll get 1 email with 7 attached files. (SERFIL is duplicated each time)
Create a single folder and put all 7 attachments in it.
  There will be 5 x 7 = 35 files, but 4 are duplicated SERFILs
A total of 31 unique files.

## Slide 9: Folder Location
Here’s a reasonable folder location. Your workflow may vary.

## Slide 10: Comparison of Results
OPUS PROJECTS 4.0 already provides a quick and easy summary of the session processing results. These are in the Table at bottom of Manager’s Page

## Slide 11: Comparison of Results – all Sessions
P2P compares the computed positions from all session solutions and shows max-min (peak-to-peak) result

## Slide 12: Comparison of Results – all GVX Vectors
P2P compares the computed positions from all GVX vectors and shows max-min (peak-to-peak) result
Similar tabulation for the GVX Vectors

## Slide 13: Comparison of Results – all Sessions
Note: LOYX was excluded in session processing

## Slide 14: Comparison of Results – all GVX Vectors
Note: 2 GVX vectors were excluded earlier.
P2P compares the computed positions from all GVX vectors and shows max-min (peak-to-peak) result

## Slide 15: Comparison of Results
In a perfect world
  the P2P columns would be close to zero.
Usual tolerance
  2 cm NORTH and EAST
  4 cm UP
But, what if there are outliers?
How do we determine which ones?
  P2P does not show us.

## Slide 16: Comparison of Results
In a perfect world
  All observations would yield vectors that match.
  All vectors would yield positions that match.
  These are 2 sides of the same coin.
I like to look at both.
WinTEQC is a big help again, but I have to do some manual copying and pasting.

## Slide 17: Comparison of Results
A good and simple first step in looking for outliers is the individual Mark Pages.
Next 7 slides show the bottom part of each mark page.

## Slide 18
863F
Blue = Session
Magenta = GVX / RTK

## Slide 19
BRMR
Blue = Session
Magenta = GVX / RTK

## Slide 20
GP99
V140 was excluded earlier – should it have been?
Blue = Session
Magenta = GVX / RTK

## Slide 21
OU03
Blue = Session
Magenta = GVX / RTK

## Slide 22
OU18
Blue = Session
Magenta = GVX / RTK

## Slide 23
W416
V135 was excluded earlier – looks like we were correct !
Blue = Session
Magenta = GVX / RTK

## Slide 24
WLP2
Blue = Session
Magenta = GVX / RTK

## Slide 25: Comparison of Results
By examining the contents of the .TXT and the .VEC files, we can take a very close look at granular results and make more careful and targeted decisions regarding what is and is not an outlier.

## Slide 26: The .TXT File contents
The .TXT file contains the computed (called “estimated”) positions for each mark in the solution.
The position is derived by computing from the HUB to the remote mark using the vectors.
If multiple marks are constrained (don’t do this), it will be a least squares computation which blends observational errors with positional errors, making it harder to error-trap.
The .TXT file is the ONLY PLACE where the computed (estimated) positions are to be found in a file.

## Slide 27: The .TXT File contents (upper part)
NGS OPUS-Projects 5.1.2 SESSION SOLUTION REPORT
===============================================
All coordinate accuracies reported here are 1x the formal
uncertainties from the solution. For additional information:
geodesy.noaa.gov/OPUS/Using_OPUS-Projects.html#accuracy
These positions were computed without any knowledge by the National
Geodetic Survey regarding the equipment or field operating procedures used.
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: 2021-041-A.sum
SOLUTION SOFTWARE: page5(2008.25)
SOLUTION DATE: 2023-06-20T14:01:18 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.795
TOTAL NUMBER OF OBSERVATIONS: 120361
TOTAL NUMBER OF MARKS: 12
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
OVERALL RMS: 1.6 cm
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-02-10T23:59:30 GPS
PROGRAM OPERATION: FULL RUN
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON

## Slide 28: The .TXT File contents (RMS summary)
BASELINE LENGTH RMS OBS OMITTED FIXED
--------------------------------------------------------------
brmr-loy2 11.497 km 1.1 cm 5258 6.7% 100.0%
gp99-loy2 14.532 km 1.9 cm 5674 12.8% 97.1%
ou03-loy2 14.825 km 1.4 cm 5001 12.1% 98.1%
ou18-loy2 15.251 km 2.2 cm 4582 24.9% 97.5%
863f-loy2 21.424 km 1.6 cm 4833 17.6% 91.4%
w416-loy2 21.627 km 2.0 cm 4486 20.7% 97.8%
ls03-loy2 24.992 km 1.5 cm 18235 5.1% 99.6%
ncel-loy2 46.939 km 1.4 cm 18174 5.3% 99.2%
ncga-loy2 56.473 km 1.6 cm 17889 6.9% 99.6%
vagp-loy2 58.603 km 1.5 cm 18500 3.1% 99.6%
asub-loy2 491.455 km 1.4 cm 17729 3.4% 89.1%

## Slide 29: The .TXT File contents (a-priori shifts)
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.005 m (0.001 m) E: -0.005 m (0.001 m) H: -0.017 m (0.002 m)
asub N: -0.002 m (0.001 m) E: 0.005 m (0.001 m) H: 0.006 m (0.002 m)
brmr N: 0.001 m (0.001 m) E: -0.003 m (0.001 m) H: -0.010 m (0.002 m)
gp99 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: 0.003 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.003 m (0.001 m) H: -0.003 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: -0.003 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.005 m (0.001 m) H: 0.014 m (0.002 m)
ou03 N: 0.000 m (0.001 m) E: -0.003 m (0.001 m) H: -0.007 m (0.002 m)
ou18 N: -0.003 m (0.001 m) E: -0.004 m (0.001 m) H: 0.017 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.004 m (0.002 m)
w416 N: 0.001 m (0.001 m) E: -0.002 m (0.001 m) H: 0.006 m (0.002 m))

## Slide 30: The .TXT File contents (lower part)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
UNCONSTRAINED MARKS
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: 863f (863f 1; 863f)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.11104925
X: 1206288.546 m 0.001 m 1206287.638 m 0.001 m
Y: -4959186.770 m 0.002 m -4959185.298 m 0.002 m
Z: 3812292.490 m 0.002 m 3812292.426 m 0.002 m
LAT: 36 56 33.74469 0.001 m 36 56 33.77511 0.001 m
E LON: 283 40 16.70066 0.001 m 283 40 16.67908 0.001 m
W LON: 76 19 43.29934 0.001 m 76 19 43.32092 0.001 m
EL HGT: -34.695 m 0.002 m -36.048 m 0.002 m
ORTHO HGT: 2.207 m 0.017 m (= EL HGT - -36.902 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4089341.276 m 1069848.933 m
EASTING (X) 381686.396 m 3693394.137 m
CONVERGENCE -0.79865833 deg 1.31781944 deg
POINT SCALE 0.99977245 0.99997271
COMBINED FACTOR 0.99977789 0.99997815
US NATIONAL GRID DESIGNATOR: 18SUF8168689341 (NAD 83)

## Slide 31: The .TXT File contents (bottom part)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
CONSTRAINED MARKS
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: loy2 (loy2 a 3; LOYOLA 2 COOP; Chesapeake, Virginia, U.S.A)
CONSTRAIN: 3-D NORMAL
N36:45:50.43110 W076:14:16.06827 -23.44m NAD_83(2011) @ 2010.0000
0.14cm 0.08cm 0.13cm NEU SIGMAS
SHIFTS N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.11104925
X: 1216986.213 m 0.001 m 1216985.298 m 0.001 m
Y: -4968828.058 m 0.001 m -4968826.570 m 0.001 m
Z: 3796431.071 m 0.001 m 3796430.998 m 0.001 m
LAT: 36 45 50.43109 0.001 m 36 45 50.46147 0.001 m
E LON: 283 45 43.93174 0.001 m 283 45 43.91017 0.001 m
W LON: 76 14 16.06826 0.001 m 76 14 16.08983 0.001 m
EL HGT: -23.441 m 0.001 m -24.817 m 0.001 m
ORTHO HGT: 13.842 m 0.017 m (= EL HGT - -37.283 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4069407.907 m 1050214.000 m
EASTING (X) 389523.825 m 3701963.852 m
CONVERGENCE -0.74092222 deg 1.37298611 deg
POINT SCALE 0.99975036 1.00000048
COMBINED FACTOR 0.99975404 1.00000416
US NATIONAL GRID DESIGNATOR: 18SUF8952469408 (NAD 83)

## Slide 32: The .TXT Position Comparison
In a few minutes, we’ll come back to the .TXT file to harvest the positions and make the position comparisons.
But first, let’s look at the .VEC files and make the vector comparisons.

## Slide 33: The .VEC Comparison
2 ways to compare the results in the .VEC files
  Use a generic text editor to combine, sort, inspect
  Use the WinTeqc utility to combine, sort, inspect
Note:
The following .VEC Comparisons are ONLY for the SESSIONS.
The GVX Vectors cannot be harvested in a similar format at this time.
However, the individual Mark Pages (slides 18-24) show a graphical comparison.

## Slide 34: The .VEC Comparison (1 of 5)
2021-041-A.vec created: 2023-06-20 18:02 UTC downloaded: 2023-06-21 16:30 UTC
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-041-A 863F LOY2 10697.6595 5 -9641.2724 16 -15861.4287 13 21423.7945 rmetpjfy/21041/Results
21-041-A BRMR LOY2 6836.0444 5 -4546.1948 16 -8048.5667 12 11496.9046 rmetpjfy/21041/Results
21-041-A GP99 LOY2 6915.7057 4 -6710.0208 16 -10878.4862 12 14532.4749 rmetpjfy/21041/Results
21-041-A OU03 LOY2 7653.7617 5 -6535.1458 17 -10886.0861 12 14825.4871 rmetpjfy/21041/Results
21-041-A OU18 LOY2 8782.6631 5 -6206.1835 17 -10814.6137 13 15251.4837 rmetpjfy/21041/Results
21-041-A W416 LOY2 4952.2346 5 -12099.6336 17 -17228.4495 13 21627.4185 rmetpjfy/21041/Results
21-041-A ASUB LOY2 471536.3981 4 129735.1800 11 48477.8996 9 491454.8793 rmetpjfy/21041/Results
21-041-A LS03 LOY2 -23718.7570 3 -7561.3823 10 -2198.4689 8 24991.7427 rmetpjfy/21041/Results
21-041-A NCEL LOY2 -4870.9458 3 27561.2872 10 37682.1648 8 46939.2822 rmetpjfy/21041/Results
21-041-A NCGA LOY2 36997.0492 3 31161.4962 10 29144.2156 8 56473.0538 rmetpjfy/21041/Results
21-041-A VAGP LOY2 30253.2246 3 -25968.9427 10 -42949.2377 8 58602.7354 rmetpjfy/21041/Results
2021-048-A.vec created: 2023-06-20 18:02 UTC downloaded: 2023-06-21 16:33 UTC
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-048-A 863F LOY2 10697.6582 5 -9641.2743 17 -15861.4244 13 21423.7916 rmetpjfy/21048/Results
21-048-A BRMR LOY2 6836.0411 4 -4546.1897 14 -8048.5673 11 11496.9011 rmetpjfy/21048/Results
21-048-A GP99 LOY2 6915.7004 4 -6710.0184 15 -10878.4845 12 14532.4700 rmetpjfy/21048/Results
21-048-A OU03 LOY2 7653.7576 5 -6535.1380 16 -10886.0895 12 14825.4841 rmetpjfy/21048/Results
21-048-A OU18 LOY2 8782.6629 5 -6206.1820 17 -10814.6108 13 15251.4809 rmetpjfy/21048/Results
21-048-A W416 LOY2 4952.2337 5 -12099.6403 16 -17228.4420 13 21627.4161 rmetpjfy/21048/Results
21-048-A WLP2 LOY2 1833.7012 3 279.8616 10 -236.6759 8 1869.9727 rmetpjfy/21048/Results
21-048-A ASUB LOY2 471536.3969 4 129735.1774 11 48477.9027 8 491454.8778 rmetpjfy/21048/Results
21-048-A LS03 LOY2 -23718.7572 3 -7561.3840 10 -2198.4673 7 24991.7432 rmetpjfy/21048/Results
21-048-A NCEL LOY2 -4870.9460 3 27561.2830 10 37682.1675 7 46939.2819 rmetpjfy/21048/Results
21-048-A NCGA LOY2 36997.0484 3 31161.4953 10 29144.2166 8 56473.0532 rmetpjfy/21048/Results
21-048-A VAGP LOY2 30253.2239 3 -25968.9412 10 -42949.2391 8 58602.7355 rmetpjfy/21048/Results
Tabulate Individual .VEC files using your favorite TEXT editor

## Slide 35: The .VEC Comparison (2 of 5)
2021-054-A.vec created: 2023-06-20 18:02 UTC downloaded: 2023-06-21 16:33 UTC
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-054-A 863F LOY2 10697.6603 4 -9641.2757 15 -15861.4255 11 21423.7941 rmetpjfy/21054/Results
21-054-A BRMR LOY2 6836.0424 4 -4546.1950 14 -8048.5679 11 11496.9044 rmetpjfy/21054/Results
21-054-A GP99 LOY2 6915.7049 4 -6710.0274 16 -10878.4841 12 14532.4760 rmetpjfy/21054/Results
21-054-A OU03 LOY2 7653.7599 5 -6535.1451 17 -10886.0872 13 14825.4867 rmetpjfy/21054/Results
21-054-A OU18 LOY2 8782.6663 5 -6206.1924 17 -10814.6071 13 15251.4845 rmetpjfy/21054/Results
21-054-A W416 LOY2 4952.2371 5 -12099.6422 17 -17228.4468 13 21627.4218 rmetpjfy/21054/Results
21-054-A WLP2 LOY2 1833.7013 3 279.8583 10 -236.6747 8 1869.9722 rmetpjfy/21054/Results
21-054-A ASUB LOY2 471536.3952 4 129735.1857 11 48477.8950 8 491454.8776 rmetpjfy/21054/Results
21-054-A LS03 LOY2 -23718.7585 3 -7561.3796 10 -2198.4715 8 24991.7435 rmetpjfy/21054/Results
21-054-A NCEL LOY2 -4870.9469 3 27561.2878 10 37682.1636 8 46939.2817 rmetpjfy/21054/Results
21-054-A NCGA LOY2 36997.0494 3 31161.4931 10 29144.2179 8 56473.0533 rmetpjfy/21054/Results
21-054-A VAGP LOY2 30253.2231 3 -25968.9401 10 -42949.2410 8 58602.7359 rmetpjfy/21054/Results
2021-055-A.vec created: 2023-06-16 14:18 UTC downloaded: 2023-06-21 16:34 UTC
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-055-A WLP2 LOY2 1833.7014 3 279.8582 9 -236.6752 7 1869.9724 rmetpjfy/21055/Results
21-055-A ASUB LOY2 471536.3990 3 129735.1858 10 48477.8965 8 491454.8814 rmetpjfy/21055/Results
21-055-A LS03 LOY2 -23718.7577 3 -7561.3819 9 -2198.4702 7 24991.7433 rmetpjfy/21055/Results
21-055-A NCEL LOY2 -4870.9457 3 27561.2856 9 37682.1656 7 46939.2819 rmetpjfy/21055/Results
21-055-A NCGA LOY2 36997.0499 3 31161.4930 10 29144.2164 7 56473.0528 rmetpjfy/21055/Results
21-055-A VAGP LOY2 30253.2244 3 -25968.9424 9 -42949.2392 7 58602.7363 rmetpjfy/21055/Results
Tabulate Individual .VEC files using your favorite TEXT editor

## Slide 36: The .VEC Comparison (3 of 5)
021-063-A.vec created: 2023-06-16 14:19 UTC downloaded: 2023-06-21 16:34 UTC
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-063-A WLP2 LOY2 1833.7009 3 279.8602 10 -236.6761 7 1869.9723 rmetpjfy/21063/Results
21-063-A ASUB LOY2 471536.3983 3 129735.1767 10 48477.8991 8 491454.8785 rmetpjfy/21063/Results
21-063-A LS03 LOY2 -23718.7580 3 -7561.3805 9 -2198.4708 7 24991.7432 rmetpjfy/21063/Results
21-063-A NCEL LOY2 -4870.9467 3 27561.2851 10 37682.1663 7 46939.2822 rmetpjfy/21063/Results
21-063-A NCGA LOY2 36997.0483 3 31161.4934 10 29144.2159 7 56473.0518 rmetpjfy/21063/Results
21-063-A VAGP LOY2 30253.2251 3 -25968.9426 9 -42949.2392 7 58602.7367 rmetpjfy/21063/Results

## Slide 37: The .VEC Comparison (4 of 5)
SORTED BY LENGTH (METERS)
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-054-A WLP2 LOY2 1833.7013 3 279.8583 10 -236.6747 8 1869.9722 rmetpjfy/21054/Results
21-063-A WLP2 LOY2 1833.7009 3 279.8602 10 -236.6761 7 1869.9723 rmetpjfy/21063/Results
21-055-A WLP2 LOY2 1833.7014 3 279.8582 9 -236.6752 7 1869.9724 rmetpjfy/21055/Results
21-048-A WLP2 LOY2 1833.7012 3 279.8616 10 -236.6759 8 1869.9727 rmetpjfy/21048/Results
21-048-A BRMR LOY2 6836.0411 4 -4546.1897 14 -8048.5673 11 11496.9011 rmetpjfy/21048/Results
21-054-A BRMR LOY2 6836.0424 4 -4546.1950 14 -8048.5679 11 11496.9044 rmetpjfy/21054/Results
21-041-A BRMR LOY2 6836.0444 5 -4546.1948 16 -8048.5667 12 11496.9046 rmetpjfy/21041/Results
21-048-A GP99 LOY2 6915.7004 4 -6710.0184 15 -10878.4845 12 14532.4700 rmetpjfy/21048/Results
21-041-A GP99 LOY2 6915.7057 4 -6710.0208 16 -10878.4862 12 14532.4749 rmetpjfy/21041/Results
21-054-A GP99 LOY2 6915.7049 4 -6710.0274 16 -10878.4841 12 14532.4760 rmetpjfy/21054/Results
21-048-A OU03 LOY2 7653.7576 5 -6535.1380 16 -10886.0895 12 14825.4841 rmetpjfy/21048/Results
21-054-A OU03 LOY2 7653.7599 5 -6535.1451 17 -10886.0872 13 14825.4867 rmetpjfy/21054/Results
21-041-A OU03 LOY2 7653.7617 5 -6535.1458 17 -10886.0861 12 14825.4871 rmetpjfy/21041/Results
21-048-A OU18 LOY2 8782.6629 5 -6206.1820 17 -10814.6108 13 15251.4809 rmetpjfy/21048/Results
21-041-A OU18 LOY2 8782.6631 5 -6206.1835 17 -10814.6137 13 15251.4837 rmetpjfy/21041/Results
21-054-A OU18 LOY2 8782.6663 5 -6206.1924 17 -10814.6071 13 15251.4845 rmetpjfy/21054/Results
21-048-A 863F LOY2 10697.6582 5 -9641.2743 17 -15861.4244 13 21423.7916 rmetpjfy/21048/Results
21-054-A 863F LOY2 10697.6603 4 -9641.2757 15 -15861.4255 11 21423.7941 rmetpjfy/21054/Results
21-041-A 863F LOY2 10697.6595 5 -9641.2724 16 -15861.4287 13 21423.7945 rmetpjfy/21041/Results
21-048-A W416 LOY2 4952.2337 5 -12099.6403 16 -17228.4420 13 21627.4161 rmetpjfy/21048/Results
21-041-A W416 LOY2 4952.2346 5 -12099.6336 17 -17228.4495 13 21627.4185 rmetpjfy/21041/Results
21-054-A W416 LOY2 4952.2371 5 -12099.6422 17 -17228.4468 13 21627.4218 rmetpjfy/21054/Results
Combine, Sort, Compare Individual .VEC files
Look for outliers in all 4 columns.
outlier
outlier
outlier
outlier

## Slide 38: The .VEC Comparison (5 of 5)
SORTED BY LENGTH (METERS)
DOY SESS REF REM DELTA X SIGX DELTA Y SIGY DELTA Z SIGZ L (METERS) PATH
-------- ---- ---- ------------- ---- ------------- ---- ------------- ---- ----------- -------
21-041-A LS03 LOY2 -23718.7570 3 -7561.3823 10 -2198.4689 8 24991.7427 rmetpjfy/21041/Results
21-048-A LS03 LOY2 -23718.7572 3 -7561.3840 10 -2198.4673 7 24991.7432 rmetpjfy/21048/Results
21-063-A LS03 LOY2 -23718.7580 3 -7561.3805 9 -2198.4708 7 24991.7432 rmetpjfy/21063/Results
21-055-A LS03 LOY2 -23718.7577 3 -7561.3819 9 -2198.4702 7 24991.7433 rmetpjfy/21055/Results
21-054-A LS03 LOY2 -23718.7585 3 -7561.3796 10 -2198.4715 8 24991.7435 rmetpjfy/21054/Results
21-054-A NCEL LOY2 -4870.9469 3 27561.2878 10 37682.1636 8 46939.2817 rmetpjfy/21054/Results
21-048-A NCEL LOY2 -4870.9460 3 27561.2830 10 37682.1675 7 46939.2819 rmetpjfy/21048/Results
21-055-A NCEL LOY2 -4870.9457 3 27561.2856 9 37682.1656 7 46939.2819 rmetpjfy/21055/Results
21-041-A NCEL LOY2 -4870.9458 3 27561.2872 10 37682.1648 8 46939.2822 rmetpjfy/21041/Results
21-063-A NCEL LOY2 -4870.9467 3 27561.2851 10 37682.1663 7 46939.2822 rmetpjfy/21063/Results
21-063-A NCGA LOY2 36997.0483 3 31161.4934 10 29144.2159 7 56473.0518 rmetpjfy/21063/Results
21-055-A NCGA LOY2 36997.0499 3 31161.4930 10 29144.2164 7 56473.0528 rmetpjfy/21055/Results
21-048-A NCGA LOY2 36997.0484 3 31161.4953 10 29144.2166 8 56473.0532 rmetpjfy/21048/Results
21-054-A NCGA LOY2 36997.0494 3 31161.4931 10 29144.2179 8 56473.0533 rmetpjfy/21054/Results
21-041-A NCGA LOY2 36997.0492 3 31161.4962 10 29144.2156 8 56473.0538 rmetpjfy/21041/Results
21-041-A VAGP LOY2 30253.2246 3 -25968.9427 10 -42949.2377 8 58602.7354 rmetpjfy/21041/Results
21-048-A VAGP LOY2 30253.2239 3 -25968.9412 10 -42949.2391 8 58602.7355 rmetpjfy/21048/Results
21-054-A VAGP LOY2 30253.2231 3 -25968.9401 10 -42949.2410 8 58602.7359 rmetpjfy/21054/Results
21-055-A VAGP LOY2 30253.2244 3 -25968.9424 9 -42949.2392 7 58602.7363 rmetpjfy/21055/Results
21-063-A VAGP LOY2 30253.2251 3 -25968.9426 9 -42949.2392 7 58602.7367 rmetpjfy/21063/Results
21-054-A ASUB LOY2 471536.3952 4 129735.1857 11 48477.8950 8 491454.8776 rmetpjfy/21054/Results
21-048-A ASUB LOY2 471536.3969 4 129735.1774 11 48477.9027 8 491454.8778 rmetpjfy/21048/Results
21-063-A ASUB LOY2 471536.3983 3 129735.1767 10 48477.8991 8 491454.8785 rmetpjfy/21063/Results
21-041-A ASUB LOY2 471536.3981 4 129735.1800 11 48477.8996 9 491454.8793 rmetpjfy/21041/Results
21-055-A ASUB LOY2 471536.3990 3 129735.1858 10 48477.8965 8 491454.8814 rmetpjfy/21055/Results
Combine, Sort, Compare Individual .VEC files
Look for outliers in all 4 columns.

## Slide 39: The .VEC Comparison – WinTEQC
We can harvest the .VEC Comparison using WinTeqc.
WinTeqc is available as a linked download from the NGS “User Contributed Software” page.

## Slide 40: The .VEC Comparison – WinTEQC

## Slide 41: The .VEC Comparison – WinTEQC
WinTEQC screen
Copy, then Paste to EXCEL
WinTEQC will read the.VEC files, and compute
AVERAGE and P2P for each group of repeat vectors and
“Residual” (RX, RY, RZ) for each component.

## Slide 42: The .VEC Comparison – WinTEQC
Excel screen
Paste to EXCEL

## Slide 43: The .VEC Comparison – WinTEQC
View Statistics
Summarizes the AVERAGE and P2P for quicker inspection.

## Slide 44: The POSITION Comparison
There is no attached file with a focused collection of just the POSITIONS. As stated before, the POSITIONS are only found in the .TXT file. They are not easy to harvest from there.
The OPUS Projects Manager’s Page has already provided a P2P position comparison for all sessions (see slides 11-12).
  If the P2P position comparison tabulations are all small, then logically the underlying vectors are very similar, and there are no outliers to look for.
But which session has the outlier?
  The .VEC comparison points to a problem
  The .POS comparison should confirm the problem
The WinTeqc utility is the best choice.

## Slide 45: The .POS Comparison – WinTEQC

## Slide 46: The POSITION Comparison
WinTEQC screen
Repeat 5 times, once for each .TXT file!

## Slide 47: The .POS Comparison – WinTEQC
Follow the Detailed Steps
2021-041-A.txt

## Slide 48: The .POS Comparison – WinTEQC
click COPY,
then PASTE into EXCEL

## Slide 49: The .POS Comparison – WinTEQC (1 of 2)
Remember to add your own “Session” column.
Repeat 5 times, once for each .TXT file!

## Slide 50: The .POS Comparison – WinTEQC (2 of 2)
Remember to add your own “Session” column.

## Slide 51: The POSITION Comparison
Then Sort by MARK ID
BRMR is not an outlier (see Lat/Lon).
Somehow, the units are in SURVEY FEET, rather than METERS!
I think this may have happened as a result of loading the WINDESC files after I had done the original session processing.
OPUS Projects automatically re-processed sessions
2021-041-A
2021-048-A
2021-054-A
LOY2 was the HUB and 3D constraint, so the POSITIONS are nearly identical, as expected.

## Slide 52: The POSITION Comparison
OU03 is not an outlier (see Lat/Lon).
Somehow, the units are in SURVEY FEET, rather than METERS!
I think this may have happened as a result of loading the WINDESC files after I had done the original session processing.
OPUS Projects automatically re-processed sessions
2021-041-A
2021-048-A
2021-054-A
WLP2 is not an outlier (see EllHt column).
Inspection of the 2021-063-A.TXT file shows an apparent mistake in the GEOID18 computation.

## Slide 53: The PUBLISHED Comparison
At this stage in processing in OPUS PROJECTS 5.1, there is no easy automated way to make the comparison of computed positions to published positions.
However, as we work along toward the ADJUSTMENT step (and we use a Dummy ID = 0000), then the outputs make that comparison for us.
We will have to discuss that later.

## Slide 54: The PUBLISHED Comparison
We will have to do it the hard way.
1) find the position result for a given mark.
2) find the published datasheet for the same mark.
Subtract the LAT, LON, ELLHT.
Same for the CORS.

## Slide 55: The PUBLISHED Comparison
Step 1
  Computed positions are in the individual .TXT files.
  Computed positions are also in the POS Summary.XLS spreadsheet that you created (via WinTeqc)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: brmr (brmr 1; brmr; BREADMAKER)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.11104925
X: 1210150.161 m 0.001 m 1210149.254 m 0.001 m
Y: -4964281.849 m 0.002 m -4964280.375 m 0.002 m
Z: 3804479.628 m 0.002 m 3804479.564 m 0.002 m
LAT: 36 51 16.85015 0.001 m 36 51 16.88053 0.001 m
E LON: 283 41 59.55653 0.001 m 283 41 59.53503 0.001 m
W LON: 76 18 00.44347 0.001 m 76 18 00.46497 0.001 m
EL HGT: -36.076 m 0.002 m -37.432 m 0.002 m
ORTHO HGT: 1.005 m 0.016 m (= EL HGT - -37.081 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4079540.610 m 1060141.928 m
EASTING (X) 384097.563 m 3696166.068 m
CONVERGENCE -0.77988333 deg 1.33516111 deg
POINT SCALE 0.99976549 0.99998519
COMBINED FACTOR 0.99977115 0.99999085
US NATIONAL GRID DESIGNATOR: 18SUF8409879541 (NAD 83)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
BRMR in
2021-041-A.txt

## Slide 56: The PUBLISHED Comparison
Step 2
  Find the published datasheet for the mark.
  If the mark has a PID, you can just download the datasheet. Let’s use BRMR (DG9069).
  I like to pre-print datasheets for all known PID’s and for all likely CORS. I will need them for the Final Report.

## Slide 57: The PUBLISHED Comparison
NGS Datasheet
BRMR in
2021-041-A.txt
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: brmr (brmr 1; brmr; BREADMAKER)
LAT: 36 51 16.85015 0.001 m 36 51 16.88053 0.001 m
E LON: 283 41 59.55653 0.001 m 283 41 59.53503 0.001 m
W LON: 76 18 00.44347 0.001 m 76 18 00.46497 0.001 m
EL HGT: -36.076 m 0.002 m -37.432 m 0.002 m
ORTHO HGT: 1.005 m 0.016 m (= EL HGT - -37.081 GEOID18 HGT)
1 National Geodetic Survey, Retrieval Date = JUNE 27, 2023
DG9069 ***********************************************************************
DG9069 DESIGNATION - BREADMAKER
DG9069 PID - DG9069
DG9069 STATE/COUNTY- VA/C OF NORFOLK
DG9069 COUNTRY - US
DG9069 USGS QUAD - NORFOLK SOUTH (2019)
DG9069
DG9069 *CURRENT SURVEY CONTROL
DG9069 ______________________________________________________________________
DG9069* NAD 83(2011) POSITION- 36 51 16.85018(N) 076 18 00.44343(W) ADJUSTED
DG9069* NAD 83(2011) ELLIP HT- -36.039 (meters) (06/27/12) ADJUSTED
DG9069* NAD 83(2011) EPOCH - 2010.00
DG9069* NAVD 88 ORTHO HEIGHT - 1.036 (meters) 3.40 (feet) ADJUSTED

## Slide 58: LAT/LON Comparisons
Latitude and Longitude are expressed in DMS format.
Need an easy way to estimate linear units.
BRMR LATITUDE Comparison
36 51 16.85015 from 2021-041-A.txt
36 51 16.85018 from datasheet (DG9069)
00 00 00.00003 difference in LAT
~ approx. 0.003 feet
1 second of Latitude is about 101 feet, so
0.00010 second of Latitude is about 0.0101 feet
1 second of Longitude (near Chesapeake) is about 80.8 feet, so
0.00010 second of Longitude is about 0.0081 feet
BRMR LONGITUDE Comparison
076 18 00.44347 from 2021-041-A.txt
076 18 00.44343 from datasheet (DG9069)
000 00 00.00004 difference in LON
~ approx. 0.003 feet
Varies by
COS (latitude)

## Slide 59: The CORS Datasheets
1 National Geodetic Survey, Retrieval Date = JUNE 27, 2023
DL1900 ***********************************************************************
DL1900 CORS - This is a GPS Continuously Operating Reference Station.
DL1900 DESIGNATION - LOYOLA LS03 CORS ARP
DL1900 CORS_ID - LS03
DL1900 PID - DL1900
DL1900 STATE/COUNTY- VA/C OF VIRGINIA BEACH
DL1900 COUNTRY - US
DL1900 USGS QUAD - VIRGINIA BEACH (2019)
DL1900
DL1900 *CURRENT SURVEY CONTROL
DL1900 ______________________________________________________________________
DL1900* NAD 83(2011) POSITION- 36 47 19.43646(N) 075 57 34.32984(W) ADJUSTED
DL1900* NAD 83(2011) ELLIP HT- -22.009 (meters) (05/??/20) ADJUSTED
DL1900* NAD 83(2011) EPOCH - 2010.00
DL1900 ______________________________________________________________________
~ 0.003 m

## Slide 60: Published Comparison (a-priori shifts)
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.005 m (0.001 m) E: -0.005 m (0.001 m) H: -0.017 m (0.002 m)
asub N: -0.002 m (0.001 m) E: 0.005 m (0.001 m) H: 0.006 m (0.002 m)
brmr N: 0.001 m (0.001 m) E: -0.003 m (0.001 m) H: -0.010 m (0.002 m)
gp99 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: 0.003 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.003 m (0.001 m) H: -0.003 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: -0.003 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.005 m (0.001 m) H: 0.014 m (0.002 m)
ou03 N: 0.000 m (0.001 m) E: -0.003 m (0.001 m) H: -0.007 m (0.002 m)
ou18 N: -0.003 m (0.001 m) E: -0.004 m (0.001 m) H: 0.017 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.004 m (0.002 m)
w416 N: 0.001 m (0.001 m) E: -0.002 m (0.001 m) H: 0.006 m (0.002 m)
The A-PRIORI Shifts Table will compute the comparison for you – but be careful.
For un-published marks the comparison is to the A-Priori (OPUS STATIC) position.
For published marks (PID) the comparison is to the datasheet value.
Are you sure those are the values you would compare?
Have you applied the PID’s to passive marks – should you?
What if the mark has moved since it was published?
2021-041-A.txt

## Slide 61: Published Comparison (a-priori shifts)
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.003 m (0.001 m) E: -0.003 m (0.001 m) H: -0.021 m (0.002 m)
asub N: -0.004 m (0.001 m) E: 0.006 m (0.001 m) H: 0.003 m (0.002 m)
brmr N: -0.003 m (0.001 m) E: -0.002 m (0.001 m) H: -0.005 m (0.002 m)
gp99 N: -0.008 m (0.001 m) E: 0.003 m (0.001 m) H: 0.005 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: -0.005 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.003 m (0.001 m) H: -0.007 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: 0.013 m (0.002 m)
ou03 N: -0.003 m (0.001 m) E: -0.002 m (0.001 m) H: 0.002 m (0.002 m)
ou18 N: -0.006 m (0.001 m) E: -0.004 m (0.001 m) H: 0.017 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.002 m (0.002 m)
w416 N: -0.002 m (0.001 m) E: 0.001 m (0.001 m) H: -0.004 m (0.002 m)
wlp2 N: -0.009 m (0.001 m) E: -0.004 m (0.001 m) H: 0.005 m (0.002 m)
2021-048-A.txt

## Slide 62: Published Comparison (a-priori shifts)
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.005 m (0.001 m) E: -0.005 m (0.001 m) H: -0.022 m (0.002 m)
asub N: -0.003 m (0.001 m) E: 0.007 m (0.001 m) H: 0.014 m (0.002 m)
brmr N: 0.001 m (0.001 m) E: 0.000 m (0.001 m) H: -0.035 m (0.002 m)
gp99 N: -0.002 m (0.001 m) E: 0.000 m (0.001 m) H: -0.003 m (0.002 m)
loy2 N: 0.000 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.002 m (0.001 m) H: 0.001 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.003 m (0.001 m) H: -0.001 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: 0.011 m (0.002 m)
ou03 N: 0.002 m (0.001 m) E: -0.006 m (0.001 m) H: -0.038 m (0.002 m)
ou18 N: -0.002 m (0.001 m) E: -0.005 m (0.001 m) H: 0.006 m (0.002 m)
vagp N: 0.004 m (0.001 m) E: 0.001 m (0.001 m) H: 0.000 m (0.002 m)
w416 N: 0.004 m (0.001 m) E: -0.002 m (0.001 m) H: -0.003 m (0.002 m)
wlp2 N: -0.008 m (0.001 m) E: -0.003 m (0.001 m) H: 0.001 m (0.002 m)
2021-054-A.txt

## Slide 63: Published Comparison (a-priori shifts)
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
asub N: -0.004 m (0.001 m) E: 0.003 m (0.001 m) H: 0.013 m (0.002 m)
loy2 N: -0.001 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.003 m (0.001 m) E: -0.002 m (0.001 m) H: -0.002 m (0.002 m)
ncel N: -0.004 m (0.001 m) E: -0.004 m (0.001 m) H: -0.004 m (0.002 m)
ncga N: -0.003 m (0.001 m) E: -0.005 m (0.001 m) H: 0.011 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: 0.000 m (0.001 m) H: -0.003 m (0.002 m)
wlp2 N: -0.008 m (0.001 m) E: -0.003 m (0.001 m) H: 0.001 m (0.002 m)
2021-055-A.txt

## Slide 64: Published Comparison (a-priori shifts)
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
asub N: -0.001 m (0.001 m) E: 0.005 m (0.001 m) H: 0.004 m (0.002 m)
loy2 N: -0.001 m (0.001 m) E: 0.000 m (0.001 m) H: -0.001 m (0.001 m)
ls03 N: -0.004 m (0.001 m) E: -0.002 m (0.001 m) H: 0.000 m (0.002 m)
ncel N: -0.005 m (0.001 m) E: -0.003 m (0.001 m) H: -0.005 m (0.002 m)
ncga N: -0.004 m (0.001 m) E: -0.003 m (0.001 m) H: 0.012 m (0.002 m)
vagp N: 0.003 m (0.001 m) E: -0.001 m (0.001 m) H: -0.004 m (0.002 m)
wlp2 N: -0.009 m (0.001 m) E: -0.004 m (0.001 m) H: 0.004 m (0.002 m)
2021-063-A.txt

## Slide 65: The Final CORS Selection
Based on what we’ve found out, are there any CORS we do NOT want?
  Exclude LOYX, it has data gaps.
  Are there too many CORS?
  Which CORS have short-term positions that are out-of-agreement with each other or with the Red Line (the published position)
  Local knowledge of CORS

## Slide 66
Chesapeake Project was active on days 041 thru 063
  Exclude LOYX, it has data gaps.
The Final CORS Selection

## Slide 67
ASUB - a “distant CORS”
LOY2
LS03
NCEL
NCGA
VAGP
OK
OK
OK
OK
OK
OK
The Final CORS Selection
Some bias in NORTHING, but is within green band (2 cm)
Has data spike in UP, but not during Day 041 thru Day 063
Has data spike in UP, but not during Day 041 thru Day 063
Some bias in UP, but is within green band (4 cm)

## Slide 68
SELECTED CORS LIST
ASUB
LOY2
LS03
NCEL
NCGA
VAGP
EXCLUDED CORS LIST
LOYX – data gaps
Example of odd short-term instability.
KODIAK CORS (dated 2020)
The Final CORS Selection

## Slide 69: Geographic Distribution of CORS
VAGP
NCEL
NCGA
LS03
LOY2
ASUB
LOYX

## Slide 70: QA/QC Discussion
Decisions
  All sessions seem to be valid
    VEC comparisons are good
    Position comparisons are acceptable (computed vs published, also a-priori shifts)
  Ready for Adjustments

## Slide 71: QA/QC Discussion
But, what if we find a bad session?
  Easiest approach is to re-process the session by excluding the suspect Mark or CORS – but add a name extender to the solution
    such as: 2021-041-A(no VAGP).
  This way, you can verify improvement without losing the original solution.
  Then DELETE and RENAME solutions when final decision is made. Write it up in the Project Diary and in Project Report.

## Slide 72: QA/QC of Session Processing Step
No need to go further if we have flaws.
Process each session
Tabulate and Compare VECTORS and POSITIONS
Exclude Marks with flawed observations.
Add/Del CORS.
Compare to PUBLISHED Positions
The QA/QC Circle
START
Re-process

## Slide 73
OPUS Projects Manager Training
Step 3 : Session Processing QA/QC
ngs.opus.projects@noaa.gov
End