## Slide 1
OPUS Projects Manager Training
Step 4 : Network Adjustment
ngs.opus.projects@noaa.gov

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment

## Slide 3: What’s in this training?
This presentation begins after all session processing has been completed.
Includes:
  Adjustment setup and how to perform a network adjustment.
  Examination of adjustment results.
  Necessary QA/QC steps.
  Analysis and reportage of final adjustment.
  Submit to NGS preview.

## Slide 4
The project ID and manager keyword are required to access the manager’s page from the OPUS Projects gateway page: https://geodesy.noaa.gov/OPUS-Projects/OpusProjects.shtml

## Slide 5
The project is always scanned for changes when accessed so the information will be up-to-date.

## Slide 6
In a few moments, the manager’s page appears. It looks different now that the data have been uploaded and session processing completed, so lets explore this page.

## Slide 7
Clicking on a map icon will cause information about the data files for that mark to be shown in a “bubble.”

## Slide 8
In this bubble, the mark’s ID is a convenience link to navigate to the summary page for that mark …

## Slide 9
… and the observers names are convenience links to send an email.

## Slide 10
The brightly colored lines on the map represent baselines used in the processing. Note that the processing solutions are associated with line colors in the table below the map.

## Slide 11
In the case of session solutions, moving the cursor over the label in the table causes only those baselines to be shown.

## Slide 12
The preference controls were explored in Step 1 : Creating a Project.

## Slide 13
But notice that the Session Definition and Mark Co-location and Definition cannot be altered now because some project processing has been completed. The text in those sections explains this circumstance.

## Slide 14
The Project List button will email a list of all your projects to you.

## Slide 15
The Solutions button displays the solution controls. Here, you can rename or delete solutions in this project.
This will DELETE the SOLUTION, but not the underlying SESSION (RINEX) files.

## Slide 16
“Add Project Tracking ID” allows you to enter an assigned Tracking ID (from NGS) or a Dummy ID = 0000.

## Slide 17
When the Tracking ID has been entered, several additional controls are added. These will be discussed in future training.
The Add Project Tracking ID control will grey out.
Notes: Target for removal is October, 2013.

## Slide 18
“Show File” displays one of the processing reports in a separate window. The controls were explained in Step 3 : Session Processing.

## Slide 19
“Send Email” opens a limited capability email tool in a separate window. Its controls were also explained in Step 3 : Session Processing.

## Slide 20
“Refresh PID Information” does what the advisory box states. Note that the action may invalidate Session Processing. So this action should be used carefully. It probably should have been done BEFORE Session Processing began.

## Slide 21
Jumping to the last button, “Delete Project” sends a request to delete this project. NOTE THAT THIS IS FINAL.
Clicking the OK button is the confirming action, so be careful!
There is no UNDO.

## Slide 22
The table at the bottom of the page is a summary of the project sessions, solutions and marks.
The column headers across the top of the table name all the sessions, the session solutions and/or the network adjustments.
Session solutions and/or network adjustments show a baseline indicator color; sessions that haven’t been processed do not.
Session and session solution headers are convenience links to take you to that session’s page.

## Slide 23
Explore an ORANGE-Flagged Mark

## Slide 24
A mark’s inclusion in a session or solution is indicated by the icons in the table. The specific icon used depends upon its solution results.

## Slide 25
In some projects, one or more marks will not meet the Project Preferences (see Manager’s Page). In those cases, the Mark Icon will be orange.
In this example, note that mark 863F has not met all the solution quality threshold preferences in session 2021-048-A.
OU18 and W416 are also orange.

## Slide 26
Let’s use this table to investigate the possible problem with 863F in session 2021-048-A. First, let’s go to the 2021-048-A page.
Click on the column header.

## Slide 27
In a few moments, the 2021-048-A session page replaces the manager’s page.

## Slide 28
We can quickly see that the OBS (%), percentage of observations, included in this session solution from the 863F, OU18, and W416 data files are slightly below our preferred threshold.
The other solution quality control values are acceptable.

## Slide 29
Let’s continue this investigation by going to the 863F page. Remember that we can do that by clicking on the row header.

## Slide 30
In a few more moments, the 863F summary page replaces the session page. We’ve visited a mark’s page before, but let’s explore in more detail while we continue our investigation.

## Slide 31
The next 13 slides are a detailed tour of some MARK PAGE Controls and Information, that have not yet been discussed.
Note: A few examples are taken from other projects.
Let’s pause our analysis of the ORANGE mark “863F”.

## Slide 32
Recall that the description and occupation forms appear as simple tables and cannot be modified if you are not the project manager.

## Slide 33
At the top of the page is a Google Map Services™ interactive map showing this mark and its immediate vicinity.
Classes of icons can be turned on/off and clicking on a published mark’s icon displays its datasheet.
The mark’s name in the legend at the top of the map is a pull-down menu to navigate to other mark web pages.

## Slide 34
To the left of the map are general controls for this page. The six at the top should be familiar by this time, but the remaining two are specific to this web page.

## Slide 35
“Change MARK ID” enables you to change the mark’s ID, 863F in this case, to another four character string.
Caution!
Changing the MARK ID does not alter the Show File contents, so it seems this step should precede session processing.

## Slide 36
“Remove Mark” irrevocably removes this mark and its data from this project after confirming the instruction to do so.
Clicking the OK button is the confirming action, so be careful! There is no UNDO.

## Slide 37
The Datasheet Mock-up should look familiar. Remember, only the project manager can make changes.
Empty optional fields are shaded yellow.
Empty required fields would be shaded red.

## Slide 38
In addition to controls specific to this section on the right, the label for this section includes another pull-down menu to navigate to other mark web pages.

## Slide 39
The Occupations table lists information about the data files for this mark. Note that the antenna serial number and receiver model and serial number information are captured via the RINEX upload. Check it for correctness. The information is required in Submit to NGS (bluebooking).
Notes: Changing the antenna model and height for a file already used in session processing or network adjustments will require those solutions be repeated for the changes to be included.

## Slide 40
Manage Data Files allows you to do several actions
Available or Remove from the project (this is not a “delete”)
Group with a different MARK ID instead.

## Slide 41
Save Occupations saves the edits you made in the various boxes.

## Slide 42
The Occupations table for GVX lists information about the GVX data files for this mark. Note that the antenna serial number, receiver model, and receiver serial number information are captured via the GVX upload. Check it for correctness. It can’t be edited or corrected here. The information is required in Submit to NGS (bluebooking).
You can INCLUDE/EXCLUDE a baseline.
Or, you can INCLUDE/EXCLUDE a specific vector.
Remember, to UPDATE GVX to save the changes.

## Slide 43
The Manage Coordinates Table shows many items of important information and allows control over much of the coordinate information.
If you’re wondering what is the A-PRIORI coordinate for a Mark, it is here.

## Slide 44
The Manage Coordinates action button allows control over much of the coordinate information. If you make changes it will only affect this mark. It can be confusing.

## Slide 45
The MARK Plots show the OPUS Static solutions in grey, the Session solutions in blue, the Adjustment solutions in green, and the GVX (RTK) solutions in magenta. You can toggle these on/off by clicking the “legend”. The error bars are also shown. The plot scales vary as needed.

## Slide 46
The MARK Processing Results Table shows the tabular version of the Plots.

## Slide 47
Let’s return to the ORANGE mark 863F.

## Slide 48
Let’s change to the session 2021-048-A results to confirm our findings from that session’s page.

## Slide 49
Continuing to scroll down the page, we’ll find the solution results plots.
Examining the plots, the 2021-048-A results for this mark do not look abnormal. Considering that the flagged values just exceed thresholds and the coordinates results agree well, there is no strong reason to omit mark 863F from this session.
2021-048-A

## Slide 50
We’ll accept 863F “as is” and return to the manager’s page.

## Slide 51
Return to the manager’s page.

## Slide 52
You may need to Refresh the manager’s page if you used the “Back” rather than the “Manager’s Page” button.

## Slide 53
Next, let’s set up and perform a network adjustment. Start by clicking the “Set up Adjustment” control button.

## Slide 54
Before beginning a network adjustment, the session processing results for all marks should be examined and accepted.
If you’ve performed several alternate solutions for a given session, you must select which alternative solution is to be used in the adjustment.
It would illogical and incorrect to choose 2 or more alternative solutions of the same session in an adjustment – even though OPUS PROJECTS will let you do so!
This is why we advise that you retain the ROOT in your solution naming scheme!

## Slide 55
There are many similarities between the network adjustment and session processing controls. As we did then, let’s focus on these controls but keep a small copy of the map.

## Slide 56
First, note that no marks are listed and all the baselines have been removed from the map. They will be populated as session solutions are included in the adjustment.

## Slide 57
An adjustment can have a name. Usually, it will be something like “final”. Again, we recommend keeping the ROOT. As you test several alternative adjustment scenarios, it may be simplest to choose names like final-1 final-2, final-3, etc.
Eventually, you will adopt one. You can delete or rename these later using the “SOLUTIONS” button on the Manager’s Page

## Slide 58
All completed session solutions are listed. At least one must be included. Only one solution from a session should be included if alternates exist.
Add Solution 2021-041-A
Notes: A warning message will appear and you will be prevented from including the alternate session solutions.

## Slide 59
As you start to include session solutions for your adjustment, the marks included in those sessions solutions will be listed and the baselines shown. Let’s add the remaining 4 solutions.

## Slide 60
The table of marks in the adjustment look very similar to that used in a session solution; however, there are differences.

## Slide 61
The included marks and network design are set in the sessions. They cannot be changed in the adjustment.

## Slide 62
A network adjustment uses the solution matrices before any constraints are applied as its data sources.
Constraints are still NONE, 3D, HOR-ONLY, or VER-ONLY.

## Slide 63
So, the constraint selections can be changed, and can be different from those used in the session solutions.
OPUS PROJECTS allows editing of coordinates, BUT we don’t recommend altering CORS coordinates, nor passive coordinates.

## Slide 64
All processing remains in the ITRF, so
LET OPUS CHOOSE.

## Slide 65
The geoid or hybrid-geoid model used to compute the orthometric heights is selected by OPUS, so
LET OPUS CHOOSE.

## Slide 66
OPUS strongly recommends NORMAL. LOOSE ≈ 1 m,
NORMAL ≈ 1 cm ,
TIGHT≈ 0.1 mm.

## Slide 67
OPUS “suggests” CONSTRAINTS. You should make the final decision.
Note in this case that OPUS has suggested a passive mark, OU03, as the constraint.

## Slide 68
OPUS “suggests” CONSTRAINTS. You should make the final decision.
Change it to LOY2.

## Slide 69
“Good Practice” indicates a minimally-constrained adjustment, simply called (final).
In the next 4 adjustments, additional constraint choices may be applied.
When the selections are complete, click the “Perform Adjustment” button in the control bar at the top of the window.

## Slide 70
At that time, the selections are checked, inserted in the processing queue and a printable summary is created. The adjustment rarely takes more than a few minutes once it reaches the top of the queue.

## Slide 71: Email Notification of Adjustment
When the adjustment is completed, an email is sent. The email contains a summary of the results and has full reports attached --- 7 files in all.
ATTACHMENT INVENTORY:
------------------------ --------------------
Processing Report (.txt) : network-final.txt
B-file (.bfile) : network-final.bfile
G-file (.gfile) : network-final.gfile
Processing Log (.sum) : network-final.sum
SINEX Output (.snx) : network-final.snx
Processing Report (.xml) : network-final.xml
Serfil (.serfil) : consolidated.serfil

## Slide 72
NGS OPUS-Projects 5.1.2 NETWORK ADJUSTMENT REPORT
FOR network-final
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: network-final.sum
SOLUTION SOFTWARE: GPSCOM(2008.25)
SOLUTION DATE: 2023-08-22T09:28:32 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.760
TOTAL NUMBER OF OBSERVATIONS: 603613
TOTAL NUMBER OF MARKS: 13
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.440m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-03-04T23:59:30 GPS
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
INCLUDED SOLUTION RMS SOFTWARE RUN DATE
------------------------------------------------------------------------------
1) 2021-041 A 1.6 cm page5(2008.25) 2023-06-20T14:01 UTC
2) 2021-048 A 1.4 cm page5(2008.25) 2023-06-20T14:01 UTC
3) 2021-054 A 1.5 cm page5(2008.25) 2023-06-20T14:01 UTC
4) 2021-055 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
5) 2021-063 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
First, verify the information you entered.
Evaluating network adjustments is very similar to evaluating session solutions.
network-final.txt
Notes: This will include the session solutions selected and the constraints.

## Slide 73
Next, the general solution information.
NGS OPUS-Projects 5.1.2 NETWORK ADJUSTMENT REPORT
FOR network-final
FROM PROJECT Chesapeake Tutorial Project.
SELECTED REPORTS ARE ATTACHED TO THIS EMAIL. ALL REPORTS ARE
AVAILABLE THROUGH THE PROJECT'S WEB PAGE FOR THIS SOLUTION.
ABBREVIATED SUMMARY
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: network-final.sum
SOLUTION SOFTWARE: GPSCOM(2008.25)
SOLUTION DATE: 2023-08-22T09:28:32 UTC
STANDARD ERROR OF UNIT WEIGHT: 0.760
TOTAL NUMBER OF OBSERVATIONS: 603613
TOTAL NUMBER OF MARKS: 13
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.440m NAD_83(2011) @ 2010.0000
loy2 0.14cm 0.08cm 0.13cm NEU SIGMAS
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-03-04T23:59:30 GPS
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
INCLUDED SOLUTION RMS SOFTWARE RUN DATE
------------------------------------------------------------------------------
1) 2021-041 A 1.6 cm page5(2008.25) 2023-06-20T14:01 UTC
2) 2021-048 A 1.4 cm page5(2008.25) 2023-06-20T14:01 UTC
3) 2021-054 A 1.5 cm page5(2008.25) 2023-06-20T14:01 UTC
4) 2021-055 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
5) 2021-063 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
network-final.txt
Notes: The standard error of unit weight, number of marks, frequency, observation interval, elevation cutoff, etc..

## Slide 74
BASELINE LENGTH RMS OBS OMITTED FIXED IN SOLUTION(S)
------------------------------------------------------------------------------
wlp2-loy2 1.870 km 0.7 cm 67371 12.0% 99.7% 2, 3, 4, 5
brmr-loy2 11.497 km 1.2 cm 17107 6.7% 100.0% 1, 2, 3
gp99-loy2 14.532 km 1.8 cm 15572 12.0% 98.8% 1, 2, 3
ou03-loy2 14.825 km 1.4 cm 14638 13.0% 98.9% 1, 2, 3
ou18-loy2 15.251 km 2.1 cm 12668 31.8% 98.2% 1, 2, 3
863f-loy2 21.424 km 1.5 cm 14736 16.7% 97.2% 1, 2, 3
w416-loy2 21.627 km 2.0 cm 12919 23.0% 97.3% 1, 2, 3
ls03-loy2 24.992 km 1.5 cm 90411 5.1% 99.1% 1, 2, 3,...
ncel-loy2 46.939 km 1.4 cm 90104 5.2% 97.9% 1, 2, 3,...
ncga-loy2 56.473 km 1.6 cm 88481 6.9% 95.2% 1, 2, 3,...
vagp-loy2 58.603 km 1.5 cm 91352 3.3% 97.6% 1, 2, 3,...
asub-loy2 491.455 km 1.4 cm 88254 2.9% 83.3% 1, 2, 3,...
The Baseline Summary
network-final.txt

## Slide 75
The Estimated vs A-Priori Shifts Table
MARK ESTIMATED - A PRIORI COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.003 m (0.001 m) E: -0.005 m (0.001 m) H: -0.020 m (0.001 m)
asub N: -0.004 m (0.001 m) E: 0.005 m (0.001 m) H: 0.007 m (0.001 m)
brmr N: -0.002 m (0.001 m) E: -0.002 m (0.001 m) H: -0.018 m (0.001 m)
gp99 N: -0.006 m (0.001 m) E: -0.001 m (0.001 m) H: 0.002 m (0.001 m)
loy2 N: -0.001 m (0.001 m) E: -0.001 m (0.001 m) H: -0.002 m (0.001 m)
ls03 N: -0.004 m (0.001 m) E: -0.003 m (0.001 m) H: -0.002 m (0.001 m)
ncel N: -0.005 m (0.001 m) E: -0.004 m (0.001 m) H: -0.005 m (0.001 m)
ncga N: -0.005 m (0.001 m) E: -0.005 m (0.001 m) H: 0.012 m (0.001 m)
ou03 N: -0.002 m (0.001 m) E: -0.004 m (0.001 m) H: -0.013 m (0.001 m)
ou18 N: -0.005 m (0.001 m) E: -0.005 m (0.001 m) H: 0.013 m (0.002 m)
vagp N: 0.002 m (0.001 m) E: -0.001 m (0.001 m) H: -0.003 m (0.001 m)
w416 N: 0.000 m (0.001 m) E: -0.002 m (0.001 m) H: 0.000 m (0.001 m)
wlp2 N: -0.010 m (0.001 m) E: -0.004 m (0.001 m) H: 0.002 m (0.001 m)
Do you remember where the A-Priori positions come from?
network-final.txt

## Slide 76
The individual unconstrained mark results.
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
UNCONSTRAINED MARKS
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: 863f (0007; 863f 1)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.13040785
X: 1206288.545 m 0.001 m 1206287.637 m 0.001 m
Y: -4959186.769 m 0.001 m -4959185.297 m 0.001 m
Z: 3812292.486 m 0.001 m 3812292.423 m 0.001 m
LAT: 36 56 33.74461 0.001 m 36 56 33.77504 0.001 m
E LON: 283 40 16.70063 0.001 m 283 40 16.67905 0.001 m
W LON: 76 19 43.29937 0.001 m 76 19 43.32095 0.001 m
EL HGT: -34.698 m 0.001 m -36.051 m 0.001 m
ORTHO HGT: 2.204 m 0.016 m (= EL HGT - -36.902 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4089341.274 m 1069848.930 m
EASTING (X) 381686.396 m 3693394.136 m
CONVERGENCE -0.79865833 deg 1.31781944 deg
POINT SCALE 0.99977245 0.99997271
COMBINED FACTOR 0.99977789 0.99997816
US NATIONAL GRID DESIGNATOR: 18SUF8168689341 (NAD 83)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
network-final.txt
Notes: The coordinate uncertainties and adjustments for the constrained marks.

## Slide 77
The individual constrained mark results.
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
CONSTRAINED MARKS
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: loy2 (loy2 a 3)
CONSTRAIN: 3-D NORMAL
N36:45:50.43110 W076:14:16.06827 -23.440m NAD_83(2011) @ 2010.0000
0.14cm 0.08cm 0.13cm NEU SIGMAS
SHIFTS N: -0.001 m (0.001 m) E: -0.001 m (0.001 m) H: -0.002 m (0.001 m)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.14074740
X: 1216986.212 m 0.001 m 1216985.297 m 0.001 m
Y: -4968828.059 m 0.001 m -4968826.571 m 0.001 m
Z: 3796431.070 m 0.001 m 3796430.996 m 0.001 m
LAT: 36 45 50.43105 0.001 m 36 45 50.46143 0.001 m
E LON: 283 45 43.93169 0.001 m 283 45 43.91013 0.001 m
W LON: 76 14 16.06831 0.001 m 76 14 16.08987 0.001 m
EL HGT: -23.441 m 0.001 m -24.818 m 0.001 m
ORTHO HGT: 13.842 m 0.017 m (= EL HGT - -37.283 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4069407.906 m 1050213.999 m
EASTING (X) 389523.824 m 3701963.851 m
CONVERGENCE -0.74092222 deg 1.37298611 deg
POINT SCALE 0.99975036 1.00000048
COMBINED FACTOR 0.99975404 1.00000416
US NATIONAL GRID DESIGNATOR: 18SUF8952469408 (NAD 83)
network-final.txt

## Slide 78
Returning to the manager’s page, the network adjustment is now available for review. See Show File

## Slide 79
And the network adjustment results now appear (GREEN) with the other solutions in the individual mark’s plots and tables.

## Slide 80: Final Coordinate Listings
The final adjusted coordinates are listed ONLY in the NETWORK-FINAL.TXT attachment.
They are difficult to harvest from there.
Use WinTEQC as before.
First, copy all 7 file attachments into the same folder as the session results.

## Slide 81: WinTEQC Screen

## Slide 82: WinTEQC Summary
EXCEL Screen
network-final.txt
Mark | Lat | Acc | Lon | Acc | Northing | Easting | El Hgt | Acc | Ortho | Acc
863f | 36 56 33.74461 | 0.001 | 76 19 43.29937 | 0.001 | 1069848.930 | 3693394.136 | -34.698 | 0.001 | 2.204 | 0.016
asub | 36 12 50.84465 | 0.001 | 81 40 54.64775 | 0.001 | 276616.956 | 368477.455 | 957.917 | 0.001 | 989.140 | 0.016
brmr | 36 51 16.85012 | 0.001 | 76 18 00.44353 | 0.001 | 3478148.972 | 12126504.835 | -36.058 | 0.001 | 1.023 | 0.016
gp99 | 36 53 11.57702 | 0.001 | 76 17 42.87306 | 0.001 | 1063687.678 | 3696518.617 | -34.971 | 0.001 | 2.081 | 0.016
loy2 | 36 45 50.43105 | 0.001 | 76 14 16.06831 | 0.001 | 1050213.999 | 3701963.851 | -23.441 | 0.001 | 13.842 | 0.017
ls03 | 36 47 19.43633 | 0.001 | 75 57 34.32995 | 0.001 | 1053588.581 | 3726726.773 | -22.012 | 0.001 | 15.907 | 0.019
ncel | 36 20 28.79062 | 0.001 | 76 15 29.27411 | 0.001 | 290874.902 | 855730.320 | -29.734 | 0.001 | 7.600 | 0.015
ncga | 36 26 12.65505 | 0.001 | 76 43 16.51686 | 0.001 | 300420.804 | 813921.934 | -20.457 | 0.001 | 15.669 | 0.017
ou03 | 36 53 11.86970 | 0.001 | 76 18 13.50362 | 0.001 | 3489753.585 | 12125173.089 | -34.307 | 0.001 | 2.729 | 0.016
ou18 | 36 53 08.99406 | 0.001 | 76 19 00.94255 | 0.001 | 1063563.156 | 3694587.849 | -35.288 | 0.002 | 1.727 | 0.016
vagp | 37 14 55.00835 | 0.001 | 76 29 57.73104 | 0.001 | 1103453.310 | 3677475.383 | -19.817 | 0.001 | 15.961 | 0.021
w416 | 36 57 29.21102 | 0.001 | 76 15 34.14987 | 0.001 | 1071702.295 | 3699516.665 | -33.724 | 0.001 | 3.273 | 0.017
wlp2 | 36 45 59.76739 | 0.001 | 76 15 30.56755 | 0.001 | 1050457.649 | 3700109.837 | -13.231 | 0.001 | 23.996 | 0.017
Ref Frame: 83(2011) @ 2010.00000000 ITRF20

## Slide 83: QA/QC Discussion
None of these coordinates are directly useful because
  They may include the influence of as-yet undiagnosed adjustment details.
  Minimally-constrained.
What should our next steps be?
  Perform the remaining 4 adjustments and examine the results.

## Slide 84: End Basic Network Adjustment
The next 4 Adjustments will be discussed in the next slide set (OP 5B).

## Slide 85
OPUS Projects Manager Training
Step 4 : Network Adjustment
ngs.opus.projects@noaa.gov
END