## Slide 1: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Introduction

## Slide 2: I’ve advanced to the second slide and I’m reading it.
Can you read this slide and hear me as I read it?
Can you access the web?
Is everyone comfortable?
Does anyone have any questions before we begin?

## Slide 3: OPUS Projects Managers Training Videos
https://www.ngs.noaa.gov/optrainingvideos/
Review these videos as needed.
pre-training
self review
coach others

## Slide 4: Slides vs Examples
The slides being used today are “canned” examples as a starting point for instructors.
I have elected to use the slides, and provide the data and training project with which I am familiar.
  Training today – Chesapeake Tutorial Project

## Slide 5: A few words before beginning.
OPUS Projects is a Web-based utility implying that access to the Internet and use of a Web browser are required.
JavaScript must be enabled in your browser and pop-up blocking may have to be turned off.
If you have difficulty configuring your browser, contact your instructor or the OPUS Projects team.

## Slide 6: Operating systems and browsers.
No guarantee that OPUS Projects will work with your computer is implied. It has been successfully tested on X86 PC’s in various combinations of the following…
Operating systems: Linux® and Microsoft Windows ®
Browsers: Chrome™ Firefox® Internet Explorer® 8 through 10 Opera® Safari®

## Slide 7: Workshop Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment
Step 5 : Submit to NGS
Is an optional step and will be covered in a separate training.
OPUS-Projects Manager's Training
Trainer: Dave Zenk, Northern Plains Regional Advisor
Friday, October 27, 2023
The class will run on Friday, October 27,2023 11:00pm-1:30pm ET is an OPTIONAL SESSION, and will cover procedures necessary to submit projects for inclusion in the NGS database.

## Slide 8: What’s in this training?
This presentation is a brief introduction to and overview of OPUS Projects.
The remaining presentations are a cookbook of the steps needed to complete most projects. Like most cookbooks, you will see steps completed in detail, but the technical justification for the steps will be minimal.

## Slide 9: What’s not in this training?
This training should not be considered an endorsement of any specific project design, field technique, hardware or software.
Nor does it represent specific NGS project guidelines. However, a familiarity with these guidelines may be valuable. For more information, visit:
http://www.fgdc.gov/ http://geodesy.noaa.gov/AERO/aero.html http://geodesy.noaa.gov/heightmod/

## Slide 10: What’s the bottom line?
By completing this training:
You’ll have enough information to successfully use OPUS Projects for your own projects.
You’ll be authorized to create your own projects.
You’ll be able to train others to assist you. (talk to one of the instructors for more information)

## Slide 11: A project has been created for you.
It is identical to the one shown in this training except the access information has been customized to you.
Access information (keywords) for your training project should be in your hands by this time. If you haven’t received this information, let your instructor know.
Your example project will be available for about a month to give you time to practice.
The example project is provided as a reference for you.
No formal work will be done in the example project.
You will be creating a new project, uploading data, processing sessions, and adjusting.
Notes: After about a month, you’ll receive an email warning that your training project will be deleted. If you’d like your training project to be preserved longer than a month, contact the OPUS‐Projects team.
Everybody have their project access information?

## Slide 12: The state of your training project.
Under the assumption that most of you are already familiar with OPUS, the data have already been uploaded to your example project.
Some processing has been completed in your example project as an example of results for study and practice.
The example project is provided as a reference for you.
No formal work will be done in the example project.
You will be creating a new project, uploading data, processing sessions, and adjusting.

## Slide 13: The training data set.
Because we are assuming familiarity with OPUS, we describe uploading data to OPUS quickly emphasizing aspects specific to OPUS Projects.
If you are unfamiliar with OPUS, uploading data to your project is a great chance to practice.
The data files and descriptions shown in the training are available in a ZIP file, access to which should have been furnished to you in advance of this training.
Notes: If anyone needs help downloading or extracting the contents of the ZIP file, let an instructor know during a break.

## Slide 14: What’s in the ZIP file?
The ZIP file contains:
  RINEX data files.
  Photos of the marks.
  Field Log Sheets.
  And more supporting materials.
We’ll examine the ZIP file contents later.

## Slide 15: What is the training data set?
These data are from the Chesapeake Tutorial Project.
The start and end times, data interval, ARP heights, antenna and receiver metadata are valid.
The data, photos, and descriptive information appear meaningful but should be considered arbitrary and for training purposes only.

## Slide 16: Anything else before we begin?
Please ask questions!
Feel free to “work along” with the presentations.
Review the presentations as often as you like.
Sharing and printing copies of the presentations is fine, but be aware that some of the files are large.

## Slide 17: A brief overview of OPUS Projects. By Dan Martin, Northeast Regional Advisor 11 minute video https://geodesy.noaa.gov/corbin/class_description/What_is_OPUS_Projects.shtml
“What is OPUS PROJECTS?”

## Slide 18: What is OPUS Projects?
OPUS Projects offers Web-based access to simple visualization, management and processing tools for multiple marks and multiple occupations. Some of its advantages include:
Data uploading through OPUS.
Processing using the PAGES software.
Graphical visualization and management aids.
Limited support of bluebooking.

## Slide 19: Why complicate OPUS?
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: OPUS solutions are independent of each other, but they may be indirectly related …
Marks might “share” their environment (similar atmosphere over both).
Data might “share” the same GNSS constellation geometry.
OPUS solutions may “share” some or all of the same CORS.
Etc.
These correlations can increase with project size.

## Slide 20: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: Combining your data logically can improve results:
Neutral atmosphere (tropo) corrections can be improved which, in turn, can help with other things like phase ambiguity resolution.
Common mode effects, like baselines connecting the same CORS common to different marks, can be de-correlated.
OPUS Projects tries to logically group data together:
Data from the same mark are associated with that mark.
Marks simultaneously occupied are grouped into sessions. Session processing improve consistency and accuracy.

## Slide 21: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: These concepts can be extended to other marks and other sessions.

## Slide 22: Why complicate OPUS?
network adjustment
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: Ultimately, combining session solutions into an adjustment can improve accuracy for the entire network.

## Slide 23: What’s in it for me?
OPUS solutions = pretty good, but each treated as independent and assumes “perfect” CORS.
Sessions = simultaneously-observed marks processed together in sessions increases consistency.
Adjustments = interlinking sessions through network adjustments increases accuracy.

## Slide 24: Do we really need another OPUS variation?
The practical answer is yes. The NGS and other groups have a history of projects whose specifications can’t be entirely supported by OPUS Static (or OPUS Rapid Static).
The academic answer is yes. As good as OPUS Static does, and that is very good indeed, sacrificing simplicity for flexibility can improve results.

## Slide 25: What does this mean operationally?
Plan your project
Collect data and metadata (photos and mark descriptions)
Process the data, locally
Perform a network adjustment, locally
Publish (if desired) via “bluebook”
Notes: Very broadly, you probably go through these or very similar steps for every project.

## Slide 26: What does this mean operationally?
Plan your project
Create an OPUS project
Collect data and metadata (photos and mark descriptions)
Upload data to your project using OPUS
Process the data, using OPUS Projects
Perform a network adjustment, using OPUS Projects
Publish (if desired) via OPUS Projects
Notes: The steps when using OPUS Projects are very similar, but the steps in black use OPUS Projects rather than your own resources.

## Slide 27: What does this mean operationally?
Admittedly an oversimplification, nevertheless there is value in thinking of OPUS Projects as four steps with an optional fifth step.
Creating A Project
Uploading Data
Session Processing
Network Adjustment
Submit to the NGS Integrated Database
Notes: Publishing to the NGS Integrated Database is covered separately (Bluebooking using OPUS Projects).

## Slide 28: The steps represented graphically.
Processor or Manager
Data &
Metadata
Network
Adjustment
Manager
Session
Solution
Session
Solution
Session
Solution
Session
Solution
Copy To User
Your OPUS Project
Copy To User
Copy To User
OPUS Solution
OPUS Solution
OPUS Solution
Submit to NGS
Notes: Projects exists on an NGS server and are only accessible through the OPUS Projects Web interface.
The entire white box represents a project.
The allocation of resources for a project is step 1.
The orange icons on the left represent step 2: uploading data into the project.
The green icons in the middle represent step 3: processing individual sessions and solution quality control.
The blue icons on the right represent step 4: network adjustment.
The purple icons on the far right represent the publishing options.

## Slide 29: Are there other benefits?
Exploiting a Web-based application like OPUS Projects can mean:
Less backtracking.
  Data consolidated while teams are in the field.
  Rapid data quality assessment.
Simpler logistics.
  Data are immediate availability through on-line storage.
  Automated organization.
Less worry.
  Share information.
  Share results.

## Slide 30: Limitations?
Uploads through OPUS-Static.
  Dual-frequency.
  2 hrs ≤ data span ≤ 48 hrs (≤ 2 GPS midnights).
  Observation interval = a factor of 30 (seconds).
Minimum project size.
  At least 1 mark is needed, plus the CORS.
Maximum project size.
  There are practical limits to a project’s maximum size.
  About 100 marks in a single session.
  Number of data files < a few hundred.
Notes: The number of data files < a few hundred implies:
A few marks occupied many times.
Many marks occupied a few times.

## Slide 31: G.I.G.O.
We still need surveyors. We hope OPUS Projects can help, but it can’t do your job for you.
Follow your project’s specifications.
Use best practices and careful field procedures.
Select permanent marks of public interest.
Good coordinates come from good data.
http://gis.larc.nasa.gov/
Notes: G.I.G.O. = garbage in, garbage out

## Slide 32: A little OPUS Projects history.
2005: Weston and Gwinn began initial development on OPUS Projects.
2006: Several projects were completed as part of a proof-of-concept. Although the impressions were positive, the development stalled.
2007: Development restarted.
2010: OPUS Projects goes beta.
2013: OPUS Projects goes operational.
2020: Submit to NGS
2023: GVX and more

## Slide 33: Things To Come.
OPUS Projects improves because of your critique and suggestions. Although we can’t act upon every comment, we do appreciate and consider every one. They have and will continue to steer development.
Here are a few things already in the works:
Allowing data files < 2 hrs in duration.
Enable multi-constellation (M-PAGES)
Better integration with CORS.
Publishing to the NGSIDB.
Implemented
Notes: Allowing data files < 2 hrs in duration. Target: Allow OPUS Rapid-Static and Static uploads by January, 2014.
Better integration with CORS. Target: ? Work has begun on a new interface.
Better support for publishing to the NGSIDB.
  B- and g-files are available now.
  Better integration with conventional publishing activities.
  Act as a catalyst for other improvements (simpler, faster, more reliable).

## Slide 34: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Introduction
End