## Slide 1: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Step 1 : Creating a Project

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment

## Slide 3: What’s in this training?
This presentation shows how to create a project and set its preferences in preparation for use.
The format is as a series of steps like a cookbook. Like most cookbooks, the justification for and discussion of variations in those steps will be minimal.
The intent is to get you started quickly, then leave you free to explore OPUS Projects on your own.

## Slide 4
Create a New Project
Start at the OPUS Projects gateway page: https://geodesy.noaa.gov/OPUS-Projects/OpusProjects.shtml
NGS Home Page

## Slide 5
Click the “Create” button to start Creating a Project.

## Slide 6
You’ll be taken to the “Create Project” page. Here you’ll enter your email address, a title for and brief summary of your project. Let’s work through these steps.
dave.zenk@nola.gov

## Slide 7
dave.zenk@nola.gov
Your email addresses must be less than 54 characters in length.

## Slide 8
dave.zenk@nola.gov
You must be registered to create a project. This will be verified after you enter your email address and move to the next field.

## Slide 9
OPUS Projects Manager Training is the best way to be registered to create projects. Information upcoming classes can be found at https://geodesy.noaa.gov/corbin/calendar.shtml
dave.zenk@nola.gov

## Slide 10
After entering a registered email address, the “Create” button will be enabled and you can complete the form.

## Slide 11
NGS-supplied project tracking ID is not needed unless you plan to Submit to NGS later. Leave blank or use dummy ID = 0000

## Slide 12
The default DATA CODE = AA. Leave it as is.

## Slide 13
Next, enter your project title. The project title must be less than 65 characters in length but, otherwise, has few restrictions. However, remember that short and simple are often better.
Chesapeake Training Data

## Slide 14
The project type designates the project as a HtMod (Height Modernization), FAA (Aeronautical Survey Program) or Other type of project. Most projects will be “Other”.
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data

## Slide 15
HtMod and FAA projects will receive additional scrutiny if published to insure they meet the specifications for those types of projects. Leave the type as Other for now.
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data

## Slide 16
Select your AGENCY from the drop-down list.
If you don’t have an agency code, use LOCAL ENG or LOCAL SURV or NONE. Frequent submitters can request a code from NGS.
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data

## Slide 17
You can enter the approximate location by clicking on the map or typing directly into the entry fields. Let’s set the approximate location by clicking on the map.
ZENKTDS5 New Ulm Airport (OP4.0)
36.7500
-076.2500
Chesapeake Training Data

## Slide 18
Enter the anticipated start date manually or use a pop-up calendar feature. Clicking on the entry fields causes a calendar to appear.
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data
36.7500
-076.2500

## Slide 19
You can select the month and year using the controls at the top of the calendar. Clicking on a day number causes it to be entered into the field. This project started May 01, 2013.
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data
36.7500
-076.2500

## Slide 20
If you prefer to enter the start date manually, hitting the ESC key while the calendar is visible causes the calendar to disappear, then you can enter the date using a MM/DD/YYYY format.
01/11/2022
02/10/2021
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data
36.7500
-076.2500

## Slide 21
You can type in the fields or click the increment/decrement buttons to complete the approximate size fields. Values are limited to 999 or less. New Ulm Project has 6 marks and 2 days.
05/01/2013
7
22
ZENKTDS5 New Ulm Airport (OP4.0)
Chesapeake Training Data
36.7500
-076.2500
02/10/2021

## Slide 22
6
2
When the form is complete, click Create.
Chesapeake Training Data
36.7500
-076.2500
02/10/2021
7
22

## Slide 23
Letr’s pause here, while you create your first project! (5 minutes)
6
2
Your.address@yourdomain.com
Chesapeake Training Data
36.7500
-076.2500
02/10/2021
7
22

## Slide 24
After a moment, an introduction to your newly created project will be shown. It contains information necessary for you to work with your project. You’ll also receive this information in email. Save this email for future reference.

## Slide 25
Let’s highlight the most critical information.

## Slide 26
The project identifier, and the manager and session keywords are used to access to your project.

## Slide 27
Your project identifier can be shared thereby permitting others to upload data to your project.

## Slide 28
The project identifier and the manager keyword allow you, the project manager, complete access to all parts of your project.

## Slide 29
The project identifier and session keyword offer limited access to your project’s session and mark pages. This is useful if another person is to help with data processing for example.

## Slide 30
The project‘s preferences can be accessed from the manager’s page. These should be reviewed at creation so a convenient link to the manager’s page is provided. Follow the link, if desired.
hyperlink

## Slide 31
You’ll be taken to the manager’s page for your empty project. Before proceeding, let’s take a few moments to familiarize ourselves with the general layout of this page. We’ll discuss the details in later steps of the training.

## Slide 32
At the top of the page, you may see notices about OPUS.
Rarely, a message specific to your project may appear here too. In these rare cases, no other project will see those messages.
Important: NGS will release an announcement in the near future! Watch this space for more later!

## Slide 33
The manager and session pages are built around a Google Map Services™ interactive map to help orient you in the project and region. As data are uploaded, icons representing the project’s marks and included CORS will appear on the map.

## Slide 34
The names of the MARKS and CORS will also be listed in tables to the right side of the map.

## Slide 35
Buttons to “pop up” controls are on the left side of the map.

## Slide 36
Click the “Preferences” button to pop up a window with those controls.

## Slide 37
A new window containing the preference controls will appear. For ease of viewing, we’ll zoom in and focus on each section of this window individually.

## Slide 38
The “Project Title, ID and Keywords” section is used to change those values. Note the rules for the ID and keywords. Some find these randomly generated strings challenging and prefer something more memorable. Changing these will cause an updated copy of the email introducing your project to be sent to you. We’ll leave them for now.

## Slide 39
Sometimes the project will send emails to you. You can create a list of addresses using the “CC Manager Email” controls so others also receive these emails.

## Slide 40
The “Data & Solution Quality Thresholds” cause icons and table entries to be flagged if a mark’s solution results exceed a threshold thereby indicating potential problems.

## Slide 41
These thresholds are also applied to the OPUS solutions when project data files are uploaded. If an OPUS solution exceeds a threshold, a separate email describing the condition is sent to the address on the upload form.

## Slide 42: Sample “warning” email
It is your responsibility to make your field teams aware of this possibility and that receiving one of these warnings does not mean the data file was omitted from the project.

## Slide 43
This is a good time to set these values to your project’s specifications, if any.
For training purposes only, let’s change the maximum height uncertainty to 0.060 m; the latitude and longitude uncertainties to 0.030 m.
0.060
0.030
0.030

## Slide 44
The “Data Processing Defaults” are just that; default values and selections appearing in the project’s processing forms. Like all defaults, they can be changed at the time of processing. Let’s select NORMAL for the “Constraint Weights”. We’ll discuss all these options as we move along.

## Slide 45
The “Session Definition” section gives you some control over how data files are grouped together to form sessions for processing. These values can only be changed before session processing has begun. After processing has begun, this section is disabled and an explanatory message appears. In almost all cases, these values should not be changed; however, if you feel a need to change the definition, consult with the OPUS Projects team prior to making any changes.

## Slide 46
The “Mark Co-location Definition” gives you some control over how data files are associated with a mark. You see here that data files whose OPUS solution positions fall within 1 m of one another will be grouped together. However, RINEX and some other format specifications use a mark identifier string as the first four characters of the file name. If you are confident that this will be the case and be correct for all your project’s data files, select “Mark ID”. Here again, this definition can not be changed after session processing has begun.

## Slide 47
Once you’ve reviewed the preferences and made necessary changes, click the “Save Changes and Close” button to apply these preference to your project.

## Slide 48: Session Definition Explained
A “session” is a group of observations conducted more or less simultaneously.
Ragged start and stop times are inevitable.
So, OP must do the grouping – see Manager’s preferences for %overlap and minimum duration choices.

## Slide 49: Session Definition Explained
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
Easy for OPUS PROJECTS to define sessions
Difficult for OPUS PROJECTS to define sessions
Time
Time
Gap
Time
Gap
Time
Gap
Time Gap is not obvious.
Which files go with which sessions?
Your intent is not clear.
Do any overlap by 50%
Duration exceed 1800 seconds?
Is this 3, 4, or even 5 sessions?
Time
Let’s trim RCVR 3 and RCVR 4 in the BLUE Session

## Slide 50: Session Definition Explained
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
Easy for OPUS PROJECTS to define sessions – but
Time
Time
Gap
Time Gap is now obvious, but poor “overlap” could lead to weaker solutions
And it’s still an open question as to how exactly the Green and Blue files will be grouped..(due to % overlap and minimum data duration)
Should there have been 2 GREEN Sessions and 2 BLUE sessions?
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
Time

## Slide 51: Session Definition Explained
RCVR 1
RCVR 2
RCVR 3
RCVR 4
RCVR 2
RCVR 3
RCVR 4
RCVR 1
RCVR 2
RCVR 3
RCVR 4
Difficult for OPUS PROJECTS to define sessions
Time
Time Gap is no longer obvious.
OPUS needs to intelligently use the overlapping data.
But likely to make mistakes.
Time Gap is now obvious, but poor “overlap” could lead to weaker solutions.
Project Manager should emphasize to field crews that sessions are planned, not random.
RINEX files can be trimmed to remove early or trailing times to facilitate OP sessioning later.
In the above example which way should the YELLOW RCVR 1 be trimmed?

## Slide 52
Your project is now ready for data uploading to begin.

## Slide 53: A Few Words About Impersonation
If an impersonator creates a project using your email address, the project will be created and you will receive an email saying so.
Impersonator will have the keywords and they could ADD his/her own email to the CC list (see slide 41). You will receive an email saying so. Presumably by now, you’re wondering what’s up.
You have the impersonator’s email to enable your own optional “action”
Contact OPUS PROJECTS TEAM requesting a deletion of the project. (Or just DELETE it yourself.)
If problem persists, you can ask OPUS PROJECTS TEAM to deauthorize your current email address.

## Slide 54: A Few Words About Project ID’s
If you choose to change the Project ID from its randomly assigned keyword to one of your choosing, you must choose a new Project ID (keyword) that is:
  UNIQUE among all other projects in the world
  8-character maximum / not case-sensitive
Don’t confuse PROJECT ID
with PROJECT TITLE

## Slide 55: What if I Forget? - Project ID Listing
You’ll be able to request a Project List so that you can recover lost Project Keywords.
  The listing will be sent to your email.
Example:
Project List contains hyperlinks to each project !

## Slide 56: Access to USER GUIDE (html)
The CURRENT USER GUIDE is located on the OPUS Projects page
https://geodesy.noaa.gov/OPUS-Projects/OpusProjects.shtml
Current
April 2023

## Slide 57: Access to USER GUIDE (pdf)
Click the Help ? Button.
A pop-up window will open, usually to the needed section.
Click on the symbol
Save the download.
Out of date
June 2021

## Slide 58: Chesapeake Tutorial Project
Create the Project

## Slide 59: Chesapeake Tutorial Project
Save the email to your project folder

## Slide 60: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Step 1 : Creating a Project
End