## Slide 1: What Is a GVX File and How is it Structured?

## Slide 2: NGS GVX Support Page
GVX: The GNSS Vector Exchange File Format
https://geodesy.noaa.gov/data/formats/GVX/index.shtml
Documentation
Example Files
GVX Schema

## Slide 3: GVX Documentation
https://www.ngs.noaa.gov/data/formats/GVX/gvx_documentation.pdf

## Slide 4: GVX File – 8 Data Elements
PROJECT INFORMATION
REFERENCE SYSTEM
POINT
SURVEY SETUP
EQUIPMENT
SOURCE DATA
GNSS VECTOR
SESSION
Refer to:
GVX: The GNSS Vector Exchange File Format
https://geodesy.noaa.gov/data/formats/GVX/index.shtml
Examples in this presentation are from the 066.GVX sample file.

## Slide 5: XML Structure
Extensible Markup Language = XML
<SOURCE_DATA>
  <NAME>066.jxl</NAME>
  <CREATED_DATE>2018-03-07T06:55:16</CREATED_DATE>
  <APPLICATION>
  <NAME>Trimble General Survey</NAME>
  <VERSION>2.90</VERSION>
  <MANUFACTURER>Trimble</MANUFACTURER>
  <MANUFACTURER_URL>https://www.trimble.com</MANUFACTURER_URL>
  </APPLICATION>
  <CONVERTED_BY>
    <SOFTWARE_NAME>MATLAB_jxl2gvx.m</SOFTWARE_NAME>
    <VERSION>1.0</VERSION>
    <CONVERTED_DATE>2021-01-22T22:20:38</CONVERTED_DATE>
  </CONVERTED_BY>
</SOURCE_DATA>
Nested Data Fields
Hierarchical and Grouped
Begin <xxx> and End </xxx>

## Slide 6: SOURCE_DATA Element (1 of 2)
SOURCE DATA

## Slide 7: SOURCE_DATA Element (2 of 2)
SOURCE DATA
Total of 10 sub-elements

## Slide 8: SOURCE_DATA Table
FILE |  |  | APPLICATION |  |  |  | CONVERTED BY |  |  | 
GVX_FILE_NAME | ORIG_FILE_NAME | ORIG_FILE_CREATE_DATE | APP_NAME | APP_VERSION | APP_MFG | APP_MFG_URL | SOFTWARE_NAME | VERSION | SOFTWARE_URL | CONVERTED_DATE
052.GVX | 052.JXL | 2018-02-21T07:33:50 | Trimble General Survey | 2.90 | TRIMBLE | https://www.trimble.com | MATLAB_jxl2gvx.m | 1.0 |  | 2021-03-26T20:43:32
053.GVX | 053.JXL | 2018-02-22T07:30:15 | Trimble General Survey | 2.90 | TRIMBLE | https://www.trimble.com | MATLAB_jxl2gvx.m | 1.0 |  | 2021-03-26T20:45:28
054.GVX | 054.JXL | 2018-02-23T07:55:31 | Trimble General Survey | 2.90 | TRIMBLE | https://www.trimble.com | MATLAB_jxl2gvx.m | 1.0 |  | 2021-03-26T20:45:37
066.GVX | 066.JXL | 2018-03-07T06:55:16 | Trimble General Survey | 2.90 | TRIMBLE | https://www.trimble.com | MATLAB_jxl2gvx.m | 1.0 |  | 2021-01-22T22:20:38
Uploaded Filename
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS
SOURCE DATA

## Slide 9: PROJECT_INFORMATION Element
PROJECT INFORMATION
Total of 6 sub-elements

## Slide 10: PROJECT_INFORMATION Table
GVX_FILE_NAME | TITLE | EMAIL_ADDRESS | PARTY_CHIEF | AGENCY | START_DATE | END_DATE | REMARK
052.GVX | RTN Study, Maryland | galen.scott@noaa.gov | Galen Scott | National Geodetic Survey | 2018-02-21T12:37:25.00 | 2018-02-21T23:29:01.00 | 
053.GVX | RTN Study, Maryland | galen.scott@noaa.gov | Galen Scott | National Geodetic Survey | 2018-02-22T12:33:21.00 | 2018-02-22T22:23:02.00 | 
054.GVX | RTN Study, Maryland | galen.scott@noaa.gov | Galen Scott | National Geodetic Survey | 2018-02-23T12:58:52.00 | 2018-02-23T19:36:58.00 | 
066.GVX | RTN Study, Maryland | galen.scott@noaa.gov | Galen Scott | National Geodetic Survey | 2018-03-07T11:59:51.00 | 2018-03-07T21:08:11.00 | 
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS
PROJECT INFORMATION

## Slide 11: REFERENCE_SYSTEM Element (1 of 2)
REFERENCE SYSTEM
Commonly used
Commonly used
Commonly used

## Slide 12: REFERENCE_SYSTEM Element (2 of 2)
Total of 10 sub-elements
REFERENCE SYSTEM

## Slide 13: REFERENCE_SYSTEM Table
REFERENCE SYSTEM
REFERENCE_SYSTEM |  |  |  | LINEAR_UNIT |  |  | ANGULAR_UNIT |  |  | 
GVX_FILE_NAME | ID | CODE | NAME | NAME | SIGNIFICANT_DIGITS | CONVERSION_FACTOR | NAME | SIGNIFICANT_DIGITS | CONVERSION_FACTOR | REMARK
052.GVX |  |  |  |  |  |  |  |  |  | 
053.GVX |  |  |  |  |  |  |  |  |  | 
054.GVX |  |  |  |  |  |  |  |  |  | 
066.GVX | 126 |  | NAD 83(2011) | meters |  |  | decimal degrees |  |  | 
066.GVX | 153 |  | IGS14 | meters |  |  | decimal degrees |  |  | 
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS

## Slide 14: EQUIPMENT Element (1 of 2)
EQUIPMENT

## Slide 15: EQUIPMENT Element (2 of 2)
EQUIPMENT
Total of 8 sub-elements

## Slide 16: EQUIPMENT Table
EQUIPMENT
 |  | RECEIVER |  |  | ANTENNA |  |  | 
GVX_FILE_NAME | ID | TYPE | SERIAL_NUMBER | FIRMWARE_VERSION | TYPE | CALIBRATION_TYPE | CALIBRATION_SOURCE | SERIAL_NUMBER
052.GVX |  |  |  |  |  |  |  | 
053.GVX |  |  |  |  |  |  |  | 
054.GVX |  |  |  |  |  |  |  | 
066.GVX | 00000049 |  |  |  | AdV Null Antenna | Unknown | Unknown | 
066.GVX | 00000056 | TRMR10 | 5631465932 | 5.33 | TRMR10 NONE | Absolute | IGS | 5631465932
066.GVX | 00000095 |  |  |  | AdV Null Antenna | Unknown | Unknown | 
066.GVX has 3 EQUIPMENT records.
The 3rd equipment record in 066.GVX is not shown in Figure 4.
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS

## Slide 17: SURVEY_SETUP Element (1 of 2)
SURVEY SETUP

## Slide 18: SURVEY_SETUP Element (2 of 2)
SURVEY SETUP
Total of 13 sub-elements

## Slide 19: SURVEY_SETUP Table
SURVEY SETUP
 |  |  |  | PROCESSING_SOFTWARE |  |  |  | NETWORKRTK |  |  |  |  | 
GVX_FILE_NAME | ID | SOLUTION_TYPE | OPERATOR | NAME | VERSION | SOFTWARE_URL | CORRECTOR_FORMAT | NAME | MOUNT_POINT | TYPE | IP_ADDRESS | IP_PORT | REMARK
052.GVX |  |  |  |  |  |  |  |  |  |  |  |  | 
053.GVX |  |  |  |  |  |  |  |  |  |  |  |  | 
054.GVX |  |  |  |  |  |  |  |  |  |  |  |  | 
066.GVX | 00000042 | NetworkRTK | FOB | Trimble VRS | 3.2 | https://www.trimble.com | RTCM 3.1 | KeyNetGPS | VRS_RTCM3 | VRS | 209.255.196.164 | 2101 | 
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS
066.GVX has only 1 SURVEY_SETUP record

## Slide 20: POINT Element (1 of 3)
POINT

## Slide 21: POINT Element (2 of 3)
POINT
Total of 28 sub-elements

## Slide 22: POINT Table
POINT
 |  |  |  |  |  |  |  |  | COORDINATES |  | GEODETIC_COORDINATES |  |  | GEOCENTRIC_COORDINATES |  |  | CORRELATION_MATRIX_LOCAL |  |  |  |  |  | CORRELATION_MATRIX |  |  |  |  | 
GVX_FILE_NAME | ID | NAME | CODE | EQUIPMENT_ID | ARP_HEIGHT | POINT_TYPE | NETWORK_LOCATION | TILT_COMPENSATOR | REFERENCE_SYSTEM_ID | EPOCH | LATITUDE | LONGITUDE | ELLIPSOIDAL_HEIGHT | X | Y | Z | SDN | SDE | SDU | PNE | PNU | PEU | SDX | SDY | SDZ | PXY | PXZ | PYZ
052.GVX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
053.GVX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
054.GVX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
066.GVX | 00000045 | PRS87926747413 |  | 00000049 | 0.0000 | Keyed-in |  |  | 126 | 2010.0000 | 39.935084521832 | -77.659293358481 | 169.771458608 | 1046708.79220401 | -4784306.74711840 | 4072570.41333930 | 0.0100 | 0.0100 | 0.0100 | 0.000000 | 0.000000 | 0.000000 |  |  |  |  |  | 
066.GVX | 00000057 | TANE_TR_066A_01 |  | 00000056 | 2.0000 | Fixed |  |  | 126 | 2010.0000 | 39.663351509617 | -77.183549366876 | 111.806363310 | 1090672.00390682 | -4794238.86798448 | 4049352.88271511 |  |  |  |  |  |  |  |  |  |  |  | 
066.GVX | 00000067 | TANE_TR_066A_02 |  | 00000056 | 2.0000 | Fixed |  |  | 126 | 2010.0000 | 39.663351531048 | -77.183549262873 | 111.797773989 | 1090672.01080570 | -4794238.85807641 | 4049352.87906444 |  |  |  |  |  |  |  |  |  |  |  | 
GVX_FILE_NAME | ID | NAME | CODE | EQUIPMENT_ID | ARP_HEIGHT | POINT_TYPE | NETWORK_LOCATION | TILT_COMPENSATOR
052.GVX |  |  |  |  |  |  |  | 
053.GVX |  |  |  |  |  |  |  | 
054.GVX |  |  |  |  |  |  |  | 
066.GVX | 00000045 | PRS87926747413 |  | 00000049 | 0.0000 | Keyed-in |  | 
066.GVX | 00000057 | TANE_TR_066A_01 |  | 00000056 | 2.0000 | Fixed |  | 
066.GVX | 00000067 | TANE_TR_066A_02 |  | 00000056 | 2.0000 | Fixed |  | 
COORDINATES |  | GEODETIC_COORDINATES |  |  | GEOCENTRIC_COORDINATES |  | 
REFERENCE_SYSTEM_ID | EPOCH | LATITUDE | LONGITUDE | ELLIPSOIDAL_HEIGHT | X | Y | Z
126 | 2010.0000 | 39.935084521832 | -77.659293358481 | 169.771458608 | 1046708.79220401 | -4784306.74711840 | 4072570.41333930
126 | 2010.0000 | 39.663351509617 | -77.183549366876 | 111.806363310 | 1090672.00390682 | -4794238.86798448 | 4049352.88271511
126 | 2010.0000 | 39.663351531048 | -77.183549262873 | 111.797773989 | 1090672.01080570 | -4794238.85807641 | 4049352.87906444
CORRELATION_MATRIX_LOCAL |  |  |  |  |  | CORRELATION_MATRIX |  |  |  |  | 
SDN | SDE | SDU | PNE | PNU | PEU | SDX | SDY | SDZ | PXY | PXZ | PYZ
0.0100 | 0.0100 | 0.0100 | 0.000000 | 0.000000 | 0.000000 |  |  |  |  |  | 
066.GVX has 20 POINT records.
Only the first 3 records are shown here.
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS

## Slide 23: POINT Table
POINT
066.GVX has 20 POINT records.
Only the first 2 records are shown in Figure 6.
Since the ARP_HEIGHT may change from POINT to POINT, the ARP_HEIGHT is associated with each individual point record.
These ARP_HEIGHT changes should be entered in the data collector as the survey progresses.
Listing ARP_HEIGHT in the POINT record makes editing/correcting in OPUS easier later.

## Slide 24: POINT Name sub-element
POINT
OPUS will attempt to GROUP points by Location, not MARK ID.
Current proximity is set to 1 meter.
If truly unique points fall inside 1 meter, there may be grouping errors.
After grouping, OPUS will attempt to use the first 4 characters of the NAME for the group.
If the various NAME fields are differing, which NAME will OPUS use?
If duplicative or confusing NAMEs are found, then OPUS will use “a001” etc.

## Slide 25: GNSS_VECTOR Element (1 of 2)
GNSS VECTOR

## Slide 26: GNSS_VECTOR Element (2 of 2)
GNSS VECTOR
Total of 37 sub-elements

## Slide 27: GNSS_VECTOR Table (partial - 7 of 37 shown)
066.GVX has 18 GNSS_VECTOR records.
Only the first 4 are shown here.
 |  |  |  |  | EDEF_DELTAS |  | 
GVX_FILE_NAME | ID | INITIAL_POINT_ID | TERMINAL_POINT_ID | SURVEY_SETUP_ID | DX | DY | DZ
052.GVX |  |  |  |  |  |  | 
053.GVX |  |  |  |  |  |  | 
054.GVX |  |  |  |  |  |  | 
066.GVX | V1 | 00000045 | 00000057 | 00000042 | 43963.2117028116 | -9932.1208660826 | -23217.5306241941
066.GVX | V2 | 00000045 | 00000067 | 00000042 | 43963.2186016924 | -9932.1109580128 | -23217.5342748570
066.GVX | V3 | 00000045 | 00000075 | 00000042 | 43963.2181274317 | -9932.1161507796 | -23217.5316041633
066.GVX | V4 | 00000091 | 0000009f | 00000042 | -25802.3299931402 | 11351.7529761158 | 20732.3905985337
V1, V2, and V3 all have same INITIAL POINT ID.
V1, V2, and V3 all terminate in unique TERMINAL POINT ID’s, but if you go to the POINTs Table, you can see they have similar POINT NAMEs (TANE) and share similar coordinates.
V4 uses the same SURVEY_SETUP, but has a different INITIAL POINT ID and TERMINAL POINT ID.
066.GVX has 6 vectors to TANE.
Each vector produced a POINT with a unique POINT_ID
Surveyor used similar NAMEs
  <ID>00000057</ID> <NAME>TANE_TR_066A_01</NAME>
  <ID>00000067</ID> <NAME>TANE_TR_066A_02</NAME>
  <ID>00000075</ID> <NAME>TANE_TR_066A_03</NAME>
  <ID>00000123</ID> <NAME>TANE_TR_066B_01</NAME>
  <ID>00000135</ID> <NAME>TANE_TR_066B_02</NAME>
  <ID>00000147</ID> <NAME>TANE_TR_066B_03</NAME>
OPUS will group these by location and call the grouping TANE
As each GVX File is uploaded, this table is populated inside OPUS PROJECTS

## Slide 28: GNSS_VECTOR Example (1 of 2)
GNSS VECTOR

## Slide 29: GNSS_VECTOR Example (2 of 2)
GNSS VECTOR

## Slide 30: SESSION Element
SESSION

## Slide 31: SESSION Element
SESSION
The GVX format includes a record-type to allow SESSION-processed vectors. This record type allows surveyors to use their non-OPUS vector processor and use GVX to import the vectors into an OPUS PROJECT.
This may be a less-common use of GVX, so it will not be addressed further in this slide set.
The details are explained in the GVX documentation, see Appendix A.

## Slide 32: Submit GVX files
What happens after you submit GVX files to OPUS PROJECTS?
OP will read the file(s)
  Extract all the data and decode it into internal OP database
  POINTS that fall within 1 meter will be grouped. A mark name will be assigned to the group. Not an infallible process.
  Some vectors INITIAL POINT will coincide with a known CORS and will be assigned that mark name.
  Some vectors INITIAL POINT will coincide with an already loaded passive mark and will be assigned that mark name.
  Some vectors INITIAL POINT will not coincide with an already loaded passive mark and will be assigned a mark name.
  Similar logic will be applied to TERMINAL POINTs.

## Slide 33: Submit GVX files
Ideal OP File Submission Sequence
  Upload all the STATIC Rinex files, including the base station Rinex files.
    This will prepopulate OP with the “intended” mark names for the RTK Initial Point IDs and perhaps some of the Terminal Point IDs too.
    User should examine and correct all such mark names before loading the GVX files.
  You can upload several GVX files at once, but this can lead to a few mark naming “mistakes”.
    Best practice is one GVX at a time.
    Exercise careful “in-field” and “in-office” editing of mark names within the GVX files – prior to GVX creation and submission.

## Slide 34: Submit GVX files
Confusing Mark Name example 1
What should OPUS PROJECTS do with the following POINTS having the <NAME> as shown?
066.GVX has 6 vectors to TANE.
Each vector produced a POINT with a unique POINT_ID
Surveyor used similar, but not identical NAMEs for all 6 POINTs
  <ID>00000057</ID> <NAME>TANE_TR_066A_01</NAME>
  <ID>00000067</ID> <NAME>TANE_TR_066A_02</NAME>
  <ID>00000075</ID> <NAME>TANE_TR_066A_03</NAME>
  <ID>00000123</ID> <NAME>TANE_TR_066B_01</NAME>
  <ID>00000135</ID> <NAME>TANE_TR_066B_02</NAME>
  <ID>00000147</ID> <NAME>TANE_TR_066B_03</NAME>
OPUS will group these by location and call the grouping TANE

## Slide 35: Submit GVX files
066.GVX has 6 vectors to TANE.
Each vector produced a POINT with a unique POINT_ID
Surveyor used not-similar NAMEs for all 6 POINTs
  <ID>00000057</ID> <NAME>TANE_TR_066A_01</NAME>
  <ID>00000067</ID> <NAME>TAEN_TR_066A_02</NAME>
  <ID>00000075</ID> <NAME>TNAE_TR_066A_03</NAME>
  <ID>00000123</ID> <NAME>TENA_TR_066B_01</NAME>
  <ID>00000135</ID> <NAME>TANE_TR_066B_02</NAME>
  <ID>00000147</ID> <NAME>TENE_TR_066B_03</NAME>
OPUS will group these by location and call the grouping ????
Confusing Mark Name example 2
What should OPUS PROJECTS do with the following POINTS having the <NAME> as shown?
Choose TANE, because it’s the first one?
Choose TANE, because it occurred twice?
Assign A001, because no clear choice?

## Slide 36: Submit GVX files
What happens if I upload GVX files first?
Let’s look at an example:
  Create an empty project
  Accept default “manager’s preferences”
  Upload GNSS Vectors.

## Slide 37: Submit GVX files
“Generic” Mark Names
“selected” Mark Names based on input
Connected to known CORS
Many marks will have been assigned 4 character names which are not what surveyor intended.
Could be confusing when Static RINEX files are uploaded later!

## Slide 38: Submit GVX files

## Slide 39: Submit GVX files
prs8
prs9
tane
fran
Do prs8 and prs9 have other intended names?
Edit now or later?

## Slide 40: End