## Slide 1
OPUS Projects Manager Training
Step 4 : Network Adjustment (continued)
ngs.opus.projects@noaa.gov

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment

## Slide 3: What’s in this training?
This presentation begins after all the “network-final” adjustment has been completed.
Includes:
  The remaining 4 Adjustments.
  Adjustment setup and how to perform a network adjustment.
  Examination of adjustment results.
  Necessary QA/QC steps.
  Analysis and reportage of final adjustment.
  Submit to NGS preview.

## Slide 4: The 4 Adjustments
Horizontal Free
  Aligns the adjustment to reference frame of choice, usually NAD83(2011) and to a single Lat/Lon and Ellipsoid height.
Horizontal Constrained
  Applies user’s choice of Constraints for CORS and Passive Marks.
Vertical Free
  Aligns the adjustment to reference frame of choice, usually NAD83(2011), and to a single Lat/Lon and Orthometric height.
Vertical Constrained
  Applies user’s choice of Constraints for Orthometric heights.

## Slide 5: What’s CONSTRAINABLE?
OPUS Projects allows you to constrain freely.
OPUS Projects will recommend constraints based on database – needs PID’s.
WinDesc should include the PID for each mark that has a PID.

## Slide 6: Passive Control
How to find control in your area:
  NGS Data Explorer
  https://geodesy.noaa.gov/NGSDataExplorer/
  NGS Web Map
  https://geodesy.noaa.gov/datasheets/ngs_map/
Input city, state, or lat/lon
Once marks appear, you can manually mark the center of your area with an “x” and specify a search radius
This will show you what control may be present.
Use the NGS “Passive Mark Page” to get more detailed information on each mark of interest
Notes: NGS provides several tools to aid in locating nearby marks.
The NGS Data Explorer
The NGS Web Map
Input city, state, or lat/lon
Once marks appear, you can manually mark the center of your area with an “x” and specify a search radius
This will show you what control may be present.
Use the NGS “Passive Mark Page” to get more detailed information on each mark of interest

## Slide 7: Passive Control
Try the NGS Passive Mark Page to get more information on each mark of interest https://beta.ngs.noaa.gov/datasheets/passive-marks/index.html
Input Permanent Identifier (PID)
Notes: Here’s an example of a NGS Passive Mark Page.

## Slide 8: Datasheets for the Selected Marks
BRMR (DG9069)
DG9069 ***********************************************************************
DG9069 DESIGNATION - BREADMAKER
DG9069 PID - DG9069
DG9069 STATE/COUNTY- VA/C OF NORFOLK
DG9069 COUNTRY - US
DG9069 USGS QUAD - NORFOLK SOUTH (2019)
DG9069 *CURRENT SURVEY CONTROL
DG9069 ______________________________________________________________________
DG9069* NAD 83(2011) POSITION- 36 51 16.85018(N) 076 18 00.44343(W) ADJUSTED
DG9069* NAD 83(2011) ELLIP HT- -36.039 (meters) (06/27/12) ADJUSTED
DG9069* NAD 83(2011) EPOCH - 2010.00
DG9069* NAVD 88 ORTHO HEIGHT - 1.036 (meters) 3.40 (feet) ADJUSTED
DG9069 ______________________________________________________________________
DG9069 GEOID HEIGHT - -37.081 (meters) GEOID18
DG9069 NAD 83(2011) X - 1,210,150.169 (meters) COMP
DG9069 NAD 83(2011) Y - -4,964,281.877 (meters) COMP
DG9069 NAD 83(2011) Z - 3,804,479.651 (meters) COMP
DG9069 LAPLACE CORR - -3.45 (seconds) DEFLEC18
DG9069 DYNAMIC HEIGHT - 1.036 (meters) 3.40 (feet) COMP
DG9069 MODELED GRAVITY - 979,857.5 (mgal) NAVD 88
DG9069
DG9069 VERT ORDER - FIRST CLASS II
DG9069
DG9069 Network accuracy estimates per FGDC Geospatial Positioning Accuracy
DG9069 Standards:
DG9069 FGDC (95% conf, cm) Standard deviation (cm) CorrNE
DG9069 Horiz Ellip SD_N SD_E SD_h (unitless)
DG9069 -------------------------------------------------------------------
DG9069 NETWORK 0.61 0.47 0.27 0.22 0.24 -0.04184303
DG9069 -------------------------------------------------------------------
Constraint Possible
HOR: Yes
VERT: Yes
Notes: Examine the NGS Datasheet to find published positions and method attributes.
This mark would be constrainable as HOR and VERT.

## Slide 9: Datasheets for the Selected Marks
W416 (FX0049)
FX0049 ***********************************************************************
FX0049 DESIGNATION - W 416
FX0049 PID - FX0049
FX0049 STATE/COUNTY- VA/C OF NORFOLK
FX0049 COUNTRY - US
FX0049 USGS QUAD - NORFOLK NORTH (2019)
FX0049 *CURRENT SURVEY CONTROL
FX0049 ______________________________________________________________________
FX0049* NAD 83(1986) POSITION- 36 57 29.21 (N) 076 15 34.15 (W) HD_HELD1
FX0049* NAVD 88 ORTHO HEIGHT - 3.273 (meters) 10.74 (feet) ADJUSTED
FX0049 ______________________________________________________________________
FX0049 GEOID HEIGHT - -36.997 (meters) GEOID18
FX0049 DYNAMIC HEIGHT - 3.270 (meters) 10.73 (feet) COMP
FX0049 MODELED GRAVITY - 979,869.4 (mgal) NAVD 88
FX0049 OBS GRAVITY - 979,874.0 (mgal) GRAV_OBS
FX0049
FX0049 VERT ORDER - FIRST CLASS I
Constraint Possible
HOR: No
VERT: Yes
Notes: This mark would be constrainable VERT but not HOR

## Slide 10: Datasheets for the Selected Marks
OU03 (AJ4598)
AJ4598 CBN - This is a Cooperative Base Network Control Station.
AJ4598 DESIGNATION - ODU 3
AJ4598 PID - AJ4598
AJ4598 STATE/COUNTY- VA/C OF NORFOLK
AJ4598 COUNTRY - US
AJ4598 USGS QUAD - NORFOLK NORTH (2019)
AJ4598 *CURRENT SURVEY CONTROL
AJ4598 ______________________________________________________________________
AJ4598* NAD 83(2011) POSITION- 36 53 11.86975(N) 076 18 13.50342(W) ADJUSTED
AJ4598* NAD 83(2011) ELLIP HT- -34.294 (meters) (06/27/12) ADJUSTED
AJ4598* NAD 83(2011) EPOCH - 2010.00
AJ4598* NAVD 88 ORTHO HEIGHT - 2.7 (meters) 9. (feet) GPS OBS
AJ4598 ______________________________________________________________________
AJ4598 NAVD 88 orthometric height was determined with geoid model GEOID03
AJ4598 GEOID HEIGHT - -36.982 (meters) GEOID03
AJ4598 GEOID HEIGHT - -37.036 (meters) GEOID18
AJ4598 NAD 83(2011) X - 1,209,332.458 (meters) COMP
AJ4598 NAD 83(2011) Y - -4,962,292.927 (meters) COMP
AJ4598 NAD 83(2011) Z - 3,807,317.170 (meters) COMP
AJ4598 LAPLACE CORR - -3.10 (seconds) DEFLEC18
AJ4598
AJ4598 Network accuracy estimates per FGDC Geospatial Positioning Accuracy
AJ4598 Standards:
AJ4598 FGDC (95% conf, cm) Standard deviation (cm) CorrNE
AJ4598 Horiz Ellip SD_N SD_E SD_h (unitless)
AJ4598 -------------------------------------------------------------------
AJ4598 NETWORK 0.56 0.82 0.24 0.22 0.42 -0.15152312
AJ4598 -------------------------------------------------------------------
Constraint Possible
HOR: Yes
VERT: No
Notes: This mark would be constrainable as HOR but not VERT.

## Slide 11: Datasheets for the Selected Marks
Constraint Possible
HOR: No
VERT: No
863F (BBBX81)
Notes: An OPUS Share mark would not be constrainable as HOR or VERT.

## Slide 12: Datasheets for the Selected CORS
LOY2 (DF5272)
DF5272 ***********************************************************************
DF5272 HT_MOD - This is a Height Modernization Survey Station.
DF5272 CORS - This is a GPS Continuously Operating Reference Station.
DF5272 DESIGNATION - LOYOLA 2 COOP CORS ARP
DF5272 CORS_ID - LOY2
DF5272 PID - DF5272
DF5272 STATE/COUNTY- VA/C OF CHESAPEAKE
DF5272 COUNTRY - US
DF5272 USGS QUAD - KEMPSVILLE (2019)
DF5272
DF5272 *CURRENT SURVEY CONTROL
DF5272 ______________________________________________________________________
DF5272* NAD 83(2011) POSITION- 36 45 50.43110(N) 076 14 16.06827(W) ADJUSTED
DF5272* NAD 83(2011) ELLIP HT- -23.439 (meters) (06/??/19) ADJUSTED
DF5272* NAD 83(2011) EPOCH - 2010.00
DF5272* NAVD 88 ORTHO HEIGHT - 13.85 (meters) 45.4 (feet) GPS OBS
Constraint Possible
HOR: Yes
VERT: Yes

## Slide 13: Datasheets for the Selected CORS
LOYX (DL3186)
DL3186 ***********************************************************************
DL3186
DL3186 CORS - This is a GPS Continuously Operating Reference Station.
DL3186 DESIGNATION - LOYOLA X CORS ARP
DL3186 CORS_ID - LOYX
DL3186 PID - DL3186
DL3186 STATE/COUNTY- VA/C OF WILLIAMSBURG
DL3186 COUNTRY - US
DL3186 USGS QUAD - WILLIAMSBURG (2019)
DL3186
DL3186 *CURRENT SURVEY CONTROL
DL3186 ______________________________________________________________________
DL3186* NAD 83(2011) POSITION- 37 16 35.03058(N) 076 41 43.81960(W) ADJUSTED
DL3186* NAD 83(2011) ELLIP HT- 2.208 (meters) (01/??/23) ADJUSTED
DL3186* NAD 83(2011) EPOCH - 2010.00
Constraint Possible
HOR: Yes
VERT: No

## Slide 14: Datasheets for the Selected CORS
LS03 (DL1900)
DL1900 ***********************************************************************
DL1900
DL1900 CORS - This is a GPS Continuously Operating Reference Station.
DL1900 DESIGNATION - LOYOLA LS03 CORS ARP
DL1900 CORS_ID - LS03
DL1900 PID - DL1900
DL1900 STATE/COUNTY- VA/C OF VIRGINIA BEACH
DL1900 COUNTRY - US
DL1900 USGS QUAD - VIRGINIA BEACH (2019)
DL1900
DL1900 *CURRENT SURVEY CONTROL
DL1900 ______________________________________________________________________
DL1900* NAD 83(2011) POSITION- 36 47 19.43646(N) 075 57 34.32984(W) ADJUSTED
DL1900* NAD 83(2011) ELLIP HT- -22.009 (meters) (05/??/20) ADJUSTED
DL1900* NAD 83(2011) EPOCH - 2010.00
Constraint Possible
HOR: Yes
VERT: No

## Slide 15: Datasheets for the Selected CORS
NCEL (DL6896)
DL6896 ***********************************************************************
DL6896 HT_MOD - This is a Height Modernization Survey Station.
DL6896 CORS - This is a GPS Continuously Operating Reference Station.
DL6896 DESIGNATION - ELIZABETH CITY CORS ARP
DL6896 CORS_ID - NCEL
DL6896 PID - DL6896
DL6896 STATE/COUNTY- NC/PASQUOTANK
DL6896 COUNTRY - US
DL6896 USGS QUAD - PASQUOTANK (2019)
DL6896
DL6896 *CURRENT SURVEY CONTROL
DL6896 ______________________________________________________________________
DL6896* NAD 83(2011) POSITION- 36 20 28.79081(N) 076 15 29.27392(W) ADJUSTED
DL6896* NAD 83(2011) ELLIP HT- -29.730 (meters) (05/??/21) ADJUSTED
DL6896* NAD 83(2011) EPOCH - 2010.00
DL6896* NAVD 88 ORTHO HEIGHT - 7.60 (meters) 24.9 (feet) GPS OBS
Constraint Possible
HOR: Yes
VERT: Yes

## Slide 16: Datasheets for the Selected CORS
NCGA (DL6898)
DL6898 ***********************************************************************
DL6898 HT_MOD - This is a Height Modernization Survey Station.
DL6898 CORS - This is a GPS Continuously Operating Reference Station.
DL6898 DESIGNATION - GATESVILLE CORS ARP
DL6898 CORS_ID - NCGA
DL6898 PID - DL6898
DL6898 STATE/COUNTY- NC/GATES
DL6898 COUNTRY - US
DL6898 USGS QUAD - MERCHANTS MILLPOND (2019)
DL6898
DL6898 *CURRENT SURVEY CONTROL
DL6898 ______________________________________________________________________
DL6898* NAD 83(2011) POSITION- 36 26 12.65519(N) 076 43 16.51667(W) ADJUSTED
DL6898* NAD 83(2011) ELLIP HT- -20.469 (meters) (06/??/19) ADJUSTED
DL6898* NAD 83(2011) EPOCH - 2010.00
DL6898* NAVD 88 ORTHO HEIGHT - 15.65 (meters) 51.3 (feet) GPS OBS
Constraint Possible
HOR: Yes
VERT: Yes

## Slide 17: Datasheets for the Selected CORS
VAGP (DJ5202)
DJ5202 ***********************************************************************
DJ5202
DJ5202 CORS - This is a GPS Continuously Operating Reference Station.
DJ5202 DESIGNATION - VA GLOUCESTER PT CORS ARP
DJ5202 CORS_ID - VAGP
DJ5202 PID - DJ5202
DJ5202 STATE/COUNTY- VA/GLOUCESTER
DJ5202 COUNTRY - US
DJ5202 USGS QUAD - POQUOSON WEST (2019)
DJ5202
DJ5202 *CURRENT SURVEY CONTROL
DJ5202 ______________________________________________________________________
DJ5202* NAD 83(2011) POSITION- 37 14 55.00829(N) 076 29 57.73102(W) ADJUSTED
DJ5202* NAD 83(2011) ELLIP HT- -19.814 (meters) (06/??/19) ADJUSTED
DJ5202* NAD 83(2011) EPOCH - 2010.00
Constraint Possible
HOR: Yes
VERT: No

## Slide 18: Horizontal Free Adjustment
Aligns the adjustment to reference frame of choice, usually NAD83(2011) and to a single Lat/Lon and Ellipsoid height.
Input is “network-final”
Output is “network-final-horizontal-free”

## Slide 19
OPUS Projects suggested constraint

## Slide 20
Verify your inputs

## Slide 21: Email Notification
Analysis is same as for “network-final”.
12 files attached
ATTACHMENT INVENTORY:
------------------------ -------------------------------------------
Processing Report (.txt) : network-final-horizontal-free.txt
B-file (.bfile) : network-final-horizontal-free.bfile
G-file (.gfile) : network-final-horizontal-free.gfile
Compvecs (.cvecs) : network-final-horizontal-free.cvecs
Preplt2 (.preplt2) : network-final-horizontal-free.preplt2
Chkobs (.chkobs) : network-final-horizontal-free.chkobs
Obschk (.long) : network-final-horizontal-free.obschk.long
Obschk (.short) : network-final-horizontal-free.obschk.short
Obsdes (.obsdes) : network-final-horizontal-free.obsdes
Processing Log (.sum) : network-final-horizontal-free.sum
Processing Report (.xml) : network-final-horizontal-free.xml
Serfil (.serfil) : consolidated.serfil

## Slide 22: Save 12 Files to a Folder

## Slide 23: network-final-horizontal-free.txt
NGS OPUS-Projects 5.1.2 NETWORK ADJUSTMENT REPORT
=================================================
All coordinate accuracies reported here are 1x the formal
uncertainties from the solution. For additional information:
geodesy.noaa.gov/OPUS/Using_OPUS-Projects.html#accuracy
These positions were computed without any knowledge by the National
Geodetic Survey regarding the equipment or field operating procedures used.
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: network-final-horizontal-free.sum
SOLUTION SOFTWARE: ADJUST(6.4.3)
SOLUTION DATE: 2023-08-22T11:56:56 UTC
STANDARD ERROR OF UNIT WEIGHT: 1.345
TOTAL NUMBER OF VECTORS: 60
TOTAL NUMBER OF MARKS: 13
CONSTRAINED MARKS: 1 HORIZONTAL, 0 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 -23.440m NAD_83(2011) @ 2010.0000
loy2 0.24cm 0.25cm 0.68cm NEU SIGMAS
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-03-04T23:59:30 GPS
STANDARD DEVIATION SCALARS: 2 SOURCES
1) Trimble RTK HORIZONTAL: 1.734 UP: 1.576
2) OPUSProjects HORIZONTAL: 0.446 UP: 0.259
SESSION PROCESSING INCLUDED
===========================
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
INCLUDED SOLUTION RMS SOFTWARE RUN DATE
------------------------------------------------------------------------------
1) 2021-041 A 1.6 cm page5(2008.25) 2023-06-20T14:01 UTC
2) 2021-048 A 1.4 cm page5(2008.25) 2023-06-20T14:01 UTC
3) 2021-054 A 1.5 cm page5(2008.25) 2023-06-20T14:01 UTC
4) 2021-055 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
5) 2021-063 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC

## Slide 24: network-final-horizontal-free.txt
BASELINE LENGTH RMS OBS OMITTED FIXED IN SOLUTION(S)
------------------------------------------------------------------------------
wlp2-loy2 1.870 km 0.7 cm 67371 12.0% 99.7% 2, 3, 4, 5
brmr-loy2 11.497 km 1.2 cm 17107 6.7% 100.0% 1, 2, 3
gp99-loy2 14.532 km 1.8 cm 15572 12.0% 98.8% 1, 2, 3
ou03-loy2 14.825 km 1.4 cm 14638 13.0% 98.9% 1, 2, 3
ou18-loy2 15.251 km 2.1 cm 12668 31.8% 98.2% 1, 2, 3
863f-loy2 21.424 km 1.5 cm 14736 16.7% 97.2% 1, 2, 3
w416-loy2 21.627 km 2.0 cm 12919 23.0% 97.3% 1, 2, 3
ls03-loy2 24.992 km 1.5 cm 90411 5.1% 99.1% 1, 2, 3,...
ncel-loy2 46.939 km 1.4 cm 90104 5.2% 97.9% 1, 2, 3,...
ncga-loy2 56.473 km 1.6 cm 88481 6.9% 95.2% 1, 2, 3,...
vagp-loy2 58.603 km 1.5 cm 91352 3.3% 97.6% 1, 2, 3,...
asub-loy2 491.455 km 1.4 cm 88254 2.9% 83.3% 1, 2, 3,...
UPLOADED VECTORS INCLUDED
===========================
BASELINE USED LENGTH EPOCHS(min) EPOCHS(max) PDOP(min) PDOP(max)
ou18-wlp2 2 14.221 km 301 302 2.76 2.91
w416-wlp2 2 21.253 km 301 305 1.49 1.71
863f-wlp2 2 20.521 km 301 302 1.52 1.75
ou03-wlp2 2 13.919 km 301 304 1.69 2.62
gp99-wlp2 2 13.709 km 192 313 1.52 1.58
brmr-wlp2 3 10.457 km 187 406 1.50 1.77

## Slide 25: network-final-horizontal-free.txt
MARK ESTIMATED - PRELIMINARY ADJUSTMENT COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: -0.001 m (0.003 m) E: 0.007 m (0.003 m) H: 0.019 m (0.010 m)
asub N: 0.005 m (0.003 m) E: 0.005 m (0.004 m) H: 0.007 m (0.009 m)
brmr N: -0.001 m (0.003 m) E: 0.007 m (0.003 m) H: 0.004 m (0.010 m)
gp99 N: -0.001 m (0.003 m) E: 0.006 m (0.003 m) H: 0.016 m (0.010 m)
loy2 N: 0.002 m (0.003 m) E: 0.001 m (0.003 m) H: 0.001 m (0.009 m)
ls03 N: 0.002 m (0.003 m) E: 0.005 m (0.003 m) H: -0.004 m (0.009 m)
ncel N: -0.002 m (0.003 m) E: 0.006 m (0.003 m) H: -0.010 m (0.009 m)
ncga N: 0.002 m (0.003 m) E: 0.008 m (0.003 m) H: -0.007 m (0.009 m)
ou03 N: 0.001 m (0.003 m) E: 0.004 m (0.003 m) H: -0.005 m (0.010 m)
ou18 N: -0.001 m (0.003 m) E: 0.006 m (0.003 m) H: 0.020 m (0.010 m)
vagp N: 0.001 m (0.003 m) E: 0.004 m (0.003 m) H: -0.008 m (0.009 m)
w416 N: 0.000 m (0.003 m) E: 0.007 m (0.003 m) H: 0.015 m (0.010 m)
wlp2 N: 0.001 m (0.003 m) E: 0.005 m (0.003 m) H: 0.019 m (0.009 m)
MARK ESTIMATED - PUBLISHED HORIZONTAL COORDINATE SHIFTS
------------------------------------------------------------------------------
asub N: 0.002 m (0.003 m) E: 0.010 m (0.004 m) U: 0.014 m (0.009 m) CORS
loy2 N: -0.000 m (0.003 m) E: 0.000 m (0.003 m) U: 0.000 m (0.009 m) CORS
ls03 N: -0.001 m (0.003 m) E: 0.002 m (0.003 m) U: -0.007 m (0.009 m) CORS
ncel N: -0.007 m (0.003 m) E: 0.001 m (0.003 m) U: -0.014 m (0.009 m) CORS
ncga N: -0.002 m (0.003 m) E: 0.003 m (0.003 m) U: 0.005 m (0.009 m) CORS
vagp N: 0.003 m (0.003 m) E: 0.004 m (0.003 m) U: -0.011 m (0.009 m) CORS
“Estimated” means: computed in the adjustment
“Preliminary” means: from the input adjustment.
The 4 Adjustments must be done in sequence.
But, keep track of inputs and outputs so you don’t get confused.

## Slide 26: network-final-horizontal-free.txt
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
UNCONSTRAINED MARKS
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: 863f (0008; 863 8610 F)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.13040785
X: 1206288.555 m 0.003 m 1206287.647 m 0.003 m
Y: -4959186.782 m 0.008 m -4959185.310 m 0.008 m
Z: 3812292.497 m 0.006 m 3812292.434 m 0.006 m
LAT: 36 56 33.74459 0.003 m 36 56 33.77504 0.003 m
E LON: 283 40 16.70089 0.003 m 283 40 16.67930 0.003 m
W LON: 76 19 43.29911 0.003 m 76 19 43.32070 0.003 m
EL HGT: -34.679 m 0.010 m -36.032 m 0.010 m
ORTHO HGT: 2.223 m 0.020 m (= EL HGT - -36.902 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4089341.273 m 1069848.930 m
EASTING (X) 381686.402 m 3693394.143 m
CONVERGENCE -0.79865833 deg 1.31781944 deg
POINT SCALE 0.99977245 0.99997271
COMBINED FACTOR 0.99977789 0.99997815
US NATIONAL GRID DESIGNATOR: 18SUF8168689341 (NAD 83)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

## Slide 27: network-final-horizontal-free.txt
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
CONSTRAINED MARKS
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: loy2 (0001; DF5272; LOYOLA 2 COOP CORS ARP)
CONSTRAIN: 3-D NORMAL
N36:45:50.43110 W076:14:16.06827 -23.440m NAD_83(2011) @ 2010.0000
0.24cm 0.25cm 0.68cm NEU SIGMAS
SHIFTS N: 0.002 m (0.003 m) E: 0.001 m (0.003 m) H: 0.001 m (0.009 m)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.14074740
X: 1216986.213 m 0.003 m 1216985.298 m 0.003 m
Y: -4968828.059 m 0.007 m -4968826.571 m 0.007 m
Z: 3796431.072 m 0.006 m 3796430.998 m 0.006 m
LAT: 36 45 50.43110 0.003 m 36 45 50.46147 0.003 m
E LON: 283 45 43.93173 0.003 m 283 45 43.91017 0.003 m
W LON: 76 14 16.06827 0.003 m 76 14 16.08983 0.003 m
EL HGT: -23.440 m 0.009 m -24.816 m 0.009 m
ORTHO HGT: 13.843 m 0.019 m (= EL HGT - -37.283 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4069407.907 m 1050214.001 m
EASTING (X) 389523.825 m 3701963.852 m
CONVERGENCE -0.74092222 deg 1.37298611 deg
POINT SCALE 0.99975036 1.00000048
COMBINED FACTOR 0.99975404 1.00000416
US NATIONAL GRID DESIGNATOR: 18SUF8952469408 (NAD 83)

## Slide 28: network-final-horizontal-free.cvecs
The COMPVECS (.cvecs) file compares the repeated vectors to each other prior to adjustment.
The first-observed vector becomes the basis for differencing with later-observed vectors.
In a perfect world these differences will be small.
  Tolerance is about 2 cm E, N, and 4 cm UP

## Slide 29: network-final-horizontal-free.cvecs
VECTOR RESIDUALS
-ID- -ID- ---SSN--- sR ses'n dX dY dZ dE dN dU dd
from -to- from -to- (m) (m) (m) (m) (m) (m) (m)
LOY2 LS03 0001 0003 s 0411A 23718.7575 7561.3817 2198.4673 24836.6238 2779.7614 -47.4844 24991.7428
s 0481A -0.0002 -0.0017 0.0016 -0.0006 0.0003 0.0022 -0.0006
s 0541A -0.0015 0.0027 -0.0026 -0.0008 -0.0003 -0.0039 -0.0008
s 0551A -0.0007 0.0004 -0.0013 -0.0006 -0.0007 -0.0012 -0.0007
s 0631A -0.0010 0.0018 -0.0019 -0.0005 -0.0003 -0.0027 -0.0006
LOY2 NCGA 0001 0004 s 0411A -36997.0520 -31161.4984 -29144.2104 -43348.0145 -36195.2259 -247.1819 56473.0541
s 0481A -0.0008 -0.0009 0.0010 -0.0010 0.0004 0.0011 0.0005
s 0541A 0.0002 -0.0031 0.0023 -0.0005 0.0000 0.0038 0.0004
s 0551A 0.0007 -0.0032 0.0008 -0.0001 -0.0013 0.0031 0.0009
s 0631A -0.0009 -0.0028 0.0003 -0.0015 -0.0013 0.0022 0.0020
LOY2 VAGP 0001 0005 s 0411A -30253.2212 25968.9498 42949.2353 -23206.8689 53811.2526 -266.2611 58602.7351
s 0481A -0.0007 0.0015 -0.0014 -0.0003 -0.0001 -0.0021 0.0000
s 0541A -0.0015 0.0026 -0.0033 -0.0008 -0.0009 -0.0043 -0.0005
s 0551A -0.0002 0.0003 -0.0015 -0.0001 -0.0010 -0.0012 -0.0009
s 0631A 0.0005 0.0001 -0.0015 0.0005 -0.0012 -0.0009 -0.0013
LOY2 NCEL 0001 0006 s 0411A 4870.9425 -27561.2924 -37682.1613 -1825.5275 -46903.4264 -179.5672 46939.2821
s 0481A -0.0002 -0.0042 0.0027 -0.0012 -0.0003 0.0048 0.0003
s 0541A -0.0011 0.0006 -0.0012 -0.0009 -0.0005 -0.0014 0.0005
s 0551A 0.0001 -0.0016 0.0008 -0.0003 -0.0003 0.0017 0.0003
s 0631A -0.0009 -0.0021 0.0015 -0.0014 0.0001 0.0024 -0.0001
LOY2 ASUB 0001 0007 s 0411A -471536.4062 -129735.1630 -48477.8645 -488862.3247 -47116.8405 -17931.2328 491454.8791
s 0481A -0.0012 -0.0026 0.0031 -0.0018 0.0011 0.0036 0.0015
s 0541A -0.0029 0.0057 -0.0046 -0.0015 0.0000 -0.0077 0.0017
s 0551A 0.0009 0.0058 -0.0031 0.0023 0.0008 -0.0062 -0.0021
s 0631A 0.0002 -0.0033 -0.0006 -0.0006 -0.0024 0.0022 0.0007
OPUS vectors
hubbed from LOY2

## Slide 30: network-final-horizontal-free.cvecs
VECTOR RESIDUALS
-ID- -ID- ---SSN--- sR ses'n dX dY dZ dE dN dU dd
from -to- from -to- (m) (m) (m) (m) (m) (m) (m)
LOY2 863F 0001 0008 s 0411A -10697.6582 9641.2750 15861.4277 -8096.9540 19834.7186 -47.3068 21423.7943
s 0481A -0.0013 -0.0019 0.0043 -0.0017 0.0025 0.0038 0.0030
s 0541A 0.0008 -0.0033 0.0032 -0.0000 0.0005 0.0046 0.0005
LOY2 BRMR 0001 0009 s 0411A -6836.0438 4546.1962 8048.5663 -5558.2835 10063.9838 -23.0010 11496.9045
s 0481A -0.0033 0.0051 -0.0006 -0.0020 0.0030 -0.0050 0.0036
s 0541A -0.0020 -0.0002 -0.0012 -0.0020 -0.0008 -0.0009 0.0003
LOY2 GP99 0001 0010 s 0411A -6915.7048 6710.0225 10878.4855 -5120.8989 13600.3098 -28.1104 14532.4747
s 0481A -0.0053 0.0024 0.0017 -0.0046 0.0035 -0.0019 0.0049
s 0541A -0.0008 -0.0066 0.0021 -0.0023 -0.0020 0.0062 -0.0011
LOY2 OU03 0001 0011 s 0411A -7653.7608 6535.1476 10886.0855 -5879.3679 13609.8239 -28.1470 14825.4870
s 0481A -0.0041 0.0078 -0.0034 -0.0021 0.0024 -0.0089 0.0031
s 0541A -0.0018 0.0007 -0.0011 -0.0016 -0.0002 -0.0015 0.0004
LOY2 OU18 0001 0012 s 0411A -8782.6622 6206.1853 10814.6131 -7054.1179 13522.0658 -30.0996 15251.4835
s 0481A -0.0002 0.0015 0.0029 0.0002 0.0032 0.0005 0.0028
s 0541A 0.0032 -0.0089 0.0066 0.0010 -0.0003 0.0115 -0.0008
LOY2 W416 0001 0013 s 0411A -4952.2331 12099.6361 17228.4481 -1931.6456 21540.9323 -47.0398 21627.4185
s 0481A -0.0009 -0.0067 0.0075 -0.0025 0.0022 0.0095 0.0024
s 0541A 0.0025 -0.0086 0.0027 0.0004 -0.0032 0.0088 -0.0032
LOY2 WLP2 0001 0014 s 0481A -1833.7012 -279.8615 236.6760 -1847.6353 287.9980 9.9556 1869.9727
s 0541A 0.0001 -0.0033 0.0012 -0.0007 -0.0010 0.0033 0.0005
s 0551A 0.0002 -0.0034 0.0007 -0.0006 -0.0014 0.0031 0.0004
s 0631A -0.0003 -0.0014 -0.0002 -0.0006 -0.0009 0.0009 0.0005
OPUS vectors
hubbed from LOY2

## Slide 31: network-final-horizontal-free.cvecs
VECTOR RESIDUALS
-ID- -ID- ---SSN--- sR ses'n dX dY dZ dE dN dU dd
from -to- from -to- (m) (m) (m) (m) (m) (m) (m)
863F WLP2 0008 0014 s 055AB 8863.9494 -9921.1303 -15624.7332 6267.9379 -19540.8171 -11.6323 20521.4696
s 063AB -0.0055 -0.0176 0.0074 -0.0095 -0.0036 0.0171 0.0005
BRMR WLP2 0009 0014 s 048AA 5002.3362 -4826.0476 -7811.8773 3717.0358 -9773.5854 14.2520 10456.5544
s 055AF -0.0129 0.0012 0.0057 -0.0122 0.0071 0.0000 -0.0110
s 063AE -0.0101 -0.0128 0.0195 -0.0128 0.0096 0.0197 -0.0135
GP99 WLP2 0010 0014 s 048AB 5081.9924 -6989.8908 -10641.7867 3281.2686 -13310.3746 6.9832 13708.8601
s 055AE 0.0057 -0.0008 0.0010 0.0053 -0.0005 0.0023 0.0017
OU03 WLP2 0011 0014 s 055AD 5820.0731 -6815.0107 -10649.3922 4040.9561 -13319.0771 5.8897 13918.5910
s 063AD 0.0090 -0.0228 0.0208 0.0033 0.0021 0.0319 -0.0010
OU18 WLP2 0012 0014 s 055AC 6948.9561 -6486.0332 -10577.9301 5217.4600 -13229.7882 6.1520 14221.4353
s 063AC -0.0170 -0.0086 0.0022 -0.0186 -0.0008 0.0048 -0.0060
W416 WLP2 0013 0014 s 055AA 3118.5384 -12379.5158 -16991.7470 88.8448 -21252.9772 -15.0007 21253.1682
s 063AA -0.0006 0.0153 -0.0110 0.0031 0.0002 -0.0186 -0.0002 - - - - - - - - - - - - - - - - - - - -
None EXCEED tolerance but several are close.
GVX vectors
origin at WLP2
Remember to look at each component
DX, DY, DZ DE, DN, DU

## Slide 32: network-final-horizontal-free.cvecs
- - - - - - - - - - - - - - - - - - - -
EAST Components
-1.7245 (mm) Residual Mean
4.6138 (mm) Residual Std Deviation (1 sigma)
Scale: * = ( 1) millimeters
-25.00-> -20.00 ( 0)
-20.00-> -15.00 ( 1) *
-15.00-> -10.00 ( 2) **
-10.00-> -5.00 ( 1) *
-5.00-> 0.00 ( 30) ******************************
0.00-> 5.00 ( 7) ******************************
5.00-> 10.00 ( 1) *******
10.00-> 15.00 ( 0) *
15.00-> 20.00 ( 0)
20.00-> 25.00 ( 0)
25.00-> 30.00 ( 0)
30.00-> 35.00 ( 0)
35.00-> 40.00 ( 0)
- - - - - - - - - - - - - - - - - - - -
NORTH Components
0.3250 (mm) Residual Mean
2.4386 (mm) Residual Std Deviation (1 sigma)
Scale: * = ( 1) millimeters
-25.00-> -20.00 ( 0)
-20.00-> -15.00 ( 0)
-15.00-> -10.00 ( 0)
-10.00-> -5.00 ( 0)
-5.00-> 0.00 ( 24) ************************
0.00-> 5.00 ( 16) ************************
5.00-> 10.00 ( 2) ****************
10.00-> 15.00 ( 0) **
15.00-> 20.00 ( 0)
20.00-> 25.00 ( 0)
25.00-> 30.00 ( 0)
30.00-> 35.00 ( 0)
35.00-> 40.00 ( 0)
- - - - - - - - - - - - - - - - - - - -
UP Components
2.0722 (mm) Residual Mean
8.2870 (mm) Residual Std Deviation (1 sigma)
Scale: * = ( 1) millimeters
-25.00-> -20.00 ( 0)
-20.00-> -15.00 ( 1) *
-15.00-> -10.00 ( 0)
-10.00-> -5.00 ( 3) ***
-5.00-> 0.00 ( 12) ************
0.00-> 5.00 ( 19) ************
5.00-> 10.00 ( 3) *******************
10.00-> 15.00 ( 1) ***
15.00-> 20.00 ( 2) *
20.00-> 25.00 ( 0) **
25.00-> 30.00 ( 0)
30.00-> 35.00 ( 1)
35.00-> 40.00 ( 0) *
These are approximate histograms.

## Slide 33: network-final-horizontal-free.preplt2
The PREPLT2 (.preplt2) file compiles how much each vector was adjusted within the least-squares adjustment: (V = Computed – Observed)
These are extracted and compiled from the detailed (.sum) file.
0NORMALIZED RESIDUALS
COMPUTED OBSERVED V=C-O SDV V/SDV MDE RN FROM STATION
SEC METER 3-SIGMA TO STATION(S)
SESSION ID
1 LA 36 53 11.86975N 36 53 11.86975N 0.00000 0.000 0.00 0.00 0.0000 0.00 ( 0011) ODU 3
2 LO 76 18 13.50342W 76 18 13.50342W 0.00000 0.000 0.00 0.00 0.0000 0.00 ( 0011) ODU 3
3 EH -34.294 -34.294 0.000 0.00 0.00 0.0000 0.00 ( 0011) ODU 3
4 DX 10697.6581 10697.6582 -0.0001 0.0010 -0.0659 0.0040 ( 0008) 863 8610 F
5 DY -9641.2766 -9641.2750 -0.0016 0.0028 -0.3191 0.0068 ( 0001) LOYOLA 2 COOP CORS ARP
6 DZ -15861.4247 -15861.4277 0.0030 0.0021 0.7987 0.0054 0411A
DN -19830.9123 -19830.9138 0.0015 0.0012
DE 8106.3979 8106.3984 -0.0005 0.0010 Vector 1 Solution 1
DL 0.0016 0.0016 Project ID = OPUSProjects
DU 11.2365 11.2335 0.0030 0.0046
network-final-horizontal-free.sum file

## Slide 34: network-final-horizontal-free.preplt2
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
4 0.0015 -0.0005 0.0030 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
7 0.0012 -0.0010 -0.0031 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
10 0.0008 -0.0026 0.0031 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
13 0.0010 -0.0009 -0.0027 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
16 0.0014 0.0008 0.0033 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
19 -0.0001 -0.0008 0.0099 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
22 -0.0002 -0.0003 -0.0016 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
25 -0.0002 -0.0005 -0.0012 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
28 -0.0002 -0.0008 0.0015 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
31 -0.0005 -0.0006 0.0020 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
34 -0.0007 -0.0001 -0.0017 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
37 -0.0010 0.0012 -0.0008 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
40 -0.0017 0.0010 0.0019 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
43 -0.0027 0.0020 0.0049 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
46 -0.0014 0.0012 0.0062 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
49 -0.0018 0.0006 0.0028 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
52 -0.0023 0.0017 0.0003 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
55 -0.0013 -0.0005 0.0010 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
58 -0.0013 0.0013 -0.0053 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
61 -0.0005 0.0001 -0.0034 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
64 0.0001 0.0004 -0.0033 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
67 -0.0008 0.0004 0.0009 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
70 -0.0005 0.0002 0.0005 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
73 0.0010 -0.0005 -0.0016 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
76 0.0020 0.0010 -0.0021 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
79 0.0029 -0.0003 -0.0032 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
82 0.0012 0.0006 -0.0011 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
85 0.0018 -0.0002 -0.0081 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
88 0.0031 -0.0012 0.0011 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
91 -0.0003 0.0002 -0.0023 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
network-final-horizontal-free.preplt2 file
1 of 2

## Slide 35: network-final-horizontal-free.preplt2
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
94 -0.0002 0.0014 0.0061 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
97 0.0001 0.0003 0.0028 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
100 0.0003 0.0002 0.0029 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
103 -0.0005 -0.0001 -0.0018 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
106 0.0002 0.0007 0.0026 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
109 0.0002 0.0001 -0.0021 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
112 -0.0010 -0.0023 0.0047 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
115 0.0005 0.0001 0.0000 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
118 0.0001 -0.0005 -0.0002 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
121 0.0009 -0.0005 -0.0011 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
124 0.0003 0.0000 -0.0005 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
127 -0.0004 0.0001 0.0001 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
130 0.0022 0.0001 -0.0039 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
133 0.0001 0.0000 0.0015 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
136 -0.0003 0.0006 -0.0008 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
139 0.0008 0.0009 -0.0002 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
142 0.0005 -0.0006 -0.0008 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
145 0.0147 -0.0033 0.0028 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
148 0.0138 -0.0104 0.0148 13708.8759 ( 0014) WLP2 ( 0010) GPS099
151 0.0074 0.0023 0.0216 21253.1755 ( 0014) WLP2 ( 0013) W 416
154 0.0167 -0.0059 0.0028 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
157 0.0115 -0.0028 -0.0096 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
160 0.0087 0.0132 0.0179 13918.5955 ( 0014) WLP2 ( 0011) ODU 3
163 0.0142 -0.0157 0.0125 13708.8759 ( 0014) WLP2 ( 0010) GPS099
166 0.0076 0.0090 0.0028 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
169 0.0072 -0.0007 0.0402 21253.1755 ( 0014) WLP2 ( 0013) W 416
172 0.0202 0.0036 -0.0143 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
175 0.0124 0.0158 -0.0144 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
178 0.0066 0.0099 -0.0140 13918.5955 ( 0014) WLP2 ( 0011) ODU 3
181 0.0051 0.0096 -0.0169 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
None EXCEED tolerance but several are close.
network-final-horizontal-free.preplt2 file
2 of 2

## Slide 36: network-final-horizontal-free.sum
The Adjustment Summary (.sum) file contains the detailed results of the least-squares adjustment.
The .sum file has several “sections”.
Let’s look at them top-to-bottom.

## Slide 37: network-final-horizontal-free.sum
1 NATIONAL GEODETIC SURVEY
PROGRAM ADJUST ADJUSTMENT PROGRAM PAGE 1
VERSION 6.4.3
BLUE BOOK FILE = Results/network-final.bfile
ADJUSTMENT FILE = adjust.afile
GPS FILE = gfile.new
OUTPUT FILE = adjust.sum
OUTPUT BLUE BOOK FILE = adjust.bfile
0SYSTEM TIME IS Tue Aug 22 11:56:56 2023
0******************************** A-FILE CONTENTS ********************************
** Created by OPUS-Projects for rmetpjfy at 2023-08-22T15:56:48Z.
** This is for a horizontal free adjustment.
** Coordinates are NAD 83(2011) at epoch 2010.0000.
** Coordinate standard deviations are in centimeters.
** Constraint weight is NORMAL.
** loy2 = 0001 = DF5272 = CORS = LOYOLA 2 COOP CORS ARP
CC 0001 0.24 0.25 0.68 36455043110N076141606827W -23440E
II109999999
DD3
MM3YYN Y
PP22
NLY
VS 1.734 1.576 Trimble RTK
VS 0.446 0.259 OPUSProjects
0********************************* END OF A-FILE *********************************
Constraints listing (A-FILE)
Input / Output filename listing

## Slide 38: network-final-horizontal-free.sum
***************** ADJUSTMENT FILE OPTIONS **********
ELLIPSOID SEMI-MAJOR AXIS = 6378137.000 METERS
ECCENTRICITY SQUARED = 0.006694380022903416
DEFAULT ORTHOMETRIC HEIGHT = 0.000 METERS
DEFAULT GEOID HEIGHT = 0.000 METERS
ADJUST ORTHOMETRIC HEIGHTS
SCALE SIGMAS BY A-POSTERIORI SIGMA OF UNIT WEIGHT
ABORT IF SINGULARITIES
UPDATE *80* RECORDS INTO NEW BBOOK FILENAME--adjust.bfile
DO NOT UPDATE OUTPUT B-BOOK WITH CONSTRAINED VALUES FROM A-FILE
CREATE ADJUSTED POSITIONS FILE WITH FILENAME--ADJPOS
DO NOT UPDATE BLUE BOOK AND ADJUSTMENT FILE AT THE END OF EACH ITERATION
COMPUTE A 3-DIMENSIONAL ADJUSTMENT
COMPUTE NO MORE THAN 10 ITERATIONS
DO NOT DISPLAY STATISTICS IF SOLUTION SLOWLY CONVERGES
ABORT IF MISCLOSURE EXCEEDS 0.1E+21 SIGMA
PRINT WHEN MISCLOSURES EXCEED 0.1E+21 SIGMA
CONVERGE IF RMS SUM OF SHIFTS BELOW 0.003 METERS
COMPUTE NORMALIZED RESIDUALS AND INVERSE
COMPUTE NETWORK AND LOCAL ACCURACIES
NETWORK AND LOCAL ACCURACIES WILL BE SCALED
ECHO LARGE BLUE BOOK MISCLOSURES ONLY
ECHO GPS DATA TRANSFER FILE
ECHO LARGE G-FORMAT MISCLOSURES ONLY
DISPLAY CONSTRAINTS
DISPLAY ALL GPS RESIDUALS GREATER OR EQUAL TO 0.0 MM
DISPLAY ALL NON-GPS RESIDUALS/SD GREATER OR EQUAL TO 0.0 SIGMA
DISPLAY DIRECTION RESIDUALS
DISPLAY ANGLE RESIDUALS
DISPLAY ZENITH DISTANCE RESIDUALS
DISPLAY DISTANCE RESIDUALS
DISPLAY ASTRO-AZIMUTH RESIDUALS
DISPLAY GPS RESIDUALS
DISPLAY CONSTRAINED RESIDUALS
DISPLAY RESIDUALS GROUPED AROUND INTERSECTION STAS
DISPLAY POSITION SHIFTS
DISPLAY POSITION GOOGE NUMBERS
GPS SESSION COVARIANCE MATRICES INPUT IN THE G-FILE WILL BE SCALED AS FOLLOWS:
PROJECT HORIZONTAL UP
Trimble RTK 1.734 1.576
OPUSProjects 0.446 0.259
Adjustment File Options
Note the scale factors for the GVX and OPUS vectors.

## Slide 39: network-final-horizontal-free.sum
0*** JOB STATISTICS ***
0A.) BLUE-BOOK STATISTICS
NO. *80* CONTROL RECORDS 13
NO. *85* DEFLECTION RECORDS 0
NO. *86* ELEVATION RECORDS 13
NO. DIRECTIONS 0
NO. ANGLES 0
NO. GPS VECTORS 60
NO. DOPPLER OBS. 0
NO. ZENITH DISTANCES 0
NO. DISTANCES 0
NO. AZIMUTHS 0
B.) NO. CONSTRAINTS 3
C.) NO. ACCURACIES 0
D.) NO. REJECTED OBS. 0
Job Statistics
47 OPUS Vectors + 13 GVX Vectors = 60 GPS vectors

## Slide 40: network-final-horizontal-free.sum
0NORMALIZED RESIDUALS
COMPUTED OBSERVED V=C-O SDV V/SDV MDE RN FROM STATION
SEC METER 3-SIGMA TO STATION(S)
SESSION ID
1 LA 36 45 50.43110N 36 45 50.43110N 0.00000 0.000 0.00 0.00 0.0000 0.00 ( 0001) LOYOLA 2 COOP CORS ARP
2 LO 76 14 16.06827W 76 14 16.06827W 0.00000 0.000 0.00 0.00 0.0000 0.00 ( 0001) LOYOLA 2 COOP CORS ARP
3 EH -23.440 -23.440 0.000 0.00 0.00 0.0000 0.00 ( 0001) LOYOLA 2 COOP CORS ARP
4 DX 10697.6581 10697.6582 -0.0001 0.0010 -0.0659 0.0040 ( 0008) 863 8610 F
5 DY -9641.2766 -9641.2750 -0.0016 0.0028 -0.3191 0.0068 ( 0001) LOYOLA 2 COOP CORS ARP
6 DZ -15861.4247 -15861.4277 0.0030 0.0021 0.7987 0.0054 0411A
DN -19830.9123 -19830.9138 0.0015 0.0012
DE 8106.3979 8106.3984 -0.0005 0.0010 Vector 1 Solution 1
DL 0.0016 0.0016 Project ID = OPUSProjects
DU 11.2366 11.2335 0.0030 0.0046
7 DX 6836.0421 6836.0438 -0.0017 0.0010 -0.9777 0.0037 ( 0009) BREADMAKER
8 DY -4546.1933 -4546.1962 0.0029 0.0027 0.5880 0.0065 ( 0001) LOYOLA 2 COOP CORS ARP
9 DZ -8048.5672 -8048.5663 -0.0009 0.0020 -0.2326 0.0050 0411A
DN -10062.1857 -10062.1870 0.0012 0.0012
DE 5561.5679 5561.5689 -0.0010 0.0010 Vector 2 Solution 1
DL 0.0016 0.0016 Project ID = OPUSProjects
DU 12.6135 12.6166 -0.0031 0.0045
10 DX 6915.7027 6915.7048 -0.0021 0.0009 -1.2681 0.0038 ( 0010) GPS099
11 DY -6710.0250 -6710.0225 -0.0025 0.0026 -0.5328 0.0062 ( 0001) LOYOLA 2 COOP CORS ARP
12 DZ -10878.4830 -10878.4855 0.0025 0.0020 0.6914 0.0050 0411A
DN -13598.7919 -13598.7927 0.0008 0.0011
DE 5124.9876 5124.9902 -0.0026 0.0009 Vector 3 Solution 1
DL 0.0027 0.0014 Project ID = OPUSProjects
DU 11.5140 11.5109 0.0031 0.0044
13 DX 7653.7592 7653.7608 -0.0016 0.0010 -0.8494 0.0039 ( 0011) ODU 3
14 DY -6535.1452 -6535.1476 0.0024 0.0027 0.4910 0.0066 ( 0001) LOYOLA 2 COOP CORS ARP
15 DZ -10886.0863 -10886.0855 -0.0008 0.0021 -0.2114 0.0052 0411A
DN -13607.8162 -13607.8172 0.0010 0.0012
DE 5884.0673 5884.0682 -0.0009 0.0010 Vector 4 Solution 1
DL 0.0014 0.0015 Project ID = OPUSProjects
Adjustment Details by Vector

## Slide 41: network-final-horizontal-free.sum
0RESIDUAL STATISTICS
OBSERVATION NUMBERS OF 20 GREATEST RESIDUALS (V)
171 170 173 176 150 165 153 182 162 179 156 160 163 158 147 152 175 148 166 20
OBSERVATION NUMBERS OF 20 GREATEST STANDARDIZED RESIDUALS (V/SDV)
171 182 160 170 43 163 150 165 156 162 20 60 46 175 21 153 173 113 86 94
OBSERVATION NUMBERS OF 20 GREATEST GPS DU COMPONENT RESIDUALS (V)
171 153 162 183 150 177 174 180 165 21 159 87 48 96 60 45 114 132 63 18
OBSERVATION NUMBERS OF 20 GREATEST GPS DL COMPONENT RESIDUALS (V)
165 174 177 156 150 162 147 180 159 168 183 153 171 90 45 81 54 12 114 78
TOTAL= 183 NO-CHECK= 3
MAX V= 3.0D-02 MAX V/SDV= 3.161
MIN V= -2.7D-02 MIN V/SDV= -2.140
MEAN V= 1.2D-03 MEAN V/SDV= 0.158
MAX V OBS # MIN V OBS #
DX 1.5D-02 160 -1.5D-02 163
DY 2.4D-02 173 -2.7D-02 170
DZ 3.0D-02 171 -6.1D-03 183
DN 2.0D-02 172 -2.7D-03 43
DE 1.6D-02 176 -1.6D-02 164
DL 2.1D-02 165 1.3D-04 135
DU 4.0D-02 171 -1.7D-02 183
N RMS MEAN ABS
CONTRIB. RESIDUAL RESIDUAL
NORTH 60 0.006 0.003 (METERS)
EAST 60 0.004 0.002 (METERS)
UP 60 0.008 0.005 (METERS)
0DEGREES OF FREEDOM = 144
VARIANCE SUM = 260.4
STD.DEV.OF UNIT WEIGHT = 1.345
VARIANCE OF UNIT WEIGHT = 1.81
MINUTES TO LIST RESIDUALS 0.0
Residual Statistics Section
Max and Min listed by component and Observation Number
(in Scientific Notation!)
Listed by Observation Number
Std Dev of Unit Weight ~ ~ ~ 1 ?

## Slide 42: network-final-horizontal-free.sum
0ADJUSTED POSITIONS
SSN NAME LATITUDE LONGITUDE ORTHO. HT. G. HT. E. HT.
0 1 0008 863 8610 F 36 56 33.74459N 76 19 43.29911W 2.223 -36.902 -34.679
SHIFTS (M.) 0.001S 0.007E 0.019 AZ= 0 H= 0.007 T= 0.020
SCALED SIGMAS (M.) 0.003 0.003 0.010
GOOGES 1.0D+00 1.0D+00 1.0D+00
X = 1206288.5550 Y = -4959186.7824 Z = 3812292.4967
0 2 0009 BREADMAKER 36 51 16.85008N 76 18 0.44323W 1.027 -37.081 -36.054
SHIFTS (M.) 0.001S 0.007E 0.004 AZ=100 H= 0.007 T= 0.008
SCALED SIGMAS (M.) 0.003 0.003 0.010
GOOGES 9.9D-01 9.9D-01 9.8D-01
X = 1210150.1710 Y = -4964281.8657 Z = 3804479.6392
0 3 0010 GPS099 36 53 11.57699N 76 17 42.87281W 2.097 -37.052 -34.955
SHIFTS (M.) 0.001S 0.006E 0.016 AZ=100 H= 0.006 T= 0.017
SCALED SIGMAS (M.) 0.003 0.003 0.010
GOOGES 9.8D-01 9.8D-01 9.7D-01
X = 1210070.5104 Y = -4962118.0339 Z = 3807309.5550
0 4 0011 ODU 3 36 53 11.86972N 76 18 13.50346W 2.724 -37.036 -34.312
SHIFTS (M.) 0.001N 0.004E -0.005 AZ= 0 H= 0.004 T= 0.006
SCALED SIGMAS (M.) 0.003 0.003 0.010
GOOGES 9.7D-01 9.7D-01 9.8D-01
X = 1209332.4539 Y = -4962292.9138 Z = 3807317.1583
0 5 0012 ODU 18 36 53 8.99403N 76 19 0.94231W 1.747 -37.015 -35.268
SHIFTS (M.) 0.001S 0.006E 0.020 AZ= 0 H= 0.006 T= 0.021
SCALED SIGMAS (M.) 0.003 0.003 0.010
GOOGES 9.7D-01 9.6D-01 9.7D-01
X = 1208203.5497 Y = -4962621.8721 Z = 3807245.6820
0 6 0013 W 416 36 57 29.21100N 76 15 34.14958W 3.288 -36.997 -33.709
SHIFTS (M.) 0.000S 0.007E 0.015 AZ= 0 H= 0.007 T= 0.017
SCALED SIGMAS (M.) 0.003 0.003 0.010
GOOGES 9.5D-01 9.1D-01 9.5D-01
Adjusted Positions Section

## Slide 43: network-final-horizontal-free.sum
NETWORK & LOCAL ACCURACIES (95% CONFIDENCE LEVEL)
COMPUTED USING A POSTERIORI STANDARD DEVIATION OF UNIT WEIGHT
NETWORK ACCURACIES (CENTIMETERS)
ISN SSN STATION DESIGNATION HORIZ UP
1 0008 863 8610 F 0.84 1.94 CM
2 0009 BREADMAKER 0.83 1.91 CM
3 0010 GPS099 0.84 1.93 CM
4 0011 ODU 3 0.84 1.95 CM
5 0012 ODU 18 0.84 1.96 CM
6 0013 W 416 0.84 1.95 CM
7 0014 WLP2 0.82 1.84 CM
8 0007 ASU-BOONE CORS ARP 0.83 1.83 CM
9 0001 LOYOLA 2 COOP CORS ARP 0.81 1.79 CM
10 0003 LOYOLA LS03 CORS ARP 0.81 1.83 CM
11 0006 ELIZABETH CITY CORS ARP 0.81 1.83 CM
12 0004 GATESVILLE CORS ARP 0.82 1.83 CM
13 0005 VA GLOUCESTER PT CORS ARP 0.81 1.83 CM
LOCAL ACCURACIES (CENTIMETERS) AND DISTANCE (KILOMETERS)
ISN SSN STATION DESIGNATION
FROM 1 0008 863 8610 F HORIZ UP DISTANCE
TO 5 0012 ODU 18 0.29 0.98 CM 6.40 KM
TO 6 0013 W 416 0.30 0.95 CM 6.40 KM
TO 4 0011 ODU 3 0.28 0.95 CM 6.61 KM
TO 3 0010 GPS099 0.28 0.92 CM 6.91 KM
TO 2 0009 BREADMAKER 0.27 0.87 CM 10.10 KM
TO 7 0014 WLP2 0.23 0.74 CM 20.52 KM
FROM 2 0009 BREADMAKER HORIZ UP DISTANCE
TO 3 0010 GPS099 0.27 0.85 CM 3.56 KM
TO 4 0011 ODU 3 0.27 0.90 CM 3.56 KM
TO 5 0012 ODU 18 0.28 0.92 CM 3.77 KM
TO 7 0014 WLP2 0.21 0.64 CM 10.46 KM
TO 6 0013 W 416 0.29 0.90 CM 12.04 KM
HAVE A NICE DAY!
Network & Local Accuracies Section

## Slide 44: Horizontal Constrained Adjustment
Before constraining any Horizontal (lat/lon/ellht) components, we should verify that the free-adjusted positions align closely with the potential constraints (the published values). If they do, we can trust them as constraints.
But how do we do that easily?
  The plots on the individual Mark Pages
    shows published positions in black.
  The network-final-horizontal-free.txt file
    shows “estimated – published” (see slides 25 & 46)

## Slide 45: Horizontal Constrained Adjustment
Verify potential constraints – passive marks.
BRMR (DG9069)

## Slide 46: Horizontal Constrained Adjustment
Verify potential constraints – passive marks.
OU03 (AJ4598)

## Slide 47: Horizontal Constrained Adjustment
Verify potential constraints – passive marks.
W416 (FX0049)
W416 has a benchmark height
W416 has only a hand held position – so it’s not constrainable

## Slide 48: Horizontal Constrained Adjustment
Verify potential constraints – CORS.
  could they be out-of-date?
Look at the “network-final-horizontal-free.txt”
  MARK ESTIMATED - PUBLISHED HORIZONTAL COORDINATE SHIFTS
  ---------------------------------------------------------------------------
  asub N: 0.002 m (0.003 m) E: 0.010 m (0.004 m) U: 0.014 m (0.009 m) CORS
  loy2 N: -0.000 m (0.003 m) E: 0.000 m (0.003 m) U: 0.000 m (0.009 m) CORS
  ls03 N: -0.001 m (0.003 m) E: 0.002 m (0.003 m) U: -0.007 m (0.009 m) CORS
  ncel N: -0.007 m (0.003 m) E: 0.001 m (0.003 m) U: -0.014 m (0.009 m) CORS
  ncga N: -0.002 m (0.003 m) E: 0.003 m (0.003 m) U: 0.005 m (0.009 m) CORS
  vagp N: 0.003 m (0.003 m) E: 0.004 m (0.003 m) U: -0.011 m (0.009 m) CORS
  Since there usually only a few CORS, I also suggest a manual comparison, just to be sure you understand and agree with the “network-final-horizontal-free.txt file”.

## Slide 49: Horizontal Constrained Adjustment
network-final-horizontal-free.txt
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
MARK: ls03 (0003; DL1900; LOYOLA LS03 CORS ARP)
REF FRAME: NAD_83(2011) @ 2010.00000000 ITRF2014 @ 2021.14161048
X: 1240704.971 m 0.003 m 1240704.058 m 0.003 m
Y: -4961266.678 m 0.007 m -4961265.183 m 0.007 m
Z: 3798629.540 m 0.006 m 3798629.465 m 0.006 m
LAT: 36 47 19.43641 0.003 m 36 47 19.46694 0.003 m
E LON: 284 02 25.67024 0.003 m 284 02 25.64913 0.003 m
W LON: 75 57 34.32976 0.003 m 75 57 34.35087 0.003 m
EL HGT: -22.016 m 0.009 m -23.400 m 0.009 m
ORTHO HGT: 15.903 m 0.021 m (= EL HGT - -37.919 GEOID18 HGT)
UTM COORDINATES STATE PLANE COORDINATES
UTM (Zone 18) SPC (4502 VA S)
NORTHING (Y) 4071865.517 m 1053588.584 m
EASTING (X) 414387.488 m 3726726.777 m
CONVERGENCE -0.57466944 deg 1.54186944 deg
POINT SCALE 0.99969030 0.99999607
COMBINED FACTOR 0.99969375 0.99999953
US NATIONAL GRID DESIGNATOR: 18SVF1438771866 (NAD 83)
+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
NGS Datasheet
National Geodetic Survey, Retrieval Date = AUGUST 22, 2023
DL1900 *CURRENT SURVEY CONTROL
DL1900 ______________________________________________________________________
DL1900* NAD 83(2011) POSITION- 36 47 19.43646(N) 075 57 34.32984(W) ADJUSTED
DL1900* NAD 83(2011) ELLIP HT- -22.009 (meters) (05/??/20) ADJUSTED
DL1900* NAD 83(2011) EPOCH - 2010.00
DL1900 ______________________________________________________________________
DL1900. The following values were computed from the NAD 83(2011) position.
DL1900
DL1900; North East Units Scale Factor Converg.
DL1900;SPC VA S - 1,053,588.585 3,726,726.775 MT 0.99999607 +1 32 30.7
DL1900;SPC VA S - 3,456,648.55 12,226,769.43 sFT 0.99999607 +1 32 30.7
DL1900;UTM 18 - 4,071,865.519 414,387.486 MT 0.99969030 -0 34 28.8
DL1900
DL1900! - Elev Factor x Scale Factor = Combined Factor
DL1900!SPC VA S - 1.00000345 x 0.99999607 = 0.99999952
DL1900!UTM 18 - 1.00000345 x 0.99969030 = 0.99969375
Adjusted – Published
Manual Coordinate Shift Comparison
Differences in State Plane Coordinates (SPC VA S)
Northing = -0.001 m
Easting = 0.002 m
Differences in Ellipsoid Height
= -0.007 m
network-final-horizontal-free.txt
ESTIMATED - PUBLISHED HORIZONTAL COORDINATE SHIFTS
LOY2
  N: -0.001 m (0.003 m)
  E: 0.002 m (0.003 m)
  U: -0.007 m (0.007 m)
Allowing for round-off, about the same shifts.
LS03 CORS Validation Check
1 National Geodetic Survey, Retrieval Date = AUGUST 22, 2023

## Slide 50: Horizontal Constrained Adjustment
Since we think the CORS can all be constrained and the published Passive Marks can be constrained, we can proceed with caution to the HORIZONTAL CONSTRAINED ADJUSTMENT.

## Slide 51: Horizontal Constrained Adjustment
Adjustment Setup
Note that OPUS has suggested the appropriate horizontal constraints. If you agree, click “Perform Adjustment”
What’s Constrainable?
(see slides 8-17)
NGS recommends not constraining ASUB - the distant CORS.
Make sure to un-constrain it.

## Slide 52: Horizontal Constrained Adjustment
EMAIL Notification – 7 attached files.

## Slide 53: Horizontal Constrained Adjustment
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: network-final-horizontal-constrained.sum
SOLUTION SOFTWARE: ADJUST(6.4.3)
SOLUTION DATE: 2023-08-22T14:40:18 UTC
STANDARD ERROR OF UNIT WEIGHT: 1.311
F STATISTIC TEST: PASS (1.05 < 1.52 F CRITICAL @ 99% CONFIDENCE)
TOTAL NUMBER OF VECTORS: 60
TOTAL NUMBER OF MARKS: 13
CONSTRAINED MARKS: 7 HORIZONTAL, 0 VERTICAL
brmr N36:51:16.85018 W076:18:00.44343 -36.039m NAD_83(2011) @ 2010.0000
brmr 0.27cm 0.22cm 0.24cm NEU SIGMAS
ou03 N36:53:11.86975 W076:18:13.50342 -34.294m NAD_83(2011) @ 2010.0000
ou03 0.24cm 0.22cm 0.42cm NEU SIGMAS
loy2 N36:45:50.43110 W076:14:16.06827 -23.440m NAD_83(2011) @ 2010.0000
loy2 0.24cm 0.25cm 0.68cm NEU SIGMAS
ls03 N36:47:19.43644 W075:57:34.32982 -22.009m NAD_83(2011) @ 2010.0000
ls03 0.22cm 0.33cm 0.85cm NEU SIGMAS
ncel N36:20:28.79080 W076:15:29.27391 -29.730m NAD_83(2011) @ 2010.0000
ncel 0.36cm 0.39cm 1.03cm NEU SIGMAS
ncga N36:26:12.65518 W076:43:16.51666 -20.469m NAD_83(2011) @ 2010.0000
ncga 0.22cm 0.36cm 0.84cm NEU SIGMAS
vagp N37:14:55.00829 W076:29:57.73103 -19.814m NAD_83(2011) @ 2010.0000
vagp 0.56cm 0.57cm 0.84cm NEU SIGMAS
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-03-04T23:59:30 GPS
STANDARD DEVIATION SCALARS: 2 SOURCES
1) Trimble RTK HORIZONTAL: 1.734 UP: 1.576
2) OPUSProjects HORIZONTAL: 0.446 UP: 0.259
SESSION PROCESSING INCLUDED
===========================
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
network-final-horizontal-constrained.txt
Check for:
Std error of Unit Wt ~ 1
F-Test = PASS
Scalars ~ 2? or less

## Slide 54: Horizontal Constrained Adjustment
INCLUDED SOLUTION RMS SOFTWARE RUN DATE
------------------------------------------------------------------------------
1) 2021-041 A 1.6 cm page5(2008.25) 2023-06-20T14:01 UTC
2) 2021-048 A 1.4 cm page5(2008.25) 2023-06-20T14:01 UTC
3) 2021-054 A 1.5 cm page5(2008.25) 2023-06-20T14:01 UTC
4) 2021-055 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
5) 2021-063 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
BASELINE LENGTH RMS OBS OMITTED FIXED IN SOLUTION(S)
------------------------------------------------------------------------------
wlp2-loy2 1.870 km 0.7 cm 67371 12.0% 99.7% 2, 3, 4, 5
brmr-loy2 11.497 km 1.2 cm 17107 6.7% 100.0% 1, 2, 3
gp99-loy2 14.532 km 1.8 cm 15572 12.0% 98.8% 1, 2, 3
ou03-loy2 14.825 km 1.4 cm 14638 13.0% 98.9% 1, 2, 3
ou18-loy2 15.251 km 2.1 cm 12668 31.8% 98.2% 1, 2, 3
863f-loy2 21.424 km 1.5 cm 14736 16.7% 97.2% 1, 2, 3
w416-loy2 21.627 km 2.0 cm 12919 23.0% 97.3% 1, 2, 3
ls03-loy2 24.992 km 1.5 cm 90411 5.1% 99.1% 1, 2, 3,...
ncel-loy2 46.939 km 1.4 cm 90104 5.2% 97.9% 1, 2, 3,...
ncga-loy2 56.473 km 1.6 cm 88481 6.9% 95.2% 1, 2, 3,...
vagp-loy2 58.603 km 1.5 cm 91352 3.3% 97.6% 1, 2, 3,...
asub-loy2 491.455 km 1.4 cm 88254 2.9% 83.3% 1, 2, 3,...
UPLOADED VECTORS INCLUDED
===========================
BASELINE USED LENGTH EPOCHS(min) EPOCHS(max) PDOP(min) PDOP(max)
ou18-wlp2 2 14.221 km 301 302 2.76 2.91
w416-wlp2 2 21.253 km 301 305 1.49 1.71
863f-wlp2 2 20.521 km 301 302 1.52 1.75
ou03-wlp2 2 13.919 km 301 304 1.69 2.62
gp99-wlp2 2 13.709 km 192 313 1.52 1.58
brmr-wlp2 3 10.457 km 187 406 1.50 1.77
network-final-horizontal-constrained.txt
Check for:
RMS about 1 to 2 cm
% Omitted
% Fixed

## Slide 55: Horizontal Constrained Adjustment
MARK ESTIMATED - HORIZONTAL-FREE ADJUSTMENT COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.001 m (0.002 m) E: -0.002 m (0.002 m) H: 0.012 m (0.004 m)
asub N: 0.002 m (0.001 m) E: -0.001 m (0.002 m) H: 0.012 m (0.003 m)
brmr N: 0.002 m (0.001 m) E: -0.002 m (0.002 m) H: 0.013 m (0.003 m)
gp99 N: 0.001 m (0.002 m) E: -0.002 m (0.002 m) H: 0.012 m (0.004 m)
loy2 N: 0.002 m (0.001 m) E: -0.002 m (0.001 m) H: 0.012 m (0.003 m)
ls03 N: 0.002 m (0.001 m) E: -0.002 m (0.001 m) H: 0.012 m (0.003 m)
ncel N: 0.002 m (0.001 m) E: -0.002 m (0.001 m) H: 0.012 m (0.003 m)
ncga N: 0.002 m (0.001 m) E: -0.002 m (0.001 m) H: 0.012 m (0.003 m)
ou03 N: 0.001 m (0.001 m) E: -0.001 m (0.002 m) H: 0.014 m (0.004 m)
ou18 N: 0.002 m (0.002 m) E: -0.001 m (0.002 m) H: 0.012 m (0.005 m)
vagp N: 0.002 m (0.001 m) E: -0.001 m (0.001 m) H: 0.012 m (0.003 m)
w416 N: 0.002 m (0.002 m) E: -0.002 m (0.002 m) H: 0.012 m (0.004 m)
wlp2 N: 0.002 m (0.001 m) E: -0.002 m (0.001 m) H: 0.012 m (0.003 m)
MARK ESTIMATED - PUBLISHED HORIZONTAL COORDINATE SHIFTS
------------------------------------------------------------------------------
asub N: 0.003 m (0.001 m) E: 0.009 m (0.002 m) U: 0.026 m (0.003 m) CORS
brmr N: -0.002 m (0.001 m) E: 0.003 m (0.002 m) U: -0.002 m (0.003 m) OPUS
loy2 N: 0.002 m (0.001 m) E: -0.002 m (0.001 m) U: 0.012 m (0.003 m) CORS
ls03 N: 0.001 m (0.001 m) E: -0.000 m (0.001 m) U: 0.005 m (0.003 m) CORS
ncel N: -0.005 m (0.001 m) E: -0.001 m (0.001 m) U: -0.002 m (0.003 m) CORS
ncga N: -0.000 m (0.001 m) E: 0.002 m (0.001 m) U: 0.017 m (0.003 m) CORS
ou03 N: 0.000 m (0.001 m) E: -0.002 m (0.002 m) U: -0.004 m (0.004 m) OPUS
vagp N: 0.004 m (0.001 m) E: 0.002 m (0.001 m) U: 0.001 m (0.003 m) CORS
MARK CONSTRAINT RATIOS
------------------------------------------------------------------------------
brmr N: 0.597 E: 1.288 U: 0.841 2D: 1.420 3D: 1.650 OPUS
loy2 N: 0.649 E: 0.615 U: 1.708 2D: 0.893 3D: 1.928 CORS
ls03 N: 0.277 E: 0.059 U: 0.592 2D: 0.283 3D: 0.656 CORS
ncel N: 1.512 E: 0.222 U: 0.216 2D: 1.528 3D: 1.543 CORS
ncga N: 0.054 E: 0.421 U: 2.004 2D: 0.424 3D: 2.048 CORS
ou03 N: 0.146 E: 1.046 U: 1.024 2D: 1.056 3D: 1.471 OPUS
vagp N: 0.796 E: 0.384 U: 0.128 2D: 0.884 3D: 0.893 CORS
network-final-horizontal-constrained.txt
Check for:
Small shifts
Constraint Ratios less than 3.5

## Slide 56: Horizontal Constrained Adjustment
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
22 0.0015 -0.0005 0.0025 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
25 0.0012 -0.0008 -0.0050 11496.9031 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
28 0.0008 -0.0026 0.0026 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
31 0.0010 -0.0011 -0.0048 14825.4857 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
34 0.0014 0.0008 0.0028 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
37 -0.0001 -0.0008 0.0094 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
40 -0.0002 -0.0004 -0.0018 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
43 -0.0002 -0.0005 -0.0014 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
46 -0.0002 -0.0007 0.0013 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
49 -0.0005 -0.0006 0.0020 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
52 -0.0007 -0.0001 -0.0019 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
55 -0.0010 0.0012 -0.0013 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
58 -0.0018 0.0012 0.0000 11496.9031 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
61 -0.0027 0.0020 0.0044 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
64 -0.0014 0.0010 0.0040 14825.4857 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
67 -0.0018 0.0006 0.0023 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
70 -0.0023 0.0017 -0.0002 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
73 -0.0013 -0.0005 0.0007 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
76 -0.0013 0.0013 -0.0055 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
79 -0.0005 0.0001 -0.0036 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
82 0.0000 0.0004 -0.0036 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
85 -0.0009 0.0004 0.0009 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
88 -0.0005 0.0002 0.0002 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
91 0.0010 -0.0005 -0.0021 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
94 0.0020 0.0012 -0.0040 11496.9031 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
97 0.0029 -0.0003 -0.0037 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
100 0.0013 0.0005 -0.0033 14825.4857 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
network-final-horizontal-constrained.preplt2
Check for:
DN, DE, DU less than 2cm / 4 cm

## Slide 57: Horizontal Constrained Adjustment
103 0.0017 -0.0002 -0.0087 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
106 0.0031 -0.0012 0.0006 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
109 -0.0003 0.0002 -0.0026 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
112 -0.0002 0.0014 0.0059 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
115 0.0001 0.0003 0.0026 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
118 0.0002 0.0002 0.0027 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
121 -0.0005 0.0000 -0.0018 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
124 0.0002 0.0007 0.0024 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
127 0.0002 0.0001 -0.0024 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
130 -0.0010 -0.0024 0.0045 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
133 0.0005 0.0001 -0.0001 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
136 0.0001 -0.0005 -0.0005 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
139 0.0008 -0.0005 -0.0011 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
142 0.0003 0.0000 -0.0007 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
145 -0.0004 0.0002 -0.0002 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
148 0.0022 0.0001 -0.0041 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
151 0.0001 0.0000 0.0014 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
154 -0.0003 0.0006 -0.0011 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
157 0.0008 0.0010 -0.0002 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
160 0.0005 -0.0006 -0.0010 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
163 0.0147 -0.0035 0.0044 10456.5694 ( 0014) WLP2 ( 0009) BREADMAKER
166 0.0138 -0.0104 0.0150 13708.8759 ( 0014) WLP2 ( 0010) GPS099
169 0.0074 0.0023 0.0218 21253.1755 ( 0014) WLP2 ( 0013) W 416
172 0.0167 -0.0059 0.0030 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
175 0.0115 -0.0028 -0.0094 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
178 0.0087 0.0134 0.0197 13918.5954 ( 0014) WLP2 ( 0011) ODU 3
181 0.0142 -0.0157 0.0126 13708.8759 ( 0014) WLP2 ( 0010) GPS099
184 0.0076 0.0088 0.0044 10456.5694 ( 0014) WLP2 ( 0009) BREADMAKER
187 0.0072 -0.0007 0.0404 21253.1755 ( 0014) WLP2 ( 0013) W 416
190 0.0202 0.0036 -0.0141 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
193 0.0124 0.0158 -0.0142 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
196 0.0066 0.0100 -0.0122 13918.5954 ( 0014) WLP2 ( 0011) ODU 3
199 0.0051 0.0094 -0.0153 10456.5694 ( 0014) WLP2 ( 0009) BREADMAKER
network-final-horizontal-constrained.preplt2
Check for:
DN, DE, DU less than 2cm / 4 cm

## Slide 58: Horizontal Constrained Adjustment
BLUE BOOK FILE = network-final-horizontal-free.bfile
ADJUSTMENT FILE = adjust.afile
GPS FILE = network-final-horizontal-free.gfile
OUTPUT FILE = adjust.sum
OUTPUT BLUE BOOK FILE = adjust.bfile
0SYSTEM TIME IS Tue Aug 22 14:40:18 2023
0******************************** A-FILE CONTENTS ********************************
** Created by OPUS-Projects for rmetpjfy at 2023-08-22T18:39:21Z.
** This is for a horizontal constrained adjustment.
** Coordinates are NAD 83(2011) at epoch 2010.0000.
** Coordinate standard deviations are in centimeters.
** Constraint weight is NORMAL.
** ncel = 0006 = DL6896 = CORS = ELIZABETH CITY CORS ARP
CC 0006 0.36 0.39 1.03 36202879080N076152927391W -29730E
** vagp = 0005 = DJ5202 = CORS = VA GLOUCESTER PT CORS ARP
CC 0005 0.56 0.57 0.84 37145500829N076295773103W -19814E
** ls03 = 0003 = DL1900 = CORS = LOYOLA LS03 CORS ARP
CC 0003 0.22 0.33 0.85 36471943644N075573432982W -22009E
** ou03 = 0011 = AJ4598 = USER = ODU 3
CC 0011 0.24 0.22 0.42 36531186975N076181350342W -34294E
** ncga = 0004 = DL6898 = CORS = GATESVILLE CORS ARP
CC 0004 0.22 0.36 0.84 36261265518N076431651666W -20469E
** brmr = 0009 = DG9069 = USER = BREADMAKER
CC 0009 0.27 0.22 0.24 36511685018N076180044343W -36039E
** loy2 = 0001 = DF5272 = CORS = LOYOLA 2 COOP CORS ARP
CC 0001 0.24 0.25 0.68 36455043110N076141606827W -23440E
II109999999
DD3
MM3YYY Y
PP22
NLY
VS 1.734 1.576 Trimble RTK
VS 0.446 0.259 OPUSProjects
0********************************* END OF A-FILE *********************************
network-final-horizontal-constrained.sum
Check for:
Input / Output filenames
Constraints are listed as expected
VS Scalars

## Slide 59: Horizontal Constrained Adjustment
0RESIDUAL STATISTICS
MAX V OBS # MIN V OBS #
DX 1.5D-02 178 -1.5D-02 181
DY 2.4D-02 191 -2.7D-02 188
DZ 3.0D-02 189 -5.1D-03 201
DN 2.0D-02 190 -2.7D-03 61
DE 1.6D-02 194 -1.6D-02 182
DL 2.1D-02 183 1.2D-04 153
DU 4.0D-02 189 -1.5D-02 201
N VTPV RMS RN VTPV/RN MEAN ABS
VTPV RESIDUAL
DELTA X 60 70.3 1.08 48.13 1.46 0.002 (METERS)
DELTA Y 60 77.7 1.14 48.41 1.61 0.004 (METERS)
DELTA Z 60 113.7 1.38 48.27 2.36 0.004 (METERS)
DOPPLER X 0 0.0 0.00 0.00 0.00 0.000 (METERS)
DOPPLER Y 0 0.0 0.00 0.00 0.00 0.000 (METERS)
DOPPLER Z 0 0.0 0.00 0.00 0.00 0.000 (METERS)
DIRECTION 0 0.0 0.00 0.00 0.00 0.000 (SECONDS)
H ANGLE 0 0.0 0.00 0.00 0.00 0.000 (SECONDS)
ZEN DIST 0 0.0 0.00 0.00 0.00 0.000 (SECONDS)
DISTANCE 0 0.0 0.00 0.00 0.00 0.000 (METERS)
AZIMUTH 0 0.0 0.00 0.00 0.00 0.000 (SECONDS)
OTHER 21 16.5 0.89 17.19 0.96 0.002
TOTAL 201 278.2 1.18 162.00 1.72
N RMS MEAN ABS
CONTRIB. RESIDUAL RESIDUAL
NORTH 60 0.006 0.003 (METERS)
EAST 60 0.004 0.002 (METERS)
UP 60 0.008 0.005 (METERS)
0DEGREES OF FREEDOM = 162
VARIANCE SUM = 278.2
STD.DEV.OF UNIT WEIGHT = 1.311
VARIANCE OF UNIT WEIGHT = 1.72
network-final-horizontal-constrained.sum
Check for:
Max/Min (V) Residuals, less than 2 cm (hor) & 4 cm (ver)
Std Dev Unit Wt ~ 1

## Slide 60: Horizontal Constrained Adjustment
COMPARISON OF ADJUSTED AND CONSTRAINED COORDINATES AND HEIGHTS
ADJUSTED MINUS CONSTRAINED COORDINATE SHIFTS (METERS)
CURRENTLY NO VALUES ARE PRINTED FOR VERTICAL CONSTRAINTS
ISN SSN STATION DESIGNATION DELTA NORTH DELTA EAST DELTA HORIZ DELTA UP
2 0009 BREADMAKER -0.0015 0.0031 0.0035 -0.0017
4 0011 ODU 3 0.0004 -0.0025 0.0025 -0.0042
9 0001 LOYOLA 2 COOP CORS ARP 0.0015 -0.0016 0.0022 0.0116
10 0003 LOYOLA LS03 CORS ARP 0.0006 -0.0003 0.0007 0.0046
11 0006 ELIZABETH CITY CORS ARP -0.0055 -0.0008 0.0055 -0.0018
12 0004 GATESVILLE CORS ARP 0.0001 0.0016 0.0016 0.0167
13 0005 VA GLOUCESTER PT CORS ARP 0.0044 0.0022 0.0049 0.0006
NETWORK & LOCAL ACCURACIES (95% CONFIDENCE LEVEL) NETWORK ACCURACIES (CENTIMETERS)
ISN SSN STATION DESIGNATION HORIZ UP
1 0008 863 8610 F 0.39 0.86 CM
2 0009 BREADMAKER 0.37 0.52 CM
3 0010 GPS099 0.39 0.84 CM
4 0011 ODU 3 0.37 0.70 CM
5 0012 ODU 18 0.40 0.90 CM
6 0013 W 416 0.41 0.88 CM
7 0014 WLP2 0.35 0.63 CM
8 0007 ASU-BOONE CORS ARP 0.37 0.65 CM
9 0001 LOYOLA 2 COOP CORS ARP 0.35 0.61 CM
10 0003 LOYOLA LS03 CORS ARP 0.35 0.62 CM
11 0006 ELIZABETH CITY CORS ARP 0.35 0.63 CM
12 0004 GATESVILLE CORS ARP 0.35 0.63 CM
13 0005 VA GLOUCESTER PT CORS ARP 0.35 0.62 CM
LOCAL ACCURACIES (CENTIMETERS) AND DISTANCE (KILOMETERS)
ISN SSN STATION DESIGNATION
FROM 1 0008 863 8610 F HORIZ UP DISTANCE
TO 5 0012 ODU 18 0.29 0.95 CM 6.40 KM
TO 6 0013 W 416 0.29 0.93 CM 6.40 KM
TO 4 0011 ODU 3 0.27 0.87 CM 6.61 KM
TO 3 0010 GPS099 0.27 0.89 CM 6.91 KM
TO 2 0009 BREADMAKER 0.26 0.80 CM 10.10 KM
TO 7 0014 WLP2 0.22 0.72 CM 20.52 KM
network-final-horizontal-constrained.sum
Check for:
Small Shifts
Network and Local Accuracies

## Slide 61: Vertical Free Adjustment
If we are satisfied that the Horizontal Constrained Adjustment is acceptable, we can move on the VERTICAL FREE ADJUSTMENT.
The Vertical Free Adjustment:
  Only 1 HORZ (Lat/Lon) constraint
  Only 1 ORTHO Height constraint
  HORZ ands Ortho Constraints can be different marks
  This adjustment does not provide new information
    It merely sets up the starting point for the Vertical Constrained Adjustment.

## Slide 62: Vertical Free Adjustment
Adjustment Setup
There are 7 potentially-constrainable ORTHO heights – choose only one!
Let’s choose:
LOY2 as HOR-ONLY and
BRMR as VER-ONLY(1st Order Class 2)

## Slide 63: Vertical Free Adjustment
EMAIL Notification – 7 attached files.

## Slide 64: Vertical Free Adjustment
ATTACHMENT INVENTORY:
------------------------ ---------------------------------------------------
Processing Report (.txt) : network-final-vertical-free.txt
B-file (.bfile) : network-final-vertical-free.bfile
G-file (.gfile) : network-final-vertical-free.gfile
Preplt2 (.preplt2) : network-final-vertical-free.preplt2
Processing Log (.sum) : network-final-vertical-free.sum
Processing Report (.xml) : network-final-vertical-free.xml
Serfil (.serfil) : consolidated.serfil

## Slide 65: Vertical Free Adjustment
network-final-vertical-free.txt
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: network-final-vertical-free.sum
SOLUTION SOFTWARE: ADJUST(6.4.3)
SOLUTION DATE: 2023-08-23T08:31:30 UTC
STANDARD ERROR OF UNIT WEIGHT: 1.345
TOTAL NUMBER OF VECTORS: 60
TOTAL NUMBER OF MARKS: 13
CONSTRAINED MARKS: 1 HORIZONTAL, 1 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 NAD_83(2011) @ 2010.0000
loy2 0.24cm 0.25cm NE SIGMAS
brmr 1.036m ORTHO NAVD 88
brmr 0.50cm U SIGMA
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-03-04T23:59:30 GPS
STANDARD DEVIATION SCALARS: 2 SOURCES
1) Trimble RTK HORIZONTAL: 1.734 UP: 1.576
2) OPUSProjects HORIZONTAL: 0.446 UP: 0.259
SESSION PROCESSING INCLUDED
===========================
FREQUENCY: L1-ONLY TO ION-FREE [BY BASELINE LENGTH]
OBSERVATION INTERVAL: 30 s
ELEVATION CUTOFF: 15 deg
TROPO INTERVAL: 7200 s [PIECEWISE LINEAR PARAMETERIZATION]
DD CORRELATIONS: ON
Standard Error of Unit Weight is close to 1
Scalars are same as previous adjustments.

## Slide 66: Vertical Free Adjustment
network-final-vertical-free.txt
INCLUDED SOLUTION RMS SOFTWARE RUN DATE
------------------------------------------------------------------------------
1) 2021-041 A 1.6 cm page5(2008.25) 2023-06-20T14:01 UTC
2) 2021-048 A 1.4 cm page5(2008.25) 2023-06-20T14:01 UTC
3) 2021-054 A 1.5 cm page5(2008.25) 2023-06-20T14:01 UTC
4) 2021-055 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
5) 2021-063 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
BASELINE LENGTH RMS OBS OMITTED FIXED IN SOLUTION(S)
------------------------------------------------------------------------------
wlp2-loy2 1.870 km 0.7 cm 67371 12.0% 99.7% 2, 3, 4, 5
brmr-loy2 11.497 km 1.2 cm 17107 6.7% 100.0% 1, 2, 3
gp99-loy2 14.532 km 1.8 cm 15572 12.0% 98.8% 1, 2, 3
ou03-loy2 14.825 km 1.4 cm 14638 13.0% 98.9% 1, 2, 3
ou18-loy2 15.251 km 2.1 cm 12668 31.8% 98.2% 1, 2, 3
863f-loy2 21.424 km 1.5 cm 14736 16.7% 97.2% 1, 2, 3
w416-loy2 21.627 km 2.0 cm 12919 23.0% 97.3% 1, 2, 3
ls03-loy2 24.992 km 1.5 cm 90411 5.1% 99.1% 1, 2, 3,...
ncel-loy2 46.939 km 1.4 cm 90104 5.2% 97.9% 1, 2, 3,...
ncga-loy2 56.473 km 1.6 cm 88481 6.9% 95.2% 1, 2, 3,...
vagp-loy2 58.603 km 1.5 cm 91352 3.3% 97.6% 1, 2, 3,...
asub-loy2 491.455 km 1.4 cm 88254 2.9% 83.3% 1, 2, 3,...
UPLOADED VECTORS INCLUDED
===========================
BASELINE USED LENGTH EPOCHS(min) EPOCHS(max) PDOP(min) PDOP(max)
ou18-wlp2 2 14.221 km 301 302 2.76 2.91
w416-wlp2 2 21.253 km 301 305 1.49 1.71
863f-wlp2 2 20.521 km 301 302 1.52 1.75
ou03-wlp2 2 13.919 km 301 304 1.69 2.62
gp99-wlp2 2 13.709 km 192 313 1.52 1.58
brmr-wlp2 3 10.457 km 187 406 1.50 1.77
RMS similar as in previous adjustments.
Similar as in previous adjustments.

## Slide 67: Vertical Free Adjustment
network-final-vertical-free.txt
MARK ESTIMATED - HORIZONTAL-CONSTRAINED ADJUSTMENT COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: -0.002 m (0.003 m) E: 0.002 m (0.003 m) H: -0.003 m (0.008 m)
asub N: -0.001 m (0.003 m) E: 0.001 m (0.003 m) H: -0.003 m (0.008 m)
brmr N: -0.003 m (0.003 m) E: 0.005 m (0.003 m) H: -0.004 m (0.007 m)
gp99 N: -0.002 m (0.003 m) E: 0.002 m (0.003 m) H: -0.003 m (0.008 m)
loy2 N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.003 m (0.007 m)
ls03 N: -0.001 m (0.003 m) E: 0.001 m (0.003 m) H: -0.003 m (0.008 m)
ncel N: -0.007 m (0.003 m) E: 0.001 m (0.003 m) H: -0.002 m (0.008 m)
ncga N: -0.002 m (0.003 m) E: 0.003 m (0.003 m) H: -0.003 m (0.008 m)
ou03 N: -0.001 m (0.003 m) E: -0.001 m (0.003 m) H: -0.005 m (0.008 m)
ou18 N: -0.002 m (0.003 m) E: 0.002 m (0.003 m) H: -0.003 m (0.008 m)
vagp N: 0.003 m (0.003 m) E: 0.004 m (0.003 m) H: -0.003 m (0.008 m)
w416 N: -0.001 m (0.003 m) E: 0.002 m (0.003 m) H: -0.003 m (0.008 m)
wlp2 N: -0.002 m (0.003 m) E: 0.002 m (0.003 m) H: -0.002 m (0.007 m)
MARK ESTIMATED - PUBLISHED VERTICAL COORDINATE SHIFTS
------------------------------------------------------------------------------
asub: ORTHO HGT: 0.036 m (0.008 m) DF4365 GPS HEIGHTS: 2CM/5CM STANDARDS
brmr: ORTHO HGT: 0.000 m (0.007 m) DG9069 FGCS LEVELING IN NGSIDB
loy2: ORTHO HGT: 0.002 m (0.007 m) DF5272 GPS HEIGHTS: 2CM/5CM STANDARDS
ncel: ORTHO HGT: 0.000 m (0.008 m) DL6896 GPS HEIGHTS: 2CM/5CM STANDARDS
ncga: ORTHO HGT: 0.021 m (0.008 m) DL6898 GPS HEIGHTS: 2CM/5CM STANDARDS
ou03: ORTHO HGT: 0.033 m (0.008 m) AJ4598 GPS HEIGHTS: DECIMETER ACCURACY
w416: ORTHO HGT: 0.024 m (0.008 m) FX0049 FGCS LEVELING IN NGSIDB
Generally acceptable if less than 0.040 m.
Generally acceptable if less than 0.020 m.

## Slide 68: Vertical Free Adjustment
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
4 0.0015 -0.0005 0.0030 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
7 0.0012 -0.0010 -0.0031 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
10 0.0008 -0.0026 0.0031 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
13 0.0010 -0.0009 -0.0027 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
16 0.0014 0.0008 0.0033 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
19 -0.0001 -0.0008 0.0099 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
22 -0.0002 -0.0003 -0.0016 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
25 -0.0002 -0.0005 -0.0012 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
28 -0.0002 -0.0008 0.0015 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
31 -0.0005 -0.0006 0.0020 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
34 -0.0007 -0.0001 -0.0017 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
37 -0.0010 0.0012 -0.0008 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
40 -0.0017 0.0010 0.0019 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
43 -0.0027 0.0020 0.0049 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
46 -0.0014 0.0012 0.0062 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
49 -0.0018 0.0006 0.0028 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
52 -0.0023 0.0017 0.0003 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
55 -0.0013 -0.0005 0.0010 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
58 -0.0013 0.0013 -0.0053 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
61 -0.0005 0.0001 -0.0034 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
64 0.0001 0.0004 -0.0033 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
67 -0.0008 0.0004 0.0009 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
70 -0.0005 0.0002 0.0005 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
73 0.0010 -0.0005 -0.0016 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
76 0.0020 0.0010 -0.0021 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
79 0.0029 -0.0003 -0.0032 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
82 0.0012 0.0006 -0.0011 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
85 0.0018 -0.0002 -0.0081 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
88 0.0031 -0.0012 0.0011 21627.4185 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
91 -0.0003 0.0002 -0.0023 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
94 -0.0002 0.0014 0.0061 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
97 0.0001 0.0003 0.0028 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
network-final-vertical-free.preplt2

## Slide 69: Vertical Free Adjustment
network-final-vertical-free.preplt2
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
100 0.0003 0.0002 0.0029 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
103 -0.0005 -0.0001 -0.0018 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
106 0.0002 0.0007 0.0026 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
109 0.0002 0.0001 -0.0021 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
112 -0.0010 -0.0023 0.0047 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
115 0.0005 0.0001 0.0000 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
118 0.0001 -0.0005 -0.0002 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
121 0.0009 -0.0005 -0.0011 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
124 0.0003 0.0000 -0.0005 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
127 -0.0004 0.0001 0.0001 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
130 0.0022 0.0001 -0.0039 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
133 0.0001 0.0000 0.0015 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
136 -0.0003 0.0006 -0.0008 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
139 0.0008 0.0009 -0.0002 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
142 0.0005 -0.0006 -0.0008 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
145 0.0147 -0.0033 0.0028 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
148 0.0138 -0.0104 0.0148 13708.8759 ( 0014) WLP2 ( 0010) GPS099
151 0.0074 0.0023 0.0216 21253.1755 ( 0014) WLP2 ( 0013) W 416
154 0.0167 -0.0059 0.0028 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
157 0.0115 -0.0028 -0.0096 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
160 0.0087 0.0132 0.0179 13918.5955 ( 0014) WLP2 ( 0011) ODU 3
163 0.0142 -0.0157 0.0125 13708.8759 ( 0014) WLP2 ( 0010) GPS099
166 0.0076 0.0090 0.0028 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
169 0.0072 -0.0007 0.0402 21253.1755 ( 0014) WLP2 ( 0013) W 416
172 0.0202 0.0036 -0.0143 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
175 0.0124 0.0158 -0.0144 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
178 0.0066 0.0099 -0.0140 13918.5955 ( 0014) WLP2 ( 0011) ODU 3
181 0.0051 0.0096 -0.0169 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
Generally acceptable if less than 0.040 m.
Generally acceptable if less than 0.020 m.

## Slide 70: Vertical Free Adjustment
MAX V OBS # MIN V OBS #
DX 1.5D-02 160 -1.5D-02 163
DY 2.4D-02 173 -2.7D-02 170
DZ 3.0D-02 171 -6.1D-03 183
DN 2.0D-02 172 -2.7D-03 43
DE 1.6D-02 176 -1.6D-02 164
DL 2.1D-02 165 1.3D-04 135
DU 4.0D-02 171 -1.7D-02 183
0DEGREES OF FREEDOM = 144
VARIANCE SUM = 260.4
STD.DEV.OF UNIT WEIGHT = 1.345
VARIANCE OF UNIT WEIGHT = 1.81
network-final-vertical-free.sum
Standard Error of Unit Weight is close to 1

## Slide 71: Vertical Constrained Adjustment
If we are satisfied that the Vertical Free Adjustment is acceptable, we can move on the VERTICAL CONSTRAINED ADJUSTMENT.
The Vertical Constrained Adjustment:
  Only 1 HORZ (Lat/Lon) constraint
  Choose ORTHO Height constraints
  HORZ and Ortho Constraints can be different marks
  This adjustment aligns the orthometric heights to the NAVD88 datum.

## Slide 72: Vertical Constrained Adjustment
There are 7 potentially-constrainable ORTHO heights – choose only 6 – not ASUB the distant CORS.
Let’s choose:
LOY2 as 3-D, constrains its Lat/Lon and its Ortho Height
I accidentally chose to constrain OU03.
It does not have a constrainable height.

## Slide 73: Vertical Constrained Adjustment
EMAIL Notification – 7 attached files.

## Slide 74: Vertical Constrained Adjustment
ATTACHMENT INVENTORY:
------------------------ ---------------------------------------------------
Processing Report (.txt) : network-final-vertical-constrained.txt
B-file (.bfile) : network-final-vertical-constrained.bfile
G-file (.gfile) : network-final-vertical-constrained.gfile
Preplt2 (.preplt2) : network-final-vertical-constrained.preplt2
Processing Log (.sum) : network-final-vertical-constrained.sum
Processing Report (.xml) : network-final-vertical-constrained.xml
Serfil (.serfil) : consolidated.serfil

## Slide 75: Vertical Constrained Adjustment
SUBMITTED BY: dave.zenk
SOLUTION FILE NAME: network-final-vertical-constrained.sum
SOLUTION SOFTWARE: ADJUST(6.4.3)
SOLUTION DATE: 2023-08-23T09:24:38 UTC
STANDARD ERROR OF UNIT WEIGHT: 1.367
F STATISTIC TEST: PASS (1.03 < 1.54 F CRITICAL @ 99% CONFIDENCE)
TOTAL NUMBER OF VECTORS: 60
TOTAL NUMBER OF MARKS: 13
CONSTRAINED MARKS: 1 HORIZONTAL, 5 VERTICAL
loy2 N36:45:50.43110 W076:14:16.06827 13.85m ORTHO NAD_83(2011) @ 2010.0000
loy2 0.24cm 0.25cm 1.21cm NEU SIGMAS
brmr 1.036m ORTHO NAVD 88
brmr 0.50cm U SIGMA
ou03 2.7m ORTHO NAVD 88
ou03 1.08cm U SIGMA
w416 3.273m ORTHO NAVD 88
w416 0.30cm U SIGMA
ncel 7.60m ORTHO NAVD 88
ncel 1.43cm U SIGMA
ncga 15.65m ORTHO NAVD 88
ncga 1.31cm U SIGMA
START TIME: 2021-02-10T00:00:00 GPS
STOP TIME: 2021-03-04T23:59:30 GPS
STANDARD DEVIATION SCALARS: 2 SOURCES
1) Trimble RTK HORIZONTAL: 1.734 UP: 1.576
2) OPUSProjects HORIZONTAL: 0.446 UP: 0.259
network-final-vertical-constrained.txt
F STATISTIC TEST = PASS

## Slide 76: Vertical Constrained Adjustment
INCLUDED SOLUTION RMS SOFTWARE RUN DATE
------------------------------------------------------------------------------
1) 2021-041 A 1.6 cm page5(2008.25) 2023-06-20T14:01 UTC
2) 2021-048 A 1.4 cm page5(2008.25) 2023-06-20T14:01 UTC
3) 2021-054 A 1.5 cm page5(2008.25) 2023-06-20T14:01 UTC
4) 2021-055 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
5) 2021-063 A 1.4 cm page5(2008.25) 2023-06-16T10:18 UTC
BASELINE LENGTH RMS OBS OMITTED FIXED IN SOLUTION(S)
------------------------------------------------------------------------------
wlp2-loy2 1.870 km 0.7 cm 67371 12.0% 99.7% 2, 3, 4, 5
brmr-loy2 11.497 km 1.2 cm 17107 6.7% 100.0% 1, 2, 3
gp99-loy2 14.532 km 1.8 cm 15572 12.0% 98.8% 1, 2, 3
ou03-loy2 14.825 km 1.4 cm 14638 13.0% 98.9% 1, 2, 3
ou18-loy2 15.251 km 2.1 cm 12668 31.8% 98.2% 1, 2, 3
863f-loy2 21.424 km 1.5 cm 14736 16.7% 97.2% 1, 2, 3
w416-loy2 21.627 km 2.0 cm 12919 23.0% 97.3% 1, 2, 3
ls03-loy2 24.992 km 1.5 cm 90411 5.1% 99.1% 1, 2, 3,...
ncel-loy2 46.939 km 1.4 cm 90104 5.2% 97.9% 1, 2, 3,...
ncga-loy2 56.473 km 1.6 cm 88481 6.9% 95.2% 1, 2, 3,...
vagp-loy2 58.603 km 1.5 cm 91352 3.3% 97.6% 1, 2, 3,...
asub-loy2 491.455 km 1.4 cm 88254 2.9% 83.3% 1, 2, 3,...
UPLOADED VECTORS INCLUDED
===========================
BASELINE USED LENGTH EPOCHS(min) EPOCHS(max) PDOP(min) PDOP(max)
ou18-wlp2 2 14.221 km 301 302 2.76 2.91
w416-wlp2 2 21.253 km 301 305 1.49 1.71
863f-wlp2 2 20.521 km 301 302 1.52 1.75
ou03-wlp2 2 13.919 km 301 304 1.69 2.62
gp99-wlp2 2 13.709 km 192 313 1.52 1.58
brmr-wlp2 3 10.457 km 187 406 1.50 1.77
network-final-vertical-constrained.txt

## Slide 77: Vertical Constrained Adjustment
MARK ESTIMATED - VERTICAL-FREE ADJUSTMENT COORDINATE SHIFTS
------------------------------------------------------------------------------
863f N: 0.000 m (0.003 m) E: 0.000 m (0.004 m) H: -0.016 m (0.005 m)
asub N: 0.000 m (0.003 m) E: -0.001 m (0.004 m) H: -0.016 m (0.004 m)
brmr N: 0.000 m (0.003 m) E: 0.000 m (0.004 m) H: -0.013 m (0.004 m)
gp99 N: 0.000 m (0.003 m) E: 0.000 m (0.004 m) H: -0.015 m (0.005 m)
loy2 N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.015 m (0.004 m)
ls03 N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.016 m (0.004 m)
ncel N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.016 m (0.004 m)
ncga N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.015 m (0.004 m)
ou03 N: 0.000 m (0.003 m) E: 0.000 m (0.004 m) H: -0.017 m (0.005 m)
ou18 N: 0.000 m (0.003 m) E: 0.000 m (0.004 m) H: -0.016 m (0.005 m)
vagp N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.016 m (0.004 m)
w416 N: 0.000 m (0.003 m) E: 0.000 m (0.004 m) H: -0.019 m (0.003 m)
wlp2 N: 0.000 m (0.003 m) E: 0.000 m (0.003 m) H: -0.016 m (0.004 m)
MARK ESTIMATED - PUBLISHED VERTICAL COORDINATE SHIFTS
------------------------------------------------------------------------------
asub: ORTHO HGT: 0.020 m (0.004 m) DF4365 GPS HEIGHTS: 2CM/5CM STANDARDS
brmr: ORTHO HGT: -0.013 m (0.004 m) DG9069 FGCS LEVELING IN NGSIDB
loy2: ORTHO HGT: -0.013 m (0.004 m) DF5272 GPS HEIGHTS: 2CM/5CM STANDARDS
ncel: ORTHO HGT: -0.016 m (0.004 m) DL6896 GPS HEIGHTS: 2CM/5CM STANDARDS
ncga: ORTHO HGT: 0.006 m (0.004 m) DL6898 GPS HEIGHTS: 2CM/5CM STANDARDS
ou03: ORTHO HGT: 0.016 m (0.005 m) AJ4598 GPS HEIGHTS: DECIMETER ACCURACY
w416: ORTHO HGT: 0.005 m (0.003 m) FX0049 FGCS LEVELING IN NGSIDB
MARK CONSTRAINT RATIOS
------------------------------------------------------------------------------
brmr: ORTHO HGT: 2.600 DG9069 FGCS LEVELING IN NGSIDB
loy2: ORTHO HGT: 1.074 DF5272 GPS HEIGHTS: 2CM/5CM STANDARDS
ncel: ORTHO HGT: 1.119 DL6896 GPS HEIGHTS: 2CM/5CM STANDARDS
ncga: ORTHO HGT: 0.458 DL6898 GPS HEIGHTS: 2CM/5CM STANDARDS
ou03: ORTHO HGT: 1.481 AJ4598 GPS HEIGHTS: DECIMETER ACCURACY
w416: ORTHO HGT: 1.667 FX0049 FGCS LEVELING IN NGSIDB
network-final-vertical-constrained.txt
CONSTRAINT RATIOS are less than 3.5
SHIFTS are less than 4 cm
SHIFTS are less than 4 cm

## Slide 78: Vertical Constrained Adjustment
network-final-vertical-constrained.preplt2
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
9 0.0015 -0.0005 0.0033 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
12 0.0013 -0.0010 -0.0054 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
15 0.0008 -0.0026 0.0033 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
18 0.0010 -0.0009 -0.0015 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
21 0.0014 0.0008 0.0036 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
24 -0.0002 -0.0008 0.0137 21627.4186 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
27 -0.0002 -0.0003 -0.0015 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
30 -0.0002 -0.0005 -0.0011 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
33 -0.0002 -0.0008 0.0015 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
36 -0.0005 -0.0006 0.0021 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
39 -0.0007 -0.0001 -0.0016 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
42 -0.0010 0.0012 -0.0005 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
45 -0.0016 0.0010 -0.0004 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
48 -0.0027 0.0020 0.0052 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
51 -0.0014 0.0012 0.0074 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
54 -0.0018 0.0006 0.0030 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
57 -0.0024 0.0016 0.0042 21627.4186 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
60 -0.0013 -0.0005 0.0011 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
63 -0.0013 0.0013 -0.0052 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
66 -0.0005 0.0001 -0.0033 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
69 0.0001 0.0004 -0.0033 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
72 -0.0008 0.0004 0.0010 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
75 -0.0005 0.0002 0.0006 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
78 0.0010 -0.0005 -0.0014 21423.7928 ( 0008) 863 8610 F ( 0001) LOYOLA 2 COOP CORS ARP
81 0.0021 0.0010 -0.0045 11496.9030 ( 0009) BREADMAKER ( 0001) LOYOLA 2 COOP CORS ARP
84 0.0029 -0.0003 -0.0029 14532.4730 ( 0010) GPS099 ( 0001) LOYOLA 2 COOP CORS ARP
87 0.0012 0.0006 0.0001 14825.4858 ( 0011) ODU 3 ( 0001) LOYOLA 2 COOP CORS ARP
90 0.0018 -0.0002 -0.0079 15251.4826 ( 0012) ODU 18 ( 0001) LOYOLA 2 COOP CORS ARP
93 0.0030 -0.0012 0.0049 21627.4186 ( 0013) W 416 ( 0001) LOYOLA 2 COOP CORS ARP
96 -0.0003 0.0002 -0.0022 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
99 -0.0002 0.0014 0.0062 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP

## Slide 79: Vertical Constrained Adjustment
Residual Components(m) Rej Baseline FROM: TO:
Obs# DN DE DU (m) SSN Designation SSN Designation
102 0.0001 0.0003 0.0029 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
105 0.0003 0.0002 0.0029 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
108 -0.0005 -0.0001 -0.0017 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
111 0.0002 0.0007 0.0027 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
114 0.0002 0.0001 -0.0020 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
117 -0.0010 -0.0023 0.0048 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
120 0.0005 0.0001 0.0001 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
123 0.0001 -0.0005 -0.0002 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
126 0.0009 -0.0005 -0.0010 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
129 0.0003 0.0000 -0.0004 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
132 -0.0004 0.0001 0.0002 1869.9725 ( 0014) WLP2 ( 0001) LOYOLA 2 COOP CORS ARP
135 0.0022 0.0001 -0.0038 491454.8788 ( 0007) ASU-BOONE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
138 0.0001 0.0000 0.0016 24991.7434 ( 0003) LOYOLA LS03 CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
141 -0.0003 0.0006 -0.0008 46939.2818 ( 0006) ELIZABETH CITY CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
144 0.0008 0.0009 -0.0001 56473.0534 ( 0004) GATESVILLE CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
147 0.0005 -0.0006 -0.0007 58602.7357 ( 0005) VA GLOUCESTER PT CORS ARP ( 0001) LOYOLA 2 COOP CORS ARP
150 0.0146 -0.0033 0.0052 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
153 0.0138 -0.0104 0.0146 13708.8759 ( 0014) WLP2 ( 0010) GPS099
156 0.0075 0.0023 0.0178 21253.1756 ( 0014) WLP2 ( 0013) W 416
159 0.0167 -0.0059 0.0027 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
162 0.0115 -0.0028 -0.0098 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
165 0.0087 0.0132 0.0168 13918.5955 ( 0014) WLP2 ( 0011) ODU 3
168 0.0142 -0.0157 0.0123 13708.8759 ( 0014) WLP2 ( 0010) GPS099
171 0.0075 0.0089 0.0052 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
174 0.0073 -0.0007 0.0364 21253.1756 ( 0014) WLP2 ( 0013) W 416
177 0.0202 0.0036 -0.0144 20521.4872 ( 0014) WLP2 ( 0008) 863 8610 F
180 0.0124 0.0158 -0.0146 14221.4471 ( 0014) WLP2 ( 0012) ODU 18
183 0.0066 0.0099 -0.0152 13918.5955 ( 0014) WLP2 ( 0011) ODU 3
186 0.0050 0.0095 -0.0145 10456.5692 ( 0014) WLP2 ( 0009) BREADMAKER
network-final-vertical-constrained.preplt2

## Slide 80: Vertical Constrained Adjustment
MAX V OBS # MIN V OBS #
DX 1.5D-02 165 -1.5D-02 168
DY 2.4D-02 178 -2.4D-02 175
DZ 2.8D-02 176 -4.7D-03 188
DN 2.0D-02 177 -2.7D-03 48
DE 1.6D-02 181 -1.6D-02 169
DL 2.1D-02 170 1.2D-04 140
DU 3.6D-02 176 -1.5D-02 185
0DEGREES OF FREEDOM = 149
VARIANCE SUM = 278.5
STD.DEV.OF UNIT WEIGHT = 1.367
VARIANCE OF UNIT WEIGHT = 1.87
network-final-vertical-constrained.sum

## Slide 81: Vertical Constrained Adjustment
network-final-vertical-constrained.sum
NETWORK & LOCAL ACCURACIES (95% CONFIDENCE LEVEL)
COMPUTED USING A POSTERIORI STANDARD DEVIATION OF UNIT WEIGHT
NETWORK ACCURACIES (CENTIMETERS)
ISN SSN STATION DESIGNATION HORIZ UP
1 0008 863 8610 F 0.85 1.02 CM
2 0009 BREADMAKER 0.85 0.84 CM
3 0010 GPS099 0.85 1.00 CM
4 0011 ODU 3 0.85 0.99 CM
5 0012 ODU 18 0.86 1.06 CM
6 0013 W 416 0.86 0.68 CM
7 0014 WLP2 0.83 0.83 CM
8 0007 ASU-BOONE CORS ARP 0.84 0.85 CM
9 0001 LOYOLA 2 COOP CORS ARP 0.82 0.82 CM
10 0003 LOYOLA LS03 CORS ARP 0.83 0.83 CM
11 0006 ELIZABETH CITY CORS ARP 0.83 0.83 CM
12 0004 GATESVILLE CORS ARP 0.83 0.83 CM
13 0005 VA GLOUCESTER PT CORS ARP 0.83 0.83 CM
LOCAL ACCURACIES (CENTIMETERS) AND DISTANCE (KILOMETERS)
ISN SSN STATION DESIGNATION
FROM 1 0008 863 8610 F HORIZ UP DISTANCE
TO 5 0012 ODU 18 0.30 0.99 CM 6.40 KM
TO 6 0013 W 416 0.30 0.91 CM 6.40 KM
TO 4 0011 ODU 3 0.29 0.95 CM 6.61 KM
TO 3 0010 GPS099 0.28 0.93 CM 6.91 KM
TO 2 0009 BREADMAKER 0.27 0.86 CM 10.10 KM
TO 7 0014 WLP2 0.23 0.75 CM 20.52 KM

## Slide 82: Obtain Final Coordinate Listings
Remember the “TRUTH” is in the .TXT files and only there.
The B-Files should also contain the truth, but they are hard-to-read (see slides 92-100).
  Export Adjustments Button
Use WinTeqc to harvest and then combine.

## Slide 83: Obtain Final Coordinate Listings
First, use WinTeqc to harvest
  Lat, Lon, El Hgt
  from horizontal-constrained adjustment
Second, use WinTeqc to harvest
  Ortho Hgt
  from vertical-constrained adjustment
Third, Combine the results
1st
2nd
3rd

## Slide 84: Obtain Final Coordinate Listings
Mark | Lat | Acc | Lon | Acc | Northing | Easting | El Hgt | Acc | Ortho | Acc
863f | 36 56 33.74464 | 0.002 | 76 19 43.29917 | 0.002 | 1069848.931 | 3693394.141 | -34.667 | 0.004 | 2.235 | 0.017
asub | 36 12 50.84487 | 0.001 | 81 40 54.64758 | 0.002 | 276616.963 | 368477.460 | 957.936 | 0.003 | 989.159 | 0.016
brmr | 36 51 16.85013 | 0.001 | 76 18 00.44330 | 0.002 | 3478148.975 | 12126504.855 | -36.041 | 0.003 | 1.040 | 0.016
gp99 | 36 53 11.57704 | 0.002 | 76 17 42.87287 | 0.002 | 1063687.679 | 3696518.622 | -34.943 | 0.004 | 2.109 | 0.016
loy2 | 36 45 50.43115 | 0.001 | 76 14 16.06833 | 0.001 | 1050214.002 | 3701963.850 | -23.428 | 0.003 | 13.855 | 0.017
ls03 | 36 47 19.43646 | 0.001 | 75 57 34.32983 | 0.001 | 1053588.585 | 3726726.776 | -22.004 | 0.003 | 15.915 | 0.020
ncel | 36 20 28.79062 | 0.001 | 76 15 29.27394 | 0.001 | 290874.902 | 855730.324 | -29.732 | 0.003 | 7.602 | 0.015
ncga | 36 26 12.65518 | 0.001 | 76 43 16.51660 | 0.001 | 300420.808 | 813921.940 | -20.452 | 0.003 | 15.674 | 0.017
ou03 | 36 53 11.86976 | 0.001 | 76 18 13.50352 | 0.002 | 3489753.591 | 12125173.099 | -34.298 | 0.004 | 2.738 | 0.016
ou18 | 36 53 08.99408 | 0.002 | 76 19 00.94237 | 0.002 | 1063563.156 | 3694587.854 | -35.256 | 0.005 | 1.759 | 0.017
vagp | 37 14 55.00843 | 0.001 | 76 29 57.73094 | 0.001 | 1103453.313 | 3677475.386 | -19.813 | 0.003 | 15.965 | 0.022
w416 | 36 57 29.21105 | 0.002 | 76 15 34.14964 | 0.002 | 1071702.296 | 3699516.671 | -33.697 | 0.004 | 3.300 | 0.017
wlp2 | 36 45 59.76746 | 0.001 | 76 15 30.56739 | 0.001 | 1050457.651 | 3700109.841 | -13.200 | 0.003 | 24.027 | 0.017
1st
horizontal-constrained adjustment

## Slide 85: Obtain Final Coordinate Listings
2nd
Mark | Lat | Acc | Lon | Acc | Northing | Easting | El Hgt | Acc | Ortho | Acc
863f | 36 56 33.74459 | 0.003 | 76 19 43.29911 | 0.004 | 1069848.930 | 3693394.143 | -34.686 | 0.005 | 2.216 | 0.017
asub | 36 12 50.84482 | 0.003 | 81 40 54.64757 | 0.004 | 276616.961 | 368477.460 | 957.917 | 0.004 | 989.140 | 0.016
brmr | 36 51 16.85008 | 0.003 | 76 18 00.44323 | 0.004 | 3478148.969 | 12126504.858 | -36.058 | 0.004 | 1.023 | 0.016
gp99 | 36 53 11.57699 | 0.003 | 76 17 42.87281 | 0.004 | 1063687.677 | 3696518.623 | -34.961 | 0.005 | 2.091 | 0.017
loy2 | 36 45 50.43110 | 0.003 | 76 14 16.06827 | 0.003 | 1050214.001 | 3701963.852 | -23.446 | 0.004 | 13.837 | 0.017
ls03 | 36 47 19.43641 | 0.003 | 75 57 34.32976 | 0.003 | 1053588.584 | 3726726.777 | -22.023 | 0.004 | 15.896 | 0.020
ncel | 36 20 28.79057 | 0.003 | 76 15 29.27388 | 0.003 | 290874.901 | 855730.325 | -29.750 | 0.004 | 7.584 | 0.015
ncga | 36 26 12.65513 | 0.003 | 76 43 16.51654 | 0.003 | 300420.806 | 813921.942 | -20.470 | 0.004 | 15.656 | 0.017
ou03 | 36 53 11.86972 | 0.003 | 76 18 13.50346 | 0.004 | 3489753.585 | 12125173.102 | -34.320 | 0.005 | 2.716 | 0.017
ou18 | 36 53 08.99403 | 0.003 | 76 19 00.94231 | 0.004 | 1063563.155 | 3694587.855 | -35.275 | 0.005 | 1.740 | 0.017
vagp | 37 14 55.00839 | 0.003 | 76 29 57.73088 | 0.003 | 1103453.312 | 3677475.387 | -19.832 | 0.004 | 15.946 | 0.022
w416 | 36 57 29.21101 | 0.003 | 76 15 34.14958 | 0.004 | 1071702.294 | 3699516.673 | -33.719 | 0.003 | 3.278 | 0.017
wlp2 | 36 45 59.76741 | 0.003 | 76 15 30.56733 | 0.003 | 1050457.650 | 3700109.843 | -13.218 | 0.004 | 24.009 | 0.017
vertical-constrained adjustment

## Slide 86: Obtain Final Coordinate Listings
Mark | Lat | Acc | Lon | Acc | Northing | Easting | El Hgt | Acc | Ortho | Acc
863f | 36 56 33.74464 | 0.002 | 76 19 43.29917 | 0.002 | 1069848.931 | 3693394.141 | -34.667 | 0.004 | 2.216 | 0.017
asub | 36 12 50.84487 | 0.001 | 81 40 54.64758 | 0.002 | 276616.963 | 368477.460 | 957.936 | 0.003 | 989.140 | 0.016
brmr | 36 51 16.85013 | 0.001 | 76 18 00.44330 | 0.002 | 3478148.975 | 12126504.855 | -36.041 | 0.003 | 1.023 | 0.016
gp99 | 36 53 11.57704 | 0.002 | 76 17 42.87287 | 0.002 | 1063687.679 | 3696518.622 | -34.943 | 0.004 | 2.091 | 0.017
loy2 | 36 45 50.43115 | 0.001 | 76 14 16.06833 | 0.001 | 1050214.002 | 3701963.850 | -23.428 | 0.003 | 13.837 | 0.017
ls03 | 36 47 19.43646 | 0.001 | 75 57 34.32983 | 0.001 | 1053588.585 | 3726726.776 | -22.004 | 0.003 | 15.896 | 0.020
ncel | 36 20 28.79062 | 0.001 | 76 15 29.27394 | 0.001 | 290874.902 | 855730.324 | -29.732 | 0.003 | 7.584 | 0.015
ncga | 36 26 12.65518 | 0.001 | 76 43 16.51660 | 0.001 | 300420.808 | 813921.940 | -20.452 | 0.003 | 15.656 | 0.017
ou03 | 36 53 11.86976 | 0.001 | 76 18 13.50352 | 0.002 | 3489753.591 | 12125173.099 | -34.298 | 0.004 | 2.716 | 0.017
ou18 | 36 53 08.99408 | 0.002 | 76 19 00.94237 | 0.002 | 1063563.156 | 3694587.854 | -35.256 | 0.005 | 1.740 | 0.017
vagp | 37 14 55.00843 | 0.001 | 76 29 57.73094 | 0.001 | 1103453.313 | 3677475.386 | -19.813 | 0.003 | 15.946 | 0.022
w416 | 36 57 29.21105 | 0.002 | 76 15 34.14964 | 0.002 | 1071702.296 | 3699516.671 | -33.697 | 0.004 | 3.278 | 0.017
wlp2 | 36 45 59.76746 | 0.001 | 76 15 30.56739 | 0.001 | 1050457.651 | 3700109.841 | -13.200 | 0.003 | 24.009 | 0.017
Combine the results
Verify, Then Trust
Compare to the .TXT files
(I did, checked out!)
3rd

## Slide 87: network-final (for submission)
OPUS PROJECTS automatically creates a series of files that are intended for internal use at NGS.
  These can be viewed in SHOW FILE under “network-final (for submission)”.
    Look at CHKOBS
    Look at OBSCHK (short)
    Look at OBSDES
The various “errors” may need to be corrected or at least discussed in the Project Report.

## Slide 88: network-final (for submission)
network-final (for submission).chkobs
1 2 3 4 5 6 7
1234567890123456789012345678901234567890123456789012345678901234567890123456789
--------------------------------------------------------------------------------
494 CC 27-80 NON-BLANK
004680*93*0001.7340001.576 Trimble RTK
494 CC 27-80 NON-BLANK
004690*93*0000.4460000.259 OPUSProjects
494 CC 27-80 NON-BLANK
004680*93*0001.7340001.576 Trimble RTK
494 CC 27-80 NON-BLANK
004690*93*0000.4460000.259 OPUSProjects
Summary from program chkobs:
Number of records in input file = 470, number of errors found = 4
These lines can be found at the bottom the B-File.
Error flagging is due to underlying CHKOBS coding.
No action needed.
004680*93* 1.734 1.576 Trimble RTK
004690*93* 0.446 0.259 OPUSProjects
004700*AA*

## Slide 89: network-final (for submission)
network-final (for submission).obschk (short)
NGS program obschk Version 3.9 Date(ccyy/mm/dd): 2022/11/28
BLUE BOOK B-FILE - Results/network-final-final.bfile
BLUE BOOK G-FILE - Results/network-final-final.gfile
SHORT (W/O 70I - 73I REC) OUTPUT FILE - obschk_short.sum
LONG (W 70I - 73I REC) OUTPUT FILE - obschk_long.sum
----------------------------------------------------------------------------
** (1) BLUE BOOK OBSERVATION FILE DATA CHECK
27 RECORD HI CC 56-60 IS ZERO
001150*27*00142102170000 0000
27 RECORD HI CC 56-60 IS ZERO
001730*27*00142102230000 0000
27 RECORD HI CC 56-60 IS ZERO
002070*27*00142102240000 0000
27 RECORD HI CC 56-60 IS ZERO
002410*27*00142103040000 0000
These lines can be found in the B-File.
Error flagging is due to underlying OBSCHK coding.
Alerts user to potential ARP heights of ZERO. Most of the time, the CORS ARP is ZERO.
No action needed if you are sure of your ARP heights.
001130*25*0014R0481AWLP2DZ 007 012
001140*26*BB 0481A -> OP 2021-048-A
001150*27*00142102170000 0000
001160*27*00142102172359 0000

## Slide 90: network-final (for submission)
network-final (for submission).obsdes
PROGRAM OBSDES V 2.7
Bfile (4-digit ssn) - bfile
Description file (D-file format) - dfile
Obsdes output file - obsdes.sum
------------------------------------------------------------------------------
@0001DG9069GBREADMAKER
LOYOLA 2 COOP CORS ARP
CC 13-62 STATION NAME UNMATCHED
@0002FX0049GW 416
CC 2-5 SSN UNMATCHED WITH BFILE 80 SSNS
@0003 GGPS099
LOYOLA LS03 CORS ARP
CC 13-62 STATION NAME UNMATCHED
@0004AJ4598GODU 3
GATESVILLE CORS ARP
CC 13-62 STATION NAME UNMATCHED
@0004AJ4598GODU 3 ... VA
NC
CC 206-207 STATE CODE UNMATCHED
@0005 GODU 18
VA GLOUCESTER PT CORS ARP
CC 13-62 STATION NAME UNMATCHED
These errors are all caused by a mismatch between the UPLOADED.DSC file and the CONSOLIDATED SERFIL.
See next slide

## Slide 91: network-final (for submission)
network-final (for submission).obsdes
CONSLIDATED SERFIL
LOY2 0001
LOYX 0002
LS03 0003
NCGA 0004
VAGP 0005
NCEL 0006
ASUB 0007
863F 0008
BRMR 0009
GP99 0010
OU03 0011
OU18 0012
W416 0013
WLP2 0014
UPLOADED.DSC
@0001DG9069GBREADMAKER
@0002FX0049GW 416
@0003 GGPS099
@0004AJ4598GODU 3
@0005 GODU 18
@0006 SWLP2
@0007 S863 8610 F
The user could have avoided these errors by:
1) Submitting all of the OPUS STATIC files.
2) Process the first session. Obtain the SERFIL
3) Editing the WinDesc to agree with the SERFIL
4) Uploading the edited WinDesc files.
5) Then re-process the first Session, the remaining Sessions, and Adjustments.
Consult USER MANUAL and possibly discuss with NGS acceptance personnel.

## Slide 92: Export Adjustments
Click on EXPORT ADJUSTMENTS button.

## Slide 93: Export Adjustments
You can choose to export one or more adjustments. Move the selections from the left to the right pane. Choose an export format.
A .zip file will be created and sent to your “downloads” folder.

## Slide 94: Export Adjustments
Move the file to your project folders.
  I created a folder: “OPUS PROJECTS Adjustment Exports”
  I unzipped the .zip into the …Baselines.CSV and …Marks.CSV files
The Baselines file can be used to plot the baselines and their associated metadata (14 columns!)
The Marks file contains the output and metadata for the adjustment (154 columns!)

## Slide 95: Export Adjustments
The B-file for submission combines the
  Lat/Lon and EllHt from the HOR_Constrained Adjustment
  Ortho Height from the VERT-Constrained Adjustment
The Marks.csv harvests that data (and more).
B-File for submision (partial)
003510*80*0008863 8610 F 36563374464N076194329917W VA
003520*86*0008 2216K N88 -369027 -34667A ANAD 83(2011)
esid | SeqNumHOR | DataCodeHOR | StationName | Lat (dms) | LatDir | Lon (dms) | LonDir | State | DataCodeVER | OrthoHgt (m) | OH_Code
863f | 3510 | *80* | 863 8610 F | 36° 56' 33.74464" | N | 076° 19' 43.29917" | W | VA | *86* | 2.216 | K
OH_OrderClass | OH_NGSIDB_Ind | OH_Datum | OrgCode | GeoidHgt (m) | GeoidHgtCode | EllipHgt (m) | EllipHgtCode | EllipHgtDatum | Comment_86record
 | N | 88 |  | -36.902 | 7 | -34.667 | A | A | NAD_83(2011)

## Slide 96: Export Adjustments
CAUTIONARY NOTE:
NOTES:
  The B-Files are used by NGS to load coordinates into the Integrated Database.
  For Constrained marks, the positions (and heights) in the TXT files are slightly differing from the published values
    due to “normal” constraints
    use of “tight” constraints, would minimize or avoid the slight differences
  The B-files intentionally REVERT these back to the published values, so that they are not over-written by the slightly differing adjustment.
Expect slight differences between the TXT output and the B-files.

## Slide 97: Export Adjustments
WARNING NOTE:
  At the time of this slide set (October 02, 2023) the B-File Vert-Constrained was being incorrectly created which was leading to downstream errors.
  The Export Adjustment inherited these errors.
  Specifically, there were missing trailing zeroes in the *86* records
    See example on next slide.
    See “network-final-final_marks-annotated.xls” for my highlighted comments on the errors.

## Slide 98: Export Adjustments
003510*80*0008863 8610 F 36563374459N076194329911W VA
003520*86*0008 2216K N88 -369027 -34686A ANAD 83(2011)
003530*80*0009BREADMAKER 36511685008N076180044323W VA
003540*86*0009 1036A12Y88 -370817 -36058A ANAD 83(2011)
003550*80*0010GPS099 36531157699N076174287281W VA
003560*86*0010 2091K N88 -370527 -34961A ANAD 83(2011)
003570*80*0011ODU 3 36531186972N076181350346W VA
003580*86*0011 27 G Y88 -370367 -34320A ANAD 83(2011)
003590*80*0012ODU 18 36530899403N076190094231W VA
003600*86*0012 1740K N88 -370157 -35275A ANAD 83(2011)
003610*80*0013W 416 36572921101N076153414958W VA
003620*86*0013 3273A11Y88 -369977 -33719A ANAD 83(2011)
003630*80*0014WLP2 36455976741N076153056733W VA
003640*86*0014 24009K N88 -372277 -13218A ANAD 83(2011)
003650*80*0007ASU-BOONE CORS ARP 36125084482N081405464757W NC
003660*86*0007 989140G N88 -312237 957917A ANAD 83(2011)
003670*80*0001LOYOLA 2 COOP CORS ARP 36455043110N076141606827W VA
003680*86*0001 1385 K Y88 -372837 -23446A ANAD 83(2011)
003690*80*0003LOYOLA LS03 CORS ARP 36471943641N075573432976W VA
003700*86*0003 15896K N88 -379197 -22023A ANAD 83(2011)
003710*80*0006ELIZABETH CITY CORS ARP 36202879057N076152927388W NC
003720*86*0006 760 K Y88 -373347 -29750A ANAD 83(2011)
003730*80*0004GATESVILLE CORS ARP 36261265513N076431651654W NC
003740*86*0004 1565 K Y88 -361267 -20470A ANAD 83(2011)
003750*80*0005VA GLOUCESTER PT CORS ARP 37145500839N076295773088W VA
003760*86*0005 15946K N88 -357787 -19832A ANAD 83(2011)
network-final-vertical-constrained.bfile
missing trailing zeroes

## Slide 99: Export Adjustments
003510*80*0008863 8610 F 36563374459N076194329911W VA
003520*86*0008 2216K N88 -369027 -34686A ANAD 83(2011)
003530*80*0009BREADMAKER 36511685008N076180044323W VA
003540*86*0009 1036A12Y88 -370817 -36058A ANAD 83(2011)
003550*80*0010GPS099 36531157699N076174287281W VA
003560*86*0010 2091K N88 -370527 -34961A ANAD 83(2011)
003570*80*0011ODU 3 36531186972N076181350346W VA
003580*86*0011 27 G Y88 -370367 -34320A ANAD 83(2011)
003590*80*0012ODU 18 36530899403N076190094231W VA
003600*86*0012 1740K N88 -370157 -35275A ANAD 83(2011)
003610*80*0013W 416 36572921101N076153414958W VA
003620*86*0013 3273A11Y88 -369977 -33719A ANAD 83(2011)
003630*80*0014WLP2 36455976741N076153056733W VA
003640*86*0014 24009K N88 -372277 -13218A ANAD 83(2011)
003650*80*0007ASU-BOONE CORS ARP 36125084482N081405464757W NC
003660*86*0007 989140G N88 -312237 957917A ANAD 83(2011)
003670*80*0001LOYOLA 2 COOP CORS ARP 36455043110N076141606827W VA
003680*86*0001 1385 K Y88 -372837 -23446A ANAD 83(2011)
003690*80*0003LOYOLA LS03 CORS ARP 36471943641N075573432976W VA
003700*86*0003 15896K N88 -379197 -22023A ANAD 83(2011)
003710*80*0006ELIZABETH CITY CORS ARP 36202879057N076152927388W NC
003720*86*0006 760 K Y88 -373347 -29750A ANAD 83(2011)
003730*80*0004GATESVILLE CORS ARP 36261265513N076431651654W NC
003740*86*0004 1565 K Y88 -361267 -20470A ANAD 83(2011)
003750*80*0005VA GLOUCESTER PT CORS ARP 37145500839N076295773088W VA
003760*86*0005 15946K N88 -357787 -19832A ANAD 83(2011)
network-final-vertical-constrained.bfile
OrthoHgt (m)
2.216
989.140
1.036
2.091
1.385
15.896
0.760
1.565
0.027
1.740
15.946
3.273
24.009
Missing trailing zeroes leads to flawed Export Adjustment output

## Slide 100: Review and Submit to NGS
Need Tracking ID
https://geodesy.noaa.gov/SurveyProposal/
NGS Survey Project Proposal page

## Slide 101: New Control Buttons
Without Tracking ID
WithTracking ID = 0000

## Slide 102: Review and Submit Checklist
The REVIEW and Submit to NGS Button triggers OP5.1 to examine the project for the needed list of submissions.
WinDESC, photos, field logs, and a variety of other items.
This is to be covered in a future training.

## Slide 103
The last step is to delete your project. You can keep your project on-line for as long as needed, but be courteous and “delete when complete.” Warning – clicking OK here deletes the project.

## Slide 104
Yes, I’m sure.
PERMANENTLY DELETE the Project
Click “YES, I’m Sure” or “No, please CANCEL”
This project cannot be restored.
No, Please CANCEL the request
I wish this WARNING BOX would pop-up!

## Slide 105
OPUS Projects Manager Training
Step 4 : Network Adjustment
ngs.opus.projects@noaa.gov
END