## Slide 1
OPUS Projects Manager Training
Supplement: Using WinTEQC
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
Minor edits by Dave Zenk, October 16, 2023

## Slide 2: Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment
  - Using WinTEQC for getting OP Adjustment Results

## Slide 3: Using WinTEQC for OPUS Projects Results
A copy of WinTEQC can be obtained from the NGS webpage by using the “Tools” pull down menu, then clicking on “Geodetic Software.”

## Slide 4: Using WinTEQC for OPUS Projects Results
Now click on the “User-Contributed Software” button.

## Slide 5: Using WinTEQC for OPUS Projects Results
The next page will provide a link to the U.S. Army Corps of Engineers webpage for downloading.
Save and install the program for use.
Just so you are aware:
The “User-Contributed Software” are products developed outside of NGS and any use of those programs is at your own risk.

## Slide 6
Using WinTEQC for OPUS Projects Results
OP provides the OPUS, Session, and Network Adjustment solution reports for each of these processes. The resulting solution related files need to be saved to your computer hard-drive for WinTEQC to work. Having done this for the Network Solutions, we move on to getting our final adjusted values in a usable list (format).

## Slide 7
Click the “Get OPUS Adjustment” button to load the desired solution results. First file we want to load is the constrained horizontal values.
Using WinTEQC for OPUS Projects Results

## Slide 8
Screenshot of where the “OPUS Adjustment Results” are on HDD
Using WinTEQC for OPUS Projects Results
Select the folder with the saved “Network Adjustment” solution reports and click the desired report.

## Slide 9
Once the report information is loaded, click the “Copy” button.
Using WinTEQC for OPUS Projects Results

## Slide 10
Using WinTEQC for OPUS Projects Results
The report information can now be pasted into a spreadsheet program (ex. Excel, etc.) for editing. Next we edit out the (ACC statistics columns) and ORTHO contents.

## Slide 11
Using WinTEQC for OPUS Projects Results
Having the spreadsheet trimmed down to the adjusted geometric position information, we repeat the process for getting the constrained vertical orthometric heights.
Ortho Height
Ortho Height column will be harvested from the Vertical-Constrained adjustment (slide 15)

## Slide 12
Using WinTEQC for OPUS Projects Results
Selecting the constrained vertical solution report for loading into WinTEQC…….

## Slide 13
Using WinTEQC for OPUS Projects Results
…….we “Copy” the report information for pasting into our spreadsheet program (ex. Excel, etc.) for editing.

## Slide 14
Using WinTEQC for OPUS Projects Results
The only values from the constrained vertical adjustment we have an interested in are the network adjusted orthometric heights, and those values for our “network marks”. Getting just those values, we return to our horizontal spreadsheet.

## Slide 15
Using WinTEQC for OPUS Projects Results
Having pasted and edited the adjusted orthometric height results into our spreadsheet with the adjusted geometric positions, we finish by adding the appropriate metadata (datums, etc.).
We now have a complete set of our network adjusted positions (both geometric & vertical).

## Slide 16: WinTeqc versions vary
My version (Dave Zenk) is dated 4.26.2019
  It does not contain the “Get B-File” button.
  If your version does have the Get B-File button, you can harvest the adjusted positions from the B-File (for submission).
  I can’t try it at this time
Denis shows harvesting from the
  B-File HC
  B-File VC
  Then combining

## Slide 17
You can also get the adjusted positions from the “bfile” using WinTEQC. Similar to the adjustment reports (*.txt files), the geometric & vertical values have to come from each adjustment bfile.
The difference in the format is the bfile results are comma delimited and without all of the adjustment statistics.
Using WinTEQC for OPUS Projects Results

## Slide 18
Using WinTEQC for OPUS Projects Results
Select the desired bfile to load into WinTEQC…..

## Slide 19
Using WinTEQC for OPUS Projects Results
Copy the bfile information…..

## Slide 20
Using WinTEQC for OPUS Projects Results
Then paste into desired program for editing. Same as the “report values (*.txt files)” we only need the “orthometric height” values from the vertical bfile information.
Latitude
Longitude
El Hgt
Ortho Hgt
from B-File HC
from B-File VC

## Slide 21: Verify, then Trust
I note in the current B-File (for submission) some “irregularities”.
B-files are very column-specific
Mis-aligned columns lead to errors
Missing leading zero is normal
Missing trailing zero’s is irregular
October 02, 2023

## Slide 22: B-File (for submission)
003510*80*0008863 8610 F 36563374464N076194329917W VA
003520*86*0008 2216K N88 -369027 -34667A ANAD 83(2011)
003530*80*0009BREADMAKER 36511685018N076180044343W VA
003540*86*0009 1036A12Y88 -370817 -36039A ANAD 83(2011)
003550*80*0010GPS099 36531157704N076174287287W VA
003560*86*0010 2091K N88 -370527 -34943A ANAD 83(2011)
003570*80*0011ODU 3 36531186975N076181350342W VA
003580*86*0011 27 G Y88 -370367 -34294A ANAD 83(2011)
003590*80*0012ODU 18 36530899408N076190094237W VA
003600*86*0012 1740K N88 -370157 -35256A ANAD 83(2011)
003610*80*0013W 416 36572921105N076153414964W VA
003620*86*0013 3273A11Y88 -369977 -33697A ANAD 83(2011)
003630*80*0014WLP2 36455976746N076153056739W VA
003640*86*0014 24009K N88 -372277 -13200A ANAD 83(2011)
003650*80*0007ASU-BOONE CORS ARP 36125084487N081405464758W NC
003660*86*0007 989140G N88 -312237 957936A ANAD 83(2011)
003670*80*0001LOYOLA 2 COOP CORS ARP 36455043110N076141606827W VA
003680*86*0001 1385 K Y88 -372837 -23440A ANAD 83(2011)
003690*80*0003LOYOLA LS03 CORS ARP 36471943644N075573432982W VA
003700*86*0003 15896K N88 -379197 -22009A ANAD 83(2011)
003710*80*0006ELIZABETH CITY CORS ARP 36202879080N076152927391W NC
003720*86*0006 760 K Y88 -373347 -29730A ANAD 83(2011)
003730*80*0004GATESVILLE CORS ARP 36261265518N076431651666W NC
003740*86*0004 1565 K Y88 -361267 -20469A ANAD 83(2011)
003750*80*0005VA GLOUCESTER PT CORS ARP 37145500829N076295773103W VA
003760*86*0005 15946K N88 -357787 -19814A ANAD 83(2011)
2.216
1.036
2.091
2.700
13.850
15.896
7.600
15.650
1.740
3.273
24.009
989.140
15.946
RED BOXES have missing trailing zero’s.
I find this to be an “irregularity.”
ELIZABETH CITY looks rounded to 7.60 and missing trailing zero.
October 02, 2023
Implied decimal point between columns 20 & 21

## Slide 23
OPUS Projects Manager Training
Supplement: Using WinTEQC
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
Minor edits by Dave Zenk, October 16, 2023