## Slide 1: Project Planning MARK SETTING and RECOVERY
Brian Ward
NOAA, National Geodetic Survey
Brian.Ward@noaa.gov
Notes: Im Brian Ward, Central Plains Advisor, AR. KS, MO and TN. Worked for NGS 32 years. Field for 17, AR Advisor for 11 year Regional for 3 years.

## Slide 2
Project Planning
Mark Setting
Line ties to the NSRS
Project Proposal
DSWorld
Windesc
Translev
Bluebooking
Notes: I will try to demonstrate these programs.

## Slide 3
Notes: Everything I talk about is on our website.

## Slide 4
NGS Regional Advisor Program
Notes: Regional geodetic advisors are located around the country for questions / support.
You can always call another Advisor if you cant get in touch with me. Lots of expertise in a varity of subjects related to geodesy in this group.

## Slide 5: 1892 to 1950
Notes: Early Leveling in the USA

## Slide 6: 1950 to 1975

## Slide 7: 1975 to Present

## Slide 8
Geodetic 1st Order Levels
Notes: Small All Terrain Cycles used to cover more ground.
Could level to 20 KM a day in flat terrain.
Zeiss NI002 had a swivel eye piece.
Phased in Digital Levels in early 2000. Using 1st order Digital Levels and Invar Bar Code Rods.

## Slide 9: Bench Mark Reset Document
Notes: Best source of information

## Slide 10: Mark Setting Information
Notes: Best information is in the Benchmark Rest Manual

## Slide 11: Stability Order
A = MOST RELIABLE AND EXPECTED TO HOLD POSITION/ELEVATION WELL
In a rock outcrop or ledge, exposed bedrock, large foundations on bedrock, rod drilled and cemented into bedrock...
the most reliable, are expected to hold well
B = PROBABLY HOLD POSITION/ELEVATION WELL
Deep driven stainless steel rod mark in +10’ Ft. in sleeve, massive structures and retaining walls, abutment of pier or large bridge..
will probably hold well.
C = MAY HOLD, BUT OF TYPE COMMONLY SUBJECT TO SURFACE MOTION
Concrete monument, footing of small or medium structures, retaining wall or concrete ledge.. may hold well, are commonly subject to movement
D = MARK OF QUESTIONABLE OR UNKNOWN STABILITY
Light structures, prefabricated concrete post, sidewalk, curb..
of questionable or unknown reliability
Notes: When setting marks, stability is always important. It all starts and ends with your mark setting.

## Slide 12: Bedrock Monuments
“A” Order Stability

## Slide 13: Deep Driven Rod Mark
“B” Order Stability

## Slide 14: Access Cover to Datum Point

## Slide 15: Concrete Monument
“C” Order Stability

## Slide 16: Concrete Monument

## Slide 17: Unknown Stability

## Slide 18: Project Planning
Preparation Before Setting Marks
Locate ties to the NSRS.
Decide route and number of marks to set.
Decide what type of marks to set.
Closely estimate distance of total line, including ties to NSRS.
Closely estimate distance between marks.
Design in DSWorld or other mapping app.
*Contact Utilities before you dig.
*All this information will be needed for Project Proposal.

## Slide 19: Desk Top Recon
View Project Area
Selecting NSRS Tie Marks
Select approximate location of new marks
NSRS ties must be published, leveled and adjusted orthometric heights for Order & Class you are trying to achieve.

## Slide 20: Mark Recovery Tools
DSWorld
NGS Data Explorer
Mark Recovery App

## Slide 21
DSWORLD

## Slide 23
Notes: We have tools to help find the marks. DSWorld is a good one.

## Slide 24
Notes: This is crowded, but just wanted to show an example of what to look for

## Slide 25
Notes: Getting the line where you need it. No rules concerning specific routes.

## Slide 26
Notes: Level line runs along the levee.

## Slide 29
Notes: You can see where the line needs to run. Recon old marks, locations for new marks, like bridges, rock outcrops, safe places in ROW.

## Slide 30
Notes: Look for places to set marks like, bridges, sturdy foundations..etc Talk to land owners, mark places for new marks to have utilities marked

## Slide 31
NGS DATA EXPLORER

## Slide 32
Notes: Several features, you can expand radius

## Slide 34
Notes: Map View

## Slide 35
Notes: Satellite View

## Slide 36
MARK RECOVERY FORM
Notes: When you get in the field, you can use mark recovery form.

## Slide 37
Notes: Click on find marks near me

## Slide 38
Notes: Scroll map and draw new center.

## Slide 39
Notes: This should be used for mapping only. Pictures and descriptive text will be entered in windesc.

## Slide 40: Information you need to gather
https://www.ngs.noaa.gov/surveys/mark-recovery/index.shtml
Contact underground utilities with mark locations before digging.
Notes: The following information will need to be gathered for later entry into windesc.

## Slide 41: Windesc Information
Notes: Information for new marks needs to be collected.

## Slide 42: Mark Recovery https://geodesy.noaa.gov//surveys/mark-recovery/
Logbook or Notebook (computer, tablet or paper with pen or pencil)
Datasheets (paper or computer)
Tape measure (100m tape preferred) or EDM laser
Compass
Brush hook or Machete
Flagging (to help relocate the mark for future observation)
Spray Paint (can paint arrow and “BM” on road towards bench mark)
Probe (useful for finding benchmarks that might be buried with an inch or two of soil)
Camera/Phone (for mark recover pictures)
Survey grade or hand held GPS receiver or GPS enabled phone
Garden gloves
Shovel or Trowel
Paper towel, packaged wiping cloths, rags, napkins, or other such material to clean off disks
Flat blade screwdriver (for digging and for opening rod covers)
First aid kit
Metal detector
Notes: Equipment for the field.

## Slide 43: Mark Position

## Slide 44: Scaled Position
Notes: Scaled position needs update

## Slide 45: Mark Condition

## Slide 46: Mark Photos

## Slide 47: Mark Descriptive Notes

## Slide 48: Mark Stamping & Designation

## Slide 49: Mark Type

## Slide 50: Mark Setting & Specific Setting

## Slide 51: Special Application Marks

## Slide 52: Magnetic Property

## Slide 53: Mark Stability
Windesc will assign a stability code based on the “setting” selected.

## Slide 54: Rod and Sleeve Depths

## Slide 55: Project Proposal
Information Needed

## Slide 56: Leveling Ties to the NSRS
First Order -Three mark tie required
Second Order-Two mark tie required
Notes: All line ties must meet tolerance for order and class.

## Slide 57: DSWORLD
Note Tie Marks-Pid’s & Take Pics of stamping
Note approximate number of new marks
Note type of marks to be set
Note distance of total run
Note route to be taken, start, finish, road names, State, County and Towns
Take a screen shot of project area

## Slide 58: Submit Project Proposal
Project Title
Order and Class of leveling
Beginning and approximate end date
Contact information
Photos and Sketches
Notes: Go through form

## Slide 59: Project Proposal

## Slide 60
L12345

## Slide 62: Level Line Example

## Slide 63: L12345
Line number should be used to name all files.
l12345.hgz, l12345.abs, l12345.nmo, l12345.des,,etc.
When you get your line number and sequence numbers, your project has been approved.
If an Advisor or other NGS person is assisting you, don’t hesitate to reach out.
Your ready to go!

## Slide 64: LOCUS

## Slide 65: LOCUS Results

## Slide 67: LOCUS BM ADJUSTED
0 80.13865
1 77.41014
2 74.76259
3 81.95975
4 74.90121
5 76.33121
6 76.31088
7 76.78365
8 76.69923
9 74.46135
10 74.72267
11 96.39922
12 91.99580
13 81.49440
14 96.58920
*DK2866 L 321 80.139
*DK2867 M 321 77.410
DO7488 HOFFMAN 74.763
*DK2871 INN RESET 81.960
DO7489 HOLCOMB 74.901
DO7490 O MURRAY 76.331
DO7491 N MURRAY 76.311
DO7492 F MURRAY 76.784
DO7493 ARRON KING 76.699
DO7494 T 321 74.461
DO7495 S 321 74.723
DO7496 U 321 96.399
*EJ1665 H 290 91.996
*EJ1666 J 290 81.494
*EJ1667 K 290 96.589

## Slide 68
Project Planning
Mark Setting
Line ties to the NSRS
Project Proposal
Demo!
DSWorld
Overview
County search
Project ID search
Windesc
Overview
Des.file
Translev
Overview
HGZ.file
Bluebook
Notes: I will try to demonstrate these programs.

## Slide 69
https://geodesy.noaa.gov/PC_PROD/index.shtml
DSWORLD

## Slide 70: DSWORLD DEMO

## Slide 71: Digital Leveling WINDESC
Preparing Descriptions for Passive Marks

## Slide 72: Purpose of Writing Descriptions
To make geodetic data available to surveyors, engineers, cartographers and general public
To facilitate finding the mark
To correctly identify the mark
To use the mark for new surveys
To preserve the mark for future generations

## Slide 73: Processing Sequence
Copy digital photos to photo directory
Create a new .des file and enter project info
Import description data from NGS
Renumber points if needed
Create or edit descriptions
Spell check all descriptions
Format all descriptions
Run neighbor and discrep

## Slide 74: History
Hand-written/typed-different formats for horizontal and vertical control points
WDDProc-DOS-unified format-printed
WinDesc-Windows-D-File format-web

## Slide 75: Project Header Information

## Slide 76: The Description Header
Key fields: SSN, DNR code, Rec code
Enter from left to right from the top down
Some boxes populate subsequent boxes
Contains most mark attributes
Data must meet stringent NGS standards
Data will be loaded and stored in separate tables/fields in the NGS IDB
Used to generate the official NGS Datasheet

## Slide 78: Descriptive Text
Must be easily readable
Use 3-paragraph format-location, to reach, reference distances/mark details
Go from the most general to the most specific
Use proper grammar
Check spelling
Avoid personal phone numbers
May contain special notes

## Slide 80: Descriptive Text - Do
Get at least 4 reference distances
Format all descriptions
Spell check all descriptions
Use Windesc tools to help create descriptive text

## Slide 81: Descriptive Text – Don’t
Don’t use slang
Don’t omit articles (a, an, the, etc.)
Don’t duplicate text
Don’t use the term ‘standard disk’
Don’t put positions in descriptive text

## Slide 82: Positional Information
Latitude and Longitude to 0.1 seconds for bench marks via hand-held GPS measurement
Include horizontal datum
Include source, order and technique
May include other information for use with other geodetic software such as Translev
Used for geodetic computations and corrections
Used to plot mark in Google Earth and other plotting software

## Slide 86: Wrap -up
Run through with Windesc

## Slide 87: TRANSLEV

## Slide 88: Digital Leveling
Translev
Bluebooking

## Slide 89: Purpose
To insure leveling observations meet FGCS specifications and procedures
To reduce raw leveling data into standard .lvl format and finally to .hgz format for submission to NGS

## Slide 90: Translev Program Overview
Program installation and configuration
File naming conventions
Processing leveling data
Tools
Web tools
Project submission

## Slide 91: Program Installation
WindowsNT, Windows2000, WindowsXP Professional – Must have administrative privileges
Version numbering-current 5.03.02
Remove old version before installing the new
After installing, change permissions to read/write for all users

## Slide 92: File Naming Conventions
Blue Book (.hgz)
Raw (.lev, .raw, .dat, .gsi)
Error Files (.err)
Abstracts (.abs)
Report (.rpt)
Lvl/Bok (.lvl, .bok)
New-minus-old (.nmo)
Statistics (.stt)

## Slide 93: Flow Chart
FLOW
CHART

## Slide 94
Notes: Will ask for a DES.FILE

## Slide 95
Notes: HGZ.file

## Slide 96: Translating Raw Files
Raw digital level formats - .gsi, .dat, .lev
Other formats-TDS, Digiloop, xml
Must have description file containing names, PIDs, elevations and geographic positions
Entering defaults
Rod/Instrument supporting files

## Slide 98: The .lvl File
Editing the .lvl file
Checking the .lvl file
Fixing errors in the .lvl file
Importing the .lvl file to create the *40* series records in the .hgz file
Notes: LVL Files

## Slide 99
Notes: Explain .lvl

## Slide 100
Notes: Import .lvl

## Slide 101: Importing .lvl Files
Notes: Importing .lvl

## Slide 102
Notes: HGZ File & 40 series records

## Slide 103: Creating Abstracts
Date discontinuity errors
Rejections
Rod/Instrument data
Inverse-running length differences
Refraction corrections
The Neighbor File
The Segment File
Notes: Abstracts

## Slide 104
Notes: Creating Abstract

## Slide 105
Notes: Explain Abstract

## Slide 106
Notes: HGZ File

## Slide 107: Tools
Plotting
Creating statistical reports
Creating new-minus-old reports
Astronomic positions
Temperature profile prediction
Renumbering
Time zone calculator
Notes: Tools in Windesc.

## Slide 108: Creating a Plot

## Slide 110: Creating a Statistical File

## Slide 112: Creating the New-minus-old File

## Slide 117: Web Tools
Aerial view (Google Earth)
Level projects
Updating files

## Slide 119: Level Projects for Marks

## Slide 121: Project Checklist
.hgz file created and checked
.lvl file(s) created, checked, combined
Abstract file created & checked
New-minus-old file created
Ties checked
Project report created

## Slide 122: Files for Submittal
Description (.dsc) file
Combined raw (.gsi, .lev, or .dat) file
Combined (.bok) file
VERTOBS (.hgz) file
Abstract (.abs) file
Project report (.rpt) file
CD of photos

## Slide 123: Run TRANSLEV

## Slide 124: End of Line-24 K!!