## Slide 1: Adjustment Slides

## Slide 2: Normal Adjustment Sequence
Minimum constrained geometric (horizontal)
  Constrain 1 CORS (3D) (3D=LLh)
  Checks internal consistency of network
  Compare computed vs published CORS coord.
Fully constrained geometric
  Constrain all CORS (3D) (3D=LLh)
  Produces final set of adjusted geometric coordinates (LLh)
2013-08-07
Step 4 : Network Adjustment
<number>

## Slide 3: Normal Adjustment Sequence cont.
Minimally constrained orthometic (vertical)
  Constrain 1 CORS (Hor-only) (LL) and…
  Constrain 1 NAVD 88 BM (Ver-only)
    Select Geoid18 and enter published NAVD 88 orthometric height for the constrained BM
  Compare computed orthometric heights to published orthometric heights for all other BM in project.
    Shows which are “Valid”, i.e., the computed and published height agree within some tolerance (project specs, your comfort level)
2013-08-07
Step 4 : Network Adjustment
<number>

## Slide 4: Normal Adjustment Sequence cont.
Fully constrained orthometric (vertical)
  Constrain 1 CORS (Hor-only) (LL) and
  Constrain all “valid” NAVD 88 BM (Ver-only)
    Select Geoid18 and enter published NAVD 88 orthometric heights for the constrained BM’s
  Shift of computed orthometric heights for unconstrained stations from min and full constrained adjustment should be less than what your vertical tolerance is.
  Produces final set of adjusted NAVD 88 Heights
2013-08-07
Step 4 : Network Adjustment
<number>