## Slide 1: OPUS Projects Manager Training
ngs.opus.projects@noaa.gov
Introduction

## Slide 2: A few words before beginning.
OPUS Projects is a Web-based utility implying that access to the Internet and use of a Web browser are required.
JavaScript must be enabled in your browser and pop-up blocking may have to be turned off.
If you have difficulty configuring your browser, contact your instructor or the OPUS Projects team.

## Slide 3: Operating systems and browsers.
No guarantee that OPUS Projects will work with your computer is implied. It has been successfully tested on X86 PC’s in various combinations of the following…
Operating systems: Linux® and Microsoft Windows ®
Browsers: Chrome™ Firefox® Internet Explorer® 8 through 11 Opera® Safari®

## Slide 4: Workshop Outline
Introduction
Step 1 : Creating a Project
Step 2 : Uploading Data
Step 3 : Session Processing
Step 4 : Network Adjustment

## Slide 5: What’s in this training?
This presentation is a brief introduction to and overview of OPUS Projects.
The remaining presentations are a cookbook of the steps needed to complete most projects. Like most cookbooks, you will see steps completed in detail, but the technical justification for the steps will be minimal.

## Slide 6: What’s not in this training?
This training should not be considered an endorsement of any specific project design, field technique, hardware or software.
Nor does it represent specific NGS project guidelines. However, a familiarity with these guidelines may be valuable. For more information, visit:
http://www.fgdc.gov/ http://geodesy.noaa.gov/AERO/aero.html http://geodesy.noaa.gov/heightmod/

## Slide 7: What’s the bottom line?
By completing this training:
You’ll have enough information to successfully use OPUS Projects for your own projects.
You’ll be authorized to create your own projects.

## Slide 8: A project has been created for you.
It is different than the one shown in this training and the access information has been customized to you.
Access information (keywords) for your training project should be in your hands by this time. If you haven’t received this information, let your instructor know.
Your training project will be available for about a month to give you time to practice.
Notes: After about a month, you’ll receive an email warning that your training project will be deleted. If you’d like your training project to be preserved longer than a month, contact the OPUS‐Projects team.
Everybody have their project access information?

## Slide 9: The state of your training project.
Under the assumption that most of you are already familiar with OPUS, the data has already been uploaded to your training project.
No processing has been completed in your project. However, if you’d like copies of the training processing results, let your instructor know.

## Slide 10: The training data set.
Because we are assuming familiarity with OPUS, we describe uploading data to OPUS quickly emphasizing aspects specific to Projects.
If you are unfamiliar with OPUS, uploading data to your project is a great chance to practice.
The data files and descriptions shown in the training are available in a ZIP file at https://geodesy.noaa.gov/pub/corbin/Martin-OP-Training-Feb-2023/
Notes: If anyone needs help downloading or extracting the contents of the ZIP file, let an instructor know during a break.

## Slide 11: What’s in the ZIP file?
The ZIP file contains:
20 RINEX data files with names like gree275a. All will have the extension 06o (type: 13O).
8 photos with names like DO7740-GREENSBORO_BEND-1-20130930. All will have the extension jpg or jpeg (type: JPEG image).
A pdf file for each observation of each mark in the training data set.

## Slide 12: What is the training data set?
These data are from sites in Virginia.
The start and end times, data interval, ARP heights, antenna and receiver metadata are valid.
The photos and descriptive information appear meaningful but should be considered arbitrary and for training purposes only.

## Slide 13: Anything else before we begin?
Please ask questions!
Feel free to “work along” with the presentations.
Recorded tutorials are located here: https://geodesy.noaa.gov/optrainingvideos/ Be aware that some things may have changed slightly between the time that these videos were made and the date of this training

## Slide 14: A brief overview of OPUS Projects.

## Slide 15: What is OPUS Projects?
OPUS Projects offers Web-based access to simple visualization, management and processing tools for multiple marks and multiple occupations. Some of its advantages include:
Data uploading through OPUS.
Processing using the PAGES software.
Graphical visualization and management aids.
Limited support of bluebooking.

## Slide 16: Why complicate OPUS?
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: OPUS solutions are independent of each other, but they may be indirectly related …
Marks might “share” their environment (similar atmosphere over both).
Data might “share” the same GNSS constellation geometry.
OPUS solutions may “share” some or all of the same CORS.
Etc.
These correlations can increase with project size.

## Slide 17: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: Combining your data logically can improve results:
Neutral atmosphere (tropo) corrections can be improved which, in turn, can help with other things like phase ambiguity resolution.
Common mode effects, like baselines connecting the same CORS common to different marks, can be de-correlated.
OPUS Projects tries to logically group data together:
Data from the same mark are associated with that mark.
Marks simultaneously occupied are grouped into sessions. Session processing improve consistency and accuracy.

## Slide 18: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: These concepts can be extended to other marks and other sessions.

## Slide 19: Why complicate OPUS?
network adjustment
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: Ultimately, combining session solutions into an adjustment can improve accuracy for the entire network.

## Slide 20: What’s in it for me?
OPUS solutions = pretty good, but each treated as independent and assumes “perfect” CORS.
Sessions = simultaneously-observed marks processed together in sessions increases consistency.
Adjustments = interlinking sessions through network adjustments increases accuracy.

## Slide 21: Do we really need another OPUS flavor?
The practical answer is probably yes. The NGS and other groups have a history of projects whose specifications can’t be entirely supported by OPUS.
The academic answer is probably yes. As good as OPUS does, and that is very good indeed, sacrificing simplicity for flexibility can improve results.

## Slide 22: What does this mean operationally?
Plan your project
Collect data and metadata (photos and mark descriptions)
Gather data and metadata onto one computer
Process the data
Perform a network adjustment
Publish (if desired)
Notes: Very broadly, you probably go through these or very similar steps for every project.

## Slide 23: What does this mean operationally?
Plan your project
Create an OPUS project
Collect data and metadata
Upload data to your project using OPUS
Process sessions
Perform network adjustment
Publish (if desired).
Notes: The steps when using OPUS Projects are very similar, but the steps in black use OPUS Projects rather than your own resources.

## Slide 24: What does this mean operationally?
Admittedly an oversimplification, nevertheless there is value in thinking of OPUS Projects as four steps with an optional fifth step.
Creating A Project
Uploading Data
Session Processing
Network Adjustment
Publishing to the NGS Integrated Database
Notes: Publishing to the NGS Integrated Database is covered separately (Bluebooking using OPUS Projects).

## Slide 25: The steps represented graphically.
Processor or Manager
Data &
Metadata
Network
Adjustment
Manager
Session
Solution
Session
Solution
Session
Solution
Session
Solution
Copy To User
Your OPUS Project
Copy To User
Copy To User
OPUS Solution
OPUS Solution
OPUS Solution
Publish To NGSIDB
Notes: Projects exists on an NGS server and are only accessible through the OPUS Projects Web interface.
The entire white box represents a project.
The allocation of resources for a project is step 1.
The orange icons on the left represent step 2: uploading data into the project.
The green icons in the middle represent step 3: processing individual sessions and solution quality control.
The blue icons on the right represent step 4: network adjustment.
The purple icons on the far right represent the publishing options.

## Slide 26: More Granular look (Submitting)
Propose a project and submit a Survey Proposal
Create a project in OPUS-Projects 5
Set/Verify preferences
Upload Description Files prepared in WinDesc and upload Field Logs
Upload all RINEX files to Beta OPUS-S. (Upload RINEX files for both the base stations and RTN Validation Station)
Review OPUS-S solutions
Select CORS for inclusion as control
Upload GVX file(s)
Process static sessions
Adjust the network
Upload the photos on all passive marks, upload a project report, and submit project to NGS

## Slide 27: Are there any side effects?
Exploiting a Web-based application like OPUS Projects can mean:
Less backtracking.
  Data consolidated while teams are in the field.
  Rapid data quality assessment.
Simpler logistics.
  Data are immediate availability through on-line storage.
  Automated organization.
Less worry.
  Share information.
  Share results.

## Slide 28: Limitations?
Uploads through OPUS-Static.
  Dual-frequency.
  2 hrs ≤ data span ≤ 48 hrs (≤ 2 GPS midnights).
  Observation interval = a factor of 30 (seconds).
Minimum project size.
  None
Maximum project size.
  There are practical limits to a project’s maximum size.
  About 100 marks in a single session.
  Number of data files < a few hundred.
Notes: The number of data files < a few hundred implies:
A few marks occupied many times.
Many marks occupied a few times.

## Slide 29: G.I.G.O.
We still need surveyors. We hope OPUS Projects can help, but it can’t do your job for you.
Follow your project’s specifications.
Use best practices and careful field procedures.
Select permanent marks of public interest.
Good coordinates come from good data.
http://gis.larc.nasa.gov/
Notes: G.I.G.O. = garbage in, garbage out

## Slide 30: A little OPUS Projects history.
2005: Weston and Gwinn began initial development on OPUS Projects.
2006: Several projects were completed as part of a proof-of-concept. Although the impressions were positive, the development stalled.
2007: Development restarted.
2010: OPUS Projects goes beta.
2013: OPUS Projects goes operational.

## Slide 31: Things To Come.
OPUS Projects improves because of your criticisms and suggestions. Although we can’t act upon every comment, we do appreciate and consider every one. They have and will continue to steered development.
Here are a few things already in the works:
Better integration with CORS.
Importing vectors (RTN/RTK or other) Currently in OP 5.0 (BETA)
M-Pages (Multi Constellation)
  Could allow data files <2 hrs in duration
Notes: Allowing data files < 2 hrs in duration. Target: Allow OPUS Rapid-Static and Static uploads by January, 2014.
Better integration with CORS. Target: ? Work has begun on a new interface.
Better support for publishing to the NGSIDB.
  B- and g-files are available now.
  Better integration with conventional publishing activities.
  Act as a catalyst for other improvements (simpler, faster, more reliable).

## Slide 32: OPUS Projects Manager Training
Dan Martin
Dan.martin@noaa.gov
240-676-4762
Introduction
Notes: Any questions?
I’ll ask again, can everyone see the screen and hear me?
Does everyone have connectivity to the Web?