## Slide 1: GNSS Background for OPUS Projects
Gerald L. Mader
National Geodetic Survey
Silver Spring, MD
2014-05-29
<number>
GNSS Background

## Slide 2: Background
Before we begin the OPUS Projects training, it would be a good idea to go over some background on GNSS.
Although these concepts are valid for any GNSS, occasionally we’ll explicitly discuss GPS, the only GNSS currently used in OPUS.
This is not a review of the equations, but rather a discussion of the qualitative factors that affect precision and accuracy.
This should help explain why-we-do-what-we-do and how to use OPUS Projects wisely.
2014-05-29
<number>
GNSS Background
Notes: GNSS = Global Navigation Satellite System
<number>

## Slide 3: GPS Signals
Pseudo Random Noise (PRN) code
Carrier phase
Your receiver records GPS pseudo-range and carrier phase at 2 frequencies: L1 and L2.
These data are contained in the RINEX file.
Carrier phase has an unknown initial integer bias that must be determined.
2014-05-29
<number>
GNSS Background
Notes: RINEX = Receiver Independent Exchange format (http://igscb.jpl.nasa.gov/components/formats.html).
OPUS converts uploaded files, as necessary, to the RINEX format in preparation for processing. So regardless of the format of the file uploaded to OPUS, the processing will use RINEX formatted files.
<number>

## Slide 4: RINEX File
There are only two characteristics of a RINEX file that really matter:
  Where the data was collected.
    We may need to know available references for the relative positioning.
  Observation span of the data
    Determines the technique for finding the phase biases.
      Ambiguity search for short baseline/short span.
      Least squares for longer baselines/ longer spans.
    Determines the precision of position solutions.
2014-05-29
<number>
GNSS Background

## Slide 5: RINEX File
A single RINEX file is sufficient to get a position.
  Pseudo-range point positions: ̴10m.
  Carrier phase Precise Point Position (PPP): ̴cm’s.
Why doesn’t OPUS do PPP positioning?
  Long convergence times.
  Harder to get integer biases.
  Positions not necessarily in NSRS or relative to passive control.
2014-05-29
<number>
GNSS Background

## Slide 6: Relative Positioning
OPUS, including OPUS Projects, uses relative positioning.
  The phase data between 2 receivers is explicitly differenced.
  The 2nd receiver is usually a reference at known position.
  Gives the position of 1st mark relative to the 2nd.
2014-05-29
<number>
GNSS Background

## Slide 7: Relative Positioning
Why do relative positioning?
  Positions can be computed with respect to known marks in NSRS.
  Mitigates any orbit error, and ionospheric and tropospheric propagation effects.
  Phase biases are still integers.
The connection between the 2 marks will be referred to as the baseline.
Be aware that OPUS Projects requires you to identify the mark(s) to which your project mark positions will be relative.
2014-05-29
<number>
GNSS Background

## Slide 8: Baseline Length
What is the impact of the separation between these 2 marks, A.K.A. baseline length? The principle factors that affect precision as a function of baseline length are:
  GNSS orbit accuracy.
  Signal propagation.
2014-05-29
<number>
GNSS Background

## Slide 9: GNSS Orbit Accuracy
An old rule-of-thumb says the effect of orbital errors scales by the ratio of the baseline length to the satellite distance. For the example here, that ratio would be:
OPUS uses the orbits produced by the IGS which are accurate to better than 5 cm. The likely effect of orbit accuracy on positions computed by OPUS is
5 cm  0.01 = 0.05 cm
Less than a mm – in other words, orbit error is not a significant factor.
200 km baseline
GPS satellites approximately 20,000 km above earth
200 km
20000 km
= 0.01
2014-05-29
<number>
GNSS Background
Notes: IGS = International GNSS Service
For more information about IGS orbit accuracies, see:
http://acc.igs.org/
<number>

## Slide 10: Signal Propagation
As GNSS signals pass through the Earth's atmosphere, they are distorted. These distortions are called signal propagation effects.
The offending parts of the atmosphere are commonly called the ionosphere (charged) and the troposphere (neutral), and their corrections are handled differently.
2014-05-29
<number>
GNSS Background
www.windows.ucar.edu/spaceweather/images/atmos_layers_new_gif_image.html
Notes: The troposphere is the name for the lowest (closest to the solid surface) region of the Earth’s atmosphere and where almost all the water vapor resides.
<number>

## Slide 11: Signal Propagation
When baseline lengths are very short, the signal distortions suffered at each mark are very similar and differencing, like that done in OPUS, removes these effects.
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
ionosphere
troposphere
Earth
2014-05-29
<number>
GNSS Background
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
ionosphere
troposphere
Earth
But as the baseline length increases, the signal distortions at each mark becomes increasingly different and other techniques must be employed to correct them.

## Slide 12: Ionosphere
Outermost layer of the Earth's atmosphere.
Contains positively charged atoms and negatively charged electrons.
Caused by solar radiation.
Strong day/night effect (diurnal).
Charge density is highly variable.
Limits the distance over which single frequency GNSS is usable.
2014-05-29
<number>
GNSS Background

## Slide 13: Ionosphere
Effect on GNSS signals depends on frequency.
  GPS is designed with 2 frequencies, L1 & L2, to correct for ionosphere effect.
  L1 & L2 data can be combined to form an ionosphere-free, or ion-free for short, linear combination (L3 in PAGES jargon).
  Ion-free combination eliminates ionospheric effect.
2014-05-29
<number>
GNSS Background

## Slide 14: Ionosphere
Because the ion-free combination includes two measurements (L1 & L2), it is noisier than either single frequency measurement.
So, L1-only is preferred on very short baselines where ionospheric effects are eliminated by differencing. (The increased noise of L3 can be greater than the correction.)
But this requires a rule about what distance to switch from L1-only to ion-free. Such rules are imperfect and discrete transitions are problematic.
2014-05-29
<number>
GNSS Background

## Slide 15: Ionosphere
OPUS Projects solves the L1-only to ion-free transition problem by using the L6 (in PAGES jargon) combination: L6 = L1 + w * ion(L1,L2) where ion(L1,L2) is the ion-free correction and w goes from 0 to 1 depending upon baseline length.
The function w was designed such that most of the transition occurs from 5 to 15 km.
This gradually applies the ionospheric correction as a function of baseline length, so OPUS Projects users need not worry about ionosphere.
2014-05-29
<number>
GNSS Background

## Slide 16: Troposphere
The troposphere has 2 components:
  Hydrostatic (or dry) - major component.
  Wet (water vapor) - minor component.
The hydrostatic component is very well modeled from surface pressure derived from a global, seasonal model.
The wet component can be highly variable and cannot be modeled well.
2014-05-29
<number>
GNSS Background
Notes: 9
<number>

## Slide 17: Troposphere
Elevation
Models estimate tropo delay at zenith (approx. 2.3m at sea level).
A mapping function then scales the zenith value of tropo delay as a function of elevation.
OPUS Projects adjusts the wet zenith value of the tropospheric delay at each mark.
These corrections are typically a few cm (when done correctly).
2014-05-29
<number>
GNSS Background

## Slide 18: Troposphere Azimuthal Symmetry
15°
8 km
̴30 km
2 km
̴ 8 km
The troposphere has a scale height of about 8 km (the height at which the density drops by 1/e or by about 63%). For an elevation cutoff of 15°, typical for OPUS Projects, we’re assuming the troposphere is symmetric out to a radius of ̴30km around each mark.
The scale height for the water vapor is about 2 km. So for a 15° elevation cutoff, the signal path will be above most of the water vapor beyond a radius of about 8 km.
The assumption of azimuthal symmetry, while not perfect, should be fine in almost all cases except near marine boundaries or for fast moving fronts. But even in these exceptions, it is still very good.
2014-05-29
<number>
GNSS Background

## Slide 19: Troposphere Numerical Issues
Nearby marks see the same satellites at nearly the same elevation making it difficult, numerically, to resolve these tropo corrections. This can result in “bad” tropo corrections and consequently suspicious heights.
Including data from a mark, or marks, sufficiently distant that the same satellites are seen at significantly different elevations will resolve these numerical problems resulting in “better” tropo corrections and more reliable heights.
2014-05-29
<number>
GNSS Background

## Slide 20: Troposphere Corrections
A general qualitative scheme for tropo corrections on baselines of varying lengths would be:
  Very short length: no tropo correction on either mark.
  Moderate length: correction at 1 mark (relative tropo).
  Very long length: corrections at both marks (absolute tropos).
However this would require rules for distances to impose these discrete transitions – difficult to describe for all cases thereby creating an unnecessary burden on users.
2014-05-29
<number>
GNSS Background

## Slide 21: Troposphere Corrections
A simple alternative is to always include a distant mark.
The availability of CORS makes this universally applicable.
OPUS Projects makes it easy to select and add CORS to all sessions (if not already there).
2014-05-29
<number>
GNSS Background
Notes: <number>

## Slide 22: Troposphere Corrections
OPUS Projects recommends including one or several distant marks (>800km) to stabilize the tropo corrections.
This probably seems counter-intuitive for projects covering small areas; however, the alternative, trying to subjectively judge what type of tropo corrections should be applied, has risks and often results in inconsistent processing strategies within a project.
2014-05-29
<number>
GNSS Background
Notes: Examples are given in other presentations.
<number>

## Slide 23: Troposphere Corrections
bm02 ZEN WET 13/05/01 18:00:00.00 -0.30152(0.04131)M .10+01 73
bm02 ZEN WET 13/05/01 20:00:00.00 0.15089(0.01159)M .76+00 73
bm02 ZEN WET 13/05/01 22:00:00.00 0.25114(0.01326)M .91+00 73
bm02 ZEN WET 13/05/02 00:00:00.00 -0.17600(0.01359)M .80+00 73
bm02 ZEN WET 13/05/01 18:00:00.00 0.05276(0.00456)M .10+01 151
bm02 ZEN WET 13/05/01 20:00:00.00 0.04918(0.00117)M .74+00 151
bm02 ZEN WET 13/05/01 22:00:00.00 0.05602(0.00107)M .90+00 151
bm02 ZEN WET 13/05/02 00:00:00.00 0.02847(0.00140)M .72+00 151
50km baseline without distant mark
50km baseline with distant mark
“Poor” tropo corrections
<number>
“Good” Tropo corrections
Here is an example of tropo corrections from the processing logs for a 50 km baseline with and without including a distant mark. The improvement when the distant mark is included is clear.
Tropo corrections estimated every 2 hr
2014-05-29
<number>
GNSS Background

## Slide 24: Baseline Length
After all that discussion it turns out that baseline length is not a factor for processing.
The CORS selected as a reference mark, for example, need not necessarily be the closest CORS.
However, there is another consideration that depends on baseline length.
2014-05-29
<number>
GNSS Background

## Slide 25: Mutual Visibility
For a variety of reasons, only observations above a specified elevation angle are used in processing. This elevation cutoff is typically 12 – 15 and is specified as part of the OPUS Project processing.
Because OPUS Projects uses differential processing, only satellite observations above the elevation cutoff at both ends of a baseline will be used. This is called mutual visibility.
Due to the Earth's curvature, the amount of unusable data increases with baseline length.
2014-05-29
<number>
GNSS Background
Notes: Some reasons to exclude low elevation observations:
Increased tropospheric effects that are more difficult to remove.
Increased ionospheric effects that are more difficult to remove.
Increased multipath implying noisier data with more cycle slips.
Often, more obstructions.
<number>

## Slide 26: Mutual Visibility
About how much data is unusable with baseline length?
If a baseline is about 110 km in length, a satellite will appear to have about a 1° difference in elevation from the ends of a baseline when looking “down” the baseline’s length. Less off to side of baseline.
To get an idea how much data is lost at the 1st mark while waiting for satellite to clear the cutoff at the 2nd mark, suppose a rising satellite is at the elevation cutoff at the 1st mark, but only 1° below the cutoff at the 2nd.
Maximum satellite movement of 30°/hr implies at least 2 min of data lost. For satellites not reaching zenith (slower movement), data loss of 4-5 min is more typical.
2014-05-29
<number>
GNSS Background

## Slide 27: Mutual Visibility
For data spans of 2 hr, a 5 min data loss, or about 4%, is generally considered tolerable.
To keep data loss < 5%, baseline lengths should not exceed roughly 100 km. If this is not possible, longer occupations may be necessary to compensate.
2014-05-29
<number>
GNSS Background

## Slide 28: Baseline Length Considerations
Shorter baselines have more observations.
Longer baselines improve tropo estimations.
OPUS Projects processing can, with the appropriate processing strategy, optimize these factors along with relative precision of project marks and accuracy within the NSRS.
2014-05-29
<number>
GNSS Background

## Slide 29: A New Paradigm
GNSS projects have inherent characteristics that are very different from those of optically measured geodetic networks
These differences provide an opportunity to rethink how projects should be processed

## Slide 30: Optical Surveys
In a survey done with conventional optical survey tools, a total station for example, the marks of the network are connected by direct measurement of angles and distances.
These measurements are inseparable from the marks they connect.
This creates vectors free to float in space until constrained to control.
An error at any network node will propagate through network.
2014-05-29
<number>
GNSS Background

## Slide 31: GNSS Surveys
GNSS measurements of the same network are not connected to each other.
GNSS measurements are independent.
There are no inherent connections between project marks as in optical surveying.
Computing the position of each mark relative to the same reference is optimal.
Although possible, artificially creating “chains” of dependencies among project marks is not optimal.
2014-05-29
<number>
GNSS Background

## Slide 32: An Appropriate Processing Strategy
24hr
24hr
>2hr
Hub
Select a CORS to act as the local Hub creating baselines < 100 km if possible.
  Recall that a Hub is a mark to which baseline connections are preferentially made.
  All project marks are positioned relative to the Hub, not to each other.
  Assuming the Hub is a CORS, no data from the project marks is lost because of mutual visibility.
Include a distant CORS for reliable tropo correction estimation.
  CORS (Hub) to CORS (distant) implies ample data with no mutual visibility issues.
2014-05-29
<number>
GNSS Background
Notes: Hub comes from the image of a wagon wheel hub. All spokes connect to the wheel’s hub. Similarly, all baselines try to connect to the Hub.
<number>

## Slide 33: GNSS Processing Principles
Two principles to bear in mind:
  Relative Positioning – Precision
    Project marks share common Hub. A Hub is a mark to which baseline connections are preferentially made.
    This minimizes common-mode errors.
  Absolute Positioning – Accuracy
    Hub(s) are adjusted into NSRS using multiple CORS.
Examples given in subsequent presentations.
2014-05-29
<number>
GNSS Background
Notes: <number>