## Slide 1: OPUS Projects Manager’s Training Module 5: Develop Survey Schedule

## Slide 2
An Overview of the Process
NGS map (using existing tutorials)
Windesc/Photos (already exists)
Recon/Project Planning
Develop Survey Schedule
Project Proposal
Logsheets (GDX RTN Logsheets?)
Create Project in OP/Upload RINEX
QA/QC extended solution stats for low quality CORS, possible blunders
GNSS Vectors, RTK and GVX
Uploading of WinDesc files, photos and logsheets
Preparing for session processing
Session Processing
Analyzing the solution statistics
Preliminary Adjustment, Network Adjustments Analysis, and Determining Control
Submitting your Project to NGS
Project Report
Bad, bad data!

## Slide 3
Please note, the current version of OPUS Projects may look slightly different than the screens in this presentation. The functionality generally remains the same.

## Slide 4: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 5: A Little Background Information
Understanding a little about how processing is done within OPUS Projects informs your planning and helps ensure that you observation meet your project needs.
Plan the work and work the plan

## Slide 6: Independent vs Dependent Baselines
Number of independent (non-trivial) baselines = n-1
Total number of baselines = n(n-1)/2
Independent (non-trivial)
Dependent (trivial)

## Slide 7: Sequential or (Baseline) Processing vs Simultaneous or (Session) Processing
Baseline Solution
  One baseline at a time
  Ignores mathematical correlations between baselines observed in the same session.
  Must include all independent and dependent baselines for each session
  Must be properly scaled before combining sessions into network adjustment
Session Solution
  Solution from simultaneous processing of all independent baselines with mathematical correlations between baselines

## Slide 8: Which Baselines to Create? (non-OPUS Projects)

## Slide 9: Independent Baselines Only by Session

## Slide 11: OPUS Projects uses Session Processing
By default, independent baselines for each session are created from a single “HUB”
  Think of the hub and spokes of a wheel
By default, OPUS Projects will select the most central CORS within a session and designate it as the HUB
The relationship between all (non-HUB) marks (dependent baselines) are represented by mathematical correlations.
This approach has some significant benefits, and will be discussed further in the session processing module.

## Slide 13: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 14: Which Marks to Observe together in a Session
Marks that are intervisible, e.g., a mark and it’s azimuth mark
Any group of marks for which relative “Local Accuracies” are desired
  Points that will control the beginning and end of a future traverse
  Any place where you want to maximize the internal precision between points
Existing Passive Control (especially vertical) and nearest neighbors
Vertical Control
Real Time Base Station

## Slide 15: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 16
 | Requirement | PRIMARY | SECONDARY | LOCAL
4.1 | Requirements for ALL METHODS Repeat occupations and offset time | Offset sessions/occupations by 3 to 21 hours. See Specifications for detailed explanation. |  | 
4.2 | Requirements for OPUS PP Required TOTAL Static GNSS Observation Time (T) Recommended GNSS Session Durations | 0 to 200 km T = 20 hours (2) 10 hour sessions or (3) 7 hour sessions or (4) 5 hour sessions Requires at least 1 session on a different day. | 0 to 100 km T = 4 hours 0 to 150 km T = 6 hours 0 to 200 km T = 8 hours (2) 2 hour sessions (2) 3 hour sessions (2) 4 hour sessions | 0 to 200 km T = 4 hours (2) 2 hour sessions
Table 4 - Standards for Observation Requirements by Method
4.3 | Requirements for GDX PP - Number and duration of sessions | 3 sessions 0 to 25 km 60 minutes each 25-50 km 90 minutes each Requires at least 1 session on a different day. | 3 sessions 0 to 25 km 30 minutes each 25-50 km 60 minutes each | 3 sessions 0 to 25 km 15 minutes each 25-50 km 30 minutes each
4.4 | Requirements for GDX NRTK - Number and duration of occupations | (6) 5 minutes Requires at least 3 occupations on a different day. | (3) 5 minutes | (3) 5 minutes
4.5 | Requirements for GDX SRTK - Number and duration of occupations | Not allowed | (5) 5 minutes Requires at least 2 occupations on a different day. | (4) 5 minutes Requires at least 1 occupation on a different day.

## Slide 17: Example observation scenarios for meeting the OPUS PP Offset Requirement If individual observations exceed 5 hours, then no specific offset is required

## Slide 18: Example Cont…

## Slide 19: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 20: What Resources are Available?

## Slide 21: Resources
How many field observers are available?
  Are there a different number of observers available on different days?
  Are there certain marks the require specific observers?
    Hike required
    4WD vehicle required
How many sets of equipment are available?
  Certain antenna, tripod, extension, cable length needed because of how/where the mark is set?

## Slide 22: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 23: Field Constraints - Travel
How much time is needed for all observers to get to next station/session?
  Miles/speed limits
  Traffic/City driving
  Off-road travel or hike required

## Slide 24: Field Constraints – Site Access
Hours of access
  Restricted to certain days/hours
  Gated
  Security
  High water/tide

## Slide 25: Field Constraints – Site Safety
Can the equipment be left unattended during long observations?
  Can the equipment be secured (lock, cable, etc…)

## Slide 26: Develop the Schedule
Draw sessions based on available resources
Assign Day, Start time, and duration to the first session
If conducting more than one session per day
  Determine longest travel time between session A and session B stations and use that to determine what time the next session will begin.
Write stations for each session onto schedule grid for the first day
Repeat process for next day. Stagger start time by 3-hours if it is a repeat observation
Session | Start UTC | End UTC | dd/mm/yyyy Julian Day ddd |  | 
 |  |  | John | Bill | Dan
A | 1200 | 1500 | 0001 | 0003 | 0005
B | 1530 | 1830 | 0002 | 0005 | 0004
0001
0002
0003
0005
0004

## Slide 27: Session and RINEX Naming
Sessions are named using the year, Julian Day (numerical day of year), and sequential session of the day. For example, if three sessions are observed on January 1, 2022 the three sessions would be named
  2022001A
  2022001B
  2022001C
The RINEX file for any observation is named by using the 4-character id, followed by the session, with the extension yyo where yy is the two digit year, and o designates that it is an observation file.
If we were observing station “BOXER” on the first session of the day on December 31, 2022, and we have assigned BOXER a 4-character id of BOXR, then the corresponding RINEX file will be named BOXR365A.22o

## Slide 28: RINEX File Naming Convention aaaadddb.yyo

## Slide 29
Thank you for viewing this module. Please visit [url tbd] to view additional training materials.
This module was written by XX, narrated by XX, and
recorded in November, 2022.
Visit https://geodesy.noaa.gov/OPUS-Projects/OpusProjects.shtml for more information on OPUS Projects.

## Slide 30: END
End of Module 5