# LEICA DNA03 DIGITAL LEVEL SETTINGS

The following settings can be set from the “Meas & Rec” screen which comes up when the level is first turned on.  If the level is in “PROGRAM” mode, exit the program to see the “Meas & Rec” screen.

# _______________________________________________________________________________

#### SET UNITS

From the “Meas & Rec” screen:	Press the < SHIFT > < PROG > keys.

From the “MENU” screen, select < 2  ALL SETTINGS > then press the < enter > key.

From the “ALL SETTINGS” screen, select < 4  UNITS > then press the < enter > key.

From the “SET UNITS” screen, set the following:

Distance  :	metre

Temp. 	    :	° C

Highlight < SET >, then press the < enter > key.

_______________________________________________________________________________

## SET DATE AND TIME

From the “Meas & Rec” screen:	Press the < SHIFT > < PROG > keys.

From the “MENU” screen, select < 2  ALL SETTINGS > then press the < enter > key.

From the “ALL SETTINGS” screen, select < 5  DATE / TIME > then press the < enter > key.

From the “SET DATE / TIME” screen, set the following:

Date		:	dd.mm.yyyy

Time (24HR)	:	hh:mm:ss

Highlight < SET >, then press the < enter > key.

# _______________________________________________________________________________

# SET CURVATURE CORRECTION OFF

From the “Meas & Rec” screen:	Press the < SHIFT > < PROG > keys.

From the “MENU” screen, select < 2  ALL SETTINGS > then press the < enter > key.

From the “ALL SETTINGS” screen, select < 2  MEASURING > then press the < enter > key.

From the “MEASURING SETTINGS” screen, set the following:

CodeSet	:	Before

Decimals	:	0.00001m

GSI-Format	:	GSI – 8

EarthCurv	:	No

Highlight < SET >, then press the < enter > key.

# _______________________________________________________________________________

# SET INCREMENT MODE

From the “Meas & Rec” screen:	Press the < SHIFT > < USER > keys.

From the “FUNCTIONS” screen, select <4  PtID & INCREMENT> then press the <enter> key.

From the “PtID & INCREMENT” screen, set the following:

Running PtID

PTID:		1

INCR:		1

Highlight < SET >, then press the < enter > key.

# _______________________________________________________________________________

# SET MEASUREMENT MODE

From the “Meas & Rec” screen:	Press the < MODE > key.

From the “MEASURE MODE” screen, set the following to:

Mode		:	Mean s

n		:	leave blank

n min		:	3

n max		:	10

sDevM / 20m	:	0.00002 m

Highlight < SET >, then press the < enter > key.

# _______________________________________________________________________________

#### ASSIGN “CODE” TO USER KEY

From the “Meas & Rec” screen:	Press the < SHIFT > < PROG > keys.

From the “MENU” screen, select < 1  QUICK SETTINGS > then press the < enter > key.

From the “QUICK SETTINGS” screen, toggle “USER-Key” to “Code” like the following:

Contrast  	:	50%

EarthCurv	:	No

USER-Key	:	Code

Decimals	:	0.00001m

Highlight < SET >, then press the < enter > key.

_______________________________________________________________________________