## Slide 1: Section 2
Part I : History and Context
  NGS and the NSRS
  Geodetic Control Overview
  Horizontal Datums and Reference Frames (4 Slides)
  Vertical Datums
  Historic Datums of the United States
  Decision to Modernize
Notes: Welcome to Section 2 of the Modernized National Spatial Reference System.
  I’m David Zenk, National Geodetic Survey Advisor for the Northern Plains Region.
  I will be your narrator for this section.
In this section, we’ll discuss:
Horizontal Datums and Reference Frames
Vertical Datums and
Historic Datums of the United States

## Slide 2: Horizontal Datums / (Geometric) Reference Frames
What are they?
  A coordinate system implied by points with coordinates
    Parallels, meridians, and the geocenter are defined mathematically but don’t have a physical manifestation in the real world
So, what is the difference between “system, frame, and datum” ?
  A reference system is a set of rules.
  A reference frame or datum is a practical implementation of the rules.
There could be several implementations of a single set of rules.
Notes: Let’s discuss a few terms now –
  Reference System, Reference Frame, and Datum
They share characteristics, such as size, shape, and orientation of a coordinate system and its relationship to the Earth, but they differ in their specific meaning.
  A reference system is a set of rules which define the basic parameters.
  A reference frame or datum is the practical implementation of the rules.
Therefore, there could be several implementations of a single set of rules.

## Slide 3: Horizontal Datums / (Geometric) Reference Frames
Realization is:
  Realization is defined as the practical implementation of a concept
  Coordinates are assigned to points in a way that best represents the mathematically abstract definition
    Coordinates come from geodetic surveys of the highest accuracy
    Coordinates could stand unchanged for decades (NAD 27, NGVD 29 being the best known examples)
      Piecemeal updates from re-surveys
Realization – the process of making something real , such as implementing a reference system.
Notes: A realization is defined as the practical process of implementing a concept
Coordinates are assigned to points in a way that best represents the mathematically abstract definition
Coordinates come from geodetic surveys of the highest accuracy
Coordinates could stand unchanged for decades (NAD 27, NGVD 29 being the best known examples)
And there were piecemeal updates from re-surveys
A “realization” should be time tagged, but that REALLY didn’t happen until the NAD 83(2011) epoch 2010.00 realization of the NAD 83 datum.
It was not possible to assign a specific date for earlier realizations.
Before “global reference frames”, a realization was usually constrained by other locally determinable physical measurements, such as astronomic latitude/longitude

## Slide 4: Horizontal Datums / (Geometric) Reference Frames
Historic Definitions and Roles
  National datums were adjusted from large networks
    Often fixed to one or more points in the nation
      USSD and NAD 27: Meades Ranch
      This meant plate rotation was effectively cancelled out
  Space Age / International Efforts
    BIH (Bureau international de l'heure)
    IERS (International Earth Rotation [and Reference System] Service)
      Service of the International Association of Geodesy (IAG)
      Arbiters of the International Terrestrial Reference Frame (ITRF)
Notes: Historic Definitions and Roles
  National datums were adjusted from large networks of observations
  And were often fixed to one or more points in the nation
  For the US Standard Datum (USSD) and NAD 27, that point was Meades Ranch
  This meant plate rotation was effectively cancelled out
In the Space Age, International efforts and cooperation became important.
Several prominent agencies collectively define the ITRF
  BIH (Bureau international de l'heure)
  IERS (International Earth Rotation [and Reference System] Service)
  Service of the International Association of Geodesy (IAG)
  Arbiters of the International Terrestrial Reference Frame (ITRF)

## Slide 5: Horizontal Datums / (Geometric) Reference Frames
Ideal Frames
  ITRF
    Combination of four frames (SLR, VLBI, GNSS, DORIS)
  IGS
    Post-ITRF frame
    Most accurate GNSS orbits are in this frame
  Currently the NSRS is mathematically defined:
    Three NAD 83 frames: North America, Pacific, Mariana plates
    All 3 defined with respect to ITRF94 (same as ITRF96)
    All other ITRFs defined with transformations between ITRFs
Notes: Ideal Frames
  ITRF
  Combination of four frames (SLR, VLBI, GNSS, DORIS)
  IGS
  Post-ITRF frame
  Most accurate GNSS orbits are in this frame
  Currently the NSRS is mathematically defined:
  Three NAD 83 frames: North America, Pacific, Mariana plates
  All 3 defined with respect to ITRF94 (same as ITRF96)
  All other ITRFs defined with transformations between ITRFs

## Slide 6
Part I : History and Context
  NGS and the NSRS
  Geodetic Control Overview
  Horizontal Datums and Reference Frames
  Vertical Datums (5 slides)
  Historic Datums of the United States
  Decision to Modernize
Notes: Now, let’s discuss key concepts for vertical datums.

## Slide 7: Vertical Datums
Like horizontal: “mathematical abstractions”
  “The geoid” (surface of zero elevation) defined mathematically/geometrically but doesn’t have a physical manifestation in the real world. Though “global mean sea level” is pretty close
    Which is why humans have used some level of water as a vertical datum for over 4000 years
  But, the ocean is not a level surface.
Notes: Like horizontal datums, vertical datums are “mathematical abstractions”
“The geoid” (the surface of zero elevation) is defined mathematically and geometrically, but doesn’t have a physical manifestation in the real world, though “global mean sea level” is pretty close.
Which is why humans have used some level of water as a vertical datum for over 4000 years.
Commonly “mean sea level” or some other water surface is chosen.
But, the ocean is not a level surface, due to variations in temperature, flow, current, and wind among other persistent physical effects.

## Slide 8: Vertical Datums
Realization (much like horizontal):
  Coordinates are assigned to points in a way that best represents the mathematically abstract definition
    Coordinates come from geodetic surveys of the highest accuracy
      Before national datums, they were usually constrained by other locally determinable physical measurements:
        Sea level at tide gage(s)
    Coordinates could stand unchanged for decades
      Piecemeal updates from re-surveys
Notes: Realization of a vertical datum (much like horizontal):
Coordinates (or heights) are assigned to points in a way that best represents the mathematically abstract definition
Coordinates come from geodetic surveys of the highest accuracy
Before national datums, they were usually constrained by other locally determinable physical measurements: such as sea level at tide gage(s)
Coordinates could stand unchanged for decades
And there were piecemeal updates from re-surveys

## Slide 9: Vertical Datums
Historic definitions and roles (much like horizontal):
  National datums were adjusted from large networks
    Often fixed to one or more points in the nation
      NGVD 29: 26 Tide gauges in North America
      NAVD 88: Father Point in Rimouski, Canada
  Space age / International Efforts
    GPS surveys gave fast, accurate access to a previously obscure oddity called the “ellipsoid height”, which we’ll discuss more in later slides.
Notes: Historic definitions and roles (much like horizontal):
National datums were adjusted from large networks and were often fixed to one or more points in the nation
NGVD 29: 26 Tide gauges in North America
NAVD 88: Father Point in Rimouski, Canada
Space age / International Efforts
GPS surveys gave fast, accurate access to a previously obscure oddity called the “ellipsoid height”, which we’ll discuss more in later slides.

## Slide 10
26 tide gages defining NGVD29
Notes: Here’s a map showing the 26 tide gages defining NGVD29

## Slide 11
Single station defining NAVD88
Notes: Here’s a map showingthe single station defining NAVD88

## Slide 12: Vertical Datums
Space Age
  Accurate access to the previously obscure “ellipsoid height” fueled increased research in the previously also-obscure field of “geoid modeling”
    1960s: 1 meter of error in the geoid was “negligible”
    1990s: Need for “1 cm accuracy” geoid grows quickly
  Time-intensive geodetic leveling was expected to be replaced by “GPS + geoid” And it has been, to certain extents
      Geodetic leveling continues to be the most accurate method of determining height differences over distances of 0 km to 20 km
Notes: Space Age
Gave us an accurate wat to access the previously obscure “ellipsoid height” and fueled increased research in the previously also-obscure field of “geoid modeling”
1960s: 1 meter of error in the geoid was “negligible”
1990s: Need for “1 cm accuracy” geoid grows quickly
Time and labor intensive geodetic leveling was expected to be replaced by a more efficient “GPS + geoid” approach.
Indeed, it has been, to certain extents
Geodetic leveling continues to be the most accurate method of determining height differences over distances of 0 km to 20 km

## Slide 13: Vertical Datums
International Efforts
  Much less organized (and less needed) than global horizontal frames
    Both the need for, and ability to solve the issue of, defining consistent heights across oceanic distances were somewhat sparse
  Recent global geopotential models have allowed for a geoid-based attempt
    International Height Reference System (IHRS)
      Not yet the everyday term that ITRF has become
Notes: International Efforts have been much less organized (and less needed) than global horizontal frames.
Both the need for, and ability to solve the issue of, defining consistent heights across oceanic distances were somewhat sparse
But, recent global geopotential models have allowed for a geoid-based attempt
Resulting in the International Height Reference System (IHRS)
Not yet the everyday term that ITRF has become

## Slide 14
Part I : History and Context
  NGS and the NSRS
  Geodetic Control Overview
  Horizontal Datums and Reference Frames
  Vertical Datums
  Historic Datums of the United States (4 slides)
  Decision to Modernize
Notes: Now. We’ll show the many historic datums and realizations for which NGS has been responsible and then examine the term “ellipsoid height” and how it can be used as a height reference.

## Slide 15: Horizontal Datums of the NSRS
CONUS
U.S. Standard Datum
NAD 27
NAD 83(1986)
NAD 83(“HARN”)
NAD 83(“FBN”)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
Alaska
NAD 27
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
St. Lawrence I.
St. Lawrence 1952
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
St. Matthew I.
St. Matthew 1952
St. George I.
St. George 1897
St. George 1952
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
St. Paul I.
St. Paul 1897
St. Paul 1952
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
CNMI
Guam 1963
NAD 83(1993:GU)
NAD 83(2002:GU)
NAD 83(MA11) epoch 2010.00
Guam
Guam 1963
NAD 83(1993:GU)
NAD 83(2002:GU)
NAD 83(MA11) epoch 2010.00
American Samoa
American Samoa 1962
NAD 83(1993:AS)
NAD 83(2002:AS)
NAD 83(PA11) epoch 2010.00
Puerto Rico
Puerto Rico 1940
NAD 83(1986)
NAD 83(1993:PR)
NAD 83(1997:PR)
NAD 83(2002:PR)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
Hawaii
Old Hawaiian Datum
NAD 83(1986)
NAD 83(1993:HI)
NAD 83(PA11) epoch 2010.00
U.S. Virgin Islands
Puerto Rico 1940
NAD 83(1986)
NAD 83(1993:PR)
NAD 83(1997:PR)
NAD 83(2002:PR)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
Notes: There have been about 60 datums and associated realizations over time.

## Slide 16: Vertical Datums of the NSRS
CONUS
NGVD 29
NAVD 88
Alaska
NGVD 29
NAVD 88
St. Lawrence I.
- None -
St. Matthew I.
- None -
St. George I.
- None -
St. Paul I.
- None -
CNMI
NMVD 03
Guam
GVD 63
GUVD 04
American Samoa
ASVD 02
Puerto Rico
PRVD 09
Hawaii
- None -
U.S. Virgin Islands
VIVD 09
Notes: There have been about 8 vertical datums and associated realizations over time.
Note that some locations have not had a formal datum, but were dependent on local definitions (mainly islands).
This is because it is impossible to extend traditional leveling across open water.

## Slide 17: Reminder…
WGS 84 is not part of the NSRS
  It is a military-controlled system
All civilian federal agencies are required to work in the NSRS (as per OMB A-16)
  NAD 83 is part of the NSRS
  NAD 83 ≠ WGS 84
    (there is 2+ meters of systematic bias)
Many states and municipalities choose to work in the NSRS and they often legislate this use
Notes: WGS 84 is not part of the NSRS
It is a military-controlled system
All civilian federal agencies are required to work in the NSRS (as per OMB A-16)
NAD 83 is part of the NSRS
But, NAD 83 ≠ WGS 84
There is 2+ meters of systematic bias)
Many states and municipalities choose to work in the NSRS and they often legislate this use

## Slide 18: The Geoid, and Heights
Topography
The geoid
A chosen
ellipsoid
h
h: ellipsoid height
H: orthometric height
N: geoid undulation
h
N
H
= H
+ N
*The relationship between the ellipsoid and the geoid may be swapped in some locations
Notes: Let’s review the geometry concepts of “ellipsoid height” (click through the animations and explain them)
Point of scientific clarity: The geoid is a surface that is always convex. Yes it has undulations, but geoid purists in the audience will point out to you that, measured at the scale of the Earth itself, the geoid always has a POSITIVE radius relative to the center of the Earth. But when we zoom in, just for illustrative purposes, it is nice to show an “undulating” geoid, to distinguish it from both the smooth ellipsoid and the not smooth topography.
Don’t worry that the plumb line (H) is curved.
Even at America’s largest known curved plumb line (Denali), this curvature is a SUB MILLIMETER effect.

## Slide 19: End of Section 2
Next, we’ll discuss
  Decision to Modernize (11 slides)
Notes: This is the end of Section 2.
In the next section we’ll discuss the Decision to Modernize