## Slide 1
Overview of NSRS Modernization
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
Brief overview of current and expected products
Recap of roll out plan
Current challenges

## Slide 3: Brief overview of current and expected products: Frames and datums (USA)
 | Current (USA) | Future (USA)
Reference Frames | NAD 83(2011) NAD 83(PA11) NAD 83(MA11) | ITRF2020 NATRF2022 PATRF2022 CATRF2022 MATRF2022
Coordinate epochs | 2010.00 | 2020.00 + ?
Geopotential/Vertical datums | NAVD 88 PRVD02 ASVD02 NMVD03 GUVD04 VIVD09 | NAPGD2022
Coordinate epochs | N/A | 2020.00 + ?

## Slide 4: Brief overview of current and expected products: Transformations and Coordinate Conversions (USA)
Current | Future
NCAT: NADCON (through NAD 83(2011) epoch 2010.00) VERTCON (through NAVD 88, ASVD02, etc) SPCS (1927, 1983) UTM USNG Others, not integrated into NCAT: Hybrid geoids Gravimetric geoids HTDP (deformations, mostly horizontal; 14 parameter Helmert transformations) NCAT does not support: Epoch change Height change (ellipsoid, orthometric) ITRF WGS84 | NCAT: NADCON (through N/P/C/MATRF2022 epoch 2020.00) VERTCON (through NAPGD2022 epoch 2020.00) SPCS (1927, 1983, 2022) UTM USNG GEOID2022 IFDM2022 (DANGER*) 14H NCAT supports: Epoch change (DANGER*) Height change (ellipsoid, orthometric) ITRF WGS84 Hybrid geoids will be available for research, but not incorporated into NCAT
* More about this later
GREEN = New!

## Slide 5: Brief overview of current and expected products: OPUS (USA)
Current | Future
OPUS-S: ITRF2014 PAGES to compute 3 vectors Simple average for coordinates at observation epoch Apply HTDP for definitive NAD 83 cords at 2010.00 Results can be “shared” to show the public a set of coordinates that is in conflict with NGS’s official coordinates OPUS-RS: 15 minute solutions, with no tie to any NGS databases OPUS-Projects: Bluebooking, “old way” of doing adjustments (horizontal separate from vertical) HTDP (non-stochastic horizontal motions) ADJUST ITRF2014->NAD 83(2011) epoch 2010.00 | OPUS-S: ITRF2020 M-PAGES to perform LSA for ITRF2020 coordinates at observation epoch EPP2022 for N/P/M/CATRF2022 coordinates at observation epoch Apply IFDM2022 for non-definitive coordinate guesstimates at 2020.00* Results emailed Data stored at NGS for future REC/SEC adjustments OPUS-RS will not exist OPUS-Projects is on hold until after roll-out
* IFDM2022 does not define coordinates in the NSRS

## Slide 6: Recap of the rollout plan (USA)
When | What
Most of 2025 | Each element of the NSRS is placed on the beta website (beta.ngs.noaa.gov), a webinar is likely scheduled shortly thereafter, and testing/feedback begins for that element. Primary Elements: EPP2022, SPCS2022, GEOID2022, Geometric RECs, Orthometric RECs, NCAT, OPUS
Fall of 2025 | A half-way vote of the FGDC occurs, locking down values for EPP2022, SPCS2022 and GEOID2022.
Mid/late 2026 | After all elements have been on the beta website at least six months, a final FGDC vote occurs, formalizing the modernized NSRS as the replacement for the current NSRS.
Late 2026 | NGS begins moving the current NSRS off “to a corner” of the live website (geodesy.noaa.gov) and begins moving things from the beta website up to the live website.
Sometime in 2027 | NGS shuts down access to the current NSRS.

## Slide 7: Current challenges (USA)

## Slide 8: Extra Slides

## Slide 9: Likely dates of completion - data
What | When
GEOID2022 and related models finalized | Jan 2025
ITRF2020 CORS Coordinate functions (CCFs) computed | Feb 2025
EPPs computed: NATRF2022 (in coordination with Canada) | Feb 2025
EPPs computed: CATRF2022/PATRF2022/MATRF2022 | Apr 2025
IFDM2022 initial release finalized | Apr 2025
State Plane Coordinate System of 2022 (SPCS2022) | Arp 2025
REC Geometric adjustment of ~120,000 geodetic control points (lat/lon/eht) | Jun 2025
REC Orthometric adjustment of ~900,000 geodetic control points (oht) | Jul 2025
NADCON (NAD 83(2011/PA11/MA11) epoch 2010.00 -> N/P/C/MATRF2022 epoch 2020.00 | Oct 2025
VERTCON (NAVD 88/others) no epoch -> NAPGD2022 epoch 2020.00 | Dec 2025

## Slide 10: Likely dates of completion - tools
What | When
LASER (Least squares adjustments) | Oct 2024
SPROCCET (temporal projections, including IFDM2022, DGEOID2022 and frame changes w/ 14H) | Apr 2025
NCAT (incorporation of GEOID2022) | June 2025
OPUS-S | Sept 2025
NCAT (incorporation of 14H, IFDM2022, NADCON, VERTCON) | Dec 2025
OPUS-Projects (adjustment only) | Dec 2025
OPUS-Projects (capability of NGS performing Q/A, using data in REC adjustments, and DB loading) | Early 2026

## Slide 11: Testing
As each item goes to beta.ngs.noaa.gov, the public can test it
Once all items are on beta.ngs.noaa.gov, a six-month final testing phase begins
After that final testing phase (including correcting things, if needed), NGS will call a meeting of the Federal Geodetic Control Subcommittee (FGCS) for a vote
If affirmed, the modernized NSRS begins transitioning to the live website, www.ngs.noaa.gov