## Slide 1
Versioning & Naming
Dru Smith
NOAA’s National Geodetic Survey
Jason Bond
Canadian Geodetic Survey
With lots of help from Mike Craymer, Kevin Ahlgren,
Jianliang Huang, Ryan Hardy, John Crowley, David Avalos-Naranjo

## Slide 2: Outline
NATRF2022
NAPGD2022

## Slide 3: NATRF2022 (et al.)
Initial releases:
  NATRF2022.v1.a.US.0.0.0
  NATRF2022.v1.a.CA.0.0.0
The USA will also release:
  PATRF2022.v1.a.US.0.0.0
  CATRF2022.v1.a.US.0.0.0
  MATRF2022.v1.a.US.0.0.0

## Slide 4: NATRF2022
NATRF2022.v1.a.US.0.0.0
Frame name.
Other options for the USA only:
PATRF2022
CATRF2022
MATRF2022
To which ITRF is this frame mathematically defined?
v1 = ITRF2020
v2 = Next ITRF after ITRF2020, but not an updated release of ITRF2020
Which release of the aforementioned ITRF?
a = First release of ITRF2020 (or later)
b = Second release of ITRF2020 (or later)
etc.
Country in which this frame is valid.
Country specific sub-version information for updates that are large, medium or small, respectively.
No set “rules” on what drives these sub-versions, only that they must be logical and that “a.b.c” means “large.medium.small” changes.
Updating “b” means “c” goes to 0.
Updating “a” means “b.c” goes to “0.0”

## Slide 5: Changing the name of NATRF2022
“NATRF2022” is likely to remain the name of the official frame in the USA and Canada for decades to come
Updates are tracked through the version numbering scheme in the previous slide
A new name will only come when a new frame is defined
  Meaning a new equation is adopted, defining a relationship between some ITRF and the new frame that replaces NATRF2022
  This new frame would be given a new name

## Slide 6: NAPGD2022
Consists of dozens of sub-products (spherical harmonic coefficients, grids of values, grids of standard deviations of values, etc.) distributed among these primary elements:
  GM2022
  GEOID2022
    SGEOID2022, DGEOID2022
  DEFLEC2022
    SDEFLEC2022, DDEFLEC2022
  GRAV2022
  DEM2022

## Slide 7: NAPGD2022
Further complicating this are the existence of separate products in the Guam/CNMI and American Samoa regions
  Used solely by the USA
A single version number for each element of NAPGD2022 was considered
  Abandoned after substantive debates about its complexity
    In favor of a single version for the entire datum, with caveats

## Slide 8: NAPGD2022
First release: NAPGD2022 v1 (v1a?)
Next release: NAPGD2022 v2 (v2a?)
Etc.
Version number
Sub-version code
Whether the first release is “v1” or “v1a” is still being finalized.
This character (whether null or “a”) should almost never change – see later slide.

## Slide 9: CGVD2023
Updated datum, adopting a sub-set of NAPG2022 products
NA only
Possible adoption of name NAPGD2022 in the future
  GM2022
  GEOID2022
    SGEOID2022, DGEOID2022
  DEFLEC2022
    SDEFLEC2022, DDEFLEC2022
  GRAV2022
  DEM2022

## Slide 10: CGVD2013
First release: CGVD2013 v1 (v1a?)
Next release: CGVD2023 v2 (v2a?)
Etc.

## Slide 11: NAPGD2022 – four rules for versioning
USA, Canada, Mexico agree to only ever update NAPGD2022 as a tri-country group. This includes computing updates to GEOID2022 as a tri-country effort.
The three countries agree to a semi-regular (3-5 year) cycle of evaluating NAPGD2022 for a potential version change.
  During this cycle, small, proposed changes are put aside in a “to do” list
  Emergencies/Blunders may break this rule but only if all three countries agree
    This is where a “sub-version” code of “a” or “b” might be introduced

## Slide 12: NAPGD2022 – four rules for versioning
At the end of each evaluation cycle, the three countries meet to discuss and decide whether to update NAPGD2022
  If any one country wants to update, all three countries agree to update
The “to do” list is addressed, changes are made, and the entire package of NAPGD2022 is released under a new version number
  This includes documentation on what did and did not change, and where

## Slide 13: Questions?