## Slide 1
Dr. Qassim Abdullah
Chief Scientist and Associate
Woolpert, Inc.
Understanding The new ASPRS Positional Accuracy Standards for Digital Geospatial Data
National Spatial Reference System (NSRS) Modernization Industry Workshop
NOAA’s National Geodetic Survey (NGS)
May 7-8, 2018

## Slide 2
The ASPRS Positional Accuracy Standards for Digital Geospatial Data of 2014

## Slide 3
New Standard for a New Era
Motivation Behind the New Standard:
Legacy map accuracy standards, such as the ASPRS 1990 standard and the NMAS of 1947, are outdated. (over 30 years since ASPRS1990 was written)
Many of the data acquisition and mapping technologies that these standards were based on are no longer used.
More recent advances in mapping technologies can now produce better quality and higher accuracy geospatial products and maps.
Legacy map accuracy standards were designed to deal with plotted or drawn maps as the only medium to represent geospatial data.

## Slide 4
New Standard for a New Era
Within the past two decades (during the transition period between the hardcopy and softcopy mapping environments), most standard measures for relating GSD and map scale to the final mapping accuracy were inherited from photogrammetric practices using scanned film.
New mapping processes and methodologies have become much more sophisticated with advances in technology and advances in our knowledge of mapping processes and mathematical modeling.
Mapping accuracy can no longer be associated with the camera geometry and flying altitude alone (focal length, xp, yp, B/H ratio, etc.).

## Slide 5
New Standard for a New Era
New map accuracy is influenced by many factors such as:
  the quality of camera calibration parameters;
  quality and size of a Charged Coupled Device (CCD) used in the digital camera CCD array;
  amount of imagery overlap;
  quality of parallax determination or photo measurements;
  quality of the GPS signal;
  quality and density of ground controls;
  quality of the aerial triangulation solution;
  capability of the processing software to handle GPS drift and shift;
  capability of the processing software to handle camera self-calibration,
  the digital terrain model used for the production of orthoimagery.

## Slide 6
New Standard for a New Era
These factors can vary widely from project to project, depending on the sensor used and specific methodology. For these reasons, existing accuracy measures based on map scale, film scale, GSD, c-factor and scanning resolution no longer apply to current geospatial mapping practices.
Elevation products from the new technologies and active sensors such as lidar, UAS, and IFSAR are not considered by the legacy mapping standards. New accuracy standards are needed to address elevation products derived from these technologies.

## Slide 7
The New Standard Highlights
  Sensor agnostic, data driven:
    Positional Accuracy Thresholds which are independent of published GSD, map scale or contour interval
  It is All Metric!
  Unlimited Horizontal Accuracy Classes:
  Additional Accuracy Measures
    Aerial triangulation accuracy,
    Ground controls accuracy,
    Orthoimagery seam lines accuracy,
    Lidar relative swath-to-swath accuracy,
    Recommended minimum Nominal Pulse Density (NPD)
    Horizontal accuracy of elevation data,
    Delineation of low confidence areas for elevation data
    Required number and spatial distribution of QA/QC check points based on project area

## Slide 8
The New ASPRS Standard is sensor agnostic data driven, Why?

## Slide 9
New Standard Highlights
Horizontal Accuracy Class | RMSEx and RMSEy (cm) | RMSEr (cm) | Horizontal Accuracy at 95% Confidence Level (cm) | Orthoimagery Mosaic Seamline Mismatch (cm)
X-cm | ≤X | ≤1.41*X | ≤2.45*X | ≤ 2*X
Horizontal Accuracy Standards for Geospatial Data
(unlimited horizontal accuracy classes)
= Radial RMSE = Circular RMSE = Two-dimensional RMSE of X & Y

## Slide 10
10
Common Orthoimagery Pixel Sizes | Recommended Horizontal Accuracy Class RMSEx and RMSEy (cm) | Orthoimage RMSEx and RMSEy in terms of pixels | Recommended use
1.25 cm | ≤1.3 | ≤1-pixel | Highest accuracy work
 | 2.5 | 2-pixels | Standard Mapping and GIS work
 | ≥3.8 | ≥3-pixels | Visualization and less accurate work
2.5 cm | ≤2.5 | ≤1-pixel | Highest accuracy work
 | 5.0 | 2-pixels | Standard Mapping and GIS work
 | ≥7.5 | ≥3-pixels | Visualization and less accurate work
5 cm | ≤5.0 | ≤1-pixel | Highest accuracy work
 | 10.0 | 2-pixels | Standard Mapping and GIS work
 | ≥15.0 | ≥3-pixels | Visualization and less accurate work
7.5 cm | ≤7.5 | ≤1-pixel | Highest accuracy work
 | 15.0 | 2-pixels | Standard Mapping and GIS work
 | ≥22.5 | ≥3-pixels | Visualization and less accurate work
15 cm | ≤15.0 | ≤1-pixel | Highest accuracy work
 | 30.0 | 2-pixels | Standard Mapping and GIS work
 | ≥45.0 | ≥3-pixels | Visualization and less accurate work
Recommended
Digital Orthoimagery Accuracy Examples for Current Large and Medium Format Metric Cameras

## Slide 11
Aerial triangulation results should be twice as accurate as the generated products:
    Ortho and planimetric maps ONLY:
    RMSEx(AT) or RMSEy(AT) = ½ * RMSEx(Map) or RMSEy(Map)
    RMSEz(AT) = RMSEx(Map) or RMSEy(Map) of orthoimagery
    For ortho/planimetric maps and elevation maps:
    RMSEx(AT), RMSEy(AT) or RMSEz(AT) = ½ * RMSEx(Map), RMSEy(Map)or RMSEz(DEM)
  * according to the ASPRS Positional Accuracy Standards for Digital Geospatial Data
Horizontal Accuracy Standards for Geospatial Data

## Slide 12
Control points for aerial triangulation should be twice as accurate as aerial the triangulation:
    For ortho and planimetric maps ONLY:
    RMSEx or RMSEy = 1/4 * RMSEx(Map) or RMSEy(Map),
    RMSEz = 1/2 * RMSEx(Map) or RMSEy(Map)
    For ortho/planimetric maps and elevation maps:
    RMSEx, RMSEy or RMSEz= 1/4 * RMSEx(Map), RMSEy(Map) or RMSEz(DEM)
  * according to the ASPRS Positional Accuracy Standards for Digital Geospatial Data
Horizontal Accuracy Standards for Geospatial Data

## Slide 13
Check points should be THREE as accurate as the generated products*:
For a project with ortho and planimetric maps accuracy of 24-cm or 0.79 ft., the check point should be accurate to:
RMSEx or y (check points) = 24-cm/3 = 8-cm or 0.26 ft.
  * according to the ASPRS Positional Accuracy Standards for Digital Geospatial Data
Best Practices in Determining Product Accuracy*

## Slide 14
New Standard Highlights
Vertical Accuracy Class | Absolute Accuracy |  |  | Relative Accuracy (where applicable) |  | 
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) | VVA at 95th Percentile (cm) | Within- Swath Hard Surface Repeatability (Max Diff) (cm) | Swath-to-Swath Non-Vegetated Terrain (RMSDz) (cm) | Swath-to-Swath Non-Vegetated Terrain (Max Diff) (cm)
X-cm | ≤X | ≤1.96*X | ≤3.00*X | ≤0.60*X | ≤0.80*X | ≤1.60*X
Vertical Accuracy Standards for Geospatial Data
(unlimited vertical accuracy classes)

## Slide 15
Vertical Accuracy/Quality Examples for Digital Elevation Data
Vertical Accuracy Class | Absolute Accuracy |  |  | Relative Accuracy (where applicable) |  | 
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) | VVA at 95th Percentile (cm) | Within-Swath Hard Surface Repeatability (Max Diff) (cm) | Swath-to-Swath Non-Veg Terrain (RMSDz) (cm) | Swath-to-Swath Non-Veg Terrain (Max Diff) (cm)
1-cm | 1.0 | 2.0 | 3 | 0.6 | 0.8 | 1.6
2.5-cm | 2.5 | 4.9 | 7.5 | 1.5 | 2 | 4
5-cm | 5.0 | 9.8 | 15 | 3 | 4 | 8
10-cm | 10.0 | 19.6 | 30 | 6 | 8 | 16
15-cm | 15.0 | 29.4 | 45 | 9 | 12 | 24
20-cm | 20.0 | 39.2 | 60 | 12 | 16 | 32
33.3-cm | 33.3 | 65.3 | 100 | 20 | 26.7 | 53.3
66.7-cm | 66.7 | 130.7 | 200 | 40 | 53.3 | 106.7
100-cm | 100.0 | 196.0 | 300 | 60 | 80 | 160
333.3-cm | 333.3 | 653.3 | 1000 | 200 | 266.7 | 533.3

## Slide 16
Examples on Vertical Accuracy and Recommended Lidar Point Density for Digital Elevation Data according to the new ASPRS 2014 standard
Vertical Accuracy Class | Absolute Accuracy |  | Recommended Minimum NPD (pts/m2) | Recommended Maximum NPS7 (m)
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) |  | 
1-cm | 1.0 | 2.0 | ≥20 | ≤0.22
2.5-cm | 2.5 | 4.9 | 16 | 0.25
5-cm | 5.0 | 9.8 | 8 | 0.35
10-cm | 10.0 | 19.6 | 2 | 0.71
15-cm | 15.0 | 29.4 | 1 | 1.0
20-cm | 20.0 | 39.2 | 0.5 | 1.4
33.3-cm | 33.3 | 65.3 | 0.25 | 2.0
66.7-cm | 66.7 | 130.7 | 0.1 | 3.2
100-cm | 100.0 | 196.0 | 0.05 | 4.5
333.3-cm | 333.3 | 653.3 | 0.01 | 10.0
10-cm with 2 pts/m2 is the QL2 LiDAR standard for the nationwide 3DEP

## Slide 17
Horizontal accuracy requirements for elevation data according to ASPRS2014 Standards
Photogrammetric elevation data: the horizontal accuracy equates to the horizontal accuracy class that would apply to planimetric data or digital orthoimagery produced from the same source imagery, using the same aerial triangulation/INS solution.
Lidar elevation data: use the following formula:
See Page A7, Section 7.5 Horizontal Accuracy Requirements for Elevation Data

## Slide 18
Horizontal accuracy requirements for Lidar data
What to do?
Trust the manufacturer estimate for horizontal accuracy assuming you are meeting the vertical accuracy
Use the ASPRS2014 estimation of horizontal accuracy for lidar
Altitude (m) | Positional RMSEr (cm) | Altitude (m) | Positional RMSEr (cm)
500 | 13.1 | 3,000 | 41.6
1,000 | 17.5 | 3,500 | 48.0
1,500 | 23.0 | 4,000 | 54.5
2,000 | 29.0 | 4,500 | 61.1
2,500 | 35.2 | 5,000 | 67.6
Most QL2 flown at this altitude

## Slide 19
Examples on Vertical Accuracy and Recommended Lidar Point Density for Digital Elevation Data According to the New ASPRS 2014 Standard
Vertical Accuracy Class | Absolute Accuracy |  |  | Relative Accuracy (where applicable) |  | 
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) | VVA at 95th Percentile (cm) | Within-Swath Hard Surface Repeatability (Max Diff) (cm) | Swath-to-Swath Non-Veg Terrain (RMSDz) (cm) | Swath-to-Swath Non-Veg Terrain (Max Diff) (cm)
1-cm | 1.0 | 2.0 | 3 | 0.6 | 0.8 | 1.6
2.5-cm | 2.5 | 4.9 | 7.5 | 1.5 | 2 | 4
5-cm | 5.0 | 9.8 | 15 | 3 | 4 | 8
10-cm | 10.0 | 19.6 | 30 | 6 | 8 | 16

## Slide 20
Required accuracy for the products:
Ortho Accuracy: 4 cm (RMSEx or y)
DSM Accuracy: 4 cm (RMSEz)
ASPRS Standards Requires:
  RMSEx, RMSEy or RMSEz (ground control)= ¼ * RMSEx(Map), RMSEy(Map) or RMSEz(DEM)
Ground Control for AT accuracy = 1 cm (RMSEx,y,z)
Check points for QC accuracy = 1.33 cm
Can ASPRS standards be used for UAS products?

## Slide 21
Thank you!
Qassim Abdullah:
qassim.abdullah@woolpert.com
Mapping_matters@asprs.org