## Slide 1
Update on product availability
Catherine Robin
Section Chief / CSRS Modernization Implementation Manager
Canadian Geodetic Survey
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
An updated table on product availability

## Slide 3
Product or Tool | Canada | USA
Reference Frames | ITRF2020, NATRF2022 | ITRF2020, (N/P/C/M)ATRF2022
Geopotential Datum | CGVD2013 (SGEOID2022) | NAPGD2022
Crustal Deformation Model | IFDM2022.?? | IFDM2022
Geometric Transformations - tool | TRX | NADCON
Geometric Transformations - from | NAD83(CSRS) any epoch | NAD 83 (2011/PA11/MA11) epoch 2010.00
Geometric Transformations - to | NATRF2022 any epoch | N/P/C/MATRF2022 epoch 2020.0
Vertical Transformations - tool | GPS-H | VERTCON
Vertical Transformations - from | CGVD28 CGVD2013(CGG2013A) | NAVD 88, ASVD 02, PRVD 02, NMVD 03, GUVD 04, VIVD 09, Local Tidal
Vertical Transformations - to | CGVD2013(SGEOID2022) | NAPGD2022 epoch 2020.00
Official integrated tool | None planned before 2025 | NCAT or VDatum
Grid format | GGXF (& .byn / .gvb) | GGXF
Products, Tools & Timelines of Modernization: NGS and Canada

## Slide 4
Product or Tool | Canada | USA
GNSS processing engine | SPARK, Bernese 5.4, GipsyX 2.3 | M-PAGES
Least-squares adjustment engine | CGS SINEX software, GHOST | LASER (will be in future OPUS-Projects)
Stand-alone GNSS processor | CSRS-PPP | OPUS-S
Geodetic survey processor | Bernese v5.4 | Will not exist until after 2026
Submitted data formats supported | RINEX 2/3 | RINEX 3
Projections supported | UTM, MTM, Double Stereographic | UTM, USNG, SPCS2022
Rotation model of tectonic plates | EPP2022 (N) | EPP2022 (N/P/C/M)
Information about passive marks | GEODB/Passive Control web application | Data Delivery System
Information about active control | GEODB/CACS web application | Data Delivery System
CORS / CACS networks supported | NRCan, IGS, Public ACS Networks (CACS/RACS/WCDA/Provincial/Municipal), Commercial RTK Compliance Program | IGS, NOAA CORS Network (NCN)
Products, Tools & Timelines of Modernization: NGS and Canada

## Slide 5
Timeline | Canada | USA
First alpha products released | only in Dev environment | Already: EPP2022 NAPGD2022 SPCS2022
Beta products released | Mid - late 2025 SGEOID2022 & DGEOID2022 NAD83(CSRS) v8.1 | Mid 2025 – Mid 2026
Official adoption | in parallel with the US | Late 2026
Phase out of current NSRS/CSRS | possibly after 2030 | Late 2026-Early 2027
Products, Tools & Timelines of Modernization: NGS and Canada