## Slide 1
Transformation work flows in the USA
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
Commonalities
USA approaches

## Slide 3: Commonalities
GGXF file distribution
Biquadratic interpolation

## Slide 4: USA
Use NCAT or VDatum
  They draw from the same code base

## Slide 5: NCAT
Input and output data requirements:
  2-D or 3-D
    And then which type
  Datum
  Epoch (possibly. Depends on the datum)
Limitations:
  Can go 3-D to 2-D but not the reverse
  Only certain datums will trigger a request for “epoch”

## Slide 6: Data types
2-D
  Lat/Lon
  SPCS(27, 83, 2022)
  UTM
  USNG
3-D
  Any 2-D + h
  Any 2-D + H
  X, Y, Z

## Slide 7: NCAT new functionality
Allowable datums now include all ITRFs and WGS84s
Heights can be converted from h to H and back
  This will not require hybrid geoids
14 parameter Helmert transformations
  This never changes an epoch, just a frame (subset of datums)
    Maintains geodetic control
Deformation model
  This never changes a frame, just an epoch but with mixed accuracy (Danger!)
    Loses geodetic control
Singular paths will be defined
  By opening up frame and epoch changes, multiple paths to the same answer may exist
    But only one is “NGS recommended” and will be the default
Notes: Some clever interactions between NADCON, VERTCON and GEOID2022 allow the conversion of h in any datum to H in any datum without needing hybrid geoids.

## Slide 8
NAD83_NA (260)
ITRF88 (100)
ITRF89 (110)
1
ITRF90 (120)
2
ITRF91 (180)
8
ITRF92 (210)
11
ITRF93 (220)
12
ITRF94 (230)
ITRF96 (250)
15
ITRF97 (270)
17
ITRF2000 (290)
19
ITRF2005 (340)
24
26
ITRF2008 (360)
32
ITRF2014 (420)
36
ITRF2020 (460)
13
16
NAD83_PA (320)
22
NAD83_MA (330)
23
WGS84_ORIG (140)
WGS84_G730 (200)
WGS84_G873 (240)
WGS84_G1150 (370)
WGS84_G1674 (390)
WGS84_G1762 (410)
WGS84_G2139 (450)
4
10
14
29
30
35
7
NEOS90 (170)
6
NEOS9125 (160)
PNEOS90 (150)
WGS72 (130)
5
3
SIO_MIT92 (190)
9
IGS97 (280)
18
IGS00 (300)
20
IGB00 (310)
21
IGS05 (350)
25
IGS08 (380)
27
IGB08 (400)
28
31
IGS14 (430)
33
IGB14 (440)
34
IGS20 (470)
37
CATRF2022 (510)
PATRF2022 (500)
NATRF2022 (490)
MATRF2022 (520)
39
40
41
42
An ITRF
A 14 parameter Helmert transformation
Null transformations
Two versions exist.
17
Defined/Additive direction of stored transformation
WGS72 (130)
Datum Code (Datum Number)
IGB20 (480)
38

## Slide 9
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
Note that all coordinates in this box are XYZ.
For a generic epoch, program 14H, within NCAT/VDatum will perform all of these transformations.
There is no way to exit this box, without either:
Specifying an epoch and using NADCON, or
Introducing a mark motion model, such as IFDM2022.
However, since IFDM2022 is a model, and does not define coordinates in the NSRS, NGS will be very cautious about its use, and particularly its misuse.
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: Any
ITRF96 (250)
16
Etc.
Non-definitive NATRF2022 coordinates at a different epoch
IFDM2022

## Slide 10
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
For epoch 2010.00, NADCON provides a path in/out of this box, since frame NAD83_NA is definitionally equivalent to NAD83_2011.
NCAT will know that NAD83_NA (XYZ, 2010.00) is equivalent to NAD 83(2011) epoch 2010.00 XYZ values.
It can then convert to other forms, especially f, l, h…
…which then allows for either further conversions within the same datum…
…or allows for NADCON connections out of the frame.
NAD83_2011
(255)
7A,7B,7C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_NSRS2007
(245)
X, Y, Z
USNG
UTM
SPC
f, l, h
6A,6B,6C
NATRF2022_2020
(801)
Etc.
X, Y, Z
f, l, h
USNG
UTM
SPC
Equivalent!!
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: 2010.00
ITRF96 (250)
16
Etc.
There is no connection
here. Different epochs!
But if IFDM is allowed to “define” coordinates, a connection can be made here. But that generally is not going to be allowed.

## Slide 11
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
For epoch 2010.00, NADCON provides a path in/out of this box, since frame NAD83_PA is definitionally equivalent to NAD83_PA11.
NCAT will know that NAD83_PA (XYZ, 2010.00) is equivalent to NAD 83(PA11) epoch 2010.00 XYZ values.
It can then convert to other forms, especially f, l, h…
…which then allows for either further conversions within the same datum…
…or allows for NADCON connections out of the frame.
NAD83_PA11
(296)
11A,11B,11C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_1993_HI
(286)
X, Y, Z
USNG
UTM
SPC
f, l, h
10A,10B,10C
PATRF2022_2020
(831)
There is no connection
here. Different epochs!
But if IFDM is allowed to “define” coordinates, a connection can be made here. But that generally is not going to be allowed.
Etc.
X, Y, Z
f, l, h
USNG
UTM
SPC
Equivalent!!
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: 2010.00
ITRF96 (250)
16
Etc.

## Slide 12: We can do something similar with 2020.00
The frames NATRF2022, PATRF2022, CATRF2022 and MATRF2022 will always be defined as a simple mathematical connection to ITRF2020, across any epoch
Reference epoch coordinates (RECs) will represent “snapshot” frames, starting at 2020.00
  Next one? Maybe 2025.00? Maybe 2030.00?
Let’s look at the previous slides, but from the standpoint of a 2020.00 epoch
  NATRF2022 example only shown. Can extrapolate to the other three.

## Slide 13
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
For epoch 2020.00, NADCON provides a path in/out of this box, since frame NATRF2022 is definitionally equivalent to NATRF2022_2020.
Which allows for NADCON connections out of the frame.
NAD83_2011
(255)
7A,7B,7C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_NSRS2007
(245)
X, Y, Z
USNG
UTM
SPC
f, l, h
6A,6B,6C
NATRF2022_2020
(801)
Etc.
X, Y, Z
f, l, h
USNG
UTM
SPC
Equivalent!!
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: 2020.00
ITRF96 (250)
16
Etc.
There is no connection
here. Different epochs!
But if IFDM is allowed to “define” coordinates, a connection can be made here. But that generally is not going to be allowed.

## Slide 14: Doesn’t all this lead to multiple paths?
It may seem so, but not really…
Consider this example:
  Given flh in NAD83_NSRS2007
  Want: flh in ITRF88

## Slide 15
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
For NAD83_NSRS2007, there is no epoch.
NCAT can use NADCON to get to NAD83_2011…
Or press on to NATRF2022_2020…
If NAD83_NSRS2007 had epoch 2010.00, we might make this connection…
But it doesn’t.
If NAD83_NSRS2007 had epoch 2020.00, we might make this connection…
But it doesn’t.
As such, there is no way to fulfill this request.
NAD83_2011
(255)
7A,7B,7C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_NSRS2007
(245)
X, Y, Z
USNG
UTM
SPC
f, l, h
6A,6B,6C
NATRF2022_2020
(801)
X, Y, Z
f, l, h
USNG
UTM
SPC
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: Unknown
ITRF96 (250)
16
Etc.
  Given flh in NAD83_NSRS2007
  Region: CONUS
  Want: flh in ITRF88

## Slide 16: What about the h to H conversion?
No hybrid geoids
All such conversions will run through GEOID2022

## Slide 17
NAD83_2011
(255)
7A,7B,7C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_NSRS2007
(245)
X, Y, Z
USNG
UTM
SPC
f, l, h
6A,6B,6C
NATRF2022_2020
(801)
X, Y, Z
f, l, h
USNG
UTM
SPC
  Given: h in NAD83_NSRS2007
  Region: CONUS
  Want: H in NGVD29
Here’s the basic NADCON connections we’ve already seen
Let’s reduce that down to just the heights, for ease of reading
Etc.

## Slide 18
NAD83_2011
(255)
7C
h
NAD83_NSRS2007
(245)
h
6C
NATRF2022_2020
(801)
h
  Given: h in NAD83_NSRS2007
  Region: CONUS
  Want: H in NGVD29
H
H
NAVD88
(1060)
NGVD29
(1050)
H
1001
NAPGD2022_2020
(3020)
1002
And here are the basic VERTCON connections that are/will exist in NCAT/VDatum
By definition, H(NAPGD2022, epoch “t”) =
h(N/P/C/MATRF2022, epoch “t”)
– GEOID2022(epoch “t”)
GEOID2022 epoch 2020.00
Etc.
We could draw a “hybrid geoid” connection here, but won’t:
Provides non-uniqueness of path
Raises question of “which one?” : GEOID99? GEOID03? GEOID06?

## Slide 19: So what about IFDM2022?
Danger!
IFDM2022 is a Mark Motion Model
  It is not a crustal motion model.
    It uses crustal motions to estimate mark motions
      Its sole use in a geodetic agency like ours is to estimate mark motions
        If you want crustal motion models, look to agencies like USGS whose mission is the crust, not the geodetic marks upon the crust
Notes: In the parlance of the multi-epoch least-squares adjustment (ME-LSA) problem, IFDM2022 is a “geodetic value change model” or GVCM because it is stored as changes (either linear velocities or instantaneous displacements) to the geodetic values of northing, easting and up. This is in contrast to a model of changes to parameter values (MCPV), which is derived from the GVCM, and is a representation the total linear changes, from one epoch (observation or constraint) to another epoch (the adjustment epoch), to the parameters of the ME-LSA, namely geocentric coordinates in X, Y and Z.

## Slide 20: So what about IFDM2022?
Danger!
For example, let’s say a user is interested in NATRF2022 epoch 2026.3057 coordinates on a mark
  If an SEC exists, great, they can see it
  If not, there is no way to compute such a coordinate using NGS-sanctioned methods within NGS created tools
  However, we are considering allowing users to compute such coordinates using IFDM2022
    We don’t recommend it
    We don’t like it
    We will only implement this with significant limitations, caveats and warnings
Notes: We call SPROCCET a “LASER pre-processor”

## Slide 21: NADCON and VERTCON
Updating both NADCON and VERTCON has begun!
Some initial national adjustments, yielding initial RECs have allowed a quick-and-dirty look at the upcoming transformation grids

## Slide 22: NADCON (longitude)
What we’ve been predicting
What our first iteration looks like

## Slide 23: VERTCON
What we’ve been predicting
What our first iteration looks like

## Slide 24: Thank you

## Slide 25: Questions?

## Slide 26: Extra Slides

## Slide 27: So what about IFDM2022?
Danger!
Our current version of IFDM2022 is a global model of linear velocities on a 0.1 arc degree grid, plus a series of regional displacement grids on various spacings, one for each Earthquake back to 1934.
  It is lacking in significant ways:
    Poor horizontal resolution near fault lines
    Poor vertical resolution in general
    Lack of input data in oceanic/island regions
Notes: In the parlance of the multi-epoch least-squares adjustment (ME-LSA) problem, IFDM2022 is a “geodetic value change model” or GVCM because it is stored as changes (either linear velocities or instantaneous displacements) to the geodetic values of northing, easting and up. This is in contrast to a model of changes to parameter values (MCPV), which is derived from the GVCM, and is a representation the total linear changes, from one epoch (observation or constraint) to another epoch (the adjustment epoch), to the parameters of the ME-LSA, namely geocentric coordinates in X, Y and Z.

## Slide 28: So what about IFDM2022?
Danger!
The sole use of IFDM2022 is as an input model to SPROCCET
SPROCCET’s sole use at NGS is as a pre-processor to least-squares adjustments.
  It projects through time observations, constraints and cofactor matrices from some epoch to the adjustment epoch
  Failure to take the next step (performing a constrained least-squares adjustment upon those projected data) will mean suffering unknown and possibly unknowable errors on observations and constraints.
Notes: We call SPROCCET a “LASER pre-processor”

## Slide 29: So what about IFDM2022?
Danger!
Unless a coordinate is an observation (such as from PPP) or is serving as a constraint in a least-squares adjustment, SPROCCET was not built to deal with it.
  SPROCCET does not project general coordinates through time.
  It could be forced to do so, but we don’t like it.
Notes: We call SPROCCET a “LASER pre-processor”

## Slide 30: So what about IFDM2022?
Danger!
NGS’s mission is geodetic control
We define that control in two and only two ways:
  CORS coordinate functions
  Reference epoch coordinates (RECs)
As an additional scientific add-on to our mission, we will compute survey epoch coordinates (SECs) if and only if observations exist at the survey epoch to compute said SECs
  These are useful for showing discrete coordinates in time, and thus to infer motion through time
  Inferred velocities are not definitive
  SECs are not geodetic control
Notes: We call SPROCCET a “LASER pre-processor”

## Slide 31
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
For epoch 2010.00, NADCON provides a path in/out of this box, since frame NAD83_MA is definitionally equivalent to NAD83_MA11.
NCAT will know that NAD83_MA (XYZ, 2010.00) is equivalent to NAD 83(MA11) epoch 2010.00 XYZ values.
It can then convert to other forms, especially f, l, h…
…which then allows for either further conversions within the same datum…
…or allows for NADCON connections out of the frame.
NAD83_MA11
(308)
31A,31B,31C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_2002_GC
(299)
X, Y, Z
USNG
UTM
SPC
f, l, h
30A,30B,30C
MATRF2022_2020
(891)
Etc.
X, Y, Z
f, l, h
USNG
UTM
SPC
Equivalent!!
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: 2010.00
ITRF96 (250)
16
Etc.
There is no connection
here. Different epochs!
But if IFDM is allowed to “define” coordinates, a connection can be made here. But that generally is not going to be allowed.

## Slide 32: What about the Caribbean?
In the current NSRS, the NAD 83(2011) epoch 2010.00 (and NAD 83(NSRS2007)) coordinates were computed as if they were on the North American plate
That will change with the modernized NSRS
Thus the next slide needs careful consideration

## Slide 33
All NGS frames, ITRFs and WGS84s
Connected by 14-parameter Helmert transformations
Epoch 2010.00
For epoch 2010.00, NADCON provides a path in/out of this box, since frame NAD83_NA is definitionally equivalent to NAD83_2011, whether on the North American Plate or the Caribbean plate!
NCAT will know that NAD83_NA (XYZ, 2010.00) is equivalent to NAD 83(2011) epoch 2010.00 XYZ values on the Caribbean plate.
It can then convert to other forms, especially f, l, h…
…which then allows for either further conversions within the same datum…
…or allows for NADCON connections out of the frame, on the Caribbean plate.
NAD83_2011
(255)
23A,23B,23C
X, Y, Z
USNG
UTM
SPC
f, l, h
NAD83_NSRS2007
(245)
X, Y, Z
USNG
UTM
SPC
f, l, h
22A,22B,22C
CATRF2022_2020
(861)
Etc.
X, Y, Z
f, l, h
USNG
UTM
SPC
Equivalent!!
ITRF88 (100)
ITRF2020 (460)
NATRF2022 (490)
39
Etc.
NAD83_NA (260)
Etc.
CATRF2022 (510)
PATRF2022 (500)
MATRF2022 (520)
40
41
42
ITRF2000 (290)
NAD83_PA (320)
22
NAD83_MA (330)
23
Etc.
Epoch: 2010.00
ITRF96 (250)
16
Etc.
For region “CONUS” the NAD 83(NSRS2007) to NAD 83(2011) epoch 2010.00 NADCON transformations are 6A, 6B and 6C. Here, in the PRVI region, they are 22A, 22B, 22C
There is no connection
here. Different epochs!
But if IFDM is allowed to “define” coordinates, a connection can be made here. But that generally is not going to be allowed.