## Slide 1
Overview of 2010 Geospatial Summit
Juliana P. Blackwell
Director, National Geodetic Survey
National Ocean Service, NOAA
Geospatial Summit, April 13-14, 2015
Notes: <number>

## Slide 2: Highlights
Lessons from the Past
Modernizing the National Spatial Reference System (NSRS)
  Geopotential Datum – Replacing NAVD 88
  Geometric Datum – Replacing NAD 83
Perspectives and Feedback
2
Notes: <number>

## Slide 3: Lessons from the Past
Expect years of effort
Requires a lot of geodetic expertise
Expect slow-adopters and no-adopters
Users care about differential accuracy more than absolute
Communicate, communicate, communicate
Develop support tools in advance
3
Notes: <number>

## Slide 4: Modernizing the NSRS
North American Vertical Datum of 1988 (NAVD 88)
  Destroyed marks, poor locations, no monitoring, bias, tilt
  No continent-wide consistency
  Re-leveling is expensive, doesn’t solve root issues
  Future: GPS+Geoid! Role of passive marks demoted
North American Datum of 1983 (NAD 83)
  Non-geocentric, misaligned with satellite orbits
  Legally binding in 48 states!
  Built from Bilby passive to GPS passive to CORS
  Too many “realizations”
  Future: CORS rules! Role of passive marks demoted
  Future: Plate-fixed? Remains an open question
4
Notes: <number>

## Slide 5: Perspectives and Feedback
Panel Q&A and End User Feedback
  Many users desired some form of “fixed” coordinates
  Need for passive control varies from “none” to “critical”
  Volume of federal NAD 83/NAVD 88 geospatial data is tremendous, but almost all digital or becoming digital
  Traceability back to NAD 83 or NAVD 88 very important
  Consistency of the NSRS across decades is important
Summary
  Cautious optimism and some excitement
  Adoption of true time-dependent coordinates will be slow, but some users need this information.
5
Notes: <number>

## Slide 6: Thank you
6