## Slide 1
Modernizing the National Spatial Reference System:
A 2017 update
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 3: So…what’s new in 6 months?
NAMES!!

## Slide 4: NSRS Modernization
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 5: NSRS Modernization
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 6: So…what’s new in 6 months?
NAMES!!
Mathematical Decisions!!

## Slide 7: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Remove long-standing non-geocentricity of NAD 83 frames
All four : identical to IGSxx at a TBD epoch
  2020.00?
All four : differ from IGSxx by plate rotation only
  Updated Euler Pole determination for rigid plate only

## Slide 8
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.

## Slide 9: NATRF2022 frame is rigid and fixed to rigid part of the N.A. plate
Non-rigid part of the N.A. plate
(deformation)
area

## Slide 10
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 11
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 12
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 13
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 14: Time-Dependencies as a service: NATRF2022 and actual survey epochs
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
NAD 83 forcibly combined data spanning many years (using HTDP with no vertical modeling) to compute and find one height at one epoch.
NATRF2022 will compute coordinates at survey epoch to show actual motion.
Even gridding surrounding CORS yields better subsidence rates than you have today.
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 15: Time Dependencies as a service: Intra-plate motions
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748

## Slide 16: So…what’s new in 6 months?
NAMES!!
Mathematical Decisions!!
NADCON 5.0!!

## Slide 17: The new Geodetic Toolkit
https://beta.ngs.noaa.gov/gtkweb/

## Slide 18: The new Geodetic Toolkit with NADCON 5.0
https://dev.ngs.noaa.gov/gtkweb/

## Slide 19
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83
Notes:

## Slide 20
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 21: Thank you!

## Slide 22: Questions?

## Slide 23: Plate-(pseudo)fixed frames
NAD 83(NSRS2007)
Epoch 2002.0
NAD 83(2011)
Epoch 2010.0
If NAD 83 were truly “plate
fixed” then an 8 year
epoch change would not
yield the systematic
plate rotation seen here.
(*)TRF2022 will determine
a new Euler Pole rotation
for each of 4 plates.
(*)=NA, C, T or P
NAD 83(2011) minus NAD 83(NSRS2007)

## Slide 24: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
IGSxx origin
Earth’s Surface
hNAD83
hIGSxx
fNAD83 – fIGSxx
lNAD83 – lIGSxx
hNAD83 – hIGSxx
all vary
smoothly by latitude
and longitude
same
GRS-80
ellipsoid

## Slide 25: Fixed-Epoch Transformation NAD 83 to “2022”