## Slide 1
The delayed release of the modernized National Spatial Reference System

## Slide 2: Outline
Defining “the modernized NSRS”
  This is a lengthy part of the talk. The intent is to emphasize how big the modernized NSRS is, and outline just what you get as a user of the modernized NSRS
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 3
Defining “the modernized NSRS”
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 4: What is “the modernized NSRS”?
It is a replacement for the entire current National Spatial Reference System (NSRS)
  Datums
  Coordinates
  Orbits
  Database
  Software
  Policies, procedures and philosophies
  And….skills! New hires, new training!
Let’s list the details in semi-chronological order

## Slide 5: Definitional Components

## Slide 6: Components
ITRF2020 released and adopted at NGS
  NOAA CORS Network (NCN) and IGS compute and update their CORS coordinate functions
  NGS finalizes new multi-GNSS software
  NGS and IGS compute and update their GNSS orbits
  All loaded into the NSRS database and available through the data delivery system

## Slide 7: Components
NCN fully modernized
  NGS implementing non-linear CORS coordinate functions where necessary
  NGS has in place a functioning method to keep CORS coordinate functions accurate on a day-to-day basis
  ARP/GRP discrepancies fully addressed
  CORS grading system in place
  NOAA Foundation CORS Network (NFCN) built
  NGS has the ability to expand the NCN station count by an order of magnitude
  NGS is running an RTN alignment service (RAS)
  All loaded into the NSRS database and available through the data delivery system

## Slide 8: Components
Four terrestrial reference frames* defined
  NGS has computed the Euler pole parameters (EPPs) for each plate (EPP2022)
  CORS coordinate functions available in all four frames
  All loaded into the NSRS database and available through the data delivery system
*NATRF2022, PATRF2022, CATRF2022, MATRF2022

## Slide 9: Components
Geopotential datum* defined
  GRAV-D airborne mission complete/processed
  US/Canada/Mexico geoid theory issues resolved
  GM2022, GEOID2022, DEFLEC2022, GRAV2022, DEM2022 available
  GRAV2022 tool built
  Dynamic Height calculator built
  All loaded into the NSRS database and available through the data delivery system
*NAPGD2022

## Slide 10: And at this point…literally…
There are NO coordinates on passive control
There is no software to process your surveys
There are no transformation tools
To wit: There’s no way to even use this modernized NSRS yet
Let’s keep going. There’s a lot left to do…
Things get a little less chronological at this point…

## Slide 11: Tools and Passive Control Components and their Capabilities

## Slide 12: Components
Intra-frame velocity model* defined
  2-4 new geophysics/geodynamics hires
  Comprehensive statistical evaluation of all historic and future earthquake models to achieve formal accuracy estimates for all
  Plan for keeping the model updated daily
  Long term plan to support INSAR data collection
  All loaded into the NSRS database and available through the data delivery system
*IFVM2022

## Slide 13: IFVM2022 Capability
Provides an estimate of 3-D mark movement through time
  Likely proxied by surface movement models
  Height movements expected to be poorly determined
Allows a user to approximate coordinates at a different epoch from when the observations were collected
  NGS will use this to create SECs and RECs
    Survey Epoch Coordinates (AKA “time dependent” coordinates)
    Reference Epoch Coordinates (AKA “coordinates every 5 years”)
  Users can apply this within OPUS to select their epoch(s) of choice

## Slide 14: Components
New Least Squares Adjustment software
  Contract work and/or new hires
  Replaces ADJUST, ASTA, NETSTAT, CALIBRATE, GPSCOM
  Modern language / integrated with database
  Fixes numerous approximations and inaccurate shortcuts in current software
  Rigorous equation derivation and documentation

## Slide 15: New LSA code Capability
Observation reductions
Estimation across epochs
Rigorous add/removal of observations
Support for observation equations, condition equations, fixed and stochastic constraints, hypothesis testing, Helmert blocking
Engine behind all LSA in OPUS as well as REC and SEC computations

## Slide 16: Components
State Plane Coordinates* defined
  Projection parameters for 50 states, DC, plus 5 insular areas (PR, USVI, AS, CNMI, Guam)
    Also “special use zones” as they are approved
    Each with 1-3 possible layers
  All loaded into the NSRS database and available through the data delivery system
*SPCS2022

## Slide 17: SPCS2022 Capability
Allows a user to convert flh in (N/P/M/C)ATRF2022 into SPCS
  At same epoch as flh

## Slide 18: Components
OPUS-S and OPUS-RS replaced with OPUS
  New GUI built with greater flexibility
  OPUS recommendations must be developed and coded into an autonomous prompt for the user to adopt or not
    NSRS database coordinates
    Weights
    Choice of CORSs (using CORS grading system)
  Answers viewable as part of the data delivery system
  Ability for users to submit their data file(s) to NGS

## Slide 19: OPUS Capability (1)
One GNSS file yields at any reasonable epoch(s):
  ITRF2020
    XYZ, flh
  (N/P/C/M)ATRF2022:
    XYZ, flh, SPCS2022, UTM, USNG
  NAPGD2022:
    H, N, x, h, Hdyn, g
  And uncertainty estimates of all of the above
  Users who rely upon OPUS recommendations will get a solution saying “tied to the NSRS”

## Slide 20: Components
2020 Reference Epoch Coordinates (RECs) estimated
  All* geometric (GNSS/RTN/RTK/Classical) data organized
  All* orthometric (leveling) data organized
  All gravimetric (absolute/relative) data organized
  REC project workplace built (database pull, visualization, cleaning, adjustment, checking, loading)
  All three projects executed, including answering all scientific questions (including data age)
  All loaded into the NSRS database and available through the data delivery system
*At least 1994+

## Slide 21: REC Capability
The NSRS database, through the data delivery system will allow users to see, for any PID, these adjusted NSRS coordinates, circa 2020.00:
    ITRF2020
      XYZ, flh
    (N/P/C/M)ATRF2022:
      XYZ, flh, SPCS2022, UTM, USNG
    NAPGD2022:
      H, g
    Plus many differential coordinates between PIDs
    Plus uncertainty estimates of all
These are all considered “part of the NSRS”

## Slide 22: Components
NADCON expanded
  NGS IDB pull of last NAD 83(2011/PA11/MA11) epoch 2010.00 latitudes, longitudes and ellipsoid heights
  NSRS DB pull of (N/P/C/M)ATRF2022 2020.00 latitude, longitude and ellipsoid height RECs
  Outlier cleaning
  Grid size experiments
  Build grids and error grids
  Publish report
  All loaded into the NSRS database and available through the data delivery system

## Slide 23: NADCON Capability
Transform f, l, h from/to:
“To” is default, but other frames available through EPP2022
Region | From | To
CONUS | NAD 83(2011) epoch 2010.00 | NATRF2022 epoch 2020.00
Alaska | NAD 83(2011) epoch 2010.00 | NATRF2022 epoch 2020.00
Hawaii | NAD 83(PA11) epoch 2010.00 | PATRF2022 epoch 2020.00
PR / USVI | NAD 83(2011) epoch 2010.00 | CATRF2022 epoch 2020.00
Amer. Samoa | NAD 83(PA11) epoch 2010.00 | PATRF2022 epoch 2020.00
Guam / CNMI | NAD 83(MA11) epoch 2010.00 | MATRF2022 epoch 2020.00

## Slide 24: Components
VERTCON expanded
  NGS IDB pull of last NAVD 88, PRVD 02, ASVD 02, NMVD 03, GUVD 04, VIVD 09 and LT normal orthometric and orthometric heights
  NSRS DB pull of NAPGD2022 2020.00 orthometric height RECs
  Outlier cleaning
  Grid size experiments
  Build grids and error grids
  Publish report
  All loaded into the NSRS database and available through the data delivery system

## Slide 25: VERTCON Capability
Transform H from/to:
Region | From (no epochs) | To
CONUS | NAVD 88 | NAPGD2022 epoch 2020.00
Alaska | NAVD 88 | NAPGD2022 epoch 2020.00
Hawaii | Local Tidal | NAPGD2022 epoch 2020.00
PR | PRVD 02 | NAPGD2022 epoch 2020.00
USVI | VIVD 09 | NAPGD2022 epoch 2020.00
Amer. Samoa | ASVD 02* | NAPGD2022 epoch 2020.00
Guam | GUVD 04 | NAPGD2022 epoch 2020.00
CNMI | NMVD 03 | NAPGD2022 epoch 2020.00
*Currently deprecated

## Slide 26: Components
Survey Epoch Coordinates (SECs) estimated
  All* geometric (GNSS/RTN/RTK/Classical) data organized
  All* orthometric (leveling) data organized
  All gravimetric (absolute/relative) data organized
  SEC project workplace built (database pull, visualization, cleaning, adjustment, checking, loading)
  Dozens of projects executed, including answering all scientific questions (including size of adjustment windows)
  All loaded into the NSRS database and available through the data delivery system
*At least 1994+

## Slide 27: SEC Capability
The NSRS database, through the data delivery system will allow users to see, for any PID, these adjusted NSRS coordinates, at survey epoch (the time the data was collected):
    ITRF2020
      XYZ, flh
    (N/P/C/M)ATRF2022:
      XYZ, flh, SPCS2022, UTM, USNG
    NAPGD2022:
      H, g
    Plus many differential coordinates between PIDs
    Plus uncertainty estimates of all
These are all considered “part of the NSRS”

## Slide 28: Components
OPUS-Projects replaced with OPUS
  New GUI built with greater flexibility, fully supporting GNSS, leveling, classical and gravity surveys
  OPUS recommendations developed and coded into an autonomous prompt for the user to adopt or not
    NSRS database coordinates
    Weights
    Choice of CORSs (based on CORS grading system)
  Special support for CBLs, airport surveys and other special survey types particular to the mission of NGS and NSRS users
  Answers viewable as part of the data delivery system
  Ability for users to submit their data file(s) to NGS

## Slide 29: OPUS Capability (2)
Survey projects with one or more geodetic observation files yields at any reasonable epoch(s), some or all of the below as adjusted coordinates:
  ITRF2020
    XYZ, flh
  (N/P/C/M)ATRF2022:
    XYZ, flh, SPCS2022, UTM, USNG
  NAPGD2022:
    H, g
  Differential values between some/all points
  Uncertainty estimates of all of the above
  Users who rely upon OPUS recommendations will get a solution saying “tied to the NSRS”

## Slide 30
Defining “the modernized NSRS”
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 31: Original Timeline
In 2007, NGS assumed we would be done by 2018
  Optimistic GRAV-D planning
  Incomplete picture of the entire modernized NSRS
By 2013, a finish of 2022 seemed correct
  Still, the “big picture” wasn’t clear
  Optimism and enthusiasm within NGS was high for many years
By 2020 three issues derailed that date:
  Final clarity on the complexity of the task
  Loss of personnel without backfill
  “2020”
Notes: A friend called 2020 “the longest decade of our lives”

## Slide 32
Defining “the modernized NSRS”
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 33: Progress 2007 through 2020
Clarity: Three “Blueprint” documents fully outlined the modernized NSRS
GRAV-D coverage grew from 0% to 81.6%
xGEOID models, built on GRAV-D, every year from 2014-2020
  xGEOID20 will be first Canada/Mexico/USA joint model, but not the last!
Software to build NADCON and VERTCON grids was entirely rebuilt
  And was used to create NADCON 5.0 release 20160901 and VERTCON 3.0 release 20190601
Notes: NGS has not been idle. For thirteen years, we made significant strides forward.

## Slide 34: Progress 2007 through 2020
18 of 36 NOAA Foundation CORS Network stations operational
SPCS2022 is nearly complete
Multi-GNSS PAGES replacement: 2015-2022
Switch from ITRF2008 to ITRF2014
  Numerous time saving steps implemented, so the switch to ITRF2020 will go even faster
Notes: NGS has not been idle. For thirteen years, we made significant strides forward.

## Slide 35: Progress 2007 through 2020
A scoping study on how best to build IFVM2022 was funded and completed in partnership with Scripps I.O.
A least squares adjustment contract was funded and work begun in 2020
OPUS-Projects was modified to allow Bluebooking
  Laying down the foundation of “work in OPUS, submit data to NGS”
Notes: NGS has not been idle. For thirteen years, we made significant strides forward.

## Slide 36: Progress 2007 through 2020
OPUS-Projects support for RTK/RTN vectors from 2017-2020 (expected release)
  This is the first step toward a fully integrated GNSS+RTN+RTK/Classical/Leveling/Gravity OPUS
Scoping study on organizing raw GNSS data
  Since the current NSRS relies upon processed vectors, and not raw GNSS, the raw GNSS data is poorly organized
    40 person-years to get all half million or so raw GPS files properly associated with a PID, an antenna type and an antenna height
      NGS will rely upon processed vectors for the first REC and SEC adjustments
Notes: NGS has not been idle. For thirteen years, we made significant strides forward.

## Slide 37
Defining “the modernized NSRS”
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 38: Drivers of delay
Government shutdowns
  Three shutdowns in 2018 alone
    Grounded GRAV-D on the brink of its Pacific survey
      Pacific: Expensive, difficult to plan
      Effectively put GRAV-D’s Pacific schedule behind by 1 year

## Slide 39: Drivers of delay
Growing complexity
  As new components were thought of, they often led to additional projects and unforeseen work
  Example: “We need to have time-dependent coordinates”
    But the IDB doesn’t support this
      We need a new database!
        But we also need to define things like “adjustment windows” and “redundancy” and “simultaneous”
        And we need new least squares adjustment software which supports this
          But we have to treat leveling differently from GPS
            And speaking of which, why are we still a GPS-only shop?
              We need multi-GNSS software!
                But that’ll take years! Better get started!

## Slide 40: Drivers of delay
Personnel
  “It seems that every time I look under the hood at NGS, I see a Maserati engine in an office with a budget of a VW bug.”
    Admiral Timothy Gallaudet, Deputy NOAA Administrator
  NGS has both lost and gained significant talent over the last 13 years
    But overall has run a slight deficit in gain/loss
    The CORS team is a fraction of its former size
    However, we’ve been lucky that new hires have been phenomenal
Notes: I put the quote from Admiral Gallaudet here as a reminder – NGS is often running on fumes, and yet we get the job done. It’s nice to see that acknowledgement from on high.

## Slide 41: Drivers of delay
“2020”
  Grounding of GRAV-D flights
    Substantive impact on delay
  Moving to a 100% telework situation for months
    Only moderately impacted the delay

## Slide 42
Defining “the modernized NSRS”
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 43: Rebooting the timeline
The “long pole in the tent” is GRAV-D
  Much of the GRAV-D remaining work is in the Pacific, which raises the question of “phased rollouts”
  Pacific is expensive, difficult to schedule
Correct, On Budget, On Time: Pick two
  With the likelihood of a multi-year delay, we picked “Correct” and “On Budget”
    Do the work right
    Do it with the resources we have

## Slide 44: Rebooting the timeline
Other major high-resource/lengthy issues:
  Replace PAGES
  Fully modernize the NOAA CORS Network
  Complete rebuild of OPUS
  New least squares adjustment library built
  Define, design and build an RTN alignment service
    10+ years of promises…

## Slide 45: Rebooting the timeline
Chain dependencies
  If NGS wishes to roll out NADCON simultaneously with the modernized NSRS:
    NADCON needs reference epoch coordinates (RECs)
    RECs require
      LSA engine
        Contract and money
      Organized raw GNSS, vector GNSS and classical data
        GPS campaign for transformations has to be done
      An environment for visualizing and computing
        Time to build this environment
      A database for storing everything
      Time for experimenting on age-limiting data
      IFVM2022 completely built and available
      N/P/C/MATRF2022 fully defined
        Needs EPPs computed
          Requires a fully modernized NCN
        ITRF2020 fully adopted at NGS
          Requires new orbits in IGS20
          New CORS coordinate functions
            Requires the GRP/ARP issue be resovled satisfactorily
Notes: I purposefully made this fit on one slide, with tiny font to make a point. This is a MASSIVE chain dependency. If users WANT us to put NADCON out with the roll-out, it requires ten other things or so to happen FIRST.

## Slide 46
Defining “the modernized NSRS”
The original timeline
Progress from 2007 through 2020
Drivers of delay
Rebooting the timeline
Phased rollouts or not
Conclusion

## Slide 47: Phased Roll-outs
NGS has a long history of phased rollouts
  Note that I didn’t say “glorious” or “successful”
Phased roll-outs mean a piecemeal service over the years
I am opposed to this approach to the modernized NSRS if it is avoidable

## Slide 48: Phased Rollouts - History
NAD 83 released in 1986
  NADCON released in 1990
    Impact: Four years without any way to transform NAD 27 to NAD 83
NAVD 88 released in 1991
  VERTCON released in 1994
    Impact: Three years without any way to transform NGVD 29 to NAVD 88

## Slide 49: Phased Rollouts - History
The HARN projects, 1990-1997
  State-by-state GPS surveys and adjustments, “feathered together” over 8 years
    In order to roll-out one state at a time, rather than making everyone wait 8 years for a national adjustment
    ~ 40 separate “realizations” of NAD 83 in CONUS
    Impact: Confusion
      “NAD 83(1992)” exists in Alabama and Arizona (and others), but they aren’t really the same thing
      NADCON (pre 5.0) provided four different values at the four corners monument due to four different HARNs at that point

## Slide 50: Phase Rollouts - History
After the HARN projects, we decided to repeat this approach with the FBNs (1996-2001)
  Impact: More confusion
    Some FBNs replaced a HARN, some did not
    NADCON supported HARN and FBN realizations inconsistently

## Slide 51: Phased Rollouts - Possibilities
Are there any phased rollouts which can be implemented without unacceptable difficulties?
  Maybe.

## Slide 52: Phased Rollout – Option 1
Finish GRAV-D over CONUS and then roll-out NAPGD2022 for CONUS only
Problems
  A CONUS-only grid for GEOID2022 would be used for years before the North America-wide grid for GEOID2022 is available. Will NGS force the early grid to remain fixed, or update it when the later, larger grid is ready?
  GEOID2022 will rely upon a global GM2022 model. But if GRAV-D isn’t done, neither is GM2022. Any new GRAV-D data will change GM2022 and has the potential to change geoid undulations anywhere in the world, though with the greatest impacts being those near the newly collected gravity.

## Slide 53: Phased Rollout – Option 2
Finish GRAV-D over North America and then roll-out NAPGD2022 for North America only
Problems
  GEOID2022 will rely upon a global GM2022 model. But if GRAV-D isn’t done, neither is GM2022. Any new GRAV-D data will change GM2022 and has the potential to change geoid undulations anywhere in the world, though with the greatest impacts being those near the newly collected gravity.
  Requires the Aleutians and Hawaii to be done. Considering that these are wrapped up in the overall Pacific plan for GRAV-D, it is unlikely they will be done more than 2 years from Guam/CNMI and Am. Samoa. Why do a phased roll-out for just a 2 year gain?

## Slide 54: Phased Rollout – Option 3
Do not roll out NADCON and VERTCON with the N/P/M/CATRF2022 and NAPGD2022
Problems:
  You’ll wait years to transform your NAD 83 and NAVD 88 data into the modernized NSRS

## Slide 55: Phased Rollout – Option 4
Rollout N/P/C/MATRF2022 before NAPGD2022
Problems:
  Mix of old and new NSRS coordinates:
    NATRF2022 ellipsoid heights, but NAVD 88 orthometric heights? They have no definitional relation, so how do we even do that?

## Slide 56: Phased Rollout – Option 5
Roll-out a version of OPUS that does not allow users to choose their own epochs
  Removes the need for IFVM2022 completion
Problems:
  This effectively limits users to their survey epochs only, with no comparison to older surveys
  Substantially reduces the usefulness of OPUS and thus the quantity of data being submitted to NGS through it

## Slide 57: Conclusion
The modernized NSRS is delayed beyond 2022
  2024-2025 most likely
There is no way to accelerate this
  Can’t make people work faster or harder when they are already at maximum capacity
  Can’t make the troubles of 2020 go away
Phased roll-outs have been considered
  For now, they are off the table

## Slide 58: Thank you

## Slide 59: Questions?