## Slide 1
Preparing for NSRS Modernization:
Guidelines for governments,
corporations and individuals
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
Brief overview
  4 new reference frames and 1 new geopotential datum
  New Types of Coordinates
  Data vs Tools
  Timeline
Six steps to prepare yourselves for the transition

## Slide 3: Brief overview
Notes: NGS has been talking about the modernized NSRS for years. This overview is brief, assuming attendees are familiar with most aspects of it already.

## Slide 4: Federal Users of the NSRS
Notes: Many of these users also sit on the Federal Geodetic Control Subcommittee, so there is a feedback loop between the providers of geodetic control (NGS) and the users of that control.

## Slide 5: Brief overview: 4 new reference frames and 1 new geopotential datum

## Slide 6: Replacing NAD 83
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 7: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  Will include:
  GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022
  More
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
A HUGE component of this
effort is GRAV-D:
Gravity for the Redefinition of
the American Vertical Datum

## Slide 8: Brief overview: New Types of Coordinates

## Slide 9: A two-track approach to coordinates
An estimated “snapshot” of entire network
Every 5 or 10 years
Similar to NAD 83(2011) epoch 2010.00
Reference Epoch Coordinates
Survey Epoch Coordinates
Time-dependent!
Reflects coordinates at time of observation
Multiple SECs can show changes over time

## Slide 10: Re-prioritization: a “data first” approach

## Slide 11: Re-prioritization
There are 33 active projects within NGS explicitly dedicated to NSRS modernization
  In an agency of ~200 people….resources are spread thin
Meanwhile the current NSRS slowly deteriorates
  Marks subside without checking
  CORSs drift away from their published coordinate functions
  The passive control network deviates from active control

## Slide 12: Re-prioritization
NGS has recently decided to release all of the modernized NSRS data before we have fully completed all support tools
If we do not take this approach, we are not likely to see the modernized NSRS defined and released until 2030

## Slide 13: Data
Upon release, the modernized NSRS will consist of this data:
  The NOAA CORS Network (NCN) operating on ITRF2020
  NATRF2022, PATRF2022, MATRF2022, CATRF2022 defined relative to ITRF2020
  NAPGD2022, including:
    GM2022, GEOID2022, DEFLEC2022, GRAV2022
  Geometric (XYZ / flh) and orthometric (H) reference epoch coordinates (RECs) at 2020.00 at those passive control with the observations to support such coordinates
  Geometric (XYZ / flh) and orthometric (H) survey epoch coordinates (SECs) at survey epochs between about 1994 and 2020 at those passive control with the observations to support such coordinates
  State Plane Coordinates of 2022 (SPCS2022), plus UTM and USNG
  NADCON
    Connecting NAD 83(2011/MA11/PA11) epoch 2010.00 to N/P/M/CATRF2022 epoch 2020.00
  VERTCON
    Connecting NAVD 88, PRVD02, ASVD02, NMVD03, GUVD04 and VIVD09 to NAPGD2022 epoch 2020.00

## Slide 14: Tools
At a minimum, NGS is targeting these tools upon release:
  A DDS capable of yielding:
    RECs on some kind of datasheet
    Information on CORSs
  A downloadable version of LASER
  A browser-based online multi-GNSS service:
    Like OPUS-S
    Like OPUS-Projects 5.x
  NCAT and Vdatum capable of invoking NADCON, VERTCON and SPCS2022

## Slide 15: What comes after…
Next steps after the initial release of the modernized NSRS include:
  Integrating leveling, classical data and gravity into OPUS
  Full integration of all old tools into NCAT and Vdatum
  SECs for pre-1994 (AKA “pre-NCN”) years, plus SECs for post-2020

## Slide 16: Timeline

## Slide 17: Timeline
Resources are being diverted from tool building to the assurance of quality data first and foremost
As such, based on this new approach, NGS anticipates the release of all data, and limited tools, by the middle of 2025.
Work on additional tools will continue in the out-years

## Slide 18: Preparing yourselves: Six steps to successfully transitioning to the modernized NSRS

## Slide 19: Stay Calm
Many ways of doing business will stay the same
  Static coordinates, like NAD 83(2011) epoch 2010.00 are now “RECs”
  Leveling remains the most accurate way to measure local height differences
Many new tools will (finally) support long-established practices
  OPUS-Projects now supports RTK/N data
  Low-distortion projections will be in SPCS2022

## Slide 20: Stay Calm
Many new things are helpful, but optional
  SECs will show time-dependency on passive marks, but shouldn’t be used as geodetic control
  The ITRF is the foundation of the modernized NSRS, but you aren’t required to use it
NADCON and VERTCON will be there for you
  Every latitude, longitude and height will change by decimeters to meters overnight
  But these changes will be modeled into NADCON and VERTCON at release

## Slide 21: Familiarize yourself with the modernized NSRS
Read the Blueprint documents, especially #3
  https://geodesy.noaa.gov/library/
Check out the presentation library
  https://geodesy.noaa.gov/web/science_edu/presentations_library/
Check out the NGS webinar series, new and old:
  https://geodesy.noaa.gov/web/science_edu/webinar_series/
Subscribe the NSRS Modernization newsletter:
  https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 22: Ask those agencies and companies that you rely on about their transition plans
Despite previous mandates from the FGCS, some federal agencies took years to get onto the current NSRS, if at all…
  Some still use the 1912 vertical datum
    Never heard of it? It came before NGVD 29, which came before NAVD 88 which is about to be replaced
Many companies are quick to adopt
  Contact your reps at ESRI, Trimble, Blue Marble, Leica, Topcon, Javad, MicroSurvey, etc.
    Many of them have been in contact with NGS and so we expect their software to support things quickly

## Slide 23: Organize your historic data archives
When a new frame or datum is released, NGS always recommends these choices, in decreasing order of accuracy:
  Re-survey points of interest
  Re-adjust old observations to control in the new system
  Transform using NADCON and/or VERTCON
Your fastest, but least accurate, way to get into the modernized NSRS is through NADCON and VERTCON
  Built into NCAT and Vdatum
  Available publicly, so software vendors can incorporate it into their products and services

## Slide 24: Check out NGS tools as they are released
Updates to OPUS-Projects 5.x coming soon will lean us into the modernized NSRS:
  M-PAGES for multi-GNSS processing
  No more bluebooking
  Use of ITRF2020
  New methods of doing LSA with new tool “LASER”
SPCS2022 released by end of CY2022
Alpha versions of NADCON and VERTCON by end of CY2023

## Slide 25: Embrace the future
The planet is round, dynamic and complicated
  Consider switching to the ITRF
  Do not expect coordinates to stay the same for years
Passive marks have a very new role
  Monitoring motion, not holding a static coordinate indefinitely
  Tie your surveys to the NOAA CORS Network
Going leveling? Pack your GNSS equipment!
  Leveling won’t yield absolute heights without height control, which will come from GNSS + geoid

## Slide 26: In summary…
Big changes are coming
You can prepare if you
  Stay Calm
  Familiarize yourself with the modernized NSRS
  Reach out to agencies and companies upon which you rely
  Organize your historic data archives
  Check out NGS tools as they are released
  Embrace the Future

## Slide 27: Thank you!

## Slide 28: Questions?