## Slide 1
The Last Mile:
Final push for new datums, progress, and what is still to come
Dan Martin
Northeast Regional Geodetic Advisor
Dan.martin@noaa.gov
240-676-4762
New Hampshire Land Surveyors Association
December 06, 2024

## Slide 2: Today’s Topics
Modernization Progress
  GRAV-D
  GPSonBM
  Laser, SPROCCET
  Beta
    OPUS 5 (GNSS)
  Alpha Page
  NCN Station Page
  CORS Time Series Tool
  Modernized OPUS Tools
OPUS Projects 5.2 (Production)
    GVX
    Publish
    Online Videos and Tutorials
NOS NGS 92
NSRS Mod Timeline
  Rollout, Testing Replacement

## Slide 3: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2020 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2020 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…
Notes: We’ll talk about that ‘plate fixed’ later.
Now wait a minute Jeff, what is the IGS? You just explained the ITRF and told us about that!!
IGS Reference Frame is pretty much equivalent to the ITRF, created by the Intl. GNSS Service, of which NGS is a contributing partner.
The Intl. GNSS Service, let’s take a look at their website for a minute.
-pronounced “oiler” poles

## Slide 4
Notes: -there’s four reference frames because there are four major tectonic plates within the NGS Area of Responsibility.
-As the National Geodetic Survey, we’re part of the DoC so we must cater to all US States and Territories
-thus we’ve got four tectonic plates in our Area of Operations, so four Ref Frames
-But…

## Slide 5: Names
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 6: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID18
  DEFLEC18
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
one vertical datum
pole-to-equator

## Slide 7: Recent Progress

## Slide 8: GRAV-D Project Overview
Overall Target: 2 cm accuracy orthometric heights from GNSS and a geoid model
GRAV-D Goal: Create gravimetric geoid accurate to 1 cm where possible using airborne gravity data
GRAV-D: Two thrusts of the project
  Airborne gravity survey of entire country and its holdings
  Long-term monitoring of geoid change
Leveraging partnerships to improve and validate gravity data
Notes: Target is to be able to achieve 2 cm accuracy orthometric heights (where possible) using a GNSS receiver and a geoid model
Roughly 1 cm uncertainty from GNSS and 1 cm from the geoid model
GRAV-D
Phase 1: snapshot of the entire country to provide a consistent data set
Phase 2: long term monitoring of geoid change – in development
Work with partners to incorporate additional gravity data, particularly surface gravity data, validate existing data, and monitor change

## Slide 9: Data Collection Scope
Entire U.S. and territories
  Total Square Kilometers: 15.6 million
  Initial target area for 2022 deadline
  ~200 km buffer around territory or shelf break if possible
Notes: Project Scope:
Scope of the project: cover roughly 15.6 million square kilometers – contiguous united states, Alaska, Hawaii, Guam, and American Samoa
In order to blend with satellite altimetry data the airborne survey is done to the continental shelf where possible or ~ 200 km beyond the shoreline or border, whichever is further
Deadline of 2022 for datum rollout, which means a target of 2021 to finish the airborne survey
Priority areas were defined as Alaska and coastal areas
Challenges:
Fixed annual budget and time  design of surveys had to fit within an annual budget of $3.5 million and meet the deadline
This was a major factor in setting altitude and line spacing

## Slide 10: Gravity Survey Plan
National Scale Part 1
  Predominantly through airborne gravity
  With Absolute Gravity for ties and checks
  Relative Gravity for expanding local regions where airborne shows significant mismatch with existing terrestrial

## Slide 11: Airborne Gravity Current Coverage
http://www.ngs.noaa.gov/GRAV-D/data_products.shtml

## Slide 12: GRAV-D Progress
100% of target area flown!
Re-flew some older, lower quality lines
Flying Canadian Rockies
Beginning to plan some Terrestrial Gravity to densify relative gravity in areas with interesting gravity signals.
Planning absolute gravity 10-15 sites in the NW to support GeMS (Geoid Monitoring Service)

## Slide 13: Geoid Monitoring Service GeMS
Following slides taken from presentations by Kevin Ahlgren, GeMS Project Manager

## Slide 14: Monitoring Geoid Change: Static vs. Dynamic From Damiani, 2017 Geospatial Summit
Static, except for model updates
Deforms, subsides, uplifts at all length scales
Changes along with large-scale gravity change (caused by mass movement)
The height that U.S. National Spatial Reference System Users need
Calculated from geoid models
Measured with GPS
In a changing world, Ḣ ≈ ḣ - Ṅ.
Option 1: Provide a series of static geoids, updated whenever change somewhere in the U.S. reaches 0.5 cm. [Not NGS’ choice]
Option 2: Provide a static geoid (N0) and geoid change over time (Ṅ) so that orthometric heights remain accurate to 1 cm at all times. Ht = ht-(N0+ Ṅ*t) [NGS’ choice]
h = ellipsoidal height;
N = geoid height (undulation);
H = orthometric height
In a static world, H ≈ h - N
2022 aim is to achieve 1 cm geoid height accuracy (wherever possible) and 1 cm ellipsoidal height accuracy.

## Slide 15: GeMS Project Status
Research and Development
  Scope:
    What can NGS do? What can NGS not do?
    What are the costs, benefits, and risks of doing or not doing a particular element within GeMS?
  Status:
    Nearly completed (95% done).
  Deliverables:
    NOS NGS Technical Report 69: A Preliminary Investigation of the NGS’s Geoid Monitoring Service (GeMS)
    Alpha Products: xDGEOID19 – a dynamic geoid model will be available for testing with xGEOID19.
    Supporting Tools: Software, documentation, and details.
    Recommendations that will drive subsequent GeMS stages.
Operations and Development (TBD)
Refinement and Improvement (TBD)

## Slide 16: xDGEOID20
Alpha model based on secular trend from GRACE (NASA GSFC mascon v02.4, Luthcke, et al. 2013)).
Units: mm/yr.
Contour Interval: 0.5 mm/yr

## Slide 17: GPSonBM for Transformation Tool

## Slide 18: All in all, an amazing effort

## Slide 19: LASER
Least squares Adjustments: Statistics, Estimates and Residuals
Contract began in August 2020
Solves many LSA problems
    Has been tested on historic NGS archives
  Uses the pre-existing Eigen library of linear algebra routines

## Slide 20: A (probably incomplete) history of LSA software at NGS
INERT1 (1982) …….. Inertial
HOACOS (1979)…… Precursor to Adjust
HAVAGO (1979)……. Precursor to Adjust for 3D djustments
ADJUST ……………. Horizontal, modified for GPS, used by OP
GPSCOM/LLSOLV...Used to compute CORS network, early OP
ASTA………………...Geodetic leveling
NETSTAT …………...Built for 2007 adjustment, used again in 2011
APOGEE…………….Relative Gravity
CALIBRATE……….. Calibration Baselines
Additionally, LSAs are encompassed within this NGS software tool:
PAGES
Also, there is the following stand-alone set of matrix manipulation subroutines:
Heart Of Gold (1984)

## Slide 21: Concerns: General
Inconsistency
  Different languages, different variable names, and different times lead to inconsistency in code
    Some programs might be perfectly compatible, but it’s difficult to know with such a vast number of authors and code over the years.
Lack of generality
  Code written to adjust only one type of geodetic observation has limited usefulness to other applications
Languages: FORTRAN, C++, MATLAB are all in use today
Scalability

## Slide 22: Software for PRojecting Observations, Constraints and Cofactor matrices/Errors through Time (SPROCCET)
Replaces HTDP
Support for orthometric data
Use of Geodetic Data eXchange (GDX) format
Use of IFDM2022
Error propagation through time
Distinct modules for 14-parameter Helmert transformations and deformation models

## Slide 24
Currently in BETA!!
Capable of ingesting all GNSS observables currently supported by the global infrastructure
Capable of using more than two frequencies.
Capable of ingesting RINEX 2 or 3
  Version 2 only supports GPS and GLONASS, Galileo (to a limited extent)
  Submission of proprietary data will result in RINEX 2.11 (limitation of TEQC). NGS will ONLY accept RINEX submission in the near future.
Capable of using pseudorange and phase.
Uses a single-difference processing strategy.
M-PAGES can support NGS strategic objectives.
M-PAGES = Multi-GNSS PAGES
January 26, 2021
Multi-GNSS OPUS : First Call for Internal Testing

## Slide 26: CORS Info (Moved Beta=>Prod)
https://geodesy.noaa.gov/CORS/ncn_station_pages/index.html?stationID=CTNE

## Slide 27: NSRS Modernization Alpha Site
Provides examples of the content, format, and structure of select data and products that NGS plans to release as a part of the Modernized NSRS
Products found on this page are for testing purposes only and do not contain any authoritative NGS data or tools

## Slide 32: What’s New in OPUS World?
OPUS Projects 5.1 moved to Production
  Current version 5.2
  Full support for Bluebooking
  Supports the uploading, QA/QC, adjustment, and submission for publication of real-time kinematic (RTK) vectors in the GVX file format.
  Working to replace mandatory, instructor-led Managers training with self-paced, online videos and tutorials.
  OPUS 5.0 in Beta (includes M-PAGES)
    Multi-constellation

## Slide 33: GNSS Vector EXchange Format (GVX)
Website: https://www.ngs.noaa.gov/data/formats/GVX/index.shtml
Detailed documentation
Schema (XSD)
Example vector files
GVX is written in Extensible Markup Language (XML)
Designed to store and carry data in plain text format
Flexible representation of arbitrary data structures
Extensible – new elements can be added later without breaking applications
Both machine-readable and human-readable
Schemas can be used to define “must haves” and “should haves”

## Slide 34: GVX Do’s and Don’t’s
Make sure your manufacturer supports GVX
Collect RTK/RTN observations
  Recommend between 3 and 6, 5-min observations, some should be on a different day
  Make sure that you are storing the vector in addition to coordinates
  If RTN, make sure the vector is from a Physical Reference Station, not from a Virtual Reference Station
  If Base is not a NCN station, collect static data on it to be processed in OP

## Slide 35: GVX Do’s and Don’t’s Cont…
Load observations to your office software
  some manufactures allow the creation of GVX in the data collector.
  Convert your vector(s) to GVX Format
Upload to an OPUS Project

## Slide 36: Design for OPUS-Projects and GVX
[Adapted from Weaver et al. 2018]
GVX file (from RTK survey or baseline processing in other software)
375-800 km
OPUS-Projects (from static GNSS session processing)
RTK Base or “From” Mark
RTK Rover or “To” Mark
Vector
Vector in GVX File
375-800 km

## Slide 37: Three Cases for RTK/RTN Bases
RTN Base = CORS
Automatically attaches GVX vectors to official coordinates for CORS
Constrain CORSs
RTK/RTN Base = Not a CORS and new to NGS
Upload static GPS data logged at the base during the days of the RTK survey
Perform session baseline processing to connect to CORSs
Constrain CORSs
3. RTK/RTN Base = Not a CORS but has a datasheet
Could constrain coordinates on datasheet
Or, upload static data at the RTN base, logged during the days of the RTK survey; perform session baseline processing; constrain CORSs

## Slide 40
CORS Page short-term series only shows last 90 days

## Slide 43: ,

## Slide 44: October 09, 2024

## Slide 45: Modernization Timeline
In 2022, NGS diverted resources from tool-building to data assurance
  “Limited tools, excellent coordinates”
  Set a goal of roll-out by 2025
NGS is on-track to roll out the modernized NSRS by the middle of 2025.
Work on additional tools will continue in the out-years

## Slide 46: Rollout, Testing, Replacement
NGS will roll out components of the modernized NSRS over time (2025-2026)
As each component is rolled out, it can be tested
Once the final component (likely VERTCON) is rolled out (likely late 2025), testing will continue for at least 6 months
Once enough testing is done, and all modernized NSRS components seem stable and correct, the FGCS will vote (likely 2026)
If affirmative, the modernized NSRS will replace the current NSRS

## Slide 47: Initial rollout
NGS promised many things in the three Blueprint documents
Not all can be built in a timely manner
So when we say “rollout”, we mean initial rollout, which is at least the minimum viable products needed to replace the current NSRS with the modernized NSRS
Future products and services supporting the modernized NSRS will be rolled-out after the FGCS vote

## Slide 48: Rollout: Alpha, Beta, Live
NGS will use three different websites (URLs) as we roll-out the modernized NSRS:
  Live: www.ngs.noaa.gov
    Will hold the current NSRS until the modernized NSRS has been fully tested and the FGCS has voted to replace the current NSRS with the modernized NSRS
  Beta: beta.ngs.noaa.gov
    Re-designed to hold modernized NSRS products only
    Every component of the modernized NSRS will be placed here
    Products assumed to be complete and correct
    For testing
    Subject to change or deletion
  Alpha: alpha.ngs.noaa.gov
    “Incomplete, early, possibly incorrect”
    Not everything will go on alpha

## Slide 49: Snapshot of the modernized NSRS at the end of initial rollout
Not everything promised in the Blueprint documents will be built in time for the initial rollout. But the following will be:
  ITRF2020, N/P/C/MATRF2022, NAPGD2022, SPCS2022
  NSRS Database, new datasheets for marks and stations
  RECs
  OPUS-S with multi-GNSS
  OPUS-Projects (GPS only):
    GDX, SPROCCET, LASER, NSRS DB submission
    The ability for NGS to generate RECs from OPUS submissions in a timely manner

## Slide 50: Rollout onto Beta
ITRF2020 on NCN
EPP2022
IFDM2022
SPCS2022
GM2022
GEOID2022
DEFLEC2022
GRAV2022
DEM2022
OPUS-S (GNSS)
Geometric RECs
in N/P/C/MATRF2022
Orthometric RECs
in N/P/C/MATRF2022
NADCON 6?
VERTCON 4?
beta.ngs.noaa.gov:
www.ngs.noaa.gov:
ITRF2020 on NCN
OPUS-S (GNSS)
OPUS-Projects (GPS)
(Bluebooking, HTDP, ADJUST, NGS IDB, Datasheets)
OPUS-Projects (GPS)
(GDX, SPROCCET, LASER, NSRS DB, New Datasheets)
SPCS 83
N/P/C/MATRF2022
NAPGD2022
Mid 2024
NAD 83
NAVD 88
Late 2024
Early 2025
Late 2025
GEOID18
DEFLEC18
OPUS-Share
OPUS-RS (GPS)
NADCON 5
VERTCON 3

## Slide 51: Testing into replacement
From late 2025 into sometime in 2026, all modernized NSRS components on Beta will go through testing and feedback
After the FGCS vote, a few months of work remain:
  The FGCS will issue an FRN officially announcing the adoption of the modernized NSRS
  The beta website may be wiped of submitted data*
  All modernized NSRS components moved to the Live website
Notes: Notes: NGS is considering what to do with data submitted during testing. The cleanest solution is to delete it as “test data” and not attempt to move it onto the Live website. If we were to consider moving it to Live, we would need to re-submit the data to ourselves, which is a tremendous amount of work. It is best to assume that NGS will ask submitters to re-submit after the switch.

## Slide 52: Summary
The modernized NSRS is coming soon!
  Starting this year!
All components should be on Beta by 2025
  For testing only!
It won’t replace the current NSRS until an FGCS vote (2026)
NGS will continue to support the current NSRS through the rollout and testing of the modernized NSRS
We encourage you to test each component as it is released

## Slide 53
https://geodesy.noaa.gov/library/pdfs/NOAA_TM_NOS_NGS_0092.pdf

## Slide 54: NOAA Technical Memorandum NOS NGS 92 Classifications, Standards, and Specifications for GNSS Geodetic Control Surveys Using OPUS Projects
Directly supports GNSS Surveys using OPUS-Projects, NAD 83 and NAVD 88
  Includes Real-time techniques
Directly ties survey design, observations, and procedures to accuracies
Backed-up by documented research
Specifications can live outside the document

## Slide 55
Classifications will not be on datasheet, but are used to describe the intended use

## Slide 56: Observation Type Definitions
OPUS PP – Static, OPUS Projects
GVX PP - post-processed static or rapid static data using external software
GVX NRTK – Network RTK/RTN (Virtual Reference Station (VRS) method, Master Auxiliary Concept (MAC), etc.
GVX SRTK – Single Base RTK from realtime base station or conventional base/rover

## Slide 57: Observation Requirements

## Slide 58: Observation Requirements cont..

## Slide 59: Modernized OPUS-S
Removal of OPUS-Share and OPUS-RS
15 min to 48 hours of data*
RINEX-only upload
Multi-GNSS processing (M-PAGES)
Simultaneous baseline processing
Updated CORS Selector
9-character CORS IDs
New frames: ITRF2020, N/P/M/CATRF2022, SPCS2022
New geoid and vertical frame: GEOID2022, NAPGD2022

## Slide 60: OPUS-Projects
Submitting to NGS:
  Removal of project proposal requirement
  Removal of description file requirement
Tracking number for all projects = NGS Survey Project Number
Updated CORS Selector
9-character CORS IDs
Automate adding Distant CORS

## Slide 61: OPUS-Projects
GPS-only: Session adjustment via PAGES
Removal of Gpscom and ADJUST
SPROCCET is the LASER pre-processor, replacing HTDP
LASER replaces ADJUST (2 sets of network adjustments)
New datasheets via the DDS
New frames: ITRF2020, N/P/M/CATRF2022, SPCS2022
  Results in specific frame (epoch) will vary by adjustment
New geoid and vertical frame: GEOID2022, NAPGD2022

## Slide 62: Thank You! Questions?
Dan Martin
Northeast Regional Geodetic Advisor
ME, NH, VT, MA, CT, RI, NY, NJ
Dan.martin@noaa.gov
240-676-4762
Presentation will be available at:
https://www.ngs.noaa.gov/web/science_edu/presentations_library/