## Slide 1
The Modernized
National Spatial Reference System
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
BLUF
Refresher on NSRS Modernization
Magnitudes and Transformations
Timeline
Rollout/testing/replacement

## Slide 3: Bottom Line, Up Front

## Slide 4: BLUF
In 2026, the coordinates of every point on every map, chart, airport survey or other geospatial data set will change.
  Every latitude, longitude and ellipsoid height will change from its current values by +/- 2 meters (median) with extremes up to 4 meters
  Every orthometric (“Mean Sea Level”) height will change from its current values by +/-2 meters (median) with an unknown limit on change due to (as yet) unquantified subsidence impacts

## Slide 5: Refresher on NSRS Modernization

## Slide 6: The National Spatial Reference System
The NSRS
Official coordinate system for the USA
Defined by the National Geodetic Survey (NGS)
  Approved by the Federal Geodetic Control Subcommittee (FGCS)
    The FAA is a member
Required to be used by all civilian Federal Government agencies
  OMB A-16
  Geospatial Data Act
Often used by many state and local government agencies or private surveyors

## Slide 7: Extent of the current NSRS
Geometric Reference Frames:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
Truly global but used regionally
Geoid models/Vertical Datums:
Regional
  Conterminous US (CONUS; “Lower 48”)
  Alaska
  Hawaii
  Territories: Puerto Rico, U.S. Virgin Islands, American Samoa, Guam, CNM

## Slide 8: What about WGS 84?
WGS 84 is not part of the NSRS
  WGS 84 is a military system, with their own rules.
  No civilian agency (including the FAA) should be using WGS 84.
  However, NGS recognizes the appeal of WGS 84:
    Global
    Geocentric / aligned with GPS
  For these very reasons, the Modernized NSRS will also be global and geocentric / aligned with GPS.
    A proposal is provided at the end of this briefing

## Slide 9: NSRS Modernization
Has been ongoing since 2007
This talk presumes some existing knowledge of NSRS Modernization. For finer details look here:
  NGS Presentation Library (https://geodesy.noaa.gov/web/science_edu/presentations_library/)
  NGS New Datums Page (https://geodesy.noaa.gov/datums/newdatums/index.shtml)
  The Blueprint Documents (https://geodesy.noaa.gov/datums/newdatums/policy.shtml)

## Slide 10: Preeminence of ITRF
North American Terrestrial Reference Frame of 2022 (NATRF2022)
Caribbean Terrestrial Reference Frame of 2022 (CATRF2022)
Pacific Terrestrial Reference Frame of 2022 (PATRF2022)
Mariana Terrestrial Reference Frame of 2022 (MATRF2022)
Remove the rotation of the North American Plate
Remove the rotation of the Caribbean Plate
Remove the rotation of the Pacific Plate
Remove the rotation of the Mariana Plate
ITRF2020
EPP2022
EPP for “Euler pole parameters”
(a way of describing a plate’s rotation)
Why 5 frames?
The ITRF is the international gold standard, and is fixed to no particular plate (latitude/longitude will drift ~ few cm/year). It is global and geocentric.
The USA has population centers on four plates, and many users wish to see the drift of latitude and longitude “hidden” over time, so we fix the frames to those four plates. They will also be global (but meant to be used on one plate) and geocentric.

## Slide 11: NSRS Modernization in (very) brief
Hybrid geoids
NAPGD2022
GEOID2022
Bluebooking
FORTRAN
Disparate tools
Outdated manuals
GVX / OPUS
Modern coding
Integrated tools
Updated manuals
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
ITRF2020
NATRF2022
PATRF2022
CATRF2022
MATRF2022
NAVD 88
ASVD 02
PRVD 02
NMVD 03
GUVD 04
VIVD 09

## Slide 12: Magnitudes and Transformations

## Slide 13: Magnitudes
When should the FAA care about this?
  When accuracy needs are around 4 meters or smaller
    No: Barometrically determined altitudes
    Yes: Cat III ILSs, Airport surveys

## Slide 14: Changes from NAD 83 to NATRF2022

## Slide 15: Changes from NAVD 88 to NAPGD2022

## Slide 16: Everything must shift

## Slide 17: Everything must shift
RED: NAD 83 coastline against NAD 83 imagery
GREEN: Coastline shifted into NATRF2022 but
the imagery remains on NAD 83
Shifts ~1 meter

## Slide 18: Transformation tools
NADCON
  Latitudes, longitudes, ellipsoid heights
  NAD 83 to ITRF2020, NATRF2022, PATRF2022, MATRF2022, CATRF2022
VERTCON
  Orthometric (“MSL”) heights
  NAVD 88 (and others) to the NAPGD2022
Both of these tools are built into NGS’s flagship product NCAT
  NCAT : NGS Coordinate Conversion and Transformation Tool

## Slide 19: What to do with historic charts?
Is the accuracy expected to be better than a few meters?
Stop. You won’t likely gain much by transforming
Do you have trusted metadata which puts the chart in the NSRS? (Note, WGS 84 is not part of the NSRS)
No
Yes
Stop. Transformation tools only work in the NSRS and only if you trust the metadata
No
Use NCAT to update the datums (available for testing in late 2025)
Yes

## Slide 20: Timeline

## Slide 21: Timeline
In 2022, NGS diverted resources from tool-building to data assurance
  “Limited tools, excellent coordinates”
  Set a goal of roll-out by 2025
NGS is on-track to roll out the modernized NSRS by the middle of 2025.
Work on additional tools will continue in the out-years

## Slide 22: Rollout, Testing, Replacement

## Slide 23: Rollout, Testing, Replacement
NGS will roll out components of the modernized NSRS over time (2024-2025)
As each component is rolled out, it can be tested
Once the final component (likely VERTCON) is rolled out (likely late 2025), testing will continue for at least 6 months
Once enough testing is done, and all modernized NSRS components seem stable and correct, the FGCS will vote (likely 2026)
If affirmative, the modernized NSRS will replace the current NSRS

## Slide 24: Rollout: Alpha, Beta, Live
NGS will use three different websites (URLs) as we roll-out the modernized NSRS:
  Live: www.ngs.noaa.gov
    Will hold the current NSRS until the modernized NSRS has been fully tested and the FGCS has voted to replace the current NSRS with the modernized NSRS
  Beta: beta.ngs.noaa.gov
    Soon to be re-designed to hold modernized NSRS products only
    Every component of the modernized NSRS will be placed here
    Products assumed to be complete and correct
    For testing
    Subject to change or deletion
  Alpha: alpha.ngs.noaa.gov
    “Incomplete, early, possibly incorrect”
    Not everything will go on alpha

## Slide 25: Current NSRS during rollout and testing
While the modernized NSRS is being rolled out and tested, the current NSRS will remain the official NSRS of the United States
  This will not change until the FGCS vote (probably 2026)
URL www.ngs.noaa.gov will only hold current NSRS

## Slide 26: Testing into replacement
From late 2025 into sometime in 2026, all modernized NSRS components on Beta will go through testing and feedback
After the FGCS vote, a few months of work remain:
  The FGCS will issue an FRN officially announcing the adoption of the modernized NSRS
  The beta website may be wiped of submitted data*
  All modernized NSRS components moved to the Live website
    Submissions will then begin in earnest and won’t be deleted
  All current NSRS components moved “elsewhere”
    No further submissions to the NGS IDB will be allowed at this point
Notes: Notes: NGS is considering what to do with data submitted during testing. The cleanest solution is to delete it as “test data” and not attempt to move it onto the Live website. If we were to consider moving it to Live, we would need to re-submit the data to ourselves, which is a tremendous amount of work. It is best to assume that NGS will ask submitters to re-submit after the switch.

## Slide 27: After testing and the FGCS vote
beta.ngs.noaa.gov:
geodesy.noaa.gov:
OPUS-Projects (GPS)
(Bluebooking, HTDP, ADJUST, NGS IDB, Datasheets)
ITRF2020 on NCN
EPP2022
IFDM2022
SPCS2022
GM2022
GEOID2022
DEFLEC2022
GRAV2022
DEM2022
OPUS-S (GNSS)
Geometric RECs
in N/P/C/MATRF2022
Orthometric RECs
in N/P/C/MATRF2022
NADCON 6?
VERTCON 4?
OPUS-Projects (GPS)
(GDX, SPROCCET, LASER, NSRS DB, New Datasheets)
N/P/C/MATRF2022
NAPGD2022
ITRF2020 on NCN
OPUS-S (GNSS)
SPCS 83
NAD 83
NAVD 88
GEOID18
DEFLEC18
OPUS-Share
OPUS-RS (GPS)
NADCON 5
VERTCON 3
All submissions provided during testing may get deleted
“Elsewhere”

## Slide 28: After testing and the FGCS vote
“Elsewhere”
geodesy.noaa.gov:
OPUS-Projects (GPS)
(Bluebooking, HTDP, ADJUST, NGS IDB, Datasheets)
ITRF2020 on NCN
EPP2022
IFDM2022
SPCS2022
GM2022
GEOID2022
DEFLEC2022
GRAV2022
DEM2022
OPUS-S (GNSS)
Geometric RECs
in N/P/C/MATRF2022
Orthometric RECs
in N/P/C/MATRF2022
NADCON 6?
VERTCON 4?
OPUS-Projects (GPS)
(GDX, SPROCCET, LASER, NSRS DB, New Datasheets)
N/P/C/MATRF2022
NAPGD2022
ITRF2020 on NCN
OPUS-S (GNSS)
SPCS 83
NAD 83
NAVD 88
GEOID18
DEFLEC18
OPUS-Share
OPUS-RS (GPS)
NADCON 5
VERTCON 3
All submissions from this point forward get saved
No submissions to the NGS IDB allowed any longer

## Slide 29: A radical idea…
The FAA should consider abandoning the plate fixed components of the NSRS
  This obviously means updating OMB A-16…(see earlier)
  In favor of the global, plate-independent ITRF2020 frame
  NGS will support ITRF2020 positioning as well as four “plate fixed” frames
  The ITRF2020 and WGS 84 are actually closely aligned to each other
Why?
  Consider flying from Denver to Honolulu
    In Denver, the NATRF2022 latitude/longitude will look constant in time
    In Honolulu, the PATRF2022 latitude/longitude will look constant in time
      But they don’t look constant when compared to each other
      Why not just switch to a system which accepts and embraces the dynamic earth? : ITRF2020

## Slide 30: Summary
The modernized NSRS is coming soon!
  Starting this year!
All components should be on Beta by 2025
  For testing only!
It won’t replace the current NSRS until an FGCS vote (2026)
NGS will continue to support the current NSRS through the rollout and testing of the modernized NSRS
We encourage you to test each component as it is released

## Slide 31: Thank you!

## Slide 32: Questions?