## Slide 1: SUBDAILY ALIAS AND DRACONITIC ERRORS IN THE IGS ORBITS
Jake Griffiths & Jim Ray
NOAA/National Geodetic Survey
Acknowledgement: Kevin Choi
Harmonics of 351 d evident in all IGS products
  origin still unknown: local multipath or GPS orbits ?
Study orbital response due to IERS diurnal & semi-diurnal (subdaily) EOP tide errors
  simulate response: compare conventional orbits to those determined using pseudo real-Earth (“fake”) model
  beating of subdaily tides causes signatures at other periods
  compare signatures with IGS orbit discontinuity results
Subdaily model errors enter orbits at various periods, including odd harmonics of 351 d
  24 h sampling causes input errors to alias at unexpected periods
AGU Fall 2011, Session G54A-01, San Francisco, 9 December 2011

## Slide 2: Harmonics of GPS Draconitic Year are Pervasive
GPS-sun geometry repeat period
  “draconitic” year = 351.2 d
  1st & 2nd harmonics overlay
  seasonal signals
IGS station coordinates (2006)
  in all dNEU components
  up to at least 6th harmonic
later found in all IGS products:
  “geocenter” variations
  polar motion rates (esp 5th & 7th)
  LOD (esp 6th)
  orbit discontinuities (esp 3rd)
strong fortnightly signals also common
signals clearer in reprocessed results
02
% of GPS Stations
Frequency (cycles per year)
dE
dN
dU
(from X. Collilieux et al., 2011)

## Slide 3: Possible Origins of Draconitic Signals
1) local multipath effect at stations
  station-satellite geometry repeats every sidereal day, approximately
  2 GPS orbital periods during 1 Earth inertial revolution
    actual GPS repeat period = (1 solar day - ~245 s)
    sidereal period (K1) = (1 solar day - 235.9 s)
  for 24-hr sampling (e.g., data analysis), alias period → GPS draconitic year
2) mismodelling effect in satellite orbits
  empirical solar radiation parameters intrinsically linked to orbital period
  but no precise mechanism proposed yet
this presentation examines impact of errors in a priori IERS model for subdaily tidal EOP variations on GPS orbits
  EOP tide errors at ~12 hr couple directly into GPS orbit parameters
  EOP tide errors at ~24 hr may couple into other estimates
  subdaily EOP total magnitudes are ~1 mas = 13 cm shift @ GPS
  IERS model is known to have visible errors, which could reach the 10 to 20% level
03

## Slide 4: Simulate Impact of Subdaily EOP Errors
process ~3 years of GPS orbits with IERS & “fake” models
  “fake” model subdaily admittances differ by ~20%
  model intended to mimic a real-Earth model
  subdaily tides beat to generate spectral differences at other periods
04
Frequency (cycles per day)
Power Density (mm2 / cpd)

## Slide 5: Simulate Impact of Subdaily EOP Errors
04
Frequency (cycles per day)
Power Density (mm2 / cpd)
process ~3 years of GPS orbits with IERS & “fake” models
  difference conventional & EOP-test orbits @ 15 min intervals
  compute spectra of differences for each SV, stack & smooth
  compare spectral differences: input model errors vs. orbital response

## Slide 6: Simulate Impact of Subdaily EOP Errors
04
Frequency (cycles per day)
Power Density (mm2 / cpd)
long-period errors absorbed mostly by daily EOPs, not orbits
process ~3 years of GPS orbits with IERS & “fake” models
  difference conventional & EOP-test orbits @ 15 min intervals
  compute spectra of differences for each SV, stack & smooth
  compare spectral differences: input model errors vs. orbital response

## Slide 7: Simulate Impact of Subdaily EOP Errors
04
Frequency (cycles per day)
Power Density (mm2 / cpd)
short- period errors go into orbits
process ~3 years of GPS orbits with IERS & “fake” models
  difference conventional & EOP-test orbits @ 15 min intervals
  compute spectra of differences for each SV, stack & smooth
  compare spectral differences: input model errors vs. orbital response

## Slide 8: Simulate Impact of Subdaily EOP Errors
04
Frequency (cycles per day)
Power Density (mm2 / cpd)
bump in background power – resonance of ~2 cpd subdaily tide errors and GPS orbital period?
process ~3 years of GPS orbits with IERS & “fake” models
  difference conventional & EOP-test orbits @ 15 min intervals
  compute spectra of differences for each SV, stack & smooth
  compare spectral differences: input model errors vs. orbital response

## Slide 9: Spectra of Orbital Responses to Subdaily EOP Errors – Near 1 cpd
at diurnal period, EOP model errors absorbed into orbits, esp cross- & along-track
05
Frequency (cycles per day)
Power Density (mm2 / cpd)
only 2 subdaily tidal lines excited above background orbit noise
unexpected peak in cross-track – probably a beat effect

## Slide 10
at semi-diurnal period, EOP model errors absorbed mostly into orbit radial (via Kepler’s 3rd law)
06
Frequency (cycles per day)
Power Density (mm2 / cpd)
Spectra of Orbital Responses to Subdaily EOP Errors – Near 2 cpd

## Slide 11: Compare Simulated EOP Signatures with IGS Orbits
Basic problem is lack of an independent “truth” for IGS orbits
  but can compute discontinuities between daily orbit sets
  doing so aliases subdaily differences into longer-period signals
  to compare, also compute EOP-induced orbit differences once daily
IGS ORBIT JUMPS
  fit orbits for each day with BERNE (6+9) orbit model
  parameterize fit as plus 3 SRPs per SV component
  fit 96 SP3 orbit positions for each SV as pseudo-observations for Day A
  propagate fit forward to 23:52:30 for Day A
  repeat for Day B & propagate backwards to 23:52:30 of day before
  compute IGS orbit jumps at 23:52:30
SIMULATED EOP SIGNATURES
  difference conventional & EOP-test orbits at 23:45:00 only
Compute IGS orbit jumps over ~5.6 yr, test orbits over ~2.8 yr
07

## Slide 12: Spectra for IGS orbit jumps & EOP-test orbit diffs
08
Frequency (cycles per day)
Power Density (mm2 / cpd)
IGS orbit jumps computed from Berne model fit to adjacent days
  compute spectra for each SV orbit jump set, stack & smooth
  “calibrated” for errors due to (fit + extrapolation) method

## Slide 13: Spectra for IGS orbit jumps & EOP-test orbit diffs
background power follows ~flicker noise on seasonal time scales
bands at 29, 14, 9 & 7 d; peaks offset from expected periods
excitation at harmonics of GPS draconitic year
08
Frequency (cycles per day)
Power Density (mm2 / cpd)
most peaks in ~29, ~14, ~9 and ~7 d bands do not coincide with aliases of subdaily EOP tidal errors for simple daily sampling
peaks at mostly odd harmonics of GPS draconitic

## Slide 14
08
Frequency (cycles per day)
Power Density (mm2 / cpd)
conventional GPS orbits using IERS model
EOP-test orbits using pseudo real-Earth (“fake”) model
spectra of orbit differences computed at 23:45:00
Spectra for IGS orbit jumps & EOP-test orbit diffs
background power is relatively flat, with bumps at seasonal time scales

## Slide 15
offset peaks in ~14, ~9 and ~7 bands due to simple daily sampling of input errors
08
Frequency (cycles per day)
Power Density (mm2 / cpd)
Spectra for IGS orbit jumps & EOP-test orbit diffs

## Slide 16
aliasing subdaily errors responsible for some harmonics of 351 d
  peaks at other harmonics likely caused by aliasing of other errors
08
Frequency (cycles per day)
Power Density (mm2 / cpd)
1st, 3rd, 4th, & 10th harmonics also caused by subdaily EOP errors
Spectra for IGS orbit jumps & EOP-test orbit diffs
other harmonics -- aliasing of other errors

## Slide 17: Summary & Conclusions
09
Harmonics of 351 d pervasive in all IGS products
Simulated orbital response to IERS subdaily EOP tide model errors
  compared conventional orbits to EOP-test orbits at 15 min intervals
Beating of subdaily EOP tides causes spectral differences at other periods
  long-period errors go into EOPs
  short-period errors go mostly into orbits
  bump in background noise at 2 cpd -> resonance with GPS orbital period
Compared IGS orbit discontinuities to EOP-test orbit differences at 23:45:00
  24 h sampling causes subdaily EOP tide errors to alias at ~14, ~9 and ~7 d bands -> peaks offset from expected periods
  peaks at several (mostly odd) harmonics of 351 d
IERS diurnal & semi-diurnal tide model errors are source for subdaily alias and some draconitic errors in IGS orbits

## Slide 18: Questions?

## Slide 19: Additional Slides

## Slide 20: Spectrum of Daily EOP Differences due to Subdaily EOP Tidal Model “Errors”
M2 aliases into PM-x and PM-y; O1 aliases into LOD
1st draconitic harmonic enters PM-x & LOD
Frequency (cycles per day)
Power Density (mas2 or s2/ cpd)

## Slide 21
Frequency (cycles per day)
Power Density (mm2 / cpd)
background power is lower
errors absorbed in all three components
Spectra of Orbital Responses to Subdaily EOP Errors – Near 3 cpd

## Slide 22
Frequency (cycles per day)
Power Density (mm2 / cpd)
same near 4 cpd
Spectra of Orbital Responses to Subdaily EOP Errors – Near 4 cpd