## Slide 1
NGS Products Update
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
Alabama Society of Prof. Land Surveyors
2017 Annual Conference
Pelham, Alabama
October 18, 2017

## Slide 2: Presentation Outline
1. - NADCON 5.
2. - Updated NGS Database.
- OPUS Additions.
4. - OPUS Projects with Bluebooking features.
5. - Questions.

## Slide 3: NADCON - Historical Overview
1989 : NAD 83(1986) released
  1990: NADCON v1.0 released: NAD27 <--> NAD83 (86)
  1990-1997: NADCON v2.1 NAD27 <--> NAD83 (HARN)
  DOS based program, PC based
  1997-2005: NADCON v2.1 NAD27 <--> NAD83 (HARN / FBN)
          Only 19 states had significant shifts from HARN to FBN
          Program expanded to handle FBN changes
          Program still DOS / PC based
  2004: NADCON v4.2 SAME TRANSFORMATIONS
          Efforts made to improve NADCON, JAVA based / Windows driven menus
          Program expanded to handle FBN changes

## Slide 4: Historical Overview Cont.
  2007: GEOCON v1.0 NAD83 (HARN / FBN) <--> NAD83 (2007)
          Transformations from last NAD83, pre-2007 epoch
          Program expanded to provide ability of on-line computations
          Program built for transformations to be relative to “national” adjustment
  2011: GEOCON11 v1.0 NAD83 (2007) <--> NAD83 (2011)
          GEOCON expanded to go with latest NAD83 adjustment
          Program expanded to provide ability of on-line computations
  2012: GEOCON & 11 v1.0 SAME TRANSFORMATIONS
          Program improvements / bug fixes
  2012: GEOCON v2.0 SAME TRANSFORMATIONS
          One combined “GEOCON” program
          HARN & FBN Adjustment results accounted for on state by state basis
          2007 & 2011 Nationwide

## Slide 5: Historical Overview: Problems
Multiple DOS based programs
Lack of documentation
Inconsistent decision making
  Accuracy reporting
  State vs nationwide grids
  Skipping over transformations
“Missteps” made by NGS…
    Too many to list, can read in the report.

## Slide 6: What is NADCON v5.0?
How?
Fresh pull of IDB
New suite of analysis tools
New grids from scratch
No realizations skipped
Make available through Geodetic Toolkit
Transformations and error estimates for any point within a regional boundary, provided through biquadratic interpolation off of a grid
Lat/lon in arcseconds
Ellipsoidal height in meters

## Slide 7: NADCON 5 in the Geodetic Toolkit
CURRENTLY
IN
BETA

## Slide 8
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
X, Y, Z
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83

## Slide 9
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 10
It will “hold” everything.
  GNSS, leveling, gravity, DoV, etc.
  CORS and surveys
  Equipment descriptions & histories, site logs, etc.
  Models
  Guidelines & strategies
It’s a tool, not just an archive of results.
  Searches and filters.
  Statistics
  Plots
  Reports
  - Database will enable ability to track position changes over time
New NGS Database

## Slide 11
It’s common for projects to collect several types of data, e.g. gravity&GNSS, leveling&GNSS, static&kinematic GNSS. They’re related so let’s not treat them as separate.
OPUS-for-everything is a working name for a proposed web app to consolidate and process all data from a project.
“Feeding” the database.

## Slide 12
OPUS-for-everything

## Slide 13
Improved view and features for session / marks table.
Changes to how OPUS Projects defines sessions.
Ability to Add / Delete CORS
Better baseline processing.
Adjustments using NGS software ADJUST.
Auto creation of B-file & G-file.
OPUS-Projects – new Bluebooking features

## Slide 14
OPUS-Projects – new Bluebooking features

## Slide 15
OPUS-Projects – new Bluebooking features

## Slide 16
OPUS-Projects – new Bluebooking features
Notes: https://www.youtube.com/playlist?list=PLsyDl_aqUTdFY6eKURmiCBBk-mP4R10Dx

## Slide 17
More information on all updated products can be found on the NGS website at: www.ngs.noaa.gov

## Slide 18
? ? QUESTIONS ? ?