## Slide 1: Status the Vertical Network in NE and Modernization of the Vertical Datum
USACE Vertical Datums Workshop
Concord, MA
August 11, 2010
Dan Martin
National Geodetic Survey
Vermont State Advisor
Notes: <number>

## Slide 2: NGSIDB BM Status (1st, 2nd order)
 | CT | MA | ME | NH | RI | VT
In NGSIDB | 2599 | 1125 | 5401 | 1092 | 1380 | 2158
Poor | 31 | 24 | 118 | 20 | 19 | 17
Not Found | 281 | 150 | 1048 | 218 | 196 | 363
Not Rec since Monumented | 533 | 254 | 1659 | 216 | 160 | 461
Last Rec ≤ 1990 | 1570 | 584 | 4475 | 689 | 857 | 374
Last Rec ≤ 1980 | 160 | 499 | 3434 | 531 | 277 | 331

## Slide 3: NE Vertical Control

## Slide 4: We need to set more marks
???

## Slide 5
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Weren’t adopted in Canada
  Were determined by leveling from a single point, allowing cross-country error build up
<number>
Why isn’t NAVD 88 good
enough anymore?
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD
Notes: Clarification on the word “convenient” – this is used to mean “there isn’t always a bench mark around when you need one – sometimes you have to find one far away and level from it to your site of interest”
<number>

## Slide 6
NAVD 88 suffers from:
A zero height surface that:
  Has been proven to be ~50 cm biased from the latest, best geoid models (GRACE satellite)
  Has been proven to be ~ 1 meter tilted across CONUS (again, based on the independently computed geoid from the GRACE satellite)
<number>
Why isn’t NAVD 88 good
enough anymore?
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD

## Slide 7
Short term fixes:
  Provide fast methods of expanding NAVD 88 in areas where it is needed
Long term fixes:
  Re-level some / all of NAVD 88
  Replace NAVD 88 bench marks
<number>
Possible ways to fix
NAVD 88
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD

## Slide 8
Short term fix: Height Modernization GPS surveys
  Have provided a fast way to disseminate NAVD 88 bench mark heights to new marks through the use GPS and a constrained least squares adjustment
  NOAA TM NOS NGS 58 and 59 guidelines
  Keeps NAVD 88 useful and accessible, but does not address the majority of problems of NAVD 88 itself
<number>
Possible ways to fix
NAVD 88
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD
Notes: <number>

## Slide 9
Long term fix: Re-level some/all of NAVD 88
Re-leveling NAVD 88 would cost
  between $200 Million and $2 Billion
This wouldn’t fix all of the problems associated with the use of bench marks though
2010 Feb 24 - Briefing for P. Sandifer
Possible ways to fix
NAVD 88
<number>
Notes: Use this slide for public presentations.
<number>

## Slide 10
Long term fix: Replace NAVD 88
Find a method of defining a vertical datum that seeks to fix all of the known issues with NAVD 88
Best option: Define the datum as a given geoid model and realize it through GNSS technology
  GRAV-D
<number>
Possible ways to fix
NAVD 88
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD
Notes: Why is this the best option? Because it addresses:
Different datums existing for CONUS, Hawaii, PR/VI (and, theoretically, Canada, Mexico, and the Caribbean and Central American countries)
Sparseness of bench marks
Error build up as one gets far from an origin point
Financial and personnel realities
Fragility of bench mark network
<number>

## Slide 11
Long term fix: Replace NAVD 88 (continued)
GRAV-D Trade-offs: Datum is only realizable to 2 cm at best at any given point (GNSS error + geoid error)
  However, this is an improvement over NAVD 88 realization error
  The datum could then be disseminated locally through very precise geodetic leveling
<number>
Possible ways to fix
NAVD 88
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD
Notes: Although the idea of a GNSS/geoid vertical datum will mean realization errors generally no better than 2 cm at any given location, this is better than NAVD 88 which has leveling error build up away from Father point. Additionally, the ability to know the datum through a single GNSS receiver at any point of convenience will mean that leveling from existing bench marks to “bring in” the datum will no longer be necessary.
Nothing currently can replace geodetic leveling for precise local differential height dissemination. GRAV-D is not meant to replace leveling of that sort, but instead to provide immediate 2 cm access to the datum anywhere, so that (if necessary) leveling can then be performed very precisely off of that starting point to locations of interest.
<number>

## Slide 12
Example 1: Flood insurance survey
1954-1991: Subsidence
House
BM
House
BM
1954: Leveling Performed
to bench mark
1991: Original 1954 leveling data is used to compute the NAVD 88 height which is then published for this BM
Obviously the true height relative to the NAVD 88
zero surface is not the published NAVD 88 height
H88(published)
H88(true)
NAVD 88 zero height surface
<number>
How will I access the new
vertical datum?
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD
Notes: <number>

## Slide 13
Example 1: Flood insurance survey
House
BM
House
BM
H88(published)
H88(true)
NAVD 88 zero height surface
Using Existing Techniques:
Find bench mark (if you can)
Get published NAVD 88 height
Level off of bench mark
No account for subsidence!
<number>
How will I access the new
vertical datum?
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD

## Slide 14
Example 1: Flood insurance survey
House
BM
House
BM
NAVD 2018(?) zero height surface = geoid
Using Future Techniques:
Find bench mark if you wish, or
set a new one of your choosing
Use GNSS/OPUS to get an
orthometric height in the new datum
Level off of bench mark as needed
Subsidence is accounted for by CORS
and a geoid that are monitored
constantly!
H(2018?) from GNSS/geoid
<number>
How will I access the new
vertical datum?
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD

## Slide 15
<number>
The NGS 10 year plan (2008-2018)
http://www.ngs.noaa.gov/INFO/NGS10yearplan.pdf
The GRAV-D Project
http://www.ngs.noaa.gov/GRAV-D
Socio-Economic Benefits of CORS and GRAV-D
http://www.ngs.noaa.gov/PUBS_LIB/Socio-EconomicBenefitsofCORSandGRAV-D.pdf
Additional Information
Federal Geospatial Summit
11-12 MAY 2010 Silver Spring, MD