## Slide 1
GPS on Bench Marks
Webinar
March 15, 2017
Notes: <number>

## Slide 2
Why?
~27,000 GPS on bench marks used to create GEOID12B
~40,000 at a distance more than 30 km from a BM used in 12B
~300,000 bench marks with SCALED positions
~200,000 bench marks not recovered in 30 years
There are ~430,000 published
First and Second Order Bench Marks
United States and Territories
Notes: <number>

## Slide 4
Who and How?
Surveyors
  OPUS-Share
  OPUS-Projects
Surveyors and Geocachers
  Mark Recovery
  RTK
  Handheld
  Cell phone
Notes: <number>

## Slide 5
Different Heights
H - Orthometric Height (elevation)
h - Ellipsoid Height
N – Geoid Height/Undulation
Notes: <number>

## Slide 6
What is a residual and
how is it calculated?
H ≈ h - N
residual = H + N - h
Causes can be from:
Old/bad leveled height, bad ellipsoid height
Time between heights, stability/movement
Limited data in area
Notes: <number>

## Slide 7
GEOID12B GPS on BM dataset
Rejection Codes (flag)
S
h
H
N
Code S – The State Advisor (now called Regional Geodetic Advisors) recommended it be dropped (subsidence, stability, etc.)
Code h – The residual ellipsoid height errors from the NAD 83 (2011) project indicated that the point was too noisy
Code H – The orthometric height was suspect
Code N – The residual errors during geoid modeling were too high
Notes: <number>

## Slide 8
Dave Zilkoski GPS World article
Analyzing NGS’ GPS on benchmark dataset
Used to make GEOID12B
Discusses evaluating residuals
http://gpsworld.com/analyzing-ngs-gps-on-bench-mark-dataset-used-to-make-geoid12b/
Notes: <number>

## Slide 9
Zilkoski, GPS World
http://gpsworld.com/analyzing-ngs-gps-on-bench-mark-dataset-used-to-make-geoid12b/
Notes: <number>

## Slide 10
28.5 cm difference
30km apart
Zilkoski, GPS World
http://gpsworld.com/analyzing-ngs-gps-on-bench-mark-dataset-used-to-make-geoid12b/
Notes: <number>

## Slide 11
Questions?
GPS on Bench Marks team
ngs.gpsonbm@noaa.gov
March 15, 2017