## Slide 1: Comparison of Extensive Aerogravity Surveys to EGM’s Daniel R. Roman, Simon A. Holmes, Sandra A. Preaux, Theresa M. Diehl, and Vicki Childers
IUGG Session G06S3: World Height System
Melbourne, Australia June 28-July 07, 2011

## Slide 2: 244 Surveys with Significant Biases
<number>
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System Comparison of Extensive Aerogravity Surveys to EGM’s
Saleh et al.
In prep. JG
Notes: The bias from the residuals formed WRT EGM2008 was greater than the SD.
Larger ones can be resolved by GRACE/GOCE.
Smaller surveys cannot and can contribute multi-dm level geoid errors.
These are just the ones I expect to find – not necessarily all of those that exist.
Hence, the need for a robust campaign to detect and fix such systematic problems.
<number>

## Slide 3: Discussion of GRAV-D intent
Goal of a cm-level accurate geoid
Must meld different gravity sources
To do this: must resolve systematic errors in gravity observations
  Compare aerogravity to satellite data
  Constrain aerogravity to GRACE/GOCE
  Combined satellite & airborne gravity field model- somewhere between deg 100-250
  Use aerogravity to fix errors and bridge spectral gap with terrestrial surveys
  Derive shortest wavelengths from high resolution terrain and density models
  Develop a seamless gravity field to 10,800
Rigorously transform to generate geoid heights and DoV’s
<number>
satellite models (GRACE/GOCE)
terrain and density models
airborne and surface gravity
Variance (m2)
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s
Transition Band
Notes: GRACE/GOCE model is used to constrain long wavelength portion of Aerogravity
In turn, Aerogravity is used to fix terrestrial data errors
GRACE/GOCE, Aerogravity, Terrestrial Gravity, and Terrain-Gravity Effects are spectrally merged in a EHM to produce a EGM with local significance to North America.
The further southward we expand the terrestrial data – the better control will be in overlap with a South American model
Countries and regions that do not provide data will be somewhat mitigated by use of GRACE/GOCE & TGE.
<number>

## Slide 4: Cumulative RMS Geoid Differences
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System Comparison of Extensive Aerogravity Surveys to EGM’s
<number>
Notes: First plot of differences. Go over concepts of what is shown.
The basic idea is that lower differences would mean the models were in better agreement – such as is seen through about degree 70 for all three scales/regions.
So the lower a curve stays, the better the comparison and the better the expected agreement, which facilitates melding the data.
All regions rapidly increase above about degree 100. Hence, the idea is to meld in the aerogravity over this span to better account for the gravity field.
<number>

## Slide 5: GPSBM2009
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System Comparison of Extensive Aerogravity Surveys to EGM’s
<number>
NAVD 88
has a known
bias & trend
WRT GRACE

## Slide 6: Cumulative RMS Geoid Differences
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System Comparison of Extensive Aerogravity Surveys to EGM’s
<number>
Notes: This is the first example of a triple difference. The three colors no longer represent different regions but different comparisons instead.
Previously, only the difference between the GOC02S and EGM2008 models was given.
Now there are three models to compare; hence, three separate differences to plot.
The main idea here is that the better agreeing data will come in on the lowest two curves (i.e., blue and green here foe EGM2008).
The bias and trend were removed in the GPSL data to make a harmonic model that fit at the edges with the surrounding EGM (either GOC02S or EGM2008 for each difference).
Even so, there are still long wavelength differences as such a simple trend and bias removal doesn’t adequately describe the problems in the NAVD 88.
This demonstrates why we cannot rely on GPS/leveling by itself to evaluate global models.
However, our interest lies in the band of 100-250, so lets focus there and compare again.
<number>

## Slide 7: Cum. RMS Geoid Diff. > Degree 100
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System Comparison of Extensive Aerogravity Surveys to EGM’s
<number>
Range 100-250
Over CONUS
It is Cumulative
Transition Band
Notes: This image only shows the cumulative differences starting at Degree 100 – as opposed to the previous one which was from Degree 2.
This effectively focuses on the bandwidth of interest (100-250).
Note that EGM2008 (blue and green lines) is lower through about degree 200 but then the GPSL shows better agreement.
We now see very rough agreement through about degree 150, though a much better agreement would be needed to meld these data (preferably under 1 cm).
Nothing definitive can be said about comparison of GPS/leveling except that it does not offer much hope for achieving a cm-level geoid even in combination with satellite data.
<number>

## Slide 8: AK08 Residual Gravity Profiles
<number>
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s
Notes: Generated using the Newton 1.1 Software
The profiles are residual gravity anomalies at altitude in comparison to EGM2008.
Noteworthy are the systematic differences seen from profile to profile with significant lateral extent and amplitude.
It appears that signal is missing from EGM2008 in this region. How to substantiate this? Comparison with GOCE.
<number>

## Slide 9: Cum. RMS Geoid Diff. > Degree 100
<number>
Range 100-250
Over AK08 only
It is Cumulative
Transition Band
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s
Notes: Focusing in on the spectral band of interest (starting at degree 100 to accumulate differences), we now see that AK08 does better.
Unfortunately, GOC02S seems to fare worse – higher two lines (red and green).
The hope was to see better agreement between all three, especially closer to degree 100. This would facilitate merging the data.
<number>

## Slide 10: Band Limited Spectra – Deg. 100-250
GOCO2S – EGM2008
AK08 – EGM2008
<number>
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s
Notes: However, all is not lost. While GOC02S may not yet agree sufficiently yet in the overlap band, it does highlight similar problems in EGM2008.
The earlier slide showing the AK08 residual gravty is now shown as a height anomaly (right image).
The same features present in the residual gravity are seen here as well – and also in the GOC02S differences.
This indicates that the source of these features lies in EGM2008.
There is a greater power in the GOC02S-EGM2008 residuals that might indicate the need for some regularization of the GOCE gravity fields.
<number>

## Slide 11: Error Estimates From 3-way Differences
<number>
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s
Notes: For the transition band (Nmin=100 to Nmax=250), this contains estimates for the cumulate geoid error for each of EGM2008, GOC02S and AK08_v121010, over the AK08 survey area. The AK08 stay below cm-level out to about degree 200.
While this is higher than the stated goal of cm-level accuracy, this is actually an area of significant relief where the goal would be closer to 3-5 cm total error.
So this does look on track for success.
<number>

## Slide 12: DISCUSSION
GRAV-D aims to combine satellite, airborne and terrestrial data for an improved geoid model
Such a model should achieve cm-level accuracy in flat, coastal regions to 3-5 cm in mountains
This presentation compared aerogravity and EGM’s in the transition band (Degree 100-250)
We expected that an AK08/GOC02S comparison would improve upon EGM2008
<number>
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s

## Slide 13: DISCUSSION
However, AK08 conforms more closely with EGM2008 than GOC02S
Note though that GOC02S does confirm some AK08 deviations from EGM2008
The cumulative differences in AK08 suggest that GRAV-D might achieve the desired goals
To enhance combination, it is desirable that GOCE be consistent through degree 200
<number>
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s

## Slide 14: Questions ?
Melbourne, Australia June 28-July 07, 2011
IUGG Session G06S3: World Height System
Comparison of Extensive Aerogravity Surveys to EGM’s
<number>