## Slide 1: A comparison of Airborne Vector Gravimeter Measurements with the Geoid Slope Validation Survey 2014
Ferguson S1, Wang YM2, S. Elieff1, X Li3, S Holmes4, K Ahlgren2 and R Xi1
1 Sander Geophysics Ltd. Canada
2 National Geodetic Survey, NOAA, USA
3 DST Inc. USA
4 SGT Inc. USA
IAG-IASPEI 2017 Kobe | Japan | July 30 - August 5, 2017
<number>
Notes: <number>

## Slide 2: Geoid Slope Validation Survey 2014
    GSVS14 is the second survey conducted by the NGS to test differential accuracy of the gravimetric geoid model.
    It was conducted in Iowa, predominantly along Highway 30, from Denison to Cedar Rapids
    ~ 200 miles (325 km) long, 204 survey benchmarks
    Medium-high, relatively flat area ranging from 740 feet to 1,440 feet above sea level
    gravimetrically complex (Midcontinent Rift)
Notes: <number>

## Slide 3: AIRGrav System Airborne Inertially Referenced Gravimetry
  AIRGrav designed and built specifically for airborne gravity surveying by SGL
  10 years of R&D following by 16 years of survey flying, 12 gravimeters
  Three axis (x y z) gyro stabilized platform,
  three (x y z) accelerometers
  Dual frequency GPS receivers
  Gravity = inertial accelerations – GPS accelerations
  Raw gravity data sampled at 128 Hz
Notes: <number>

## Slide 4: SGL Flight Information
  June 28, 2015
  Repeat line flown West then East
  600 m ellipsoidal (~ 400 m AGL at East end, ~200 m AGL at West end)
  320 km long
  ~ 55 m/s (200 km/h)
  Also flown next day at 2185 m ellipsoidal, 58 m/s, West and East (results not presented here)
Notes: <number>

## Slide 5: AIRGrav Data Processing Steps
  Kalman Filter combination of GPS positions and gravimeter accelerations
  Multiple GPS solutions used to minimize acceleration noise
  3 gravity components are estimated states in the filter
  EGM 2008 used during processing to loosely constrain horizontal component estimates, which are corrupted by uncertainty in gyro drift
  100 s (5.5 km) full wavelength filter applied
Notes: <number>

## Slide 6: East-West Component of Gravity Disturbance
  Blue = West
  Red = East
  Std dev from mean = 0.582 mGal
  W std dev from EGM2008 = 1.27 mGal
  E std dev from EGM2008 = 1.21 mGal
Notes: <number>

## Slide 7: North-South Component Gravity Disturbance
  Blue = West
  Red = East
  Std dev from mean = 0.567 mGal
  W std dev from EGM2008 = 1.35 mGal
  E std dev from EGM2008 = 1.62 mGal
Notes: <number>

## Slide 8: Vertical component of Gravity Disturbance
  Red = West
  Blue = East
  Std dev from mean = 0.418 mGal
  W std dev from EGM2008 = 1.62 mGal
  E std dev from EGM2008 = 1.67 mGal
Notes: <number>

## Slide 9: SGL Geoid Profile Computation
<number>
Method of line-integration (Jekeli and Kwon 2002)
High resolution global gravity model EIGEN6c4 was used in the remove-restore fashion
Downward continuation correction is computed from EIGEN6c4 model
Notes: <number>

## Slide 10: Harmonic Downward Continuation Correction to the Geoid (Eigen6c4, Unit in mm)
<number>
Notes: <number>

## Slide 11
<number>
Notes: <number>

## Slide 12: Collocated points between the SGL flight and GSVS14 traverse
<number>
Notes: <number>

## Slide 13: Geoid height differences (SGL flight – GSVS14) at the collocated points
<number>
Notes: <number>

## Slide 14: Conclusions (1)
3 components of the gravity disturbance observed by AIRGrav agree with EGM2008 around 1.4 mGal.
The geoid height differences between the SGL and NGS - GSVS14 geoid profiles is ±0.9 cm at 10 collocated points, one order better than the results of Serpas and Jekeli (2005) due to the high quality AIRGrav data.
The off-track corrections are critical because of strong gravity field variation in the region.
The harmonic downward continuation correction is in the order of a few cm and has to be applied.
<number>
Notes: <number>

## Slide 15: Conclusions (2)
  Horizontal gravity components (HGC) are a direct measure of the slope of the equipotential surface at flight level
  HGC can be integrated directly to calculate equipotential surface at the flight altitude see Jekeli and Kwon (2002)
  HGC contain wavelengths down to about 5km full wavelength with sub-cm repeatability
  HGC can be combined with satellite models to encompass full spectrum of gravity field
  HGC can be used to verify geoid models
  Similar to the astrogeodetic leveling, HGC can be used in geoid computation along flight lines.
Notes: <number>